## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TI - QoS Considerations for High Rate WPAN MAC]
Date Submitted: [18 September 2000]
Source: [Jin-Meng Ho] Company: [Texas Instruments Incorporated]
Address: [12500 TI Blvd, Dallas, Texas 75243]
Voice:[(214) 480-1994], FAX: [(972) 761-6987], E-Mail:[jinmengho@ti.com]
Re: [Revision 1, three new slides added to clarify new mechanisms for channel access and processes for slaves joining a piconet. Reduced the Galois field from GF (64) to GF(32) for the Reed-Solomon codes.]
Abstract: [This presentation outlines TI’s MAC proposal to 802.15.3 High Rate Task Group]
Purpose: [To communicate the proposal for consideration by the standards team]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Texas Instruments QoS Considerations For High Rate WPAN MAC
Jin-Meng Ho
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243

## Slide 3: Objectives
Access Code
LSB
72
PHY Header
MAC Header
MSDU
PHY Rate
3
24
7
FEC
Minislot Offset
RS(9,5)
Length
Reserved
PHY HEC
3
3
6
8
MPDU
PHY Header
47
47
0-65535
Protocol Version
2
8
8
Type
RS(13,9)
Reserved
MAC HEC
4
3
2+8
16
MAC Header
RA
TA
ACK_BM
Length
3
24
Link ID
2
Sequence Bit Map
8
ACK_BM
Maintain backward compatibility with 802.15.1
Conform with the 802 layering architecture
Support important multimedia applications including VoIP, video, and others defined by TG3
Make efficient use of the high rate PHY, while maintaining simplicity
Improve channel utilization over 802.15.1
802.15.1
802.15.3 with QoS

## Slide 4: Outline
Link management
  enables QoS based link setup for multimedia transport
  activates multiple links between stations for simultaneous multiple services per station
Link control
  provides effective channel access mechanisms for sending VBR and bursty traffic
  enforces QoS contracts and fair bandwidth usage as well as reduces RF interference
Link utilization
  enhances transmission rules to render MAC less sensitive to future PHY and Application layer changes, while better utilizing lower layer services and accommodating various applications
  extends frame structure to accommodate new data rates, coding schemes, and acknowledgment/ retransmission policies

## Slide 5: QoS Support
Traffic taxonomy
  service class
    delay sensitive constant bit rate (DS-CBR)
    delay sensitive variable bit rate (DS-VBR)
    delay tolerant available bit rate (DT-ABR)
  service priority
    DS-CBR: prescheduled (on SCO links)
    DS-VBR: priorities 7-5 (priority 7 = highest priority)
    DT-ABR: priorities 4-0, priority 0--best effort
QoS description
  service class/priority
  token rate/bucket size
  peak rate
  delay/delay variation
  flush timeout (“0” indicates no acknowledgment and “>0” indicates acknowledgment required)

## Slide 6: LMP PDU Extensions
LMP_DS-CBR_link_req: DS-CBR link for transporting DS-CBR session traffic
  Link ID: gives identification of multiple DS-CBR links between two stations
  Direction: indicates whether the link is for transmission from or to the requesting station
  Supervision TO: states the supervision timeout for the link
  DDS-CBR and TDS-CBR : corresponding to DSCO and TSCO, respectively
  dDS-CBR : marks the offset, in minislots, from the slot boundary defined by DDS-CBR
LMP_QoS_link_req: QoS link for transporting DS-VBR or DT-ABR (except best effort) session traffic
  Link ID: gives identification of multiple QoS links between two stations
  Direction: indicates whether the link is for transmission from or to the requesting station
  Supervision TO: states the supervision timeout for the link
  QoS values: specify the QoS expectations of the link
LMP_remove_DS-CBR_link_req, LMP_remove_QoS_link_req
No LMP PDU required with ACL link for transporting best-effort session traffic

## Slide 7: MAC Link Extensions--SCO
SCO links--802.15.1 stations
  between master and slave only
  periodic paired slots for voice traffic only
  only three periods, 2, 4, and 6 slots, allowed
  allocated bidirectionally per voice call
DS-CBR links--802.15.3 stations
  from any station to any other station within same piconet
  periodic minislots for delay sensitive constant bit rate (DS-CBR) traffic
  configurable period as determined by QoS values
  allocated unidirectionally per DS-CBR session
  subject to adjustment by master at/for a given time

## Slide 8: MAC Link Extensions--ACL
ACL links--802.15.1 stations
  single link between master and slave only
  paired slots for asynchronous (best effort) data only
  allocated bidirectionally per frame transmission
ACL links--802.15.3 stations
  best effort link from any station (linkID = 0)
  aperiodic minislots for asynchronous (best effort) data
  allocated unidirectionally per sequence of frame transmissions
QoS links--802.15.3 stations
  multiple links from any station to any other station within same piconet
  quasiperiodic minislots for DS-VBR session traffic
  allocated by permit (separate/piggyback) per quasiperiod
  available minislots for DT-ABR session traffic
  allocated by reservation and permit/multi-permit per data burst

## Slide 9: MAC Extensions
Slot as frame transmissison unit: for legacy stations only
Alternate slot use by master and slave: for legacy stations only
Minislot as frame transmission unit: 1 slot = 8 minislots + 8 IFSs
Frame transmission across multiple minislots: no IFS in between
Acknowledgment and retransmission: sequential and selective
Minislot allocation for traffic transport: controlled by master
Permit and M-Permit control frames: efficient access mechanisms
Direct transmission between stations: provided for 802.15.3 stations
Hold, Sniff, Park modes: slot based for legacy stations
minislot based for 802.15.3 stations
Frame structure: existing format for legacy stations
new format for 802.15.3 stations
Frame format: known prior to transmission/reception
PHY rate selection: Instructed by MAC
802.15.1 PHY if legacy related, 802.15.3 PHY if MAC extended

## Slide 10: 802.15.3 Frame Format
PHY Header: transmitted at the lowest high rate (LHR)
  PHY Rate: modulation technique and bit rate pertaining to MPDU
  FEC: forward error correction scheme pertaining to MPDU
  Minislot Offset: offset of frame start from slot boundary (in minislots)
  Length: length of frame (in minislots)
  PHY HEC: PHY header error check
  RS(12,6): shortened Reed-Solomon code over GF(32)
MPDU: coded and transmitted according to PHY Rate and FEC values in PHY Header
Access Code
LSB
72
PHY Header
MAC Header
MSDU
PHY Rate
3
30
7
FEC
Minislot Offset
RS(12, 6)
Length
Reserved
PHY HEC
3
3
6
8
MPDU
PHY Header
60
105
0-65535

## Slide 11: 802.15.3 MAC Header
MAC Header
  Protocol Version: highest protocol version implemented by the station
  Type: management, control, data-noack, data-ack, etc.
  RA: receiver’s address, i.e., receiver’s AM_ADDR (0 for broadcast)
  TA: transmitter’s address, i.e., transmitter’s AM_ADDR (0 for master)
  REC_FB: reception feedback, comprising a LinkID pertaining to the link being acknowledged, and a Ack Bit Map wherein a “1”/”0” in the nth (n = 0-7) position indicates the positive/negative reception of a frame sent in the nth minislot (numbered from the point when no frames transmitted from the link with LinkID are pending acknowledgment) (no link shall have any new frames transmitted if it has 8 transmitted frames pending acknowledgment)
  Length: length of MSDU in bits
  MAC HEC: MAC header error check
  RS(21, 11): shortened Reed-Solomon code over GF(32)
Protocol Version
2
8
9
Type
RS(21, 11)
Reserved
MAC HEC
4
3
2+8
16
MAC Header
RA
TA
REC_FB
Length
3
50
LinkID
2
Ack Bit Map
8
REC_FB

## Slide 12: 802.15.3 Management Frames
Management frames (Type 0000): for sending LMP PDUs
  Opcode: management frame opcode as defined by 802.15.1 spec
  MSDU Body: LMP message
  CRC/FEC: error checking and correction, coded according to FEC value in PHY Header
Opcode
8
MSDU Body
4
m
Management frame MSDU
CRC
n
FEC

## Slide 13: 802.15.3 Control Frames
Control frames (Type 0001): for sending link control info
  Subtype: 0001 for Permit frames, 0010 for M-Permit frames
  TX_Mini (in minislots):
    maximum transmission time for the station addressed by the Permit frame
    maximum transmission time for the stations mapped in the M-Permit frame
  ADDR_BM: address bit map, wherein a “1” (”0”) in the nth (n=0-7) position indicates the station with an AM_ADDR value of n is (not) given a transmission opportunity by this M-Permit frame
  CRC/FEC: error checking and correction, coded according to FEC value in PHY Header
Subtype
4
5
m
Permit frame MSDU
CRC
n
FEC
TX_Mini
Reserved
7
Subtype
4
ADDR_BM
5
m
M-Permit frame MSDU
CRC
n
FEC
TX_Mini
Reserved
7
8

## Slide 14: 802.15.3 Data-NoAck/Data-Ack Frames
Data-NoAck/Data-Ack frames (Type 0100/0101): for sending L2CAP messages requiring no/ acknowledgment
  LinkID: identification of the link between transmitting/receiving stations
  Seq_L: sequence number for identifying MAC frames of the same L2CAP frame (frames received with same Seq_L are discarded but acknowledged if required)
  Seq_M: minislot number for identifying transmitted frames pending acknowledgment (when all frames transmitted are acknowledged, the transmitting station restarts Seq_M from 0)
  TX_Mini: piggybacked permit of maximum transmission time (in minislots) allowed for the slave receiving this frame
  More: piggybacked indication by sending slave of whether there are (no) more data waiting at this slave, via a 1 (0) in the first bit, and if so, the highest service priority of the waiting traffic, via the next 3 bits
  CRC/FEC: error checking and correction, coded according to FEC value in PHY Header (no necessarily appearing as shown)
LinkID
3
5
m
Data-NoAck/Data-Ack frame MSDU
CRC
n
FEC
Seq_L
Reserved
5
Seq_M
TX_Mini/More
L2CAP data
2
5
0 - (65515-m-n)

## Slide 15: Channel Access Mechanisms
DS-CBR traffic
  prescheduled, and sent periodically, through the setup of DS-CBR link by LMP_DS-CBR_link_req
DS-VBR traffic
  from station to master/station: transmitted after quasi-periodic Permit/M-Permit frames sent by master, with More field used to piggyback indication of waiting data
DT-ABR traffic
  directly transmitted as guided by Permit and M-Permit frames send by master, or through reservation as done by piggyback using More field or by use of Permit and M-Permit frame
Permit/M-Permit frames
  sent by master as often as warranted by QoS contracts indicated through LMP_QoS-link_req messages, and in view of channel bandwidth availability
Channel bandwidth usage/allocation
  determined by master based on QoS values of admitted traffic as indicated through LMP_QoS-link_req messages, or on best effort in the case of no link setup

## Slide 16: Frame Transmission Illustrations
Datn 0-1
Datn 1-0
Datn 0-1
Datn 0-1
Datn 1-0
Datn 1-2
Datn 1-0
Datn 2-1
Datn 1-2
Datn 2-1
Datn 1-2
Datn 2-1
Datn 0-#
Datn 0-#
Datn 0-#
Datn 0-#
Datn 0-#
Datn 0-#
Permit 4
Data 4-3
M-Permit
Data 1-0
Data 3-4
Data 4-0
Permit 1
Data 1-0
Data 0-3
Data 3-0
Permit 4
Data 4-0
Data 0-4
Data 4-3
TX-alter
Datn 1-2
Datn 0-#
Datn 0-#
Datn 0-1
M-Permit
Data 2-6
Data 4-0
Data 6-2
Data 0-1
Permit 2
Data 2-6
Permit 3
Data 3-4
Data 4-3
Permit 4
Data 4-0
Data 0-1
Permit 6
Data 6-2
Permit 4
Data 0-1
Data 0-2
Data 2-6
Data 0-3
Slot 2m
Slot 2m + 1
Slot 2m + 2
Slot 2m + 3
Slot 2m + 4
Slot 2m + 5
Slot 2m + 6
Slot 2m + 7
Slot 2m + 8
Slot 2m + 9
Slot 2m + 10
Slot 2m + 11
Datn 0-1: DS-CBR Data_NoAck frame (voice) from master to slave 1 on DS-CBR link
Datn 1-0: DS-CBR Data_NoAck frame (voice) from slave1 to master on DS-CBR link
Datn 1-2: DS-CBR Data_NoAck frame (voice) from slave 1 to slave 2 on DS-CBR link
Datn 2-1: DS-CBR Data_NoAck frame (voice) from slave 2 to slave 1 on DS-CBR link
Datn 0-#: DS-CBR Data_NoAck frame (voice) broadcast from master on DS-CBR link
Datn 0-#: DS-CBR Data_NoAck frame (video) from master to slave 1 on DS-CBR link
Data 4-3: DS-VBR Data_Ack frame (video) from slave 4 to slave 3 on QoS link
Data 0-m: DT-ABR Data_Ack frame (data) from master to slave m on QoS link
Data n-0: DT-ABR Data_Ack frame (data) from slave n to master on QoS link
Data p-q: DT-ABR Data-Ack frame (data) from slave p to slave q on ACL link
Data 4-0
Data 4-3
Data 4-3
Data 4-3
(1,
1/2/3/4)
(2,
2/4/6)
(2)
(1)
(1)
(2)
(3)
(1)
(1)
(6)
(1)
(4)
(2)

## Slide 17: Frame Transmission Descriptions
Datn 0-1, Datn 1-0, Datn 1-2, Datn 2-1, Datn 0-#, Datn 0-#:
DS-CBR Data_NoAck frames prescheduled and sent on DS-CBR links
Permit 4 (TX_Mini = 2) on slot 2m:
Permit sent by master to slave 4 for 2 minislots of transmission time
Data 4-3 beginning on slot 2m:
DS-VBR Data_Ack frame (video) sent by slave 4 to slave 3 in response to preceding Permit 4
M-Permit (TX_Mini = 1, ADDR_BM = 01111000) on slot 2m+1:
Multi-permit sent by master to slaves 1, 2, 3, and 4 for 2 minislots each of transmission time
Data 1-0, Data 3-4, Data 4-0 on slot 2m+1:
Data_Ack frames (data) sent by slaves 1, 3, and 4 in response to preceding M-Permit
No data sent by slave 2 even though it could have used the minislot after slave 1
Data 0-3 (TX_Mini = 2) on slot 2m+2:
Data_Ack frame (data) sent by master to slave 3 with a piggybacked permit of 2 minislots
Data 0-4 (TX_Mini = 3) on slot 2m+3:
Data_Ack frame (data) sent by master to slave 4 with a piggybacked permit of 3 minislots
Data 4-3 (More = 1001) and Data 4_0 (More =0000) on slot 2m+3
Data_Ack frames (one for video and one for data) sent by slave 4 in response to preceding piggybacked permit, with a piggybacked indication of more traffic having priority as high as 1 (DT-ABR) and no more traffic, respectively, waiting at this slave for transmission
Datn 0-1
Datn 1-0
Datn 0-1
Datn 1-2
Datn 2-1
Datn 1-2
Datn 0-#
Datn 0-#
Datn 0-#
Datn 0-#
Permit 4
Data 4-3
M-Permit
Data 1-0
Data 3-4
Data 4-0
Permit 1
Data 1-0
Data 0-3
Data 3-0
Permit 4
Data 4-0
Data 0-4
Data 4-3
TX-alter
Datn 1-2
Datn 0-#
Datn 0-#
Datn 0-1
Slot 2m
Slot 2m + 1
Slot 2m + 2
Slot 2m + 3
Slot 2m + 4
Slot 2m + 5
Data 4-0
(1,
1/2/3/4)
(2)
(1)
(1)
(2)
(3)

## Slide 18: Frame Transmission Descriptions
Datn 0-1
Datn 1-0
Datn 1-0
Datn 2-1
Datn 1-2
Datn 2-1
Datn 0-#
Datn 0-#
M-Permit
Data 2-6
Data 0-1
Permit 2
Data 2-6
Permit 3
Data 3-4
Data 4-3
Permit 4
Data 4-0
Data 0-1
Permit 6
Data 6-2
Permit 4
Data 0-1
Data 0-2
Data 2-6
Data 0-3
Slot 2m + 6
Slot 2m + 7
Slot 2m + 8
Slot 2m + 9
Slot 2m + 10
Slot 2m + 11
Data 4-3
Data 4-3
Data 4-3
(2,
2/4/6)
(1)
(1)
(6)
(1)
(4)
(2)
M-Permit (TX_Mini = 2, ADDR_BM = 00101010) on slot 2m+6:
Multi-permit sent by master to slaves 2, 4, and 6 for 2 minislots each of transmission time
Data 2-6, Data 4-0, 6-2 on slot 2m+6:
Data_Ack frames (data) sent by slaves 2, 4, and 6 in response to preceding M-Permit
Each slave may piggyback acknowledgment (in REC_FB field) to frames sent to it
Each slave may also piggyback information of traffic (in More field) waiting at its transmit queues
Slave 4 uses only one minislot here to send its buffered traffic, but the following slave(s) ignore this.
Data 0-1 (TX_Mini = 0) on slot 2m+7:
Data_Ack frame (data) sent by master to slave 1 with a piggybacked permit of no minislots
Data 6-2
Data 4-0
Channel access for bursty traffic can be handled efficiently through M-Permit frames sent by Master and More field piggybacked in frames sent by slaves:
Master send, without wasting much channel bandwidth, an M-Permit frame, whenever bandwidth is available, that allocate a small number of minislots to slaves that are active but have not sent data on a periodic basis.
Those slaves that have data to send use the More field to indicate more data buffered
Master allocates additional minislots to such slaves via Permit or M-Permit frames.

## Slide 19: Piconet Joining Processes
1. Master regularly (subject to bandwidth availability) sends Permit frames containing a broadcast RA field (=000) and a TX_Mini field whose value is an integer multiple of the number of minislots, i, needed for transmitting an ID frame at the lowest transmission rate mandated for an 802.15.3 device.
2. A slave seeking to join a piconet waits until receiving such a Permit frame; it then partitions the minislots specified by the TX_mini field into a number of adjoining groups each of i consecutive minislots, and then sends its ID frame into a randomly chosen group of minislots out of those groups.
3. If master successfully receives an ID frame out of one of the groups of minislots defined above, it will begin the process of admitting that slave into the piconet.
4. If master detects one or more collisions in the said groups of minislots, it will, within a preset time limit, send another Permit frame containing a broadcast RA field (=000) and a TX_Mini field whose value is chosen for a rapid resolution of the collisions.
5. 2-4 is repeated until no more collision is detected or master decides to suspend the issuance of Permit frames as defined above even though there may be devices still attempting to join the piconet.

## Slide 20: Summary
This presentation has, taking into account backward compatibility and conventional layering principle, introduced
1. QoS parameters to describe QoS traffic
2. LMP_DS-CBR_link_req and LMP_QoS_link_req LMP messages to set up MAC links for the transport of CBR and other QoS traffic
3. Minislots and their organization in the context of slots as presently defined to reduce the transmission time of management, control, and data frames, and to facilitate channel bandwidth allocation, in response to increasing PHY rates
4. Frame formats that comprise well specified PHY and MAC headers as well as component fields, which together provide a new foundation for an effective QoS MAC that can operate on a variety of PHYs
5. Management, Control, and Data_NoAck/Data_Ack frames for effective management, control, and utilization of the channel bandwidth in support of QoS transport
6. Channel access mechanisms that can efficiently handle both delay-sensitive and delay-tolerant traffic, of CBR, VBR, or bursty type
7. Piconet joining processes for 802.15.3 devices that are highly efficient