## Slide 1
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Physical Layer proposal for the High Rate 802.15 Standard]
Date Submitted: [July 2000]
Source: [Walt Davis] Company: [Motorola]
Address: [1303 E. Algonquin Road, Fourth Floor, Schaumburg, IL 60196]
Voice:[(847) 576-3311], FAX: [(847) 576-5292], E-Mail:[Walt.Davis@email.mot.com]
Re: [ PHY layer submission, in response of the Final Call for Proposal ]
Abstract: [This contribution is a WPAN proposal for a high performance 30 Megabit per second, 5GHz system that addresses the requirements of a large number of wireless multimedia applications. The system is based on proven, low cost RF technology at the Physical Layer level, and on an extension of the BlueTooth TDMA protocol at the MAC layer. It provides for real-time transport of a number of real-time data streams while offering the advantages of quick time to market via the use of proven technology and low system cost due to the use of simple receivers and transmitters. It also provides for the low power drain that is essential for personal portable applications by making extensive use of protocol based battery saving techniques.]
Purpose: [Response to WPAN-HRSG Call for Applications]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Motorola, Inc.
Physical Layer
Submission to the IEEE P802.15
Wireless Personal Area Networks
High Rate Working Group
Notes: Page <number>
<header>
<date/time>

## Slide 3: Wireless Multimedia Application
Basic Requirement:
Enable the high-speed, wireless interconnection of consumer devices to support the transfer of large multi-media data files and high speed, real-time data streams.
Typical Applications:
  Video distribution from set-top boxes to remote
  TV sets, VCR to portable screen, computer to projector, etc.
  In-home Internet connectivity from set-top boxes to
  personal devices and computers
  Wireless video camera linkages
  Wireless Audio and Video distribution for
  Home Theater Systems

## Slide 4: Wireless Multimedia Application
Basic Requirement:
Enable the high-speed, wireless interconnection of consumer devices to support the transfer of large multi-media data files and high speed, real-time data streams.
Applications:
  Low cost, high speed networking
    Communications devices to peripherals
    Computer to computer
    Computer to printer
    Digital camera to printer
    Appliance to appliance

## Slide 5: Application Requirements
Physical Layer
• Operating Frequencies
• RF Range / Coverage
• Number of channels
• Channel Noise Immunity
  Error Tolerance
  Delay Spread
  Tolerance
• Security
• Co-existence / compatibility
with other systems
• Operating frequency /
license requirements
System
• Transparent System
Operation
• QoS
• Data Throughput Rate
• System Range / Coverage
• Cost
• Security
• Low Power
• Low Complexity
• Low Development risk
• Time to Market
Categories
MAC Layer
• QoS
• Security
• Low Complexity
• Low Development risk
• Cost

## Slide 6
1. System Operation:
Direct FM, Half-Duplex, isochronous operation that supports real-time multimedia data transport among up to 63 nodes. The system supports a mesh topology that allows peer-to-peer, point-to-point and point-to-multipoint operation.
2. Operating Frequencies:
5.15 to 5.35 GHz (Unlicensed operation)
3. Modulation Technique:
4-Level Direct FM with + 7.5 MHz peak deviation
4. Modulation Rate:
15 MegaSymbols per second of Four Level FM = 30 Megabits per second.
Description of Physical Layer Submission

## Slide 7
Why Direct FM?
Description of Physical Layer Submission

## Slide 8
Description of Physical Layer Submission
Complex Modulation Schemes Require High S/N Ratios

## Slide 9
Description of Physical Layer Submission
Complex Modulation Schemes Require High S/N Ratios

## Slide 10
Description of Physical Layer Submission
Direct FM Operates at Low S/N Ratios

## Slide 11
Description of Physical Layer Submission
Direct FM Operates at Low S/N Ratios

## Slide 12
1. System Operation:
Direct FM, Half-Duplex, isochronous operation that supports real-time multimedia data transport among up to 63 nodes. The system supports a mesh topology that allows peer-to-peer, point-to-point and point-to-multipoint operation.
2. Operating Frequencies:
5.15 to 5.35 GHz (Unlicensed operation)
3. Modulation Technique:
4-Level Direct FM with + 7.5 MHz peak deviation
4. Modulation Rate:
15 MegaSymbols per second of Four Level FM = 30 Megabits per second.
Description of Physical Layer Submission

## Slide 13
5. .Signal Bandwidth:
12 MHz at –20 dB:
-20 dB BW
= ~ 12 MHz
Spectrum of Transmitted Signal
+7.5 MHz
-7.5 MHz
+15 MHz
-15 MHz
Description of Physical Layer Submission

## Slide 14
6. .Number of Channels:
13 channels spaced 15 MHz
Description of Physical Layer Submission

## Slide 15
7. .Antenna System:
A simple array of very low cost directional antennas that can be etched patterns on the transceiver printed circuit board or substrate. (At 5 GHz, a quarter wave stub is 0.6 inches long)
8. Delay Spread Protection:
The combination of the low capture ratio (5 to 6 dB) and the directional selectivity provided by the antenna system provide excellent immunity to multi-path generated delay spread.
~90 Beam Width
Example of Directional Antenna Patterns
Description of Physical Layer Submission

## Slide 16
9. Receiver Architecture:
Figure 5
Commercialized 5.15-5.35 GHz Transceiver
A
Transceiver
5.15-5.35 GHz
T-R
Switch
Antenna
Selector
A
Limiter
•
•
Discriminator
Level Sensor
Recovered
Data
A
A
•
•
•
Frequency
Synthesizer
A
VCO
(f-280)/2
X2
Ref
osc
Channel
Setup
A
A
VCO
f/2
Modulation Input
A
Receiver
Transmitter
280 MHz
Filter
280 MHz
IF Demodulator
Power
Amplifier
Description of Physical Layer Submission

## Slide 17
9. Receiver Architecture:
Figure 6
Cost Reduced 5.15-5.35 GHz Transceiver
A
Transceiver
5.15-5.35 GHz
T-R
Switch
Antenna
Selector
•
•
ZERO I.F.
Amp/Filter/Demod.
Recovered
Data
A
A
•
•
•
Frequency
Synthesizer
A
X2
Ref
osc
Channel
Setup
A
VCO
f/2
Modulation Input
A
Receiver
Transmitter
Power
Amplifier
Description of Physical Layer Submission

## Slide 18
10. Receiver Sensitivity:
–90 dBm for 1E-4 BER
11. Transmitter Architecture:
  Conventional direct FM
12. Transmitter Power Output:
  200 milliwatts maximum
13. Operating System Range:
>10 meters with <20 milliwatts output power for clear line-of-site operation
>10 meters with <200 milliwatts output power for transmissions through obstacles
Description of Physical Layer Submission

## Slide 19
Description of Physical Layer Submission
Channel
Source
Encode
Channel
Encode
Tx_Signal
Modulate
Encrypt
Transmit
Rx_Signal
Channel
Decode
Source
Decode
Receive
Demodulate
Decrypt
Data Flow Model

## Slide 20
Manufactureability - Commercial 5 GHz System
5 GHz Transceiver
MAC and I/O