## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 00205r2P802.15_TG3-MAC-Proposal-for-High-Rate-WPAN
Date Submitted: 27 October, 2000
Source: Patrick Kinney Company Intermec Technologies
Address 550 Second St. S.E., Cedar Rapids, IA, USA
Voice:+1.319.369.3593, FAX: +1.319.369.3299, E-Mail:pat.kinney@intermec.com
Re: Revision to the earlier proposal for TG3 MAC
Abstract: Presentation format of Proposed MAC for 802.15.3
Purpose: For consideration as the baseline of the MAC for 802.15.3
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: TG3 MAC Proposal for High Rate WPAN
This MAC proposal has been improved from its earlier submission. Significant changes include a QoS mechanism from A Heberling’s MAC proposal, Selective rejection ACKs, RTS/CTS is now optional, and revised numbers for throughput and current drain.
Document 00/218r1 provides the technical backup for this presentation.

## Slide 3
Targeted Applications for PicoLink (1Mb/s)
Cable replacement (point to point)
  Barcode scanner to portable/mobile computer
  Printer to portable/mobile computer
Personal area connectivity (peer to peer)
  hand held computer to numerous peripheral devices including scanners, printers, wide area network radios, etc.
PEN*KEY 6500
Picking Application
Scan Item 000123456
Description: Tide Liq., 50oz.
Scan Location: BAY 31
Enter Quantity: 40
Take to Location: Dock 5A
Keyboard
Keypad
Help
Exit

## Slide 4
High Rate WPANs
Existing WPANs
Newly Targeted Applications

## Slide 5
WPAN Solution Requirements
Very low cost
Low power consumption
Small size
Minimal attach/detach times
Interference immunity
Ease of use
Standardized interfaces
Unlicensed, international usability

## Slide 6
PicoLink™ Advantages
Proven: Shipping for two years in a 1 Mb/s WPAN
Very low cost
Low power consumption
Small size (ASIC gate count and F/W size)
Fast response times, quick attach times
Superior trade-off between response time and current drain
Ease of use
Temporary split networks
Adaptability to different usage scenarios (PAN & Infrastructured)

## Slide 7
Picolink™ Configurations
Personal
Area
Network
Infrastructured
Network
Access Point
PowerShip terminal
Astra Printer
DADS Terminal
EST
PowerPad
Ethernet

## Slide 8: Picolink™ Configurations
Personal
Area
Network
PowerShip terminal
Astra Printer
DADS Terminal
EST
PowerPad
Personal Area Network (PAN; Peer-to-Peer)
  Multiple Networks co-habitate (20 or more have been tested at current 1 MHz data rate, but this attribute is strongly dependent upon the PHY)
  Dynamic PAN and device IDs with network initiation
  Network maintained devices coming and going
  Temporary devices and Networks also supported

## Slide 9
Picolink™ Configurations
Limited Infrastructured
Network
Access Point
Ethernet
Limited Infrastructured Network
  Main device (access point) typically has power at all times (for fast access)
  Support for up to 10 devices
  Ethernet access points with higher layer protocol

## Slide 10: MAC Protocol Criteria
Transparent to Upper Layer Protocols
Ease of Use
  Unique 48 bit address
  Simple network join/un-join procedure
  Device registration
CSMA:
  Proven in current wired and wireless networks
  Superior performance in high bandwidths

## Slide 11: MAC Protocol Criteria
RTS/CTS: to avoid the hidden node issue, an optional RTS/CTS mode is supported with the Contention Access Period
ACK: To support a virtual error free delivery system ACKs are supported. Selective rejection is offered to reduce the ACK overhead
Peer to peer transmission reduces bandwidth requirements for non-master data transfers.

## Slide 12: MAC Protocol Criteria
Delivered Data Throughput
  For the proposed raw data rate of 22 Mbps a throughput of 20 Mbps is anticipated (e.g. large transfer, Rx-Tx to 10µS, 1024 byte frames)
Fast Response
  Average response time for small packets is under 5 mS for current 1 Mbps system
  Response time for TG3 will be dependent upon PHY and Superframe configuration

## Slide 13: MAC Protocol Criteria
Data Transfer Types
  Asynchronous
    short response times
    CSMA/CA; collision sense/collision avoidance (similarities to 802.11 and 802.3)
  Isochronous: time bounded delivery using the Heberling MAC’s QoS mechanism
  Mixed traffic load management
    slots for Async and Isoch

## Slide 14: MAC Protocol Superframe
Maintain station synchronization
coordinate sleep cycles
FH coordination (if necessary)
Asynchronous slot/cycle assignments
Isochronous slot/cycle assignments
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period

## Slide 15: MAC Protocol Superframe: Contention Access Period
All control messages such as:
attachment requests
authentication responses
slot cycle requests
In addition short data frames could be sent in this period
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period

## Slide 16: MAC Protocol Superframe: Contention Free Period
Asynchronous slots are composed of cycles assigned to stations
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period

## Slide 17: MAC Protocol Criteria
Topology
  Minimum number of active connections
    Up to 10 nodes per network
  Ad hoc network
    Fully supported
    Temporal ad-hoc networks are also supported
  Access to portal
    Any node on the network can provide a portal to another network
    Multiple portals are possible

## Slide 18: MAC Protocol Criteria
Reliability
  Master redundancy
    in a peer to peer network the “master” merely coordinates the scheduled services. Data transfers occur between the desired nodes without assistance from the “master”
    Any node on the network can assume the master(coordinator) role either by request from the master or by disappearance of the master

## Slide 19: MAC Protocol Criteria
Reliability (cont’d)
  Loss of connection
    The proposed system does provide a method for detection and recovering from the loss of a link
    System has options allowing it to conserve current drain by allowing periodic searches for link re-establishment rather than continuous searches

## Slide 20: MAC Protocol Criteria
Power Management Types
  Sleeping
    Multiple time increments for sleeping are selectable, e.g. 1,2…beacon periods
  Wakeup
    Schedule service intervals allow the MAC to adapt to various PHY wakeup times
  Polling
    Beacons are scheduled and allow the nodes to wakeup listen for any pending messages and then go back to sleep if there are no messages

## Slide 21: MAC Protocol Criteria
Power Consumption of MAC controller
  State .8µ .25µ .18µ
  Transmit (mA): 30 18 9
  Receive (mA): 30 18 9
  Sleep (µA): 30 18 9
  Other Power Consumption Features
    Programmable search duty cycle during loss of connect
    Slave to slave links require less energy in a Peer to Peer topology than a Master/Slave topology

## Slide 22: MAC Protocol Criteria
Security
  Authentication: Propose a Public Key method
  Privacy: Propose the use of the 802.15.1 algorithm
Quality of Service
  Time bounded algorithm from Heberling’s MAC using slot cycle TDMA

## Slide 23: MAC Protocol Criteria
Cost/Complexity
  Baseband controller
    functionality described for the HR MAC is estimated to be 10,000 gates.
  Code size
    under 32 Kbytes w/o proposed enhancements