## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Multi-Rate QAM Physical Layer (8-40 Mbps) Proposal for High Rate WPA N
Date Submitted: 20 October 2000
Source: Jeyhan Karaoguz
Address: Broadcom Corporation, 16215 Alton Parkway, Irvine, CA 92619
Voice: 949 585 6168
E-Mail: jeyhan@broadcom.com
Contributors: Chris Hansen, Brima Ibrahim, Reza Rofougaran, Nambi Seshadri, Broadcom Corp.
Re: Call for Proposals for IEEE P802.15.3 High Rate Task Group
Abstract: This proposal describes a multi-rate QAM physical layer operating in the unlicensed 2.4 band. The proposed system provides adaptive data rates from 8 Mbit/sec to 40 Mbit/sec depending on application requirements and channel conditions.
Purpose: To be considered as a candidate PHY layer technology for IEEE P802.15.3 specification
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Presentation Outline
Original PHY layer proposal
  Frequency Hopping Multi-Rate Quadrature-Amplitude-Modulation with Trellis Coding (FH QAM-TCM)
  8, 12, 16, 20 Mbit/sec PHY layer data rates
  5 MHz signal bandwidth
Added enhancements to achieve higher data rates
  10 MHz signal bandwidth, but no frequency hopping
  Addition of 24, 32, 40 Mbit/sec data rates
  8 independent fixed channels in 2.4 GHz band
  Same original QAM-TCM scheme
Simulation results
System architecture and complexity
Updated evaluation criteria

## Slide 3: Original PHY Layer Proposal
1
2
3
Hopping sequence #
. . .
5 MHz
2400 MHz
2483.5 MHz
5 MHz bandwidth Frequency Hopping (FH) transmission system operating in 2.4 GHz band
Multi-Rate Quadrature Amplitude Modulation with Trellis Coding

## Slide 4: Original PHY Layer Proposal
Takes advantage of recently amended FCC 15.247 rules that allow 5 MHz bandwidth Frequency Hopping systems
Adjustable transmit power 0 dBm to 20 dBm allowing scalability in range and data rates
1600 hops/sec FH system for backward compatibility with 802.15.1/Bluetooth devices
Minimum Mean Squared Error Decision Feedback Equalization (MMSE-DFE) receiver to combat delay spread
Variable length coded frame size (suitable due to TCM)
PHY layer design based on extensive field test results (up to 17 m indoor coverage) conducted by UCLA Electrical Engineering Department

## Slide 5: Added Enhancements
A new “non-hopping” 10 MHz bandwidth transmission mode (compliant with FCC 15.249 rules, up to +8.8 dBm transmit power)
New transmission mode enables three higher data rates: 24, 32, 40 Mbits/sec
10 MHz
2400 MHz
2483.5 MHz
16/32/64 QAM-TCM
Channel
1
Channel
3
Channel
4
Channel
5
Channel
2
Channel
6
Channel
7
Channel
8

## Slide 6: Added Enhancements
Higher data rates are achieved by increasing the modulation rate from 4 Mbaud to 8 Mbaud (10 MHz bandwidth with 25% excess bandwidth)
8 simultaneous full throughput high rate WPANs are supported in the 2.4 GHz band
At higher data rates (24, 32, 40 Mbit/sec), transmission efficiency is increased by eliminating fast frequency hopping
  Tx-Rx and Rx-Tx turnaround times are reduced by a factor of ten
Maintained all other features of our original proposal, i.e.:
  16/32/64 QAM with trellis coding
  MMSE-DFE based receiver
  Variable length trellis-coded frame size

## Slide 7: Physical Layer Summary
Enhanced multi-rate QAM-TCM proposal combines the robustness and extended range of 5 MHz bandwidth frequency hopping system with the transmission efficiency of non-hopping 10 MHz bandwidth system
Multi-Rate QAM-TCM PHY layer operates at modulation rates of 4 and 8 Mbaud with signal bandwidths of 5 and 10 MHz, respectively
Enhanced proposal supports data rates ranging from 8 Mbit/sec to 40 Mbit/sec depending on application, range, and channel conditions
Simple 8-State/2-D TCM applied to 8-PSK, 16/32/64 QAM signal constellations (spectral efficiencies of 2/3/4/5 bits/symbol)
MMSE-DFE equalization at the receiver to combat delay spread
Signal acquisition and equalization are both based on a short preamble

## Slide 8: Signal Constellations
16-QAM TCM (12 Mbit/s)
32-QAM TCM (16 Mbit/s)
64-QAM TCM (20 Mbit/s)
8-PSK TCM (8 Mbit/s)

## Slide 9: 8-State Multi-Rate TCM Encoder
T
+
T
T
+
8-PSK
Encoder
16-QAM
32-QAM
64-QAM
2-D Output
to Pulse Shaping
Filter
C
bo
b1
b2
b3
b4
2,3,4,5
bits/symbol
8/16/32/64 QAM TCM
Mode Selection

## Slide 10: 8-State/ 2D Trellis Coded Modulation
D0
D4
D2
D6
D1
D5
D3
D7
D4
D0
D6
D2
D5
D1
D7
D3
D2
D6
D0
D4
D3
D7
D1
D5
D6
D2
D4
D0
D7
D3
D5
D1
D0
D4
D2
D6
16-QAM Set Partitioning
D0
D4
D2
D6
D1
D5
D7
D3
C0
C2
C1
C3
B1
B0
8-State Trellis Diagram

## Slide 11: Coding Gains for 8-State QAM TCM

## Slide 12: Variable Length Frame Format
Preamble: Low overhead preamble for fast packet-by-packet MMSE-DFE equalization
Tail: Beneficial for reaching a known TCM state at the end of a burst transmission
Preamble
CRC
Tail
Message Body
3 T
64 T

## Slide 13
Delay Spread Performance
Exponential decaying Rayleigh fading channel
  Per IEEE P802.15-00/110r12 section 4.8.1
  Symbol time (inverse of modulation rate) = 125 ns, channel sampling time = 31.25 ns (1/4 of symbol time)
  Channel duration is 1 usec (32 samples)
Simulation Parameters
  Feed-forward equalizer spans 8 symbol intervals, feedback filter spans 6 symbol intervals
  1000 random channels generated for each RMS delay spread simulated
  Various RMS delay spreads up to 105 nsec were simulated
  Average received signal level is -59 dBm (14 dB higher than minimum required sensitivity)
  Frame size is 4096 bits
Results
  Proposed Frequency Hopping QAM PHY layer easily outperforms the 25 nsec delay spread tolerance requirement
  Operating at 40 Mbit/s, better than 1% frame error rate is achieved for greater than 95% of the channels simulated for up to 105 nsec RMS delay spread

## Slide 14
MMSE-DFE Delay Spread Performance

## Slide 15
MMSE-DFE Delay Spread Performance

## Slide 16: Multi-Rate QAM TCM Transmitter
Randomizer
and CRC
Generator
Preamble
Generator
TCM
Encoder
Transmit Control
I/Q Modulator
DACs and LPFs
Inter-
polator
X 2n
Pulse
Shaping
Filter
X 2n
Data
Control
IF and RF Stages

## Slide 17: High-Speed Wireless Indoor Prototype System
2.4 GHz 5 Mbaud multi-mode QAM (4, 16, 64-QAM) built by UCLA researchers
System implementation and distortion issues such as real-time adaptive equalization, timing and carrier recovery, inter-modulation distortion, and phase noise are reflected in the measurements
Prototype system description and results are published in the IEEE Journal on Selected Areas in Communications, March 2000, “Field Trial Results for High-Speed Wireless Indoor Data Communications” by J.F. Frigon, B. Daneshrad, J. Putnam, E. Berg. R. Kim, T. Sun and H. Samueli.
IF to RF
Up-Converter
RF to IF
Down-Converter
IF to Baseband
Converter
Baseband
to IF Converter
Low IF
Out
Data
CLK
BER
Tester
Out
In
Low IF
In
Data
CLK
Baseband QAM Modulator
Baseband QAM Demodulator
NF = 6.5 dB
IP3 = -36.5 dB
Laptop
PC
fc = 2.44 GHz
BW3dB = 5 MHz

## Slide 18: Field Test Results
Field test environment
  UCLA Engineering building 5th floor laboratories
  Modern construction with reinforced concrete with metal support structures
  Rooms contain a set of lab benches with equipment (square rooms with 9.7 m2 area)
Total of 3600 experiments carried out
  1200 measurements within one room (24.8 ns rms delay spread)
  1200 measurements between rooms (35.4 ns rms delay spread)
  1200 measurements between a room and hallway (31.2 ns rms delay spread)
0 dBm transmit power used for measurements within one room
  -43.5 dBm of measured average received power
  24 dB of measured average SNR (with MMSE-DFE)
  SNR > 14.5 dB for %90 of the time (with MMSE-DFE)
  SNR > 10 dB for %95 of the time (with MMSE-DFE)
  As much as 14 dB SNR degradation observed without an MMSE-DFE in the receiver
Results showed that MMSE-DFE equalized system is not ISI but noise limited
  5 dBm transmit power would guarantee 20 Mbps transmission over 90% of the channels encountered (requires 19.5 dB SNR)

## Slide 19: Designed System Performance
BER and PER (512 Bytes)
  10-5 (BER) and 4 x 10-2 (PER)
  19.5 dB SNR requires for 64 QAM TCM
Receiver Sensitivity (AWGN10 MHz BW + Noise Figure + SNR10-5 BER)
  -73 dBm for 64-QAM TCM, 40 Mbit/sec
  -76 dBm for 32-QAM TCM, 24 Mbit/sec
  -79 dBm for 32-QAM TCM, 16 Mbit/sec
  -85 dBm for 8 -PSK TCM, 8 Mbit/sec
Inter-modulation Performance
  -35 dBm to -45 dBm inter-modulating signals while receiving at 3 dB above sensitivity level
  Results in input IP3 from -6.5 dBm to -21.5 dBm
Spurious Noise
  -45 dB below carrier power (out of band spurious)
Phase Noise
  -37 dBc (total integrated over 10 MHz signal bandwidth), -85 dBc/Hz @ 50 kHz

## Slide 20: Regulatory Update
As of August 22, 2000, FCC amended the Part 15 rules to allow for frequency hopping spread spectrum transmitters use 5 MHz wide channels (15 hopping channels in the 2400 - 2483.5 MHz band)
  With the new rule change, from a scalability point of view, our 5 MHz bandwidth frequency hopping QAM transmission mode has the ability to transmit up to 21 dBm power for an extended range beyond 10 meters

## Slide 21: Transmitter Complexity
Digital Baseband Processing
  Randomizer
  Preamble generator
  TCM encoder
  Pulse shaping filter
  Total digital gate complexity: 10K gates
Analog Front-end
  Dual 8-bit DACs (16 Msamples/sec)
  Baseband to RF up-conversion
  0 dBm output on-chip PA (5 dB back-off from 1 dB compression point)
  RF synthesizer block (VCO, PLL, etc) shared with receive section
Power Consumption (Analog + Digital) (0 dBm)
  ~76 mW for .18u technology

## Slide 22: Receiver Complexity
Digital Baseband Processing
  Square-Root-Raised-Cosine Filter: 25% excess bandwidth
  Feed-forward equalizer: 8 symbol interval span
  Decision feedback sequence estimation (6 taps for the feedback filter)
  Signal acquisition block
  8-State 2-D Viterbi decoder
  Total digital gate complexity: 85K gates
Analog Front-end
  Dual 8-bit A/D converter (16 Msamples/sec)
  AGC
  RF-to-IF down conversion block
  IF-to-baseband down conversion
  RF synthesizer block (VCO, PLL etc.) shared with transmit section
Power Consumption (Analog + Digital)
  ~180 mW for .18u technology

## Slide 23
Dual Mode 802.15.1/3 Radio Architecture
Due to frequency hopping (1600 hops/sec) nature of the proposed high rate WPAN proposal, only RF filters need to be programmable while the rest of the blocks are shared between 802.15.1 and 802.15.3 modes
LNA
PA
Mixer
BPF
IF to Baseband
Conversion
PGA
Mixer
LPF
1/5/10 MHz
Programmable
LO
Generation
Control
Channel
Select
PLL
To Baseband
Processor
From Baseband
Modulator
Control
interface
Dual-mode 802.15.1/3 Radio Chip
TDD
switch
1/5/10 MHz
Programmable
.
IF BW
Programmable
.

## Slide 24
Dual Mode 802.15.1/3 Overall System Architecture
Flash
Program
Memory
(32K)
Mixed Signal Baseband Core (Mod/Demod)
8-bit Dual DAC
8-bit Dual ADC
TX/RX square-root-raised-cosine filters
TCM encoder
Signal acquisition
Channel estimation
Feed-forward equalizer
Decision-feedback sequence estimator
Total Digital Gate Count: 95K
MAC Controller
Dual mode 802.15.1/3 MAC
Integrated micro-processor
Integrated SRAM
Data buffers
External memory interface
Host interfaces
Dual-mode
802.15.1/3
Radio
Crystal
.
0.18u CMOS
18 mm2
Total chip area
(including MAC)
0.18u CMOS
31 mm2
UART, USB,
PCI, etc.
Overall System Components
1. Dual-mode radio chip
2. Baseband PHY/MAC chip
3. Flash program memory
4. Crystal

## Slide 25: General Solution Criteria Update
Unit Manufacturing Cost
  As shown on pages 21, 22, 23, 24, the addition of 10 MHz non-hopping transmission mode leads to a 13% increase in chip area for the dual-mode 802.15.1/3 radio (from 16 mm2 to 18 mm2 ), and leads to a 35% increase in chip area for the mixed-signal baseband core (from 23 mm2 to 31 mm2 )
  Based on the revised chip area estimates, unit manufacturing cost for the resulting two chip solution (0.18u CMOS) is still well under the 1.5 x Bluetooth 1 cost target as defined in IEEE P802.15-00/110r12
Intermodulation Performance
  Proposed system can handle an intermodulation signal power of 25-35 dB over minimum required sensitivity level (-73 dBm) plus 3 dB
  Results in input IP3 from -6.5 to -21 dBm

## Slide 26: General Solution Criteria Update
Interference and Susceptibility
  Based on the design of front-end and baseband filters for 10 MHz bandwidth non-hopping system (reflected in the presented system cost and complexity), proposed system achieves the following interference blocking performance:
    “Out-of-Band” blocking performance (interfering signal power level while the wanted signal is at -70 dBm)
      30 MHz - 2000 MHz: -10 dBm
      2000 MHz - 2399 MHz: -27 dBm
      2498 MHz - 3000 MHz: -27 dBm
      3000 MHz - 12.75 GHz: -10 dBm
    “In-Band” blocking performance (excluding co-channel and adjacent channel)
      Interference protection is greater than 35 dB

## Slide 27: General Solution Criteria Update
Jamming resistance
  It was shown in IEEE 802.15-00/211r4 that 5 MHz signal bandwidth frequency hopping system achieves much better than 50% throughput for all jamming scenarios stated in the evaluation criteria document
  As shown below, with the addition of 10 MHz signal bandwidth non-hopping transmission mode, the proposed system still achieves better than 50% throughput for the required jamming scenarios
  With respect to microwave oven interference:
    10 MHz non-hopping mode allows for 8 static channels in 2.4 GHz band
    By employing a channel selection scheme (similar to one described in IEEE 802.15-00/200) that avoids wideband interference sources, a throughput of 100% can be achieved
  With respect to an 802.15.1 piconet transmitting HV1 voice packets
    An 802.15.1 device hops at a rate of 1600 hops/sec
    Probability of that an 802.15.1 hop frequency coincides with the proposed 10 MHz bandwidth static channel is 10/75 which results in a system throughput of 87%

## Slide 28: General Solution Criteria Update
Jamming resistance (continued)
  With respect to an 802.15.1 device transmitting DH5 voice packets
    In this mode, an 802.15.1 device is effectively hopping 5 times slower (320 hops/sec) than in the previous case while using all of the 75 available channels
    Probability that the 802.15.1 device hop frequency coincides with the proposed 10 MHz bandwidth fixed channel is still 10/75 resulting in a throughput of 87%
  With respect to an 802.15.3 data connection operating in an uncoordinated manner transferring a DVD video stream compressed with MPEG2
    Probability that the 802.15.1 system’s hop frequency coincide with the proposed 10 MHz bandwidth channel is 10/75 resulting in a throughput of 87%
  With respect to an 802.11a piconet
    Proposed system achieves 100% throughput since the frequency band of operation is 2.4 GHz band
  With respect to an 802.11b piconet transmitting DVD video stream compressed with MPEG2
    By employing a channel selection scheme (similar to the scheme described in IEEE 802.15-00/200) that avoids wideband interference sources, a throughput of 100% can be achieved

## Slide 29: General Solution Criteria Update
Multiple Access
  Multiple access is the ability of the coordinated systems to simultaneously share the medium
  It was shown in IEEE 802.15-00/211r4 that 5 MHz signal bandwidth frequency hopping system handles all three multiple access scenarios given in the evaluation criteria document
  As shown below, with the addition of 10 MHz signal bandwidth non-hopping transmission mode, the proposed system still handles all three multiple access scenarios given in the evaluation criteria document
  With respect to three systems (each containing 2 nodes) where all three systems transmitting a DVD video stream compressed with MPEG2
    In this case, each system (with the addition of 10 MHz non-hopping transmission mode) can simultaneously achieve the required 4.5 Mbps in a time-division multiplexed mode since the PHY layer data rate is 40 Mbps or in a frequency-division multiplexed mode since there are eight independent fixed 10 MHz channels

## Slide 30: General Solution Criteria Update
Multiple Access (continued)
  With respect to the desired system transferring a DVD video stream compressed with MPEG2 as the other two transferring asynchronous data with a payload of 512 bytes
    In this case, the desired system would use 4.5 Mbps bandwidth while the remaining two systems transfer asynchronous data with the remaining 35.5 Mbps data rate in a time-division-multiplexed manner
  With respect to the desired system and one other system transferring asynchronous data with a payload size of 512 bytes while the third system transferring a DVD video stream compressed with MPEG2
    Similar to the second scenario given above, two systems can utilize up to 35.5 Mbps data bandwidth whereas the DVD video transfer can take place at a 4.5 Mbps rate in a time-division-multiplexed manner

## Slide 31: General Solution Criteria Update
Coexistence
  Coexistence is defined as the net throughput of an alternate system in the presence of the proposed system divided by the net throughput of the alternate system with no other interferers or systems present
  It was shown in IEEE 802.15-00/211r4 that the coexistence performance of 5 MHz signal bandwidth frequency hopping system is more than adequate per evaluation criteria requirements
  As shown below, the coexistence performance of the 10 MHz bandwidth non-hopping mode is also more than adequate per evaluation criteria requirements
  To evaluate the coexistence performance of the new mode with alternate systems, we again rely on the results presented in the jamming performance section
  With respect to an 802.15.1 system with one HV1 voice transmission active
    Considering the worst case scenario of transmissions by the proposed system completely jamming the 802.15.1 HV1 transmissions when their hopping frequencies coincide with the 10 MHz non-hopping channel, the throughput of the 802.15.1 system would still be 87% (see the jamming performance section), which results in a better than 60% throughput for the 802.15.1 system
    Thus, IC1=1

## Slide 32: General Solution Criteria Update
Coexistence (continued)
  With respect to an 802.15.1 system transferring data with DH5 packets bi-directionally
    Probability that the proposed 10 MHz non-hopping system channel frequency coincides with the 802.15.1 piconet hop frequency is approximately 10/75 (see the jamming performance section), which results in a better than %60 throughput for the 802.15.1 system
    Thus, IC2=1
  With respect to an 802.11b network transferring data with 500 byte packets bi-directionally
    By employing a channel selection scheme (similar to the scheme described in 802.15-00/200) that avoids wideband interference sources, a throughput of 100% can be achieved
    Thus, IC3=1
  With respect to an 802.11a data connection transferring a MPEG2 DVD video stream
    Considering that the proposed system operates in the 2.4 GHz band, the 802.11a system can achieve a throughput of 100%
    Thus, IC4=1

## Slide 33: General Solution Criteria Update
Coexistence (continued)
  With respect to an 802.11b network transferring an MPEG2 DVD video stream
    Similar to the 802.11b scenario given above, the 802.11b network will still achieve a throughput of 100%
    Thus, IC5=1
  Consequently, the total value for coexistence evaluation: 2*IC1 + 2*IC2 + IC3 + IC4 + IC5 = 7
Interoperability
  Frequency hopping mode of the proposed solution (1600 Hops/sec) will be interoperable with Bluetooth 1 solution

## Slide 34: General Solution Criteria Update
Manufacturability
  Both 5 and 10 MHz bandwidth modes of the proposed solution is based on proven frequency hopping and QAM technologies (similar ICs already exist)
Time-to-Market
  Chips for the proposed solution would be available well before 1Q2002
Regulatory Impact
  Proposed solution is already compliant with the FCC 15.247/249 rules
Maturity of Solution
  A prototype consisting of similar chips already exists
Scalability
  Proposed solution provides scalability in all of the following areas: (1) power consumption (1, 10, 100 mW), (2) data rate (8, 12, 16, 20, 24, 32, 40 Mbps), (3) frequency band of operation (can operate both in 2.4 or 5 GHz bands), (4) cost, and (5) function

## Slide 35: Physical Layer Solution Criteria Update
Size and Form Factor
  As shown on page 24, die and package size for the 40 Mbps solution is estimated to fit in a form factor much smaller than a compact flash type-1 card
Minimum MAC/PHY Throughput
  Proposed system can deliver a net data throughput greater than 20 Mbps since the highest PHY layer data rate is 40 Mbps
High End MAC/PHY Throughput
  Proposed system can deliver up to 40 Mbps PHY layer data rate
Frequency Band
  Operates in the 2.4 GHz band
Number of Simultaneously Operating Full-Throughput PANs
  Since the proposed system supports 8 independent fixed 10 MHz channels, it can support 8 simultaneously operating full-throughput PANs

## Slide 36: Physical Layer Solution Criteria Update
Signal Acquisition Method
  Preamble based
Range
  Covers 10m radius with 0 dBm transmit power
  Larger coverage possible with > 0 dBm transmit power
Sensitivity
  -73 dBm (64-QAM/TCM at 40 Mbps)
Delay Spread Tolerance
  Can handle RMS delay spreads of up to 105 nsec (with less than 1% FER for > 95% channels) (see pages 14, 15)
Power Consumption
  Total power consumed during transmit: 76 mW (.18u CMOS technology)
  Total power consumed during receive: 180 mW (.18u CMOS technology)

## Slide 37
General Solution Evaluation Matrix
Note: Evaluation of the proposed solution is highlighted

## Slide 38
General Solution Evaluation Matrix
Note: Evaluation of the proposed solution is highlighted

## Slide 39
PHY Solution Evaluation Matrix
Note: Evaluation of the proposed solution is highlighted