## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: TI PHY Submission to TG3
Date Submitted: November 6, 2000
Source: Anand Dabak Company Texas Instruments
Address 12500 TI Blvd, MS 8632, Dallas, TX 75243, USA
Voice:214.480.4389, FAX: 972.761.6967, E-Mail:dabak@ti.com
Re: original document.
Abstract: Submission to Task Group 3 for consideration as the High Rate PHY for 802.15.3
Purpose: Evaluation of Proposal.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Physical Layer Submission to Task Group 3
Anand Dabak
Texas Instruments

## Slide 3: High Speed WPAN
Criteria document specifies the following data rates :
  Audio: 128, 448, 896, 1280, 1450, 1536 kbps
  Video: 2.5, 7.3, 9.8, 18 Mbps
  Computer graphics: 15, 38 Mbps
Propose a 2.4 GHz ISM band high speed WPAN consisting of three modes
  Mode 1: Bluetooth 1.0
  Mode 2: Maximum data rate up to 3.9 Mbps
  Mode 3: Maximum data rate up to 44 Mbps

## Slide 4: Salient Features
Interoperability with Bluetooth
High throughput: Up to 41 Mbps throughput
Coexistence with Bluetooth and 802.11b.
Resistance to microwave, Bluetooth, 802.11b jamming
Low cost: cost < 1.5 x Bluetooth
Low sensitivity level: -86 dBm
Low power consumption
Designed for FCC compliance
Compatibility with Bluetooth MAC
Low risk approach
99 percentile coverage in a 10 m radius, same as Bluetooth 1.0

## Slide 5: Mode 3 System Specifications

## Slide 6: Link Margin

## Slide 7: Fading Margin
Points where required frame error rate is not met
10 m

## Slide 8: Fading Margin
Fading margin of 17 dB offers 99 % coverage in 10 m radius
-70 dBm
-80 dBm
-60 dBm
-90 dBm
-50 dBm
Power received
Probability

## Slide 9: Slot Format
Sync
field
ARQ
field
Packet
50

s
50

s
Preamble
Header
ARQ
information
CRC
Frame 1
Frame 2
...
Frame N

## Slide 10: ARQ Format
ARQ is performed on all of the frames inside the payload. Each bit in the ARQ payload corresponds to the corresponding frame.
25 sec turn around time
Sync. field
Payload (up to 128 bits)
CRC
25 sec turn around time
100 s ARQ Frame Length

## Slide 11: TDD Scheme
Slave responds with ARQ packet only in case of a unidirectional link
Master does not send an ARQ packet in case of a unidirectional link
Master -> Slave
Slave -> Master
Sync.
field
Payload
…
100

s
ARQ
Turn-
around
25

s
50

s
50

s
Sync.
field
Payload
…
100

s
ARQ
Turn-
around
50

s
50

s
25

s

## Slide 12: Throughput
Assume we use 16 QAM with rate 1/2 coding
Assume we have 100 segments in each packet
Therefore each packet takes 200+100*100=10.2 ms
Each segment has a payload of 2088 bits
Assume we perform PLS every 50 of these packets
Therefore throughput is 2088*50*100/(10.2*50+7.5) = 20.17 Mbps
A similar calculation shows that we meet the high end throughput of 40 Mbps using uncoded 16 QAM. Throughput = 4240*50*100/(10.2*50+7.5) = 40.97 Mbps

## Slide 13: Mode 3
Begin transmission in mode 1 and identify good 22 MHz bands.
Negotiate to enter mode 3.
After spending a time T2 in mode 3 come back to mode 1 for time T1.
Identify good 22 MHz bands.
Again negotiate to enter mode 3, this time possibly on a different 22 MHz band.
Regulatory issues similar to 802.11
Time allocation T1 and T2 negotiated between the Master and Slave in the beginning depending upon data rate requirements of the Slave.
Master maintains synchronization of all other Mode 1 devices in the piconet
Sniff, Beacon, Paging, for other mode 1 devices.

## Slide 14: Mode 3 (Example)
Master
Slave 1
Slave 2
Slave 3
Mode 1
Mode 3
Mode 1
Mode 1
Mode 3
Mode 1
Mode 3
Mode 1
Mode 3

## Slide 15: Exponential 802.15.3 Channel
TRMS = 10, 25 ns

## Slide 16: Probe, Listen and Select (PLS)
Intelligently avoids microwave ovens, 802.11b, etc.
Frequency diversity
Microwave
802.11(b) interference
2402 MHz
2480 MHz
PLS selects this band
for mode 3

## Slide 17: Turbo Codes
Serial concatenated convolutional code (SCCC):
  No error floor
  Choose low complexity code. Complexity less than 802.11 (b) convolutional code. Offers better performance compared to 802.11 (b) convolutional code.
  Implemented and tested the Turbo codes.
  4 state outer and 2 state inner code
D
D

D

## Slide 18: Simulations (AWGN)

## Slide 19: Delay Spread Tolerance
A MMSE-DFE is employed to combat multipath spread
  6 taps ( half-symbol spaced ) feedforward and up to 3 taps feedback filters are used
  Taps are calculated from channel estimate performed during sync word
  Taps can be adapted using LMS
    Combats interference
Feedforward Filter
-
Feedback Filter
Output from square root raised cosine filter
To turbo decoder

## Slide 20: Delay Spread Results

## Slide 21: Dual Mode Radio, RF Cost Estimation
802.15.1 and 802.15.3 share
  Antenna
  Antenna filter
  Tx/Rx Switch
  LNA
  Transmit modulator
  Power amplifier
Additional blocks needed
  RF/baseband conversion mixers for 802.15.3
  Low pass filters
  AGC amplifier (+/- 20 dB)
The total RF chip area is less than 20 mm2 in RFBiCMOS

## Slide 22: Digital Technology
Digital technology allows integration and hence cost, power reduction
  Adding new features onto an existing chip leads to a small increase in cost.
Baseband
Silicon area
increase
Cost
increase

## Slide 23: Baseband Blocks
Baseband blocks
  2, 8 bit A/D’s at 22 MHz each.
  2, 6 bits D/A’s at a speed of 44 MHz.
  A 16 tap half symbol spaced square root raised cosine filter.
  A 6 tap half symbol spaced feed forward and up to 3 tap symbol spaced feed back equalizer.
  The Turbo decoder size is a total of 50 K gates and 13 Kbytes of RAM.

## Slide 24: Baseband (Continued)
Gate count and silicon area in 0.13  technology.
0.13  technology
  Highly integrated solution takes advantage of Moore’s Law that the cost of digital solutions decreases by a factor of 2 every 18 months. Moore’s Law does not apply to analog solutions, which decrease in cost much more slowly.

## Slide 25: Power Consumption (Receive)

## Slide 26: Power Consumption (Transmit)

## Slide 27: Cost Comparison
Estimated cost increase for (802.15.3 + 802.15.1) solution over 802.15.1 only solution:
  RF cost increase is 25 %
  Baseband cost increase is 60 %
Overall cost of (802.15.3 + 802.15.1) < 1.5Xcost of 802.15.1.

## Slide 28: Time to Market
Shares most blocks with other wireless systems
  Reuse 802.15.1 and 802.11(b) RF solutions
  Turbo decoder employed in 3G WCDMA systems
  Equalizer similar in design to 802.11(b), but simpler due to much smaller delay spreads.
  Other blocks including A/D converters, D/A converters are readily available.
Hence can leverage off of other closely related existing wireless systems.
Hence short time to market.

## Slide 29: Conclusions
Our solution
  Satisfies minimum throughput of 20 Mbps
  Can go up to 40 Mbps for high bandwidth applications
  Maintains same link margin as Bluetooth 1.0 hence has 99 % coverage in a 10 m radius
    Same indoor operation range for Bluetooth 1.0 and 802.15.3.
    User will not have communication signal fade in and out.
  Allows high level of integration allowing cost to fall exponentially following Moore’s Law.
  Low cost solution (< 1.5 X Bluetooth 1.0)
  Low power consumption of less than 150 mW on transmit and receive
  Rapid time to market by leveraging off of existing wireless systems