## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LinCom Wireless Proposal for High Rate WPAN PHY ]
Date Submitted: [27 October 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: [00356r0, 00357r0, 00358r0, 00197r3, 00198r3]
Abstract: [A PHY proposal by LinCom Wireless, Inc., supporting a High Rate WPAN PHY and system]
Purpose: [Response to the High Rate WPAN CFP]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: LCW PHY A Proposal for a High Data Rate WPAN Physical Layer

## Slide 3: About LinCom Wireless, Inc.
Formerly the Commercial Business Units of LinCom Corp
Spun off as a separate corporation in April 2000
Wholly owned subsidiary of Titan Corp., San Diego, CA
26 year history of developing Satellite and Terrestrial Digital Wireless Communications technology
30+ technical professionals dedicated to Systems Engineering, ASIC and embedded software development
Develop IP, ASICs, FW and board/module level products for Wireless LAN, PAN and Home Networking markets
Provide Systems Engineering services in commercial SatCom, PCS and short range wireless markets

## Slide 4: The Wireless Home Network Application
Enable the wireless interconnection of electronic devices within the home
  30m range, including thru-wall propagation
  High throughput, in excess of 30 Mbps
  Real time and non-real time data
  Multiple simultaneous connections
  Support prioritization and guaranteed bandwidth, minimum latency
  Enable coexistence, interoperability, coordination between all home wireless devices
  Coexist and perhaps interoperate with “visiting” or legacy devices designed to other standards

## Slide 5: “Systems” Implications
PHY needs to support high data rate, low latency, highly secure, multimedia capable, fully networked personal wireless communications in the indoor propagation channel
Also support multiple simultaneous data, voice, video and interactive multimedia links
  Over 30 Mbps sustained, low latency, low error throughput
Need to overcome the onerous propagation channel
  LCW PHY needs to provide powerful multipath mitigation, error correction and spatial diversity
  MAC needs to support “smart” ARQ to improve throughput, latency
Bluetooth PHY and MAC embedded for compatibility with 802.15.1
An integrated, specifically designed PHY and MAC pair BEST addresses all these requirements
  But, that’s not what we are doing here
  The LCW PHY can mate with any other MAC
    Won’t work quite as well as with the LCW MAC

## Slide 6: LCW PHY Description
LCW PHY provides high throughput, low latency, low BER
Coded nQAM signaling provides data rates of 1, 2, 10, 20, 30, 40 Mbps
Antenna Diversity, Adaptive Equalization, Reed Solomon FEC improve high end throughput
Low power operation per FCC 15.249
Interoperable with IEEE 802.11DS, coexists with on-channel 802.11b
Embedded 802.15.1 modem provides interoperability with Bluetooth
“Bluetooth class” device in size, cost, power consumption

## Slide 7: LCW PHY Modulation
LCW-1 is 1 Mbps (11 chip) Barker encoded DBPSK
LCW-2 is 2 Mbps (11 chip) Barker encoded DQPSK
LCW-10 is 10 Mbps RS(220,200) encoded DBPSK
LCW-20 is 20 Mbps RS(220,200) encoded DQPSK
LCW-30 is 30 Mbps RS(220,200) encoded 8QAM
LCW-40 is 40 Mbps RS(220,200) encoded 16QAM
All produce 11 MSps 802.11 DSSS-like 22 MHz spectrum
All use the 802.11 PLCP header, with appropriate service field extensions, and slightly different preambles
  LCW-1, 2, 10 and 20 use the identical 802.11b 96 us short preamble
  LCW-30 uses a 96 us preamble featuring DBPSK, DQPSK and 8QAM symbols to aid equalizer training
  LCW-40 uses a 96 us preamble featuring DBPSK, DQPSK and 16QAM symbols to aid equalizer training
802.15.1 Modem is embedded into the PHY

## Slide 8: LCW PHY- Channelization
Channelization
  4 overlapping 20 MHz channels
    fc= 2412, 2432, 2452, 2472 MHz
    1 MHz overlap on each side
    Same as 802.11b European Overlapped Channelization
  3 standard 25 MHz channels
    fc= 2412, 2437, 2462 MHz
    Same as 802.11 USA Non Overlapped Channelization
  Offset Raised Cosine pulse shaping
    Reduces sidebands by more than 50 dBc
    Enables compliance with US FCC emissions limits above 2.835 MHz
CCA mechanism is identical to 802.11
802.11b 5.5 and 11 Mbps CCK, PBCC are not supported
Full 802.15.1 PHY is included, is mode switchable with LCW
  RF architecture supports both QAM and GFSK up/down conversion
  Baseband hardware includes both 802.15.3 and 802.15.1 modems

## Slide 9: LCW PHY Equalization and Diversity
Powerful equalizer minimizes and “whitens” the burst errors characteristic of the 25 ns Delay Spread “Naftali” channel
  Converges as rapidly as possible to the precise channel estimate (less the multipath components) and tracks for the packet duration
    Need PHY preamble of adequate length (hundreds of symbols) to train equalizer and generate the appropriate tap coefficients
    Then continuously adapt, update coefficients, symbol by symbol, over the entire duration of the frame (up to 8000 Bytes)
Antenna Diversity is also necessary
  The Naftali Model produces channel instantiations that cannot be equalized up to 5% of the time
  The LCW PHY integrates a spatial diversity switching mechanism into the Equalizer convergence algorithm
    Switch if the Equalizer hasn’t converged midway through training sequence
  Adequate antenna diversity then reduces non-equalizable channel instantiations to below 1%

## Slide 10: LCW PHY FEC and ARQ
Strong Reed-Solomon Block Code “localizes” if not corrects whitened burst errors
  RS(220,200) corrects 10 of 200B in a block
  The decoder sets a flags if the block is uncorrectable
  RS(220,200) is efficient (R=10/11), adds little overhead
  No interleaving is necessary, so no innate latency is introduced
  Convolutional codes are less efficient (R=1/2, 3/4)
  Turbo Codes feature large interleavers, produce much latency
Nevertheless, packets will be dropped (Diversity + Equalization + FEC = 1% FER)
  Automatic Repeat Request (ARQ, or retransmission) MAC protocols are essential to improve error performance
  But don’t have to retransmit entire packet, just the flagged uncorrectable blocks

## Slide 11: Throughput, Latency and Error Performance
Key communications performance metrics for a wireless network
  Throughput- Net data transmission rate
  Latency- Time Delay caused by transmission(s)
  Corrected Bit Error Rate- 1/ (Number of bits between errors)
“Best” combination for a specific application involves tradeoffs
  High throughput can be readily achieved with large packets
  Large packets ordinarily imply large retransmission latencies
  Very low latencies can be achieved at the expense of error rate
  Low error rates can be had with large (retransmission) latencies
Performance is inextricably tied to details of the specific PHY and MAC implementation
  Analyzing a specific PHY with a “generic” MAC produces no meaningful results
  All 7 proposed PHYs were analyzed against the LCW MAC

## Slide 12: Throughput, Latency and Error Analysis
Analysis Conditions
  Very nasty multipath propagation medium (25 ns Rayleigh “Naftali” channel)
  Require high sustained throughputs
    Support 3 MPEG2 channels (6 Mbps ea, 18 Mbps total, min)
  Desire low peak latencies for interactive multimedia
    8 ms is consistent with pleasant voice
  Very low error rates
    Broadcast digital video demands an error event no more than once per hour
    Translates to a BER better than 1x10-10
    For a packet data environment, use CBER = 1x10-10
Scenario 1- One way transmissions from A to B
Scenario 2- One way A-B and Bidirectional C-D transmissions

## Slide 13: PHY FER Performance in 25ns DS Multipath 11 MSps nQAM, 52x312 OFDM
Representative
PHYs
TI-44
TI-33, TI-22
LCW-40
LCW-30
Kdk-22
SG-21.7
LCW-20
Mot/Rad

## Slide 14: PHY and MAC Throughput, Latency, CBER Scenario 1

## Slide 15: PHY and MAC Throughput, Latency, CBER Scenario 2

## Slide 16: Coexistence, Interoperability and Harmony
The LCW PHY supports coexistence, interoperability with Bluetooth
  While operating in 802.15.1 mode, and paired with an appropriate Bluetooth MAC obviously coexists and interoperates
  While operating in 802.15.3 mode, takes a hit whenever a BT hops into its 14 MHz Nyquist BW, less than 20% of the time
The LCW PHY supports coexistence with 802.11b
  Paired with an appropriate MAC, CCA and CSMA/CA protocol will defer to co-channel transmissions of the appropriate carrier center frequency and move to a different channel
The LCW PHY supports Harmony with 802.11b
  Paired with the LCW MAC, will demodulate and interpret the PLCP header for the transmission duration information
  Can force an “equitable” sharing of the single channel by “cheating” on PCF, DCF protocols and PIFS, DIFS timing

## Slide 17: LCW vs TG3 General Solution Criteria
2.1 Unit Manufacturing Costs
  Are intimately associated with specific MAC, PHY implementation
  Direct BB/RF Conversion architecture minimizes BOM cost
  Present day silicon technology supports single chip integration of
    RF Zero IF transceivers at 2.4 GHz
    Digital nQAM modems, adaptive equalizers, RS FECs
    80+ MIP processors suitable for software 802.11-like MACs, including encryption, QOS
    High speed SRAM
  0.18u CMOS process is available in low cost fabrication facilities
  0.13u CMOS process is now being introduced
  LCW Module available Q102 for <1.5x 802.15.1 cost
    Will enable further integration of SRAM, flash memory on chip
  Criteria Comparison = +1

## Slide 18: LCW vs TG3 General Solution Criteria
2.2.2 Interference and Susceptibility
  Inband, Non-Cochannel, Non-Adjacent Channel > 35 dBc
  Out of Band > 35 dBc
  Criteria Comparison = +1
2.2.3 Intermodulation Resistance
  Measured IP3 of representative RF front end= -3 dBm
  IM level produced by 2 -35 dBm tones= -99 dBm
  SOI level, LCW-40= -77 dBm (Sensitivity +3 dB)
  SIR, LCW-40= 22 dB
  Criteria Comparison = +1
2.2.4 Jamming Resistance
  No devices will jam
  Criteria Comparison = +1

## Slide 19: LCW vs TG3 General Solution Criteria
2.2.5 Multiple Access
  All scenarios work with LCW-30, 40
  Criteria Comparison = +1
2.2.6 Coexistence
  LCW coexists > 80% with devices 1, 2
  LCW coexists 100% with devices 3, 4, 5
  Criteria Comparison = +1
2.3 Interoperability
  An 802.15.1 PHY and MAC is embedded into LCW, achieving a dual mode radio switchable between 802.15.1 and 802.15.3
  Criteria Comparison = +1
2.4.1 Manufacturability
  802.11b equipment of similar complexity available in 2001
  Criteria Comparison = +1

## Slide 20: LCW vs TG3 General Solution Criteria
2.4.2 Time to Market
  LCW will be available Q102
  Criteria Comparison = +1
2.4.3 Regulatory Compliant with existing FCC (15.249), ETSI 300-328
  Criteria Comparison = 0
2.4.4 Maturity of Solution
  LCW is a reduction, extension of 802.11b PHY and 802.11 MAC
  Criteria Comparison = +1
2.4.5 Scalability
  LCW is scalable in data rate, frequency band, and function
  Criteria Comparison = +1
2.6 Location Awareness
  RSSI statistics distinguish device locations to resolution in meters
  Criteria Comparison = 0

## Slide 21: LCW vs TG3 PHY Criteria
4.1 Size and Form Factor
  Smaller than Compact Flash Type 1, Q102
  Criteria Comparison= +1
4.2.1 Minimum Delivered Data Throughput
  PHY Header, MAC header, Payload, SIFS, EACK, PIFS
  LCW-40, 8000 B payload = 34.89 Mbps
  LCW-30, 8000 B payload = 26.99 Mbps
  LCW-20, 8000 B payload = 18.55 Mbps
  Criteria Comparison= +1
4.2.2 High End Delivered Data Throughput
  PHY Header, MAC header, Payload, SIFS, EACK, DIFS
  LCW-40, 8000B payload = 34.89 Mbps
  Criteria Comparison= 0
4.3 Frequency Band of Operation 2.40-2.483 GHz, unlicensed
  Criteria Comparison= 0

## Slide 22: LCW vs TG3 PHY Criteria
4.4 Number of simultaneously operating full rate WPANs
  4 LCW-40s can operate with slight frequency overlap
  Criteria Comparison= 0
4.5 Signal Acquisition identical to 802.11
  Criteria Comparison= 0
4.6 Range not less than 30 meters, indoors (home)
  RS FEC plus equalization and diversity provide necessary range
  Criteria Comparison= 0
4.7 Sensitivity, 10E-5 BER
  LCW-20= -86 dBm
  LCW-30= -83 dBm
  LCW-40= -80 dBm
4.8 Multipath Tolerance
  Adaptive equalizer mitigates > 25 ns delay spread
  Criteria Comparison= +1
4.9 PHY Power Consumption consistent with 0.5 W system power
  Criteria Comparison= +1

## Slide 23: Summary
LCW PHY results from a “Systems Design” approach to the HRWPAN
  Specifically designed to integrate with the LCW MAC
  Nevertheless can mate robustly and efficiently with other MACs
LCW PHY enables extraordinary transmission performance
  Simultaneous high throughput, low error rate and low latency
Integrated modulation, multipath mitigation and coding
  DBPSK, DQPSK, 8QAM, 16QAM
  Integrated Adaptive Equalizer and Antenna Diversity
  Reed Solomon Forward Error Correction
Small, low power, low cost yet very high performance
Coexistence, Interoperability and Harmony with preexisting wireless networking standards
The LCW PHY is a compelling choice for the HRWPAN standard