## Slide 1
Slide <number>
<footer>
Jul 29, 2026
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Kodak - High Rate MAC Proposal]
Date Submitted: [07July2000]
Source: [Allen D. Heberling] Company: [Eastman Kodak Co.]
Address: [1669 Eastman Ave. Rochester, NY, 14650-2015]
Voice:[(716) 588-1939], FAX: [(716) 722-9053], E-Mail:[allen d.heberling@kodak.com]
Re: [ ]
Abstract: [This presentation outlines Kodak’s MAC proposal to 802.15.3 High Rate Task Group]
Purpose: [To communicate the proposal for consideration by the standards team]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Eastman Kodak High Rate MAC Proposal to IEEE 802.15.3
Allen D. Heberling
Eastman Kodak Company
1669 Eastman Ave.
Rochester, NY, 14650-2015

## Slide 3: Overview
Summary
MAC Architectural Overview
802.15.3 MAC Proposal 1
802.15.3 MAC Proposal 2
802.15.3 MAC Protocol Criteria
Conclusions

## Slide 4: Summary
EK MAC Proposals 1 & 2:
reuse 85-90% of the existing 802.15.1 protocol software components
introduce minimal modifications to the existing 802.15.1 protocol
EK MAC Proposal 2:
introduces a bandwidth efficient MAC algorithm for high rate communications

## Slide 5: 802.15.1 MAC Architectural Overview
L2CAP functionality
(see ref: 00113r0P802.15_TG3_802.15-Reusable-SW-Components.doc )
MLME functionality(ibid. )
Baseband Functionality(ibid.)

## Slide 6: Baseband Decomposition
BB_Controller_prc (Link Controller)
ACL_prc
BB_phy
  BB_plcp
  BB_pmd

## Slide 7: Current Baseband Behavior
Fixed minimum time slot duration
Frequency Hop sequencing algorithm
FH dwell time
Synchronization beacon
Preamble and Access Code structure

## Slide 8: 802.15.3 MAC Proposal Assumptions
Dual mode PHY capable of 1 Mega-symbol per second and 22 Mbps Tx/Rx rates.
Highspeed PHY does not perform frequency hopping.
MAC processor capable of handling 22 Mbps data rates.

## Slide 9: 802.15.3 MAC Proposal 1
Retain L2CAP functionality
Retain MLME functionality
Retain these Baseband capabilities
  Link controller
  ACL-process
  Maintain Access Code format (except current preamble length)
  Maintain Packet Header format

## Slide 10: 802.15.3 MAC Proposal 1 continued...
maintain these header bit processes:
  HEC generation and checking
  whitening and de-whitening
maintain these payload bit processes:
  CRC generation and checking
  encryption and decryption
  whitening and de-whitening

## Slide 11: 802.15.3 MAC Proposal 1 continued...
Maintain current time slot order and duration:
  Master, Slave
  625 usec
maintain synchronization beacon(only if peer nodes are in hold and/or park mode)

## Slide 12: 802.15.3 MAC Proposal 1 continued...
Modifications to the existing 802.15.3 MAC
Suspend FH sequencing and dwell time during turbo mode
use an alternate preamble during turbo mode

## Slide 13: Issues with MAC Proposal 1:
Fixed time slot scheme limits a 22 Mbps radio’s raw data rate to 11 Mbps.
Protocol bit overhead reduces effective throughput rate to approximately 10.5 Mbps
Current protocol does not support direct peer to peer(slave to slave) traffic.

## Slide 14: 802.15.3 MAC Proposal 2
Retain L2CAP functionality
Retain MLME functionality
Retain these Baseband capabilities
  Link controller
  ACL-process
Maintain Access Code format (except current preamble length)
Maintain Packet Header format

## Slide 15: 802.15.3 MAC Proposal 2 continued...
Maintain these header bit processes:
  HEC generation and checking
  whitening and de-whitening
Maintain these payload bit processes:
  CRC generation and checking
  encryption and decryption
  whitening and de-whitening
Maintain synchronization beacon(only if peer nodes are in hold and/or park mode)

## Slide 16: 802.15.3 MAC Proposal 2 continued…
Modifications to the existing 802.15.3 MAC
Suspend FH sequencing and dwell time during turbo mode
Use an alternate preamble during turbo mode
Employ an implicit time token scheduling algorithm

## Slide 17: Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm
Characteristics:
Mini Time Slots - currently 2.
Slot lengths up to 1514 bytes (550.5 usec) in length.
Slots may be designated as Isochronous or Asynchronous.
An Isochronous slot may be subdivided to support multiple time dependent data streams.

## Slide 18: Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm
Characteristics continued:
Asynchronous slot may be sub-divided to allow graceful performance degradation.
Effective Throughput Rate =
MacPayLdTime/(MacPayLdTime+MacProtocol_HdrOvrHdTime) =
21 Mbps
Protocol Efficiency= EffectiveThroughputRate/PhyTransmissionRate =
93.2%

## Slide 19: Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm
Min. Latency = (PktLnth/TxRate)+ (Nslot-1)xTAW
(8192 bits/22mpbs) + (2 - 1)x10usec
392.4 usec
Maximum Latency = (PktLnth/TxRate) xNslot
(8192 bits/22mbps)x2
744.7 usec

## Slide 20
Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm

## Slide 21: Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm

## Slide 22: Shared Slot Assignment with an Implicit Time Token Scheduling Algorithm

## Slide 23: Issues with MAC Proposal 2
Proposal 2 in order to support peer to peer(slave to slave) communications needs to add an additional address field.

## Slide 24: MAC Protocol Criteria

## Slide 25: MAC Protocol Criteria

## Slide 26: MAC Protocol Criteria

## Slide 27: MAC Protocol Criteria

## Slide 28: MAC Protocol Criteria

## Slide 29: Conclusion
EK MAC proposal 2 provides these positive attributes:
  Low Cost
  Minimum Risk
  Efficient Use of HighRate Bandwidth

## Slide 30: Conclusion
EK MAC proposal 2 provides these positive attributes:
  Time to Market
  Coexistence with 802.15.1
  Supports Ad-hoc coordination of multiple independent piconets