## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LinCom Wireless Proposal for High Rate WPAN MAC ]
Date Submitted: [27 October 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: [00355r0, 00357r0, 00358r0, 00197r3, 00198r3]
Abstract: [A MAC proposal by LinCom Wireless, Inc., supporting a High Rate WPAN PHY and system]
Purpose: [Response to the High Rate WPAN CFP]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: LCW MAC A Proposal for a High Data Rate WPAN Medium Access Controller

## Slide 3: About LinCom Wireless, Inc.
Formerly the Commercial Business Units of LinCom Corp
Spun off as a separate corporation in April 2000
Wholly owned subsidiary of Titan Corp., San Diego, CA
26 year history of developing Satellite and Terrestrial Digital Wireless Communications technology
30+ technical professionals dedicated to Systems Engineering, ASIC and embedded software development
Develop IP, ASICs, FW and board/module level products for Wireless LAN, PAN and Home Networking markets
Provide Systems Engineering services in commercial SatCom, PCS and short range wireless markets

## Slide 4: The Wireless Home Network Application
Enable the wireless interconnection of electronic devices within the home
  30m range, including thru-wall propagation
  High throughput, in excess of 30 Mbps
  Real time and non-real time data
  Multiple simultaneous connections
  Support prioritization and guaranteed bandwidth, minimum latency
  Enable coexistence, interoperability, coordination between all home wireless devices
  Coexist and perhaps interoperate with “visiting” or legacy devices designed to other standards

## Slide 5: “Systems” Implications
MAC needs to support high data rate, low latency, highly secure, multimedia capable, fully networked personal wireless communications in the indoor propagation channel
Also support multiple simultaneous data, voice, video and interactive multimedia links
  Over 30 Mbps aggregate, sustained, low latency throughput
Help overcome, “tame” the onerous propagation channel
  PHY needs to provide powerful multipath mitigation, error correction
  LCW MAC supports “smart” ARQ to improve throughput, latency
An integrated, specifically designed PHY and MAC pair BEST addresses all these requirements
  But, that’s not what we are doing here
  The LCW MAC has been modified to mate with other PHYs
    Won’t work quite as well as with the LCW PHY

## Slide 6: LCW MAC Description
LCW MAC Basics
Fundamental MAC protocol is CSMA/CA PCF, akin to 802.11
Adds Slave to Master “morphing”, direct Slave to Slave communications
Provides enhanced security and QOS
Enhanced security features:
  Device registration
  Authorization
  Mutual authentication
  128 bit encryption
  User transparent key generation and maintenance
Real time voice, audio, video and interactive multimedia support
Also provides 802.15.1 support
Full, “distinct and separable” 802.15.1 MAC included to support a dual mode HRWPAN/Bluetooth radio
To avoid legalities, NO further Bluetooth IP is reused by LCW MAC

## Slide 7: LCW MAC Transmission Enhancement
In concert with an appropriate PHY, the LCW MAC improves transmission robustness, throughput and latency performance
Most PHYs provides high raw data rates, multipath mitigation and error correction
LinCom PHY also segments packets into 200B blocks, and performs real time Reed Solomon FEC coding/decoding
LCW MAC then provides for “smart” retransmissions using “Enhanced ACK” (EACK) and“Enhanced ARQ” (EARQ)
EACK indicates the specific packet segments received with errors not correctable by the Reed Solomon decoder
  Replaces the standard ACK
  Tells the transmitter which segments need to be retransmitted.
EARQ protocols at the source then retransmit only those specific RS encoded packet segments
  Retransmission overhead, LATENCY are reduced significantly

## Slide 8: Throughput, Latency and Error Performance
Key communications performance metrics for a wireless network
  Throughput- Net data transmission rate
  Latency- Time Delay caused by transmission(s)
  Corrected Bit Error Rate- 1/ (Number of bits between errors)
“Best” combination for a specific application involves tradeoffs
  High throughput can be readily achieved with large packets
  Large packets ordinarily imply large retransmission latencies
  Very low latencies can be achieved at the expense of error rate
  Low error rates can be had with large (retransmission) latencies
Performance is inextricably tied to details of the specific MAC and PHY implementation
  Analyzing a specific MAC with a “generic” PHY produces no meaningful results
  The LCW MAC was analyzed with all 7 proposed PHYs

## Slide 9: Throughput, Latency and Error Analysis
Analysis Conditions
  Very nasty multipath propagation medium (25 ns Rayleigh “Naftali” channel)
  Require high sustained throughputs
    Support 3 MPEG2 channels (6 Mbps ea, 18 Mbps total, min)
  Desire low peak latencies for interactive multimedia
    8 ms is consistent with pleasant voice
  Very low error rates
    Broadcast digital video demands an error event no more than once per hour
    Translates to a BER better than 1x10-10
    For a packet data environment, use CBER = 1x10-10
Scenario 1- One way transmissions from A to B
Scenario 2- One way A-B and Bidirectional C-D transmissions

## Slide 10: PHY FER Performance in 25ns DS Multipath 11 MSps nQAM, 52x312 OFDM

## Slide 11: PHY and MAC Throughput, Latency, CBER Scenario 1

## Slide 12: PHY and MAC Throughput, Latency, CBER Scenario 2

## Slide 13: Multiple Access
Multiple Access- Master alternately transmits packets to distinct Slaves
Single piconet of one Master and multiple Slaves
  The device initially establishing a network becomes the Master
  A Master may later switch roles with a designated Slave
    “Master Assignment” frame promotes the Slave, transfers the Access Control List to avoid need for reregistration of the other Slaves
  Device attributes can be used to select the “best” Master for a piconet
    AC Line powered, Power Save packet buffering support
    Data sourcing, sinking capability
    A line powered, SDRAM rich Portal makes the best Master

## Slide 14: Master Operation
PCF operation uses 802.11-like timing relationships (SIFS, PIFS)
Channelization is determined using Automatic Channel Selection
  On power up the Master Active Scans (issues Probe Requests), find a clear channel and starts transmitting Beacons
  The Slaves Active Scan to find the Master as they come online
  Should the channel later degrade, the Master may decide to move
    “Graceful” degradation lets Master find new channel and notify slaves for a coordinated frequency shift
    “Abrupt” link loss forces Master to move, slaves to find him
An offline or disabled Master will be replaced by one of his Slaves
  Lack of Beacons, unACKed transmissions determine Master loss
  First Slave needing to transmit will issue Beacons and prepare to register and authenticate the other orphaned Slaves
  Orphaned Slaves proceed to associate with the new Master

## Slide 15: Network Join, Unjoin
802.11-like Association services provide for simple network Join, Unjoin
  Slaves Active Scan upon activation (Probe Request, Response)
  Then issue Enhanced Association Request (EAR) to desired Master
    EAR includes device attribute information so that the best Master can be identified for possible later Assignment
  Master grants piconet access with an Association Response
Up to 32 Slaves at a time can be Associated with one Master
Master can broadcast a packet to multiple Slaves (Point to Multipoint)
Associated Slaves can talk directly to each other, bypassing the Master
  Initiating Slave sends Reassociation frame to desired recipient Slave
  Recipient verifies the common Master, sends Reassociation response
  Peer to Peer link is active until either party requests Disassociation

## Slide 16: Coexistence, Interoperability and Harmony
The LCW MAC supports coexistence, interoperability with Bluetooth
  While operating in 802.15.1 mode, and paired with an appropriate PHY obviously coexists and interoperates
  While operating in 802.15.3 mode, takes a hit whenever a BT hops into its 14 MHz Nyquist BW, less than 20% of the time
The LCW MAC supports coexistence with 802.11b
  Paired with an appropriate PHY, CCA and CSMA/CA protocol will defer to co-channel transmissions of the appropriate carrier center frequency and move to a different channel
The LCW MAC supports Harmony with 802.11b
  Paired with the LCW PHY, will demodulate and interpret the PLCP header for the transmission duration information
  Can force an “equitable” sharing of the single channel by “cheating” on PCF, DCF protocols and PIFS, DIFS timing

## Slide 17: Security- Registration and Authorization
The LCW MAC security protocols are designed to “undo the security damage” of eliminating cables for wireless connectivity
  Authorization grants a device access to the network
  Registration is the one-time act of Authorizing a device
  Authentication is the proof of Authorization upon every access
  Privacy is the protection against eavesdropping
Every LCW-capable device features a unique, secret factory assigned signature in addition to its MAC address
Registration
  A device “Registers” with the Master upon first network access.
  Registration can be unaided or require user intervention at one or both ends.
Upon Registration the device is Authorized to access the network in the future
  Its MAC Address is added to the Master’s Access Control List
  De-Authorization removes the MAC Address from the ACL

## Slide 18: Security- Authentication and Privacy
Upon subsequent network access the device undergoes Authentication to prove he is the authorized accessor
  A secure exchange (Diffie Helman) of MAC Address and secret signature “proves” identity
The device may demand “Reverse” or Mutual Authentication from the Master, to ensure that he is indeed accessing the network of interest
  Foils “man in the middle” attacks
A secret shared session key is automatically generated at both ends
  No need to enter PIN numbers or manual keys, ever
  Ensures communications privacy by strongly encrypting (128b RC4) exchanged messages
After the one time only Registration the user NEED DO NOTHING to obtain highly secure communications

## Slide 19: LCW MAC QOS
Need to support in-home distribution of voice, audio, video and interactive multimedia
  “Single Portal” model for distribution of content likely originating beyond the piconet, either real time broadcast or stored/cached
  PCF eliminates collisions, backoffs, retries
  Prioritization, bandwidth and latency guarantees support streaming applications
  QOS-aware Master balances Automatic Channel Selection and Data Rate Shifting to ensure connectivity and throughput when the channel degrades
LCW QOS MAC will focus solely on the home wireless interactive multimedia distribution issues

## Slide 20: MAC Miscellany
Automatic Data Rate Shifting
  LCW MAC is biased to operate at highest data rate possible
  When channel degrades, automatically downshifts to lower rate
  Defers to QOS prioritization, bandwidth, latency contracts under PCF
Power Management
  Slaves negotiate low power “sleep” intervals with Master
    An integer number of Beacon Intervals
    Slaves power down, except for time-keeping functions to wake up
    Master buffers all incoming packets for sleeping Slaves until they awake and reestablish active link
  Master’s message buffering capability depends on its Device Type
  Slaves maintain a network connection while in Power Save
  Slaves can sleep for seconds before waking to poll for stored data
Roaming, fragmentation, RTS/CTS, 802.11 adhoc are not supported

## Slide 21: LCW vs TG3 General Solution Criteria
2.1 Unit Manufacturing Costs
  Are intimately associated with specific MAC, PHY implementation
  Direct BB/RF Conversion architecture minimizes BOM cost
  Present day silicon technology supports single chip integration of
    RF Zero IF transceivers at 2.4 GHz
    Digital nQAM modems, adaptive equalizers, RS FECs
    80+ MIP processors suitable for software 802.11-like MACs, including encryption, QOS
    High speed SRAM
  0.18u CMOS process is available in low cost fabrication facilities
  0.13u CMOS process is now being introduced
  LCW Module available Q102 for <1.5x 802.15.1 cost
  Criteria Comparison = +1

## Slide 22: LCW vs TG3 General Solution Criteria
2.2.2 Interference and Susceptibility
  Inband, Non-Cochannel, Non-Adjacent Channel > 35 dBc
  Out of Band > 35 dBc
  Criteria Comparison = +1
2.2.3 Intermodulation Resistance
  Measured IP3 of representative RF front end= -3 dBm
  IM level produced by 2 -35 dBm tones= -99 dBm
  SOI level, LCW-40= -77 dBm (Sensitivity +3 dB)
  SIR, LCW-40= 22 dB
  Criteria Comparison = +1
2.2.4 Jamming Resistance
  No devices will jam
  Criteria Comparison = +1

## Slide 23: LCW vs TG3 General Solution Criteria
2.2.5 Multiple Access
  All scenarios work with LCW-30, 40
  Criteria Comparison = +1
2.2.6 Coexistence
  LCW coexists > 80% with devices 1, 2
  LCW coexists 100% with devices 3, 4, 5
  Criteria Comparison = +1
2.3 Interoperability
  An 802.15.1 PHY and MAC is embedded into LCW, achieving a dual mode radio switchable between 802.15.1 and 802.15.3
  Criteria Comparison = +1
2.4.1 Manufacturability
  802.11b equipment of similar complexity available in 2001
  Criteria Comparison = +1

## Slide 24: LCW vs TG3 General Solution Criteria
2.4.2 Time to Market
  LCW-40 will be available Q401
  Criteria Comparison = +1
2.4.3 Regulatory Compliant with existing FCC (15.249), ETSI 300-328
  Criteria Comparison = 0
2.4.4 Maturity of Solution
  LCW is a reduction, extension of 802.11b PHY and 802.11 MAC
  Criteria Comparison = +1
2.4.5 Scalability
  LCW is scalable in data rate, frequency band, and function
  Criteria Comparison = +1
2.6 Location Awareness
  RSSI statistics distinguish device locations to resolution in meters
  Criteria Comparison = 0

## Slide 25: LCW vs TG3 MAC Criteria
3.1 Fully Transparent to Upper Protocol Layers
  Criteria Comparison= 0
3.2.1 Unique 48 bit Address
  Criteria Comparison= 0
3.2.2 Simple Network Join/Unjoin
  802.11 style Association, Disassociation for non hopping PHY is much simpler than that of 802.15.1
  Criteria Comparison= 0
3.2.3 Device Registration
  Configurable from Automatic Admit-All, to Automatic by Device Type, to various levels of Restricted Access
  Criteria Comparison= 0
3.3.2 Minimum Delivered Data Throughput
  Criteria Comparison= 0
3.3.3 High End Delivered Data Throughput
  Criteria Comparison= 0

## Slide 26: LCW vs TG3 MAC Criteria
3.4. Data Transfer Types
  PCF, asynchronous and isochronous on a per packet basis
  Criteria Comparison= +1
3.5.1 Topologies supported: point/multipoint, point/point, peer/peer
  Criteria Comparison= +1
3.5.2 Maximum number of Active Connections > 10
  Criteria Comparison= +1
3.5.3 Ad Hoc Networks supported
  Criteria Comparison= 0
3.5.4 Access to a Portal supported
  Criteria Comparison= 0
3.6.2 Master Redundancy supported
  Criteria Comparison= 0
3.6.3 Loss of Connection Detection and Recovery supported
  Criteria Comparison= 0

## Slide 27: LCW vs TG3 MAC Criteria
3.7 Power Management as in 802.11
  Slaves in deep sleep maintain active piconet connections
  Criteria Comparison= +1
3.8 MAC Controller power consumption
  Consistent with 1.5W system power consumption
  Criteria Comparison= 0
3.9.1 Authentication
  Enhanced (spoof-proof) mutual authentication
  Criteria Comparison= 0
3.9.2 Privacy
  Strong Encryption (128b RC4)
  User transparent encryption key generation, distribution, and maintenance
  Criteria Comparison= 0
3.10 QOS equivalent to 802.11e supported
  Criteria Comparison= +1

## Slide 28: Summary
LCW MAC is the result of a “Systems Design” approach to the HRWPAN
  Designed to integrate with the LCW PHY
  Nevertheless mates robustly and efficiently with other 6 PHYs
LCW MAC enables extraordinary transmission performance
  Simultaneous high throughput, low error rate and low latency
“Reduced and Extended” 802.11-like MAC
  PCF Poll-response mechanism provides efficient, centralized piconet control
  Adds Auto Channel Select, Master-slave morph, peer to peer communication
  Deletes roaming, fragmentation, RTS/CTS and 802.11 adhoc
Coexistence, Interoperability and Harmony with preexisting standards
High End Security
  Simple button push or equivalent initially establishes a highly secure WPAN
  The user does NOTHING to reestablish, maintain highly secure links thereafter
Broadcast quality, interactive multimedia capable QOS
The LCW MAC is a compelling choice for the HRWPAN standard