## Slide 1
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Kodak - High Rate PHY Proposal]
Date Submitted: [10/27/00]
Source: [Grant Carlson/James D. Allen] Company: [Eastman Kodak Co.]
Address: [4545 East River Road, Rochester, NY 14650-0898]
Voice:[(716) 781-9025], FAX: [(716) 781-9733], E-Mail:[james.d.allen@kodak.com, grantbc@earthlink.net]
Re: [802.15.3 final Call for Proposals]
Abstract: [This presentation outlines Kodak’s PHY proposal to 802.15.3 High Rate Task Group]
Purpose: [To communicate the proposal for consideration by the standards team]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Kodak’s Multi-Mode High Rate PHY Proposal to IEEE 802.15.3
Presented by Grant Carlson

## Slide 3: Imaging Market Needs
Kodak needs CHEAP high speed low power radios for WPAN applications as soon as possible
Throughputs have to be higher than 8 Mbps after de-rated for ovens and overhead
Data rates higher than 22 Mbps are optional but should be considered in the standard
Compatibility with 802.15.1 Market segments is critical

## Slide 4: Imaging Market Needs
Imaging trend is toward:
  Smaller cameras,
  Fewer Batteries, but longer battery life,
  Multimedia Functions
  Smaller Memory Formats (e.g. SD)
  More Memory, Larger images,
  Easy Access to images from anywhere.

## Slide 5: Proposal Summary
1, 5.5, 11, 22, 33, 44 Mbps Data Rates (Bi-directional Half Duplex)
Base Modes
  1 Mbps - 802.15.1 (Hopping 2FSK - TG1)
  22 Mbps - GMSK (22Msps) (Primary Mode with MBCK coding option)
  44 Mbps - 16QAM (11Msps) (Optional Mode, Requires 22Mbps mode to be included)
Sub-modes
  5.5 Mbps - GMSK (Backoff Mode for 11 Mbps)
  11 Mbps - GMSK (Backoff Mode for 22Mbps)
  33 Mbps - 16QAM (Optional Backoff for 44 Mbps)
Impairment Backoff goes from 44 -> 33 -> 22 -> 11 -> 5.5 Mbps
Optional 22Mbps mode using 16QAM at 5.5Msps allows for 6 channels (per criteria 4.4 - “# of Simultaneous PANs”)

## Slide 6: Proposal Summary
2.4 - 2.5 GHz ISM Band (International)
  For international acceptance and interoperability with BT infrastructure
Minimum 3 Channels using IEEE 802.11 Channel Spacing for a Coexistence mechanism
  Alternate Spacing: 4 overlapping channels of 22 Mbps GMSK or optional 44Mbps 16QAM
  Also 6 channels with optional 22Mbps 16QAM mode
Primary 22 Mbps Mode = Low Cost, Low Complexity- Comparable to 802.15.1 (Bluetooth) Class of Devices
Scaleable Data rate options increase usefulness and life of standard

## Slide 7: Proposal Summary
Low RF Power (FCC 15.249) w/ several power level modes.
Range and power consumption consistent with WPAN Market.
Interoperable with IEEE 802.15.1 WPAN devices, by including a TG1 Mode.
TG1 Mode is intended to be a means to interoperate with TG1 Devices.

## Slide 8: Proposal Summary
Coexistence with IEEE 802.11 (2.4GHz) WLANs using Channel spacing and Carrier sense.
Primary Mode designed to reuse as much TG1 PHY as possible to keep cost and risk low, and time to market short.
Reference Support Document 00215r0P802.15_TG3_Eastman-Kodak-Support-Documents-for-PHY-Proposal.

## Slide 9: Pedigree
1
2FSK
Hopper
22
Base
Mode
TG3 MAC
11
44
33
TG1
MAC
Mbps
Dabak
Carlson
Davis/Skellern/Heberling
5.5
GMSK
QPSK
M-ary Bi-Code Keying Options
O’Farrell
Turbo Options
Optional 22 Mbps 6 channel 16QAM mode not show for clarity.
Progressive
Backoff

## Slide 10: Comparative Comments
22 Mbps GMSK is more similar to 802.15.1 than OFDM, UWB, QAM
  Increases potential for design reuse and low cost
44 Mbps is 16QAM (Optional mode) is more similar to GMSK than OFDM or UWB.

## Slide 11: Unit Manufacturing Cost
Due to Similarities between 802.15.1 and the 22 Mbps GMSK mode:
  Same IC Processes are applicable
    2 chip solution: RF and a Baseband/MAC
  Optional Antenna Diversity and Optional MBCK Coding (i.e. Supergold) have minimal cost impact.
  Less expensive, better propagation, larger international market than complete 5GHz solutions

## Slide 12: Interference and Susceptibility
Out of band blocking
-5 dBm
30 MHz-2000 MHz
-5 dBm
3-12.75 GHz
-27 dBm
2.5-3 GHz
-27 dBm
2000-2400 MHz
Interferer power
Frequency
In band blocking
+30 dBc
12-30 MHz
+50 dBc
> 30 MHz
Interferer power
Frequency offset

## Slide 13: Intermodulation Resistance, IP3
Bluetooth modulated
Interferer
Single Tone Interferer
@ MDS + 3 dB
-34 dBm
IM
IPm = IM + IMRR/(m-1) = IM + [IM - (MDS+corr-C/I)]/(m-1)
IP3 = -34 + [-34-(-80+0-13)]/(3-1) = -4.5 dBm
f1 = fc + 25 MHz
f2 = fc + 50 MHz
fc = Carrier
corr = 10log10[10(x dB)/10-1]
=10log10[10(3 dB)/10-1] = 0 dB

## Slide 14: Intermodulation Resistance, IP2
f1 = fc + n MHz, n > 25
fc = Carrier
Bluetooth modulated
Interferer
@ MDS + 3 dB
-34 dBm
IPm = IM + IMRR/(m-1) = IM + [IM - (MDS+corr-C/I)]/(m-1)
IP2 = -34 + [-34-(-80+0-13)]/(2-1) = +25 dBm
Assume 100 % AM, use highest blocking spec at +3 dB above reference sensitivity
corr = 10log10[10(x dB)/10-1]
=10log10[10(3 dB)/10-1] = 0 dB

## Slide 15: Jamming Resistance
Microwave oven
  Avoid the 8 ms/16 ms microwave oven cycle,
  > 50% throughput
802.15.1 HV1 connection
  HV1 collides (22 MHz/79 MHz)*(1.25 ms/3.75 ms) = 7.1 %
  With re-transmissions, > 50 % throughput
802.15.1 DH5 packets
  DH5 collides (22/79 MHz) = 27.8%
  With re-transmissions, > 50% throughput

## Slide 16: Jamming Resistance (cont.)
802.15.3 DVD MPEG2
  4.5 Mb/s max rate, 5.4 Mb/s with overhead.
  Uses 5.4/45 Mb/s = 12% of time, > 50% throughput with re-transmissions
802.11a
  Not in band, 100% throughput
802.11b, DVD MPEG2
  4.5 Mb/s average rate, uses 4.5/7 Mb/s = 64% capacity.
  802.11b will back off on some 802.15.3 transmissions (via CCA), > 50% throughput

## Slide 17: Coexistence setup
Free space loss
  3 m = 50 dB, 6 m = 56 dB, 7 m = 57 dB, 10 m = 60 dB, 13 m = 62 dB
Proposed system power at other receivers
-57 dBm
-50 dBm
A2
-62 dBm
-50 dBm
A1
-62 dBm
N/A
B1
N/A
B2
-62 dBm
B1
B2

## Slide 18: Coexistence (cont.)
802.15.1 HV1 connection
  HV1 collides (22 MHz/79 MHz)*(1.25 ms/3.75 ms) = 7.1 %, no re-transmissions, > 90% throughput, +1
802.15.1 DH5 packets
  DH5 collides (22/79 MHz) = 27.8%
  With re-transmissions, > 55% throughput, 0
802.15.3 DVD MPEG2
  4.5 Mb/s max rate, 5.4 Mb/s with overhead.
  Uses 5.4/45 Mb/s = 12% of time, > 70% throughput with re-transmissions, +1

## Slide 19: Coexistence (cont. 2)
802.11a
  Not in band, 100% throughput, +1
802.11b, DVD MPEG2
  4.5 Mb/s average rate, uses 4.5/7 Mb/s = 64% capacity.
  802.11b will back off on some .3 transmissions due to same channel (via CCA), > 40% throughput , 0
Score = 2*(+1)+2*(0)+(+1)+(+1)+(0) = 4

## Slide 20
22

## Slide 21: 4 Overlapping Channels
2400
2483.5
2413
2432
2451
2470
0 dBm
-42 dBm

## Slide 22: Number of Simultaneously Operating Full Throughput PANs
3 Non-overlapping channels for 802.11 coexistence using 22 Mbps GMSK or optional 44 Mbps 16QAM.
  2412 MHz, 2437 MHz and 2462 MHz
4 Overlapping channels – 22 MHz wide using 22Mbps GMSK or optional 44Mbps 16 QAM.
- 2413 MHz, 2432 MHz, 2451MHz and 2470MHz
6 Non-overlapping channels - 11MHz wide, 22Mbps, using optional 16 QAM at 5.5Msps.
- 2408MHz, 2421MHz, 2434MHz, 2447MHz, 2460MHz and 2473MHz

## Slide 23: Interoperability
Digital modem has bandwidth to demodulate 802.15.1
PHY layer has 802.15.1 PHY capability and follows 802.15.1 rules using 802.15.1 MAC
Is not interoperable with 802.11
802.15.1 and 802.15.3 modes can not operate in the same frame

## Slide 24: Time to Market
Standard Technologies
No New Inventions Required
No New Agency Regulations Required
Short “Time to Standard” and “Time to Market”
GMSK can be built at reasonable cost with discrete parts - starts market and application development before IC’s are available

## Slide 25: Scalability
Power Consumption
  Similar to 802.15.1
  Two RF power modes
  Power Management
Data Rates
  802.15.1 compatibility mode at 1 Mbps
  5.5, 11, 22 Mbps GMSK with optional 22 Mbps
  44 Mbps 16QAM (~33Mbps available with Turbo coding method, TBD with MBCK method)

## Slide 26: Scalability
Cost
  5.5, 11 and 22 Mbps GMSK and 802.15.1 modes are required.
  Optional 22 Mbps (5.5Msps) 16QAM and 33Mbps/ 44Mbps (11Msps) 16QAM modes.
Functions
  Can be implemented as
    802.15.1 only
    802.15.1 and 802.15.3
    802.15.3 only

## Slide 27: Form and Size Factor
Similar to 802.15.1 class designs
  Same RF band, digital demod can do either
  Baseband channel filters select 22MHz or 1MHz BW
  Modified BT MAC is proposed
2 Chip solution
  RF chip: 6x6 mm 0.35 um BiCMOS technology
  MAC + Baseband: 400 kgates, 6x6 mm in 0.11 um CMOS
Minimal external parts
  1 crystal, 1 RF bandpass filter and 2 LDO regulators
Compatible with Compact Flash Cards

## Slide 28: Maturity
20 Mbps Prototypes
  Built from Discrete Components
  Tested in Open Range
    To FCC 15.249 that measures average signal strength in a 1 MHz bandwidth. Prototype output power was approx. +10dbm EIRP.

## Slide 29: Range
Range of 10 meters or greater for 22 Mbps
  Receiver sensitivity is –78 dBm
    -174 dBm/Hz + 73 dBHz + 11dB Eb/No + 12 dB NF = -78 dBm
  with a corresponding BER of 1E-04
  permits more than 10 meters range inside residential house with FCC 15.249 compliant transmitter.

## Slide 30: Power Consumption estimate
12
VCO
14
1 synth
40
BB VGA's
328 mW
Total RX
100
MAC
50
Demod
50
ADC's
50
IQ dowmixer
12
LNA
mW
Block
12
VCO
18
1 synth
50
DAC's
50
Modulator
334 (408) mW
Total TX
100
MAC
40
BB VGA'a
50
I/Q upmixer
14 (88)
PA, 0 dBm (8 dBm)
mW
Block

## Slide 31: Power Consumption Backup
PA – 0 dBm Average with 7 dB backoff
  7 dBm -> 5 mW * 35% eff at P1dB = 14 mW
  For +8 dBm, power is 6.3*14 mW = 88 mW or 74 mW additional
ADC's – 44 Msps/8 bit.
  benchmark 100 mW for 88 MHz 8 bit for IP block in 0.25 um, so 25 mW in 0.11 um.
DAC's – 44 Msps/8 bit
  Less current drain than ADC's, so < 25 mW per DAC
Synthesizers
  Benchmark: LMX2350 dual Frac-N 4.6 mA at 3 V for RF

## Slide 32
NOTE: NEXT SLIDE IS A SELF RATINGS SLIDE REQUIRED TO SUBMIT CHANGE REQUESTS
PLEASE REFER TO PHY COMMITTEE REPORT FOR FINAL RATINGS

## Slide 33: Self Evaluation - General

## Slide 34: Self Evaluation - General

## Slide 35: Self Evaluation - General

## Slide 36: Self Evaluation - PHY

## Slide 37: Self Evaluation - PHY

## Slide 38: Conclusions
This Proposal Provides a Good Combination of:
  Cost with scalability to meet application needs
  Speed options and flexibility
  Coexistence/Commonality with 802.15.1
  Short Time to Market
  Minimum Risks

## Slide 39: Conclusion - Continued
We Believe the Correct Solution Should be:
  2.4 GHz band for this market space and propagation characteristics
  5 GHz is not allowed in Japan - a Significant Market for Imaging
  Single Carrier for Simplicity
  As Simple, cheap as Possible and still Meet Customer Needs.

## Slide 40: Appendix I - Criteria Ranking Comments
This appendix addresses the issues brought up in the various committee discussions, in order to make the feedback official.

## Slide 41: Appendix I - Criteria Ranking Comments
This appendix addresses the issues brought up in the various committee discussions, in order to make the feedback official.

## Slide 42: Appendix I
PHY issues for September 12th.
  Section 2.5 Rating “0” Request “+1”
    This factor requires 3 or more scaleable factors to justify a "+1 rating. We already proposed Data rate (1Mbps BT and 22 Mbps high rate), and Range (0dbm and lower power for Kiosk work at less than one meter) This lower range also implies one of the several power saving modes. Our architecture provides many ways to power only necessary systems functions. In Addition, this architecture is compatible with 2.4 or 5GHz bands, although we recommend its uses only at 2.4GHz for cost and performance reasons. This provides a count of 4.

## Slide 43: Appendix I
  Section 4.6 Rated “?”, Request “0”
    In version two of this submission we requested a change from a "?" to a "0". It may not have been noticed. Our prototype was tested in an open range to over 300 feet, at BERs of 10-6 as charted in previous submissions. Structural testing indicated ranges in excess of 10 meters. This configuration met FCC and ETSI rules for low power devices, and had a patch antenna configuration.

## Slide 44: Appendix I
  Section 4.8.2 Rated “0”, Request “+1”
    22 Mbps GMSK system requires either antenna diversity or coding (ie. Supergold) to meet 25ns delay spread.
    Optional 44Mbps 16 QAM mode requires an equalizer (i.e.. TI) or coding (i.e.. Supergold) to meet the 25ns delay spread criteria.
    The 11 Mbps and 5.5 Mbps backoff modes increase the modulation index of the FSK system to 1 and 2 respectively while occupying the same 22MHz channel bandwidth. The increase in capture effect further reduces the multi-path affects and improves robustness of the link in high noise environments.

## Slide 45: APPENDIX II
RESPONSE TO RANGE QUESTIONS
  Q: What was antenna gain for the prototype during field test?
  A: Approx. 0 dBi
  Q: What power was used for test?
  A: The power was adjusted to the signal strength requirement of 94 dBuV/m at 3 meters. (FCC 15.249)
  Q: What was the measurement interval for the test?
  A: The test was run in two modes - first a general sweep of the field was done to plan the test - Interval was 1 minute. Then the formal field test was done in one hour increments ~72,000Mb.

## Slide 46: APPENDIX II
  Q: What was the prototype receiver sensitivity
  A: -77 dBm @ 10^-6 BER