## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LCW Proposal for High Rate WPAN Combined PHY and MAC ]
Date Submitted: [13 July 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: []
Abstract: [A joint PHY and MAC proposal by LinCom Wireless Corporation for a 1 to 40 Mbps WPAN operating in the 2.4 GHz band ]
Purpose: [Response to the High Rate WPAN CFP]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: LCW- A Proposal for a High Data Rate WPAN in the 2.4 GHz Band

## Slide 3: The Wireless Home Network Application
Enable the wireless interconnection of electronic devices within the home
  30m range, including thru-wall propagation
  Low and high speed throughput
  Real time and non-real time data
  Multiple simultaneous connections
  Support prioritization and guaranteed bandwidth, latency
  Enable coexistence, interoperability, coordination between all home wireless devices
  Coexist and perhaps interoperate with “visiting” or legacy devices designed to other standards

## Slide 4: LCW Description
LCW PHY
Coded nQAM signaling provides data rates of 1, 2, 10, 20, 30, 40 Mbps
Adaptive equalization improves range, high end throughput
Low power operation per FCC 15.249
Interoperable with 1, 2 Mbps DSSS, coexists with 5.5, 11 Mbps CCK
“Bluetooth class” device in size, cost, power consumption
LCW MAC will align with 802.11e
Retains 802.11 CSMA/CA, DCF and PCF
Adds client to AP “morphing”, direct peer to peer communication
Enhanced security features device authorization, registration, mutual authentication, 128 bit encryption and user transparent key maintenance
Real time voice, audio, video and interactive multimedia support

## Slide 5: LCW PHY
LCW-1 is 1 Mbps (11 chip) Barker encoded DBPSK
LCW-2 is 2 Mbps (11 chip) Barker encoded DQPSK
LCW-10 is 10 Mbps RS(220,200) encoded DBPSK
LCW-20 is 20 Mbps RS(220,200) encoded DQPSK
LCW-30 is 30 Mbps RS(220,200) encoded 8QAM
LCW-40 is 40 Mbps RS(220,200) encoded 16QAM
All produce 11 MSps 802.11 DSSS-like 22 MHz spectrum
Channelization can be 4 WPAN-only slightly overlapping 20 MHz channels or 3 standard 802.11 25 MHz channels
All use the 802.11 PLCP header, with appropriate service field extensions, and support both long and short preamble
5.5, 11 Mbps CCK, PBCC are not supported
CCA mechanism is identical to 802.11
LCW interoperates with 802.11 DS, coexists with 802.11b

## Slide 6: LCW MAC- General
Modified 802.11 MAC to support High Rate WPANs
Single BSS consisting of one Master (AP) and multiple Slaves (clients). The device initially establishing a network becomes the Master. A Slave may later become the Master, as appropriate, and the roles may be switched
The Master controls 802.11 Association and Disassociation services. Associated Slaves may communicate directly (peer to peer) with each other
The Master uniquely supports any active Portal, and so can support 802.11 Distribution and Integration services
The Master uniquely provides and controls security services: registration, authorization, authentication and privacy
The Master controls all PCF and QOS services

## Slide 7: LCW MAC- Multiple Access
Multiple access protocol remains CSMA/CA with a positive ACK and ARQ scheme. Enhanced ACK/ARQ protocols are supported.
Enhanced ARQ provides for retransmission of only those RS blocks (codewords) received with uncorrectable errors within a given frame. The enhanced ACK indicates the codewords to be retransmitted.
Supports point/multipoint, point/point and peer/peer links
DCF and (extended, QOS capable) PCF modes are supported with identical 802.11 timing relationships (SIFS, DIFS, PIFS)
Automatic data rate shifting is supported, but may defer to QOS prioritization and guaranteed bandwidth, latency contracts
Power Management support may vary between device types, depending on individual message buffering capability
Roaming, fragmentation, RTS/CTS, 802.11 adhoc are not supported

## Slide 8: LCW MAC- Security
Every LCW-capable device features a unique, secret factory assigned signature in addition to its MAC address
A device “Registers” with the Master upon first network access. Regis-tration may require user intervention at one or both ends.
Upon Registration the device is Authorized to access the network in the future, under the aegis of the Master (ACL)
Upon subsequent network access the device undergoes Authentication to prove he is the authorized accessor, likely with a secure exchange (Diffie Helman) of MAC Address and secret signature
The device may optionally demand “Reverse” or Mutual Authentication from the Master, to ensure that he is indeed accessing the network of interest
A unique, secret shared session key is automatically generated at both ends during Authentication, and is then used to ensure communications privacy by strongly encrypting (128b RC4) exchanged messages

## Slide 9: LCW MAC- QOS
Need to support in-home distribution of voice, audio, video and interactive multimedia
  “Single Portal” model for distribution of content likely originating beyond the single BSS, either real time broadcast or stored/cached
  Prioritization, bandwidth and latency guarantees are needed to mitigate wireless network overhead (framing, gaps, ACKs)
  Enhanced PCF eliminates collisions, backoffs, retries
  QOS-aware Master reduces overhead, prevents collisions and prioritizes incoming traffic, likely over all available channels
Proposed AT&T, ShareWave and Lucent solution for 802.11e QOS supports these services (and more)
LCW QOS MAC will “streamline” this solution as needed to focus solely on the home wireless interactive multimedia distribution problem

## Slide 10: LCW vs TG3 General Solution Criteria
2.1 Unit Manufacturing Costs
  Are intimately associated with specific MAC, PHY implementation
  Direct BB/RF Conversion architecture minimizes BOM cost
  Present day silicon technology supports single chip integration of
    RFCMOS Zero IF transceivers at 2.4 GHz
    Digital nQAM modems, adaptive equalizers, RS FECs
    80+ MIP processors suitable for software 802.11-like MACs, including encryption, QOS
    High speed SRAM
  .18u CMOS process is available in low cost fabrication facilities
  LCW Module available Q401 for <1.5x 802.15.1 cost
  Criteria Comparison = +

## Slide 11: LCW vs TG3 General Solution Criteria
2.2.2 Interference and Susceptibility
  Inband, Non-Cochannel, Non-Adjacent Channel > 35 dBc
  Out of Band > 35 dBc
  Criteria Comparison = +
2.2.3 Intermodulation Resistance
  Measured IP3 of representative RF front end= -3 dBm
  IM level produced by 2 -35 dBm tones= -99 dBm
  SOI level, LCW-40= -77 dBm (Sensitivity +3 dB)
  SIR, LCW-40= 22 dB
  Criteria Comparison = +
2.2.4 Jamming Resistance
  Device 1 will jam with 16.6% probability. No others will jam.
  Criteria Comparison = +

## Slide 12: LCW vs TG3 General Solution Criteria
2.2.5 Multiple Access
  All scenarios work with LCW-30, 40
  Criteria Comparison = +
2.2.6 Coexistence
  LCW coexists > 80% with devices 1, 2
  LCW coexists 100% with devices 3, 4, 5
  Criteria Comparison = +
2.3 Interoperability
  LCW does not interoperate with 802.15.1 by itself, but readily interfaces with a companion BT device for dual mode operation
  Criteria Comparison = Same
2.4.1 Manufacturability
  802.11b equipment of similar complexity available in 2001
  Criteria Comparison = +

## Slide 13: LCW vs TG3 General Solution Criteria
2.4.2 Time to Market
  LCW-40 available Q401
  Criteria Comparison = +
2.4.3 Regulatory Compliant with existing FCC (15.249), ETSI 300-328
  Criteria Comparison = Same
2.4.4 Maturity of Solution
  LCW is a reduction and extension of 802.11b PHY and 802.11 MAC
  Criteria Comparison = +
2.4.5 Scalability
  LCW is scalable in data rate, frequency band, and function
  Criteria Comparison = +
2.6 Location Awareness
  Historical, relative RSSI statistics distinguish locations of devices
  Criteria Comparison = +

## Slide 14: LCW vs TG3 MAC Criteria
3.1 Fully Transparent to Upper Protocol Layers
  Criteria Comparison= Same
3.2.1 Unique 48 bit Address
  Criteria Comparison= Same
3.2.2 Simple Network Join/Unjoin
  Enhanced 802.11 style association, disassociation
  Criteria Comparison= +
3.2.3 Device Registration
  Configurable from Automatic Admit-All, to Automatic by Device Type, to various levels of Restricted Access
  Criteria Comparison= +

## Slide 15: LCW vs TG3 MAC Criteria
3.3.2 Minimum Delivered Data Throughput
  Short PHY Header, MAC header, Payload, SIFS, ACK
  LCW-20, 6380 B payload = 17.14 Mbps
  LCW-30, 3300 B payload = 20.21 Mbps
  LCW-40, 3300 B payload = 24.31 Mbps
  Criteria Comparison= +
3.3.3 High End Delivered Data Throughput
  Short PHY Header, MAC header, Payload, SIFS, ACK
  LCW-40, 6600 B payload = 30.24 Mbps
  LCW-40, 30800 B payload = 37.41 Mbps
  Criteria Comparison= Same
3.4.2. Data Transfer Types
  Asynchronous or isochronous on a per packet basis
  Criteria Comparison= +

## Slide 16: LCW vs TG3 MAC Criteria
3.5.1 Topologies supported: point/multipoint, point/point, peer/peer
  Criteria Comparison= +
3.5.2 Maximum number of Active Connections > 10
  Criteria Comparison= +
3.5.3 Ad Hoc Networks supported
  Criteria Comparison= Same
3.5.4 Access to a Portal supported
  Criteria Comparison= Same
3.6.2 Master Redundancy supported
  Criteria Comparison= Same
3.6.3 Loss of Connection Detection and Recovery supported
  Criteria Comparison= Same
3.7 Power Management as in 802.11, plus Dynamic Rx Block Bias
  Criteria Comparison= +

## Slide 17: LCW vs TG3 MAC Criteria
3.8 MAC Controller power consumption
  Consistent with 1.5W system power consumption
  Criteria Comparison= Same
3.9.1 Authentication
  Enhanced (spoof-proof) mutual authentication
  Criteria Comparison= +
3.9.2 Privacy
  Strong Encryption (128b RC4)
  User transparent encryption key generation, distribution, and maintenance
  Criteria Comparison= +
3.10 QOS equivalent to 802.11e supported
  Criteria Comparison= +

## Slide 18: LCW vs TG3 PHY Criteria
4.1 Size and Form Factor
  Smaller than Compact Flash Type 1, Q401
  Criteria Comparison= +
4.2.1 Minimum Delivered Data Throughput
  LCW-40, 3300 B payload = 24.31 Mbps
  Criteria Comparison= +
4.2.2 High End Delivered Data Throughput
  LCW-40, 30800 B payload = 37.41 Mbps
  Criteria Comparison= Same
4.3 Frequency Band of Operation 2.40-2.483 GHz, unlicensed
  Criteria Comparison= Same
4.4 Number of simultaneously operating full rate WPANs
  4 LCW-40s can operate with slight frequency overlap
  Criteria Comparison= Same

## Slide 19: LCW vs TG3 PHY Criteria
4.5 Signal Acquisition identical to 802.11
  Criteria Comparison= N/A
4.6 Range not less than 30 meters, indoors (home)
  RS FEC plus equalization provide necessary range
  Criteria Comparison= +
4.7 Sensitivity, 10E-5 BER
  LCW-20= -86 dBm
  LCW-30= -83 dBm
  LCW-40= -80 dBm
4.8 Multipath Tolerance
  Chip level adaptive equalizer mitigates > 50ns delay spread
  Criteria Comparison= +
4.9 PHY Power Consumption consistent with 1.5 W system power
  Criteria Comparison= Same

## Slide 20: LCW-20 Performance- AWGN, 50ns DS Multipath

## Slide 21: Summary
LCW provides for robust 1, 2, 10, 20, 30 and 40 Mbps WPAN communications in the 2.4 GHz band
LCW is based upon mature 802.11 technology
LCW is manufacturable at near Bluetooth cost points
LCW coexists with 802.15.1 and interoperates with 802.11
The basic LCW MAC provides ease of use, scalability, high data throughput, flexible network topology, and reliable, power efficient communications
The LCW MAC also supports advanced security and QOS
The LCW PHY provides for small, cost effective, high performance and low power digital wireless communication
LCW is an ideal candidate for the 802.15.3 High Rate WPAN standard