## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [LCW Proposal for High Rate WPAN Combined PHY and MAC ]
Date Submitted: [5 September 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: []
Abstract: [A joint PHY and MAC proposal by LinCom Wireless, Inc., for a 1 to 40 Mbps WPAN operating in the 2.4 GHz band, Revision 2]
Purpose: [Response to the High Rate WPAN CFP]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: LCW A Proposal for a High Data Rate WPAN in the 2.4 GHz Band

## Slide 3: About LinCom Wireless, Inc.
Formerly the Commercial Business Units of LinCom Corp
Spun off as a separate corporation in April 2000
Wholly owned subsidiary of Titan Corporation
26 year history of developing Satellite and Terrestrial Digital Wireless Communications technology
30+ technical professionals dedicated to Systems Engineering, ASIC and embedded software development
Develop IP, ASICs, FW and board/module level products for Wireless LAN, PAN and Home Networking markets
Provide Systems Engineering services in commercial SatCom, PCS and short range wireless markets

## Slide 4: The Wireless Home Network Application
Enable the wireless interconnection of electronic devices within the home
  30m range, including thru-wall propagation
  Low and high speed throughput
  Real time and non-real time data
  Multiple simultaneous connections
  Support prioritization and guaranteed bandwidth, latency
  Enable coexistence, interoperability, coordination between all home wireless devices
  Coexist and perhaps interoperate with “visiting” or legacy devices designed to other standards

## Slide 5: “Systems” Implications
High data rate, low latency fully networked digital radio communications in the indoor multipath propagation channel
  And inexpensive, too
Simultaneous asynchronous data, voice, video and interactive multimedia links
  30 Mbps+ sustained, low latency throughput
Delay spreads of 20-50 ns for a typical SFH, thru wall/floor
  Powerful equalization and FEC needed to minimize irreducible error floors characteristic of the propagation channel
  ARQ protocols essential to deal with inevitable lost packets
The integrated LCW PHY and MAC proposed herein addresses all these demanding, conflicting requirements

## Slide 6: LCW Description
LCW PHY provides high throughput and low latency
Coded nQAM signaling provides data rates of 1, 2, 10, 20, 30, 40 Mbps
Adaptive equalization, FEC improve range and high end throughput
Low power operation per FCC 15.249
Interoperable with IEEE 802.11DS, coexists with on-channel 802.11b
Embedded 802.15.1 modem provides interoperability with Bluetooth
“Bluetooth class” device in size, cost, power consumption
LCW MAC provides enhanced security and QOS, 802.15.1 support
Retains 802.11 CSMA/CA, DCF and PCF
Adds Slave (client) to Master (AP) “morphing”, direct Slave to Slave links
Enhanced security features device registration, authorization, mutual authentication, 128 bit encryption and user transparent key maintenance
Real time voice, audio, video and interactive multimedia support
Full Bluetooth MAC included to support a dual mode 802.15.1/3 radio

## Slide 7: LCW PHY- Modulation
LCW-1 is 1 Mbps (11 chip) Barker encoded DBPSK
LCW-2 is 2 Mbps (11 chip) Barker encoded DQPSK
LCW-10 is 10 Mbps RS(220,200) encoded DBPSK
LCW-20 is 20 Mbps RS(220,200) encoded DQPSK
LCW-30 is 30 Mbps RS(220,200) encoded 8QAM
LCW-40 is 40 Mbps RS(220,200) encoded 16QAM
All produce 11 MSps 802.11 DSSS-like 22 MHz spectrum
All use the 802.11 PLCP header, with appropriate service field extensions, and slightly different preambles
  LCW-1, 2, 10 and 20 use the identical 802.11b 96 us short preamble
  LCW-30 uses a 96 us preamble featuring DBPSK, DQPSK and 8QAM symbols to aid equalizer training
  LCW-40 uses a 96 us preamble featuring DBPSK, DQPSK and 16QAM symbols to aid equalizer training

## Slide 8: LCW PHY- Channelization
Channelization
  4 overlapping 20 MHz channels
    fc= 2412, 2432, 2452, 2472 MHz
    1 MHz overlap on each side
    Same as 802.11b European Overlapped Channelization
  3 standard 25 MHz channels
    fc= 2412, 2437, 2462 MHz
    Same as 802.11 USA Non Overlapped Channelization
  Offset Raised Cosine pulse shaping
    Reduces sidebands by more than 50 dBc
    Enables compliance with US FCC emissions limits above 2.835 MHz
CCA mechanism is identical to 802.11
802.11b 5.5 and 11 Mbps CCK, PBCC are not supported
Full 802.15.1 PHY is included, is mode switchable with LCW
  RF architecture supports both QAM and GFSK up/down conversion
  Baseband hardware includes both 802.15.3 and 802.15.1 modems

## Slide 9: LCW PHY- Equalization, FEC and ARQ
Powerful equalizer minimizes and “whitens” the burst errors characteristic of the 20-50 ns Delay Spread “Naftali” channel
  Converges as rapidly as possible to the precise channel estimate (less the multipath components) and tracks for the packet duration
    Need PHY preamble of adequate length (hundreds of symbols) to train equalizer and generate the appropriate tap coefficients
    Then continuously adapt, update coefficients, symbol by symbol, over the entire duration of the frame (up to 8000 Bytes)
Strong Block Code “localizes” if not corrects whitened burst errors
  RS(220,200) corrects 10 of 200B in a block , flags if uncorrectable
  RS(220,200) is efficient (R=10/11), adds little overhead
  No interleaving is necessary, so no innate latency is introduced
  Convolutional codes are less efficient (R=1/2, 3/4)
  Turbo Codes feature large interleavers, produce much latency
Nevertheless, packets will be dropped (Equalization + FEC = 1% FER)
  But don’t have to retransmit entire packet, just uncorrectable blocks

## Slide 10: LCW MAC- Medium Access
Basic MAC protocol remains DCF, or CSMA/CA with “Enhanced ACK” (EACK) and retransmission using “Enhanced ARQ” (EARQ)
  EARQ provides for retransmission of only those RS blocks received with uncorrectable errors
  EACK indicates the specific RS blocks to be retransmitted.
Optional PCF protocol uses “Poll with EACK, EARQ” as a basis for an adaptive hybrid TDMA-CSMA/CA scheme that can support QOS
Multiple Access- Master alternately transmits packets to distinct Slaves
Single piconet (BSS) of one Master (AP) and multiple Slaves (clients)
  The device initially establishing a network becomes the Master
  A Master may later switch roles with a designated Slave
    “Master Assignment” frame promotes the Slave, transfers the Access Control List to avoid need for reregistration of the other Slaves
  Device attributes can be used to select the “best” Master for a piconet
    AC Line powered, Power Save packet buffering support
    Data sourcing, sinking capability
    A line powered, SDRAM rich Portal makes the best Master

## Slide 11: LCW MAC- Master Operation
DCF and PCF modes use identical 802.11 timing relationships (SIFS, DIFS, PIFS)
Channelization is determined using Automatic Channel Selection
  The network initiator/Master Active Scans (issues Probe Requests) to find a clear channel and there starts transmitting Beacons
  The Slaves Active Scan to find the initiator/Master as they come online
  Should the channel later degrade, the Master may decide to move
    “Graceful” degradation lets Master find new channel and notify slaves for a coordinated frequency shift
    “Abrupt” link loss forces Master to move, slaves to then find him
An offline or disabled Master will be replaced by one of his Slaves
  Lack of Beacons, unACKed transmissions determine Master loss
  First Slave needing to transmit will issue Beacons and prepare to register and authenticate the other orphaned Slaves
  Orphaned Slaves proceed to associate with the new Master

## Slide 12: LCW MAC-Network Join, Unjoin
802.11-like Association services provide for simple network Join, Unjoin
  Slaves Active Scan upon activation (Probe Request, Response)
  Then issue Enhanced Association Request (EAR) to desired Master
    EAR includes device attribute information so that the best Master can be identified for possible later Assignment
  Master grants piconet access with an Association Response
Up to 32 Slaves at a time can be Associated with one Master
Master can broadcast a packet to multiple Slaves (Point to Multipoint)
Associated Slaves can talk directly to each other, bypassing the Master
  Initiating Slave sends Reassociation frame to desired recipient Slave
  Recipient verifies the common Master, sends Reassociation response
  Peer to Peer link is active until either party requests Disassociation

## Slide 13: LCW MAC- Security
The LCWMAC security protocols are designed to “undo all the security damage” of eliminating cables and embracing wireless connectivity
Every LCW-capable device features a unique, secret factory assigned signature in addition to its MAC address
A device “Registers” with the Master upon first network access. Regis-tration can be unaided or require user intervention at one or both ends.
Upon Registration the device is Authorized (added to the ACL) to access the network in the future, under the control of the Master
Upon subsequent network access the device undergoes Authentication to prove he is the authorized accessor, likely with a secure exchange (Diffie Helman) of MAC Address and secret signature
The device may demand “Reverse” or Mutual Authentication from the Master, to ensure that he is indeed accessing the network of interest
A secret shared session key is automatically generated at both ends
  No need to enter PIN numbers or manual keys, ever
  Ensures communications privacy by strongly encrypting (128b RC4) exchanged messages

## Slide 14: LCW MAC- QOS
Need to support in-home distribution of voice, audio, video and interactive multimedia
  “Single Portal” model for distribution of content likely originating beyond the piconet, either real time broadcast or stored/cached
  PCF eliminates collisions, backoffs, retries
  Prioritization, bandwidth and latency guarantees support streaming applications
  QOS-aware Master balances Automatic Channel Selection and Data Rate Shifting to ensure connectivity and throughput when the channel degrades
Proposed AT&T, ShareWave and Lucent proposal for 802.11e QOS supports these services (and more)
LCW QOS MAC will “streamline” this proposal as needed to focus solely on the home wireless interactive multimedia distribution problem

## Slide 15: LCW MAC-General
Automatic Data Rate Shifting
  LCW is biased to operate at highest data rate possible
  When channel degrades, automatically downshifts to lower rate
  Defers to QOS prioritization, bandwidth, latency contracts under PCF
Power Management
  Slaves negotiate low power “sleep” intervals with Master
    An integer number of Beacon Intervals
    Slaves power down, except for time-keeping functions to wake up
    Master buffers all incoming packets for sleeping Slaves until they awake and reestablish active link
  Master’s message buffering capability depends on its Device Type
  Slaves maintain a network connection while in Power Save
  Slaves can sleep for seconds before waking to poll for stored data
Roaming, fragmentation, RTS/CTS, 802.11 adhoc are not supported

## Slide 16: LCW vs TG3 General Solution Criteria
2.1 Unit Manufacturing Costs
  Are intimately associated with specific MAC, PHY implementation
  Direct BB/RF Conversion architecture minimizes BOM cost
  Present day silicon technology supports single chip integration of
    RF Zero IF transceivers at 2.4 GHz
    Digital nQAM modems, adaptive equalizers, RS FECs
    80+ MIP processors suitable for software 802.11-like MACs, including encryption, QOS
    High speed SRAM
  .18u CMOS process is available in low cost fabrication facilities
  LCW Module available Q401 for <1.5x 802.15.1 cost
  Criteria Comparison = +1

## Slide 17: LCW vs TG3 General Solution Criteria
2.2.2 Interference and Susceptibility
  Inband, Non-Cochannel, Non-Adjacent Channel > 35 dBc
  Out of Band > 35 dBc
  Criteria Comparison = +1
2.2.3 Intermodulation Resistance
  Measured IP3 of representative RF front end= -3 dBm
  IM level produced by 2 -35 dBm tones= -99 dBm
  SOI level, LCW-40= -77 dBm (Sensitivity +3 dB)
  SIR, LCW-40= 22 dB
  Criteria Comparison = +1
2.2.4 Jamming Resistance
  No devices will jam
  Criteria Comparison = +1

## Slide 18: LCW vs TG3 General Solution Criteria
2.2.5 Multiple Access
  All scenarios work with LCW-30, 40
  Criteria Comparison = +1
2.2.6 Coexistence
  LCW coexists > 80% with devices 1, 2
  LCW coexists 100% with devices 3, 4, 5
  Criteria Comparison = +1
2.3 Interoperability
  An 802.15.1 PHY and MAC is embedded into LCW, achieving a dual mode radio switchable between 802.15.1 and 802.15.3
  Criteria Comparison = +1
2.4.1 Manufacturability
  802.11b equipment of similar complexity available in 2001
  Criteria Comparison = +1

## Slide 19: LCW vs TG3 General Solution Criteria
2.4.2 Time to Market
  LCW-40 will be available Q401
  Criteria Comparison = +1
2.4.3 Regulatory Compliant with existing FCC (15.249), ETSI 300-328
  Criteria Comparison = 0
2.4.4 Maturity of Solution
  LCW is a reduction, extension of 802.11b PHY and 802.11 MAC
  Criteria Comparison = +1
2.4.5 Scalability
  LCW is scalable in data rate, frequency band, and function
  Criteria Comparison = +1
2.6 Location Awareness
  RSSI statistics distinguish device locations to resolution in meters
  Criteria Comparison = 0

## Slide 20: LCW vs TG3 MAC Criteria
3.1 Fully Transparent to Upper Protocol Layers
  Criteria Comparison= 0
3.2.1 Unique 48 bit Address
  Criteria Comparison= 0
3.2.2 Simple Network Join/Unjoin
  802.11 style Association, Disassociation for non hopping PHY is much simpler than that of 802.15.1
  Criteria Comparison= +1
3.2.3 Device Registration
  Configurable from Automatic Admit-All, to Automatic by Device Type, to various levels of Restricted Access
  Criteria Comparison= +1
3.3.2 Minimum Delivered Data Throughput
  Criteria Comparison= 0
3.3.3 High End Delivered Data Throughput
  Criteria Comparison= 0

## Slide 21: LCW vs TG3 MAC Criteria
3.4. Data Transfer Types
  PCF, asynchronous and isochronous on a per packet basis
  Criteria Comparison= +1
3.5.1 Topologies supported: point/multipoint, point/point, peer/peer
  Criteria Comparison= +1
3.5.2 Maximum number of Active Connections > 10
  Criteria Comparison= +1
3.5.3 Ad Hoc Networks supported
  Criteria Comparison= 0
3.5.4 Access to a Portal supported
  Criteria Comparison= 0
3.6.2 Master Redundancy supported
  Criteria Comparison= 0
3.6.3 Loss of Connection Detection and Recovery supported
  Criteria Comparison= 0

## Slide 22: LCW vs TG3 MAC Criteria
3.7 Power Management as in 802.11
  Slaves in deep sleep maintain active piconet connections
  Criteria Comparison= +1
3.8 MAC Controller power consumption
  Consistent with 1.5W system power consumption
  Criteria Comparison= 0
3.9.1 Authentication
  Enhanced (spoof-proof) mutual authentication
  Criteria Comparison= +1
3.9.2 Privacy
  Strong Encryption (128b RC4)
  User transparent encryption key generation, distribution, and maintenance
  Criteria Comparison= +1
3.10 QOS equivalent to 802.11e supported
  Criteria Comparison= +1

## Slide 23: LCW vs TG3 PHY Criteria
4.1 Size and Form Factor
  Smaller than Compact Flash Type 1, Q401
  Criteria Comparison= +1
4.2.1 Minimum Delivered Data Throughput
  PHY Header, MAC header, Payload, SIFS, EACK, DIFS
  LCW-40, 1400 B payload = 21.56 Mbps
  LCW-30, 2000 B payload = 20.61 Mbps
  LCW-20, 8000 B payload = 18.55 Mbps
  Criteria Comparison= +1
4.2.2 High End Delivered Data Throughput
  PHY Header, MAC header, Payload, SIFS, EACK, DIFS
  LCW-40, 8000B payload = 34.79 Mbps
  Criteria Comparison= 0
4.3 Frequency Band of Operation 2.40-2.483 GHz, unlicensed
  Criteria Comparison= 0

## Slide 24: LCW vs TG3 PHY Criteria
4.4 Number of simultaneously operating full rate WPANs
  4 LCW-40s can operate with slight frequency overlap
  Criteria Comparison= 0
4.5 Signal Acquisition identical to 802.11
  Criteria Comparison= 0
4.6 Range not less than 30 meters, indoors (home)
  RS FEC plus equalization provide necessary range
  Criteria Comparison= 0
4.7 Sensitivity, 10E-5 BER
  LCW-20= -86 dBm
  LCW-30= -83 dBm
  LCW-40= -80 dBm
4.8 Multipath Tolerance
  Adaptive equalizer mitigates > 50ns delay spread
  Criteria Comparison= +1
4.9 PHY Power Consumption consistent with 1.5 W system power
  Criteria Comparison= 0

## Slide 25: LCW-20 Performance- AWGN, 50ns DS Multipath

## Slide 26: Summary
LCW provides for robust 1, 2, 10, 20, 30 and 40 Mbps WPAN communications in the 2.4 GHz band
LCW is based upon mature 802.11 and 802.15.1 technology
LCW is manufacturable at near Bluetooth cost points
LCW interoperates with 802.15.1 and 802.11DS
The basic LCW MAC provides ease of use, scalability, high throughput, low latency, flexible network topology, and reliable, power efficient communications
The LCW MAC also supports advanced security and QOS
The LCW PHY provides for small, cost effective, high performance and low power digital wireless communication
LCW is an ideal candidate for the 802.15.3 High Rate WPAN standard