## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Update to Frequency Hopping Multi-mode QAM Physical Layer Proposal for High Rate WPANs]
Date Submitted: [5Sep00]
Source: [Jeyhan Karaoguz] Company [Broadcom Corporation]
Address [16215 Alton Parkway, Irvine, CA 92619 USA]
Voice:[+1 949 585 6168], FAX: [+1 949 450 0754], E-Mail:[jeyhan@broadcom.com]
Re: [-00/211r1 + the standard IEEE 802.15 template was applied by the IanG.]
Abstract: [Update to Frequency Hopping Multi-mode QAM Physical Layer Proposal for High Rate WPANs.]
Purpose: [This file contains the updates to our Frequency Hopping PHY proposal (2.4 GHz) in response to the request for size, complexity, and power by the 802.15.3 PHY Evaluation Committee.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: From: jeyhan@broadcom.com
Sent: Tuesday, September 05, 2000 4:18 PM
To: Barr John-ARES35X; stds-802-wpan@ieee.org
Cc: allen.heberling@kodak.com; Pat.Kinney@intermec.com;
jgilb@mobilian.com; 'DuVal, Mary'; james.d.allen@kodak.com
Subject: wpan/ Update to Broadcom's Frequency Hopping PHY layer
Attached power point file contains the updates to our Frequency Hopping PHY
proposal (2.4 GHz) in response to the request for size, complexity, and
power by the 802.15.3 PHY Evaluation Committee.
Best regards,
Jeyhan

## Slide 2
Jeyhan Karaoguz
Broadcom Corporation
16215 Alton Parkway
Irvine, CA 92606
Contact e-mail: jeyhan@broadcom.com
In response to request for information for size, power, and complexity
by 802.15.3 PHY subgroup
Update to Frequency Hopping Multi-mode QAM Physical Layer Proposal for High Rate WPANs

## Slide 3: Regulatory Update
As of August 22, 2000, FCC amended the Part 15 rules to allow for frequency hopping spread spectrum transmitters use 5 MHz wide channels (15 hopping channels in the 2400 - 2483.5 MHz band)
  With the new rule change, from a scalability point of view, our 5 MHz bandwidth frequency hopping multi-mode QAM proposal has the ability to transmit up to 21 dBm power for extended range beyond 10 meters

## Slide 4: Transmitter Complexity
Digital Baseband Processing
  Randomizer
  Preamble generator
  TCM encoder
  Pulse shaping filter
  Total digital gate complexity: 10K gates
Analog Front-end
  Dual 8-bit DACs (8 Msamples/sec)
  Baseband to RF up-conversion
  0 dBm output on-chip PA (5 dB back-off from 1 dB compression point)
  RF synthesizer block (VCO, PLL, etc) shared with receive section
Power Consumption (Analog + Digital) (0 dBm)
  ~67 mW for .18u technology

## Slide 5: Receiver Complexity
Digital Baseband Processing
  Square-Root-Raised-Cosine Filter: 25% excess bandwidth
  Feed-forward equalizer: 8 symbol interval span
  Decision feedback sequence estimation (4 taps for the feedback filter)
  Signal acquisition block
  8-State 2-D Viterbi decoder
  Total digital gate complexity: 75K gates
Analog Front-end
  Dual 8-bit A/D converter (8 Msamples/sec)
  AGC
  RF-to-IF down conversion block
  IF-to-baseband down conversion
  RF synthesizer block (VCO, PLL etc.) shared with transmit section
Power Consumption (Analog + Digital)
  ~108 mW for .18u technology

## Slide 6: Dual Mode 802.15.1/3 Radio Architecture
Due to frequency hopping (1600 hops/sec) nature of the proposed high rate WPAN proposal, only RF filters need to be programmable while the rest of the blocks are shared between 802.15.1 and 802.15.3 modes
LNA
PA
Mixer
BPF
IF to Baseband
Conversion
PGA
Mixer
LPF
1/5 MHz
Programmable
LO
Generation
Control
Channel
Select
PLL
To Baseband
Processor
From Baseband
Modulator
Control
interface
Dual-mode 802.15.1/3 Radio Chip
TDD
switch
1/5 MHz
Programmable
.
IF BW
Programmable
.

## Slide 7
Flash
Program
Memory
(32K)
Mixed Signal Baseband Core (Mod/Demod)
8-bit Dual DAC
8-bit Dual ADC
TX/RX square-root-raised-cosine filters
TCM encoder
Signal acquisition
Channel estimation
Feed-forward equalizer
Decision-feedback sequence estimator
Total Digital Gate Count: 85K
MAC Controller
Dual mode 802.15.1/3 MAC
Integrated micro-processor
Integrated SRAM
Data buffers
External memory interface
Host interfaces
Dual-mode
802.15.1/3
Radio
Crystal
.
0.18u CMOS
16 mm2
Total chip area
(including MAC)
0.18u CMOS
23 mm2
UART, USB,
PCI, etc.
Overall System Components
1. Dual-mode radio chip
2. Baseband PHY/MAC chip
3. Flash program memory
4. Crystal
Dual Mode 802.15.1/3 Overall System Architecture