## Slide 1
Submission Slide <number> Dr. Rajugopal Gubbi, Sharewave Inc.,
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Qos based MAC proposal for the High Rate 802.15 Standard]
Date Submitted: [July 2000]
Sources:
[Dr. Rajugopal Gubbi] Company: [ShareWave, Inc.,]
Address: [5175, Hills dale Circle, El Dorado Hills, CA 95740]
Voice:[(916) 939-9400 x 3119], FAX: [(916) 939-9434], E-Mail:[Raju.Gubbi@Sharewave.com]
[Walt Davis] Company: [Motorola]
Address: [1303 E. Algonquin Road, Fourth Floor, Schaumburg, IL 60196]
Voice:[(847) 576-3311], FAX: [(847) 576-5292], E-Mail:[Walt.Davis@email.mot.com]
Re: [ Detailed presentation of the MAC layer proposal doc-IEEE P802.15-00/209r1 ]
Abstract: [This presentation material adds more details to the presentation in doc-IEEE 802.15-00/208r1. The material presented in this doc are drawn directly from doc-IEEE 802.15-00/209r1. The introductory information regarding the proposal is already presented in doc-IEEE 802.15-00/208r1 and hence the same is briefly described in the first few slides in this doc. To make the best use of committee’s time, this presentation addresses the next level of descriptions of a few selected, but important enhancements. These enhancements include the packet format, channel access mechanism, signaling scheme, quality of service and master redundancy. The rest of the enhancements, the finer details of the commands used in all the enhancements and the procedures followed are described in doc-IEEE 802.15-00/209r1 ]

## Slide 2
Submission Slide <number> Dr. Rajugopal Gubbi, Sharewave Inc.,
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Purpose: [Response to WPAN-HRSG Call for Applications]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 3
Qos based Mac proposal for high rate 802.15 standard
Dr. Rajugopal Gubbi
Sharewave, Inc.
Walt Davis
Motorola

## Slide 4: Overview
  Introduction
  Ways to integrate with 802.15.1
  Channel access mechanism
  Packet format
  Signaling/Command packet
  Device connection procedure
  Qos - Stream connection procedure
  Qos - Selectable retransmission
  Qos - Repeater service
  Qos - Dynamic bandwidth management
  Master redundancy
  Dynamic channel selection
  Power management
  Authentication and privacy enhancements
  Device Registration

## Slide 5: Introduction
  Wherever possible, reuse the technology and implementation infrastructure of IEEE 802.15.1
  IEEE 802.15.1 like TDMA, with dynamic bandwidth allocations for better use of available bandwidth
  IEEE 802.15.1 like Master-client architecture and the master need not be collocated with Portal entity
  IEEE 802.15.1 like signaling scheme
  Agreement based connections in the network
  Stream based QoS extensions with negotiable Qos parameters per stream
  Negotiable selective retransmission scheme to reduce the retransmission overhead and increase the efficiency

## Slide 6: Introduction (contd..)
  Repeater services to those links that are currently unreliable
  Dynamic bandwidth allocation and management to improve the efficiency in use of available bandwidth
  Mechanisms for master redundancy and dynamic channel selection
  Enhanced power management scheme for maximum power save and reduced burden on the master
  Ease of use enhancements to the authentication and privacy mechanisms specified in IEEE 802.15.1
  Ease of use extensions of device registration
  The proposal provides two ways of integrating with the 802.15.1 MAC

## Slide 7: Ways to integrate with 802.15.1 - first option
  Change channel access from fixed TDMA to Dynamic TDMA
  Enhanced Qos mechanisms/policies above the 802.15.1 mechanisms
  Introduce or enhance existing mechanisms for master redundancy, dynamic channel selection, power management and device registration.
TG3-MAC
(option-1)
802.15.1-MAC
Dynamic TDM channel access
Qos policies/mechanisms
Convergence layers and other higher interfaces

## Slide 8: Ways to integrate with 802.15.1 - second option
  Enhanced Qos mechanisms/policies with dynamic TDM channel access as the core 802.15.3 MAC
  Introduce or enhance existing mechanisms for master redundancy, dynamic channel selection, power management and device registration
  Carve out a time duration for 802.15.1-MAC within each network frame for interoperability. This means that 802.15.3 only needs to refer to 802.15.1 but not alter/modify it. Further, the time reservation can be made only after recognizing the presence of an 802.15.1 network. Standardize ONLY the hooks needed for this in TG3.

## Slide 9: Ways to integrate with 802.15.1 - second option
TG3-MAC
(option-2)
802.15.1-MAC
Dynamic TDM channel access
Integrated Qos
policies/mechanisms
Convergence layers and other higher interfaces
Hooks and I/f for time allocation for 802.15.1

## Slide 10: Channel access
reQuest Slot
PHY frame body
PHY frame
One PHY frame
PHY Header
Network Frame
Network Frame
One Network Frame
One Tx Slot
Stream1
Stream2
Stream3
Stream4
Tx Slot for device-1
Tx Slot for device-2
Tx Slot for device-n
MAC Packet Body
PHY frame body (MAC packet)
MAC Header
FEC, CRC

## Slide 11: Channel access (contd..)
Enhancement to IEEE 802.15.1 TDMA
Beacon from master marks the beginning of each network frame
Each network frame is divided into a number of (unequal) tx-slots and are allocated to different devices
One or more (dis-contiguous) tx-slots may be allocated to a device
Tx-slot duration can be dynamically renegotiated
Devices transmit their data within their allocated tx-slot. Decisions about the sequence of transmission is local to the device, but the order of stream priority must be followed
Devices indicate tx of their last packet so that the next device in line for tx can reclaim any temporarily left over channel time

## Slide 12: Packet format
Frag (1 bit)
Version (2 bits)
Source CS-ID (8 bits)
Stream sequence number (total 16 bits, High 8 bits)
PP (2 bits)
Unique Subnet ID (total 16 bits, High 8 bits)
Unique Subnet ID (total 16 bits, Low 8 bits)
Destination CS-ID (8 bits)
Reserved (2 bits)
Stream sequence number (total 16 bits, Low 8 bits)
Reserved (8 bits)
Reserved (8 bits)
Stream Index (total 16 bits, Low 8 bits)
Reserved (8 bits)
Stream Index (total 16 bits, High 8 bits)
M (1 bit)

## Slide 13: Packet format (contd..)
  Version bits indicate the version of the protocol
  PP bits mark the first/last packets in Tx-slot (ignored if M=1)
  M bit to mark the packets repeated by the master
  Frag bit to inform that the next packet belongs to the same data segment as the current one.
  Client session ID (CS-ID) for each client is assigned by master
  Subnet ID common for the entire network
  Stream index to identify the stream (index=0 is for non-stream data and index=1 is for command/signaling packets)
  Stream sequence number to identify each packet within a stream

## Slide 14: Signaling/Command packet
Command-1
Command-2
Command-n
Command
payload, if any
Cmd Payload length
1
2
Bytes
Signaling similar to that in IEEE 802.15.1

## Slide 15: Signaling/Command packet (contd..)
Command-1
Command-2
Command-n
Sub-Cmd payload
Command
payload, if any
Cmd Payload length
1
2
Bytes
Sub-cmd #1
Sub-cmd payload
Sub-cmd #m
Sub-cmd Payload length
Sub-cmd #2
Sub-cmd payload
Sub-cmd Payload length
1
2
Bytes
Enhancement of Subcommands

## Slide 16: Signaling/Command packet (contd..)
Command frame Body
Command-1
Command-2
Command-n
Sub-Cmd payload
Command
payload, if any
Cmd Payload length
1
2
Bytes
Sub-cmd #1
Sub-cmd payload
Sub-cmd #m
Sub-cmd Payload length
Sub-cmd #2
Sub-cmd payload
Sub-cmd Payload length
1
2
Bytes
uBlockSeq
payload,
ublk Payload length
1
2
Bytes
1
uBlock #1
uBlock #2
uBlock #n
Bytes
ublk Seq Ack
Further enhancement of cmd micro blocks

## Slide 17: Signaling/Command packet (contd..) - Reliability
  Command packet body contains a uBlock-Seq-Ack and several uBlocks
  Each uBlock has its own seq-number and a chain of commands
  A command itself can contain a chain of subcommands
  Each of (subcommand, command, uBlock) has length indicated so that several of them can be chained together without any ambiguity
  The receiving device sends the last received uBlock seq as Ack in its command packet
  the transmitting device removes a uBlock from the next command packet if the ublock does not need retransmission or if it is timed out or an ack is received to indicate the successful reception

## Slide 18: Device connection procedure
  New clients use reQuest slot to send connection requests
  Master recognizes the request and authenticates the device
  Client sends a connection agreements to master
  Master negotiates the agreements and allocates the channel time
  The client starts using the channel time
  The client is disconnected if there is not sufficient bandwidth or there are already max number of clients in the network
Master
Client
CRQ
CRQ (with CS-ID)
CAG-req
Authentication (Challenge-response)
CAG (negotiation)
CAG-grant (with valid tx-slot)
Client uses the tx-slot
CAG-grant-ack

## Slide 19: Streams and Quality of service
  Stream is the unit of a QoS contract
  A stream is identified by Stream index, which is unique in the network
  QoS parameters of each stream are known at transmitter, receiver and the master
    Min, max and average rates for the stream
    Max burst size
    Ave packet size
    Max delay and Jitter
    Priority
    Security type
    FEC type
    Max retransmission duration
    Rx window size

## Slide 20: Stream connection procedure - tx stream request
Master
Client-A
Stream connection request
Stream connection grant (with stream ID)
Stream parameters negotiation
Stream connection grant
Stream connection-grant-ack
Client-B
Stream connection grant ack
Stream connection request (with stream ID)
Authentication (if not done already)
Stream parameters negotiation

## Slide 21: Stream connection procedure - rx stream request
Master
Client-A
Stream connection request
Stream connection grant (with stream ID)
Stream parameters negotiation
Client-B
Stream connection grant ack
(rx) Stream connection request
Authentication (if not done already)
Stream connection grant
Stream connection-grant-ack
Stream parameters negotiation

## Slide 22: Selectable retransmission
  Different streams have different needs for ACKs and retries
    ACKs take time and require Tx-Rx turnarounds that reduce the throughput. Hence they should only be used when and as needed
    With FEC, the need for frequent retries can be significantly reduced
  Re-transmission parameters are negotiated for each stream as part of stream connection process
  Rx device accumulates the retransmission requests and sends as a combined response in its tx-slot
  Tx device performs selective re-transmission (as opposed to go-back-to-n)

## Slide 23
Repeater service
Master
Client A
Client B
Master
Client A
Client B
  Peer to peer communications among the devices in the network
  When a device can not receive from another device or when there is incompatibility in power save duration, the master is requested to provide the repeater service
  The device transmitting the stream continues to do so as before. But the master repeats the data to the convenience of the rx device. The ‘M’ bit in these repeated packets is set to ‘1’ to indicate the repetition.

## Slide 24: Dynamic bandwidth management
  The tx-slot is allocated depending on the requests from the clients
  The duration of tx-slot is dynamically negotiable
  Each device indicates its request for bandwidth in the groups of priority of the streams entertained using CAG-req command
  Master allocates the bandwidth starting from the device with highest priority streams using CAG-grant command
  Master can renegotiate the bandwidth of a lower priority stream to entertain the requests from an higher priority stream using CAG-negotiate command
  All tx-slot allocations are relative to the reception of beacon from master
  If a device could not make use of its allocation in the current network frame, the next device in line for transmission can reclaim the unused time for its buffered data.

## Slide 25
Master redundancy
Master
Client A
Master
Master
Client A
Client B
(Alt Master)
No Single Point of Failure

## Slide 26: Master redundancy (contd..)
  The master knows alternate masters (AM) through the information provided by each device during the connection establishment
  The master hands over its responsibility to a suitable AM in case it can not handle the current network conditions or upon the detection of failure (or shut down) within itself.
  Self configuration of the network
  Each device in the network can be capable of being a master
  In the absence of master, multiple clients vote among themselves to choose a master and establish the network
  The criteria for the selection are drawn from requirements of a device in its real-life production form. Examples are # of external connections and device memory capacity (for data buffering)

## Slide 27: Dynamic channel selection
  Dynamic channel selection is the ability to dynamically choose the physical channel on which a single network should operate. This is used when either
    a client is searching for master
    master decides that the current channel is too severe for the network to operate
    To overcome overlapped network scenario
  This capability is a requirement for the European market for the 5.2GHz band

## Slide 28: Dynamic channel selection
Master
Client
Channel statistics (sent periodically)
Remain Quiet (to clients)
Remain Quiet ack
Severe channel -> Master decides to change channel
Master searches for a better channel
Change channel (with new ch-ID)
All devices change to new channel and resume operation
Change channel ack

## Slide 29: Power Management
  Active, Sniff, hold and park modes as in 802.15.1
  In addition, a decentralized power management scheme
  Each rx device announces its PS parameters that includes its awake duration, periodicity etc.
  Each tx device appropriately adjusts its transmission times as per the PS parameters of the destination rx device. If tx device can not handle it transfers the responsibility to the master.
  This reduces the burden on the master wherever tx devices can handle the PS params of rx device(s)

## Slide 30: Security and Authentication enhancements
  Minimal or no human interaction
    User input keys at device registration and whenever key changes
    No user interaction once the device is key is provided
  Further studies on automating the keys to avoid any user action is under study. While the mechanisms for such automation (using algorithms like Diffie-Helman for key exchange) may be required, study to understand (a) the balance between such automation and the user comfort in trusting such automation (b) the additional complexity in such automation is required before attempting to propose such extensions.

## Slide 31: Device registration
  Minimal or no human interaction
  1. User input subnet information at device registration
  2. Minimal user interaction like a button touch or a mouse click, if open enrollment is used with minimal user interface
  3. NO user interaction if open enrollment is used and all devices are admitted to the subnet
  New devices send connection req packet with special values in CS-ID and Subnet ID to indicate that it is a new registration
  Master recognizes the registration request and depending on the implementation (of master) allows the device w/ or w/o user interaction.

## Slide 32: Questions?