## Slide 1
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Kodak - High Rate PHY Proposal]
Date Submitted: [11July2000]
Source: [James D. Allen] Company: [Eastman Kodak Co.]
Address: [1669 Eastman Ave. Rochester, NY, 14650-2015]
Voice:[(716) 588-1906], FAX: [(716) 722-9053], E-Mail:[james.d.allen@kodak.com, grantbc@earthlink.net]
Re: [802.15.3 final Call for Proposals]
Abstract: [This presentation outlines Kodak’s PHY proposal to 802.15.3 High Rate Task Group]
Purpose: [To communicate the proposal for consideration by the standards team]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Kodak’s High Rate PHY Proposal to IEEE 802.15.3
Presented by Jim Allen

## Slide 3: Summary
15, 30 and 45 Mbps Data Rates
MSK, QPSK and 8PSK Bi-directional Half Duplex
Low Cost - Comparable to 802.15.1 (Bluetooth) Class of Devices
2.4 - 2.5 GHz ISM Band (International)
  for International Acceptance
  for Interoperability with BT infrastructure and applications
Minimum 3 Channels, 4 channels with 1 MHz overlap
Low RF Power Operation ( approx. 0dBm)
Range and Power Consumption similar to 802.15.1

## Slide 4: Summary
Interoperable with IEEE 802.15.1 WPAN Devices
Presence Detection Capability for 802.15.1 Signals
Coexistence with IEEE 802.11 (2.4GHz) WLANs
Position for Low Cost sharing Majority of IEEE 802.15.1 Software and Hardware components.
Reference Support Document 00215r0P802.15_TG3_Eastman-Kodak-Support-Documents-for-PHY-Proposal

## Slide 5: Comparative Comments
Same Scheme as 802.15.1 but:
  Doesn’t hop
  Faster MAC
  Wider BW
  Different Base-Band Signal

## Slide 6: Unit Manufacturing Cost
Due to Similarities with BT
  Same IC Processes are applicable
  Cost about $1 more for External Components.
  Slightly More Cost for Antenna System (Stearable Array)
Potentially Less Expensive than 5GHz Solutions.

## Slide 7: Interference and Susceptibility
Out of band blocking | 
Frequency | Interferer power
30 MHz-2000 MHz | -5 dBm
2000-2400 MHz | -27 dBm
2.5-3 GHz | -27 dBm
3-12.75 GHz | -5 dBm
In of band blocking | 
Frequency offset | Interferer power
10-30 MHz | +30 dBc
> 30 MHz | +50 dBc

## Slide 8: Intermodulation Resistance, IP3
Bluetooth modulated
Interferer
Single Tone Interferer
@ MDS + 3 dB
-34 dBm
IM
IPm = IM + IMRR/(m-1) = IM + [IM - (MDS+corr-C/I)]/(m-1)
IP3 = -34 + [-34-(-80+0-13)]/(3-1) = -4.5 dBm
f1 = fc + 25 MHz
f2 = fc + 50 MHz
fc = Carrier
corr = 10log10[10(x dB)/10-1]
=10log10[10(3 dB)/10-1] = 0 dB

## Slide 9: Intermodulation Resistance, IP2
f1 = fc + n MHz, n > 25
fc = Carrier
Bluetooth modulated
Interferer
@ MDS + 3 dB
-34 dBm
IPm = IM + IMRR/(m-1) = IM + [IM - (MDS+corr-C/I)]/(m-1)
IP2 = -34 + [-34-(-80+0-13)]/(2-1) = +25 dBm
Assume 100 % AM, use highest blocking spec at +3 dB above reference sensitivity
corr = 10log10[10(x dB)/10-1]
=10log10[10(3 dB)/10-1] = 0 dB

## Slide 10: Jamming Resistance
Microwave oven
  Detection algorithm avoids the 8 ms/16 ms microwave oven cycle, > 50% throughput
802.15.1 HV1 connection
  HV1 collides (18 MHz/79 MHz)*(1.25 ms/3.75 ms) = 7.6 %
  With re-transmissions, > 50 % throughput
802.15.1 DH5 packets
  DH5 collides (18/79 MHz) = 22.8%
  With re-transmissions, > 50% throughput

## Slide 11: Jamming Resistance (cont.)
802.15.3 DVD MPEG2
  4.5 Mb/s max rate, 5.4 Mb/s with overhead.
  Uses 5.4/45 Mb/s = 12% of time, > 50% throughput with re-transmissions
802.11a
  Not in band, 100% throughput
802.11b, DVD MPEG2
  4.5 Mb/s average rate, uses 4.5/7 Mb/s = 64% capacity.
  802.11b will back off on some .3 transmissions (via CCA), > 50% throughput

## Slide 12: Coexistence
802.15.1 hops into receiver bandwidth
Discriminator can detect BT 1 Mbps symbol rate
Rules for coexistence could be determined with 802.15.1
Channel structure is close to 802.11 to better co-exist with DSSS systems

## Slide 14: 4 Overlapping Channels
2400
2483.5
2413
2432
2451
2470
0 dBm
-42 dBm

## Slide 15: Interoperability
Digital modem has bandwidth to demodulate 802.15.1
PHY layer has FH capability and follows 802.15.1 rules
MAC controls PHY Mode
Is not interoperable with 802.11
.1 and .3 modes can not operate in the same Frame

## Slide 16: Time to Market
Standard technologies
No New Inventions Required
No New Agency Regulations Required

## Slide 17: Scalability
Power Consumption
  Similar to 802.15.1
  Two RF power modes
  Power Management
Data Rates
  Variable from 15 to 45 Mbps
  802.15.1 compatibility mode

## Slide 18: Scalability
Cost
  TBD - Depends on implementation
Functions
  Can be implemented as 802.15:
    .1 only
    .1 and .3
    .3 only

## Slide 19: Form and Size Factor
Similar to 802.15.1 class designs
  Same RF band, digital demod can do either
  Baseband channel filters can select 10 or 1 MHz spacing (VLIF with IR mixers for 802.15.1)
  BT MAC is re-used for high rate, available for compatibility
2 Chip solution
  RF chip: 6x6 mm 0.35 um BiCMOS technology
  MAC + Baseband: 400 kgates, 6x6 mm in 0.11 um CMOS
Minimal external parts
  1 crystal, 1 RF bandpass filter and 2 LDO regulators
Compatible with Compact Flash Cards

## Slide 20: Maturity
Prototypes
  Built from Discrete Components
  Tested in Open Range

## Slide 21: Range
Range of 10 meters or greater
  at a receiver sensitivity of -70dBm
  with a corresponding BER of 1E-03 or -04
  permits more than 10 meters range inside residential house with 0dbm xmtr.

## Slide 22: Number of Simultaneously Operating Full Throughput PAN
20 MHz wide RF Channel with root-raised cosine data filter allows 4 full Channels with 1 MHz overlap
  2413 MHz, 2432 MHz, 2451 MHz and 2470 MHz
Three non-overlapping channels for 802.11 coexistence
  2412 MHz, 2437 MHz and 2462 MHz

## Slide 23: Power Consumption estimate
Block | mW
LNA | 12
IQ dowmixer | 50
1 synth | 14
VCO | 12
BB VGA's | 40
ADC's | 50
Demod | 50
MAC | 100
Total RX | 328 mW
Block | mW
PA | 14
I/Q upmixer | 50
BB VGA'a | 40
Modulator | 50
1 synth | 18
VCO | 12
DAC's | 50
MAC | 100
Total RX | 334 mW

## Slide 24: Power Consumption Backup
PA – 0 dBm with 7 dB backoff for high rate mode
  7 dBm -> 5 mW * 35% eff at P1dB = 14 mW
ADC's – 60 MHz/8 bit.
  benchmark 100 mW for 88 MHz 8 bit for IP block in 0.25 um, so 25 mW in 0.11 um.
DAC's – 60 MHz/8 bit
  Less current drain than ADC's, so < 25 mW per DAC
Synthesizers
  Benchmark: LMX2350 dual Frac-N 4.6 mA at 3 V for RF

## Slide 25: Self Evaluation - General

## Slide 26: Self Evaluation - General

## Slide 27: Self Evaluation - General

## Slide 28: Self Evaluation - PHY

## Slide 29: Self Evaluation - PHY

## Slide 30: Conclusion
This Simple Proposal Provides a Good Combination of:
  Cost
  Speed
  Coexistence/Commonality with 802.15.1
  Time to Market
  Minimum Risks

## Slide 31: Criteria Changes
Propose PHY Criteria is Data Rate, and listed Independent of MAC.
Propose Max. 2.4GHz channel bandwidth is limited to 20 MHz to support 802.11 channel plan

## Slide 32: Appendix I - Criteria Ranking Comments
This appendix addresses the issues brought up in the various committee discussions, in order to make the feedback official.

## Slide 33: Appendix I
PHY issues for September 12th.
  Section 2.5 Rating “0” Request “+1”
    This factor requires 3 or more scaleable factors to justify a "+1 rating. We already proposed Data rate (1Mbps BT and 22 Mbps high rate), and Range (0dbm and lower power for Kiosk work at less than one meter) This lower range also implies one of the several power saving modes. Our architecture provides many ways to power only necessary systems functions. In Addition, this architecture is compatible with 2.4 or 5GHz bands, although we recommend its uses only at 2.4GHz for cost and performance reasons. This provides a count of 4. In addition, one of the original functions of our architecture and implementation included an IF capable of receiving control, or low bandwidth signals from the ~400MHz band even without the RF Rcvr or Xmtr sections being powered. Although not currently in our plans, this architecture still has that potential for this function and should be considered a feature for this body of experts to consider.

## Slide 34: Appendix I
  Section 4.6 Rated “?”, Request “0”
    In version two of this submission we requested a change from a "?" to a "0". It may not have been noticed. Our prototype was tested in an open range to over 300 feet, at BERs of 10-6 as charted in previous submissions. Structural testing indicated ranges in excess of 10 meters. This configuration met FCC and ETSI rules for low power devices, and did have a patch antenna configuration.

## Slide 35: Appendix I
  Section 4.8.2 Rated “0”, Request “+1”
    The capture effect of 2 and 4 FSK systems, tend to reduce the multi-path affects when the incident signal strength exceeds any reflected signal by about 6 db. Consequently, this criteria should include magnitude aspects in addition to time. Walt Davis has volunteered to present simulation data to support the field and lab results we observed in our prototypes. It is being planed for the September meeting. Since this affect simplifies the architecture for a given price/performance point, I would like to argue for a +1 rating.