## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 5 September 2000 ]
Source: [ T O’Farrell & L.E. Aguado] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332004 ], FAX: [ +44 113 2332032 ], E-Mail:[ enrique@supergold.com ]
Re: [ Physical layer modulation proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution presents a coded modulation proposal for the physical layer part of the High Rate WPAN standard. This scheme is evaluated based on the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Supergold Communication
Supergold Communication is a campus start up company that specialises in solutions for wireless communications:
  Sequence Coded Modulation
  Sequence/Code Design
  Synchronisation
By efficiently exploiting the distance properties of sequences/codes, Supergold’s solutions balance the trade-off between bandwidth efficiency, BER performance and complexity.
Supergold’s solutions can be beneficially applied in
  WPAN
  WLAN
  Wireless Infrared
  Cellular Mobile

## Slide 3: Sequence Coded Modulation for High Rate WPAN PHY
QPSK / OQPSK chip modulation  constant amplitude
M-ary symbol modulation
Simple single-error-correcting concatenated RS(127,125) code
> 3 dB coding gain over QPSK @ 10-6 BER
High spectral efficiency: 22 Mbit/s data rate in 22MHz
Propose to operate in 2.4 GHz ISM band (can operate in 5 GHz band)

## Slide 4: Properties of the sequence coded modulation (cont.)
Based on pre-existing technology
  Feasible solution
  Short Development time
Works in the 2.4 GHz ISM band with 802.11 channelisation
  Cost effective
  Allows for 802.11 - 802.15.1 and 802.15.3 co-existence
Very low baseband complexity
Meets robustness criteria
Dual mode 802.15.1 / 802.15.3

## Slide 5: Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts, Intersil]
Rx Noise Figure: 15 dB (inexpensive implementation)
Rx Noise Bandwidth: 22 MHz
Rx Noise Floor: -174+10*log(22*106)+15 = -85.6 dBm
Implementation Loss Margin: 5 dB
Antenna Gain: 0 dB

## Slide 6: Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Refflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6 = 70.9 dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2*0 + 5 = 75.9 dB
Operating SNR is 10 dB for 10 -6 BER
Tx Power: Noise Floor + SNR + Loss = -85.6 dBm + 10 dB + 75.9 dB
Tx Power  0 dBm

## Slide 7: PHY Block Diagram

## Slide 8
RF Functionality
  All RF blocks shared for 802.15.1 and 802.15.5 modes. No blocks repeated.
  Transmit power = 0dBm
  No RFPA back-off
  CMOS process
BB Functionality
  3-bit Rx ADCs
  6-bit AGC ADC
  ~ 30K gates for BB processor
  CMOS
1 chip implementation, 1 crystal, 2 filters (front-end, SAW IF)

## Slide 9: General Solution Criteria
Unit Manufacturing Cost
  Similar architecture to IEEE 802.11
  Much simpler baseband processing than 802.11b
  Low power PA (0 dBm Tx Power)
  Shared RF architecture for 802.15.1 and 802.15.3 modes
  Similar to 802.15.1 equivalent UMC at 2H 2000

## Slide 10: General Solution Criteria
Signal Robustness
Interference and Susceptibility
  Analysis based on co-channel interference simulation of multiple access and CW interference
  BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S (MAI) = -6 dB co-channel
    J/S (CW) = -7 dB co-channel
  Adjacent+1 channel power atenuation > 50 dB min.
  Interference protection > 40 dB

## Slide 11: General Solution Criteria
Interference and Susceptibility (cont.)
System performance in the presence of interference

## Slide 12: General Solution Criteria
Intermodulation Resistance:
  Evaluation including model of RF chain pending
Jamming Resistance
  Evaluation including model of RF chain pending

## Slide 13: General Solution Criteria
Multiple Access
  22 Mbit/s bit rate  Throughput in [17.5, 20] Mbit/s range.
  Coordinated time-multiplexing used for multiple access to shared channel.
  No constraint when multiplexing an MPEG2 stream (4.5 Mbit/s) with 512-byte asynchronous packets (max. 234s).
    CASE 1: three MPEG2 streams (at 4.5Mbit/s) share the total throughput (min.) 17.5Mbit/s.
    CASE 2 and 3: one MPEG2 stream takes 4.5 Mbit/s whilst the asynchronous services share the remaining throughput in a time-multiplexing manner.

## Slide 14: General Solution Criteria
Coexistence
  With 802.11b by using common channelisation.
  With 802.15.1 as (to be) given by TG2.
  With 802.11a by being in disjoint bands.
Interoperability
  Dual mode terminal for interoperability with 802.15.1, working at 2.4 GHz.
  Common channelisation could support interoperability with 802.11

## Slide 15: General Solution Criteria
Technical Feasibility
Manufactureability
  System architecture utilises pre-existing 802.11b and 802.15.1 technology.
  Baseband processing functionality similar to existing applications.
Time to Market
  Pre-existence of technology will ensure short development cycle
  Only PHY part proposed
  Available earlier than 1Q2002

## Slide 16: General Solution Criteria
Regulatory Impact
  The proposed scheme is compliant with regulatory standards
Maturity of Solution
  The system utilises existing 802.11b and 802.15.1 technology
  Underlying modulation is constant amplitude QPSK
  Baseband processing less complicated than CCK
  Baseband scheme tested in a general purpose hardware demonstrator

## Slide 17: General Solution Criteria
Scalability
Power Consumption
  Transmit power can be changed with impact on either range or throughput (through change in coding rate).
Data Rate
  Coding level can be adjusted to fit power and channel conditions.
Frequency Band of Operation
  This modulation scheme can be applied at both 2.4 GHz and 5 GHz
Cost
  Changing the level of coding or power would not significantly affect the unit cost.
Function
  Equalisation can be introduced into the scheme inorder to enhance resistance to time dispersive channels with large delay spreads.

## Slide 18
General Solution Criteria
Location Awareness
Direct sequence signalling with 12.5 Mchip/s Chip Rate
  Capable of providing sufficient spacial resolution for an interpolation algorithm to establish location
Correlation processing
  BB processor already uses correlators for sync and data recovery
Preamble / packet
  Either the preamble or a separate short packet can carry a suitable sequence with good autocorrelation properties

## Slide 19: PHY Layer Criteria
Size and Form Factor
  Dual mode RF / BB parts integrated in one PHY chip.
  Three external components: crystal oscillator, front-end filter and SAW IF filter.
  One chip for dual mode 802.15.1 / 802.15.3 MAC.
  Size smaller than a Compact Flash Type 1 card.

## Slide 20: PHY Layer Criteria
MAC/PHY Throughput
Minimum MAC/PHY Throughput
  Offered data rate: 22 Mbit/s, 21.65 Mbit/s with coding PHY overhead
High End MAC/PHY Throughput
  One throughput level is offered

## Slide 21: PHY Layer Criteria
Frequency Band
  This proposal is aimed at the 2.4 GHz ISM band, but is also be applicable to the 5GHz ISM band.
Number of Simultaneously Operating Full Throughput PANs
  The IEEE 802.11 channelisation is adopted
  Up to 3 co-located networks could share the 2.4 GHz ISM band with no co-channel interference
  Up to 5 co-located networks could share the 5 GHz ISM band with no co-channel interference
Range
  For 0 dBm Tx. Power, range > 10 m (for link budget presented)

## Slide 22: PHY Layer Criteria
Sensitivity
BER v. Eb/N0 Performance in the AWGN channel

## Slide 23: PHY Layer Criteria
Sensitivity
BER v. SNR Performance in the AWGN channel

## Slide 24: PHY Layer Criteria
Sensitivity
PER v. SNR Performance in the AWGN channel

## Slide 25: PHY Layer Criteria
Delay Spread Tolerance
System Performance in the multipath channel for TRMS = 25 ns

## Slide 26: PHY Layer Criteria
Delay Spread Tolerance
  The BER criterion = 10-3 is met for TRMS = 25 ns with no equalisation
  A delay spread of 25ns is tolerated for more than 90% of the channels with FER < 1% at Eb/N0 = 17.5 dB
  No equalisation required

## Slide 27: PHY Layer Criteria
Power Consumption
  0 dBm transmitted power
  Constant amplitude  No RFPA back-off.
  Low baseband processor complexity
    very low complexity FEC
    no equaliser
    small BB processor gate count
 Power consumption below 0.5 Watts

## Slide 28: Pugh Matrix - General Solution Criteria

## Slide 29: Pugh Matrix - General Solution Criteria

## Slide 30: Pugh Matrix - PHY Layer Criteria

## Slide 31: Pugh Matrix - PHY Layer Criteria