## Slide 1: IEEE 802.11 and 802.15 Review Presented at Spread-Spectrum Workshop August 14-15, 2000 Baltimore MD.

## Slide 2: Agenda
Overview of IEEE 802
Current IEEE 802.11 Standard
New Developments within IEEE 802.11
Developments within IEEE 802.15
Next Meetings
Questions and Answers

## Slide 3: IEEE 802
IEEE Established in 1884 (AIEE & IRE)
IEEE December 1999 Membership was 360,000; 66% USA & 33% Non-USA
IEEE produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
IEEE holds annually more than 300 major conferences and
IEEE has more than 800 active standards with 700 under development.

## Slide 4: IEEE Standards Association
Chair
SEC (17)
VOTING MEMBERSHIP (500)
IEEE 802
SPONSOR
US TAG
ISO/IEC
JTC1/SC6
APPEALS
PRESS RELEASES
RULES
COMPUTER
SOCIETY SAB
NESCOM – PARS
REVCOM – STDS
PATENTS
IEEE-SA STDS BD
IEEE-SA BD OF GOV
PUBLISHING
LMSC BALLOTS
SUPPORT
TRAINING
IEEE STDS
STAFF

## Slide 5: Objectives of IEEE 802
Enable IEEE 802 to develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of due process, consensus,openness, balance and rights of appeal.
Electronic distribution of standards.

## Slide 6: IEEE 802 Organization
Executive Officers
Working Group Officers
= Active
= Hibernation
= Disbanded
= Wireless

## Slide 7: Current IEEE 802.11 Standard
Wireless Local Area Networks (WLAN)
Medium Access Control (MAC) Layer
Currently includes five Physical (PHY) Layers
  Frequency Hopping Spread Spectrum
  Direct Sequence Spread Spectrum
  Infrared
  11 Mbps in 2.4 GHz
  54 Mbps in 5 GHz

## Slide 8: MAC Layer
Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
Infrastructure Network (Access Point)
Ad-Hoc Network (No Access Point)
Automatic Repeat Request (ARQ)
Power Saving Mode
Wireless Equivalent Privacy (WEP)
MAC Management

## Slide 9: FHSS Physical Layer
2.4 GHz ISM Band
1 and 2 Mbps
2 or 4 level Gaussian FSK
79 channels
Hopping Rate > 2.5 hops/sec.
1 Watt maximum (100 - 500 mw typical)

## Slide 10: DSSS Physical Layer
2.4 GHz ISM Band
1 and 2 Mbps
Differential Binary and Quadrature PSK
Processing Gain: 11 chips per bit.
Three 20 MHz channels in ISM Band.
1 Watt maximum (100 - 500 mw typical)

## Slide 11: 11 Mbps in 2.4 GHz (TGb)
Extension to original DSSS
Includes 5.5 and 11 Mbps modes
Backward compatible with original DSSS
Uses Complementary Code Keying (CCK) modulation
Three channels within 2.4 GHz Band
Uses Existing MAC Layer

## Slide 12: 54 Mbps in 5 GHz
Operates in the U-NII 5 GHz band
Uses Orthogonal Frequency Division Multiplexing (OFDM) Modulation
Information on multiple subcarriers
Many data rates depending on modulation on subcarriers and FEC
  From 6 to 54 Mbps
Uses Existing MAC Layer

## Slide 13: Industry Supporting Org.
Wireless Ethernet Compatibility Alliance (WECA)
  To insure OEM products are compliant to IEEE 802.11 b 2.4 GHz 11 Mbps standard
  Wi-Fi certification
  To ensure interoperability between multi-vendor products compliant to IEEE 802.11b 2.4 GHz 11 Mbps standard

## Slide 14: 802.11 New Developments
MAC Layer Enhancements (TGe)
  Add Quality of Service to support voice
  Enhance Security beyond WEP
Inter-Access Protocol (TGf)
  Define a standard protocol between access points to support features like roaming handoff
Higher Rate Study Group
  Increase 2.4 GHz system to > 20 Mbps

## Slide 15: IEEE 802.15
Standards for Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks (e.g. 8-16 nodes)
  Communication of devices within a Personal Operating Space

## Slide 16: IEEE 802.15
802.15.1 (Standard)
  IEEE Standard of Bluetooth™ Specification
802.15.2 (Recommended Practice)
  Model and Facilitate Coexistence of WPAN & WLAN devices
802.15.3 (Standard)
  A High-Rate (> 20 Mbps) WPAN
Radio2 Study Group
  Track Bluetooth2 and recommend an action.
Low Rate Study Group
  Raw Data Rate = 2Kb/sec to 200Kb/sec

## Slide 17: IEEE 802.15

## Slide 18: IEEE 802.15

## Slide 19: IEEE 802.15 Process Status
Idea for standard
Find Sponsor
Submit PAR
Approve PAR
Organize Task Group
Develop draft standard
Ballot draft standard
Approve draft standard
Publish approved standard
Radio2 SG
Low Rate SG
Task Group 3
Task Group 2
Task Group 1

## Slide 20: IEEE 802.15 Draft Status
Write scope and purpose
Examine related standards and publications
Draft outline
Fill in outline
Revise, revise, revise
Finalize document
Radio2 SG
Low Rate SG
Task Group 3
Task Group 2
Task Group 1

## Slide 21: IEEE 802.15 Task Group 1
IEEE 802.15 Task Group 1 is converting the Bluetooth Specification into an IEEE Standard
  Convert to IEEE Format
  Adding System Description Language (SDL) diagrams
  Letter Ballots, Comments, and Comment Resolution.

## Slide 22: IEEE Task Group 1
802.10 SECURITY
*802 OVERVIEW & ARCHITECTURE
802.1 MANAGEMENT
802.2 LOGICAL LINK CONTROL
802.1 BRIDGING
802.9
MAC
802.9
PHY
802.11
MAC
802.11
PHY
802.12
MAC
802.12
PHY
802.14
MAC
802.14
PHY
802.15
MAC
802.15
PHY
802.3
MAC
802.3
PHY
802.4
MAC
802.4
PHY
802.5
MAC
802.5
PHY
802.6
MAC
802.6
PHY
DATA
LINK
LAYER
PHY
LAYER
802.16
MAC
802.16
PHY
Source: IEEE Std P802.15.1 D0.7.2

## Slide 23: Focus on L2CAP and Below
Physical
LMP
WAE
vCard/vCal
AT
Commands
TCS BIN
SDP
Audio
WAP
IP
UDP
TCP
OBEX
RFCOMM
Host Controller Interface
PPP
L2CAP
Baseband
Source: IEEE Std P802.15.1 D0.7.2

## Slide 24: Task Group 1 Deliverables
PAR Related Deliverables
  June 2001 - IEEE-SA distribution channels
    IEEE Std 802.15.1-2001
    Includes SDL Model Files for above
Non-PAR Related Deliverables
  December 2000, via IEEE-Press
    Bluetooth™ Pocket Guide, Volume 1, etc.
  June 2001 - IEEE-SA distribution channels
    IEEE 802.15 Handbook: A Designer's Companion

## Slide 25: IEEE 802.15 Task Group 2
Problem: Both IEEE 802.11 and Bluetooth operate in the same 2.4 GHz ISM Band.
Problem: Bluetooth enabled devices will likely be portable and will need to operate in an IEEE 802.11 WLAN environment.
Problem: There will be some mutual interference

## Slide 26: Task Group 2 Deliverables
Coexistence Model
  Model describing the mutual interference of WLAN and WPAN upon one another.
Coexistence Mechanisms
  Mechanisms or techniques to facilitate coexistence of WLAN and WPAN devices.
Both to be documented in an IEEE Recommended Practice

## Slide 27: Coexistence Model
The purpose of this model is:
  To understand under what circumstance there is a coexistence problem and under what circumstances there is not a problem.
  To develop supporting evidence to justify the recommended suggested practices and possible standards modifications.

## Slide 28: Coexistence Model
PHY Layer Models
MAC Layer Models
Data Traffic Models
RF Propagation Models
Coexistence Model

## Slide 29: Coexistence Model
Physical Layer Models
  Models of the 802.11 and 802.15 PHY layers which will predict the impact of mutual interference when multiple devices are operating simultaneously.
  Currently modeling PHY in MatLab.

## Slide 30: Coexistence Model
MAC Layer Models
  Model the WLAN and WPAN MAC layers.
  Currently modeling in Opnet
  802.11 Model available
  Building 802.15 model

## Slide 31: Coexistence Model
Data Traffic Model
  Model the data traffic flow based upon different application scenarios for both the WLAN and WPAN networks
    Voice traffic
    File transfer
    Warehouse data collection
    Video & Others

## Slide 32: Coexistence Model
RF Propagation Model
  Model RF signal power levels at the different WPAN and WLAN nodes based on an RF propagation model.
  Consider different application scenarios and physical distribution of devices

## Slide 33: Coexistence Mechanisms
Coexistence Mechanisms Facilitate Coexistence of WPAN & WLAN devices
We will be doing a Call for Submission of Coexistence Mechanisms in September.
Presentations are planned for
  November 2000
  January 2001

## Slide 34: Coexistence Mechanisms
Collaborative Mechanisms
  Some form of communication between the WLAN and WPAN
  Use this link to provide sharing of medium
Non-Collaborative Mechanisms
  No communication between WLAN and WPAN
  Minimize mutual interference

## Slide 35: IEEE 802.15 Task Group 3
Define a standard for a WPAN with a data rate of at least 20 Mbps
Must coexist with 802.11 and Bluetooth
Desirable to be backward compatible with Bluetooth
Held a call for submissions over last few months
Submissions were made in May and July

## Slide 36: Task Group 3
The submissions covered
  Physical Layer
  MAC Layer
  Both
Total of 14 submissions
Developed an Evaluation Criterion
Currently performing evaluation

## Slide 37: Task Group 3
Broad Range of Submissions
2.4 GHz
  Wide Band FSK
  Wide Band QPSK
  Wide Band QPSK and QAM
5 GHz
  Hyper-PAN
Ultra Wide Band (UWB)
  Xtreme Spectrum

## Slide 38: 802.15 Radio2 Study Group
Provide formal reports to the WG, updating the membership on the BT 2.0 Specification
Liaison from 802.15 to Bluetooth SIG.
Provide a plenary week tutorial to IEEE 802. Target November 2000.
If warranted, develop PAR and Five Criteria

## Slide 39: Low-Rate WPAN Study Group
Put together a Project Authorization Request (PAR) for a low-rate WPAN
Less than 200 kbps
Support at least 16 nodes in a network
10 meters range
Battery life of months to infinite
Low cost relative to target device

## Slide 40: Low-Rate WPAN Study Group
Applications
  Sensors & Actuators
  Toys
  Smart Badges
  Health Monitoring
  Computer Peripherals
  Remote Control
  Home Automation
  Automatic Meter Reading

## Slide 41: More Information
Bob O’Hara and Al Petrick, The IEEE 802.11 Handbook: A Designers Companion, IEEE Press, 1999.
www.ieee802.org/11/
www.ieee802.org/15/

## Slide 42: Next 802.11 & 802.15 Meeting
Joint IEEE 802.11 & 802.15 Interim Meeting
September 18-22, 2000
Scottsdale Arizona, Radisson Resort & Spa.

## Slide 43: Questions and Answers
Any Questions?