## Slide 1
Coexistence Liaison Report #2
Bluetooth Coexistence Working Group
  Chartered by Bluetooth SIG to address coexistence issues of Bluetooth with other devices operating in the 2.4 GHz ISM unlicensed band
  Chaired by Tod Sizer of Lucent
  Members include Lucent, Motorola, Ericsson, Toshiba, 3COM

## Slide 2
Coexistence Liaison Report #2
Simulations
  Matlab
  Time & Frequency simulations - assume a particular time usage (due to specific traffic models) together with frequency hoping scenarios to establish collision rate between Bluetooth and the interfering system

## Slide 3
Coexistence Liaison Report #2
Recent Work
  OpNet Tutorial from Taylor Salman
  Internal papers covering Fading Model and Path Loss Model
  Audio samples in WAV format output from two CVSD Corruption Simulators
  Input requirements to Bluetooth Radio 2 Group

## Slide 4
Coexistence Liaison Report #2
Audio samples in WAV format output from two CVSD Corruption Simulators
  Lost packet filled with white background noise encoded in binary as alternating ones and zeros of the same size as the lost packet(s). Assumes packet headers have been corrupted during transmission, allowing the decoder to recognize a corrupt packet and handle it accordingly.
  Assumes packet headers have been left intact, preventing the decoder from recognizing the packet as corrupt. 50% of the “lost” packets are recognized as corrupt and treated as above, while the other 50% are filled with random bits simulating the corrupted payload.

## Slide 5
Coexistence Liaison Report #2
Face-to-Face Meeting
  Expected in mid October
  Plans to begin testing of real hardware