## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3 MAC Criteria Pugh Matrix Evaluation Results ]
Date Submitted: [17 September, 2000]
Source: Name [Allen Heberling, Chairperson for TG3 MAC-subcommittee ]
Company [Eastman Kodak Company]
Address [4545 E. River Road, Rochester, NY 14650-0898]
Voice:[716-781-9328], FAX: [716-781-9733], E-Mail:[allen.heberling@kodak.com]
Re: []
Abstract: [Review of TG3 MAC criteria evaluation process and the results of same. ]
Purpose: [To report the results of the TG3 MAC subcommittee’s evaluation of the MAC criteria pugh matrix]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: TG3 MAC Criteria Pugh Matrix Evaluation Results

## Slide 3: Overview
TG3 MAC Proposers and Proposals
References Used
Review Process
Results
Analysis of Results
Conclusions
Recommendations

## Slide 4: MAC Subcommittee Participants
Proposers
  Marc de Courville
  Walter Davis/Rajugopal Gubbi
  Allen Heberling
  Pat Kinney/ Joe Kubler
  Carlos Rios
  David Skellern

## Slide 5: TG3 MAC Proposals
Davis: doc: 208r1 and 209r1
de Courville doc: 128r0
Heberling: doc: 212r0 and 213r1
Kinney: doc: 208r0 & 218r0
Rios: doc: 197r1 & 198r2
Skellern: doc: 196r0 & 196r1

## Slide 6: Additional Documents
Doc: 110r(11&12) TG3-Criteria-Definitions
Doc: 245r8 TG3-Proposal-Evaluations

## Slide 7: Review Process
Proposers submitted MAC criteria Pugh Matrix Self Evaluation sheets
Data were entered into MAC subcommittee’s MAC criteria work sheet in doc: 245rx
Proposers and other interested parties participated in weekly teleconference calls which started 8/2 and concluded 9/15.
Participation averaged 17 802.15 members per call.

## Slide 8: Review Process Continued
Purpose of MAC subcommittee conference-calls:
  to provide peer review challenges to each proposer’s MAC criteria self evaluation ratings.
  To reach consensus by the subcommittee regarding which value should be assigned to each proposer’s MAC criterion evaluation.

## Slide 9: Review Process Continued
To provide clarifications to the MAC criteria definitions defined in doc: 110r11.
  For Example: MAC subcommittee identified criteria that were:
    PHY dependent,
    OR
    Partially defined.

## Slide 10: Review Process Continued
MAC subcommittee identified these criteria as Phy dependent:
  Multiple Access
  Location Awareness
  Minimum Delivered Data Throughput
  Maximum Delivered Data Throughput

## Slide 11: Review Process Continued
MAC subcommittee identified these criteria as partially defined:
  Simple Network Join/Unjoin Procedures
  Device Registration
  Power Management types

## Slide 12: Review Process Continued
Examples of MAC criteria partially defined continued:
  Authentication
  Privacy
  Quality of Service

## Slide 13: Results of the MAC Criteria Pugh Matrix Review Process
M. de Courville withdrew his advocacy for a HiperPan MAC for 15.3.
Proxies R. Gubbi & G. Parks modified the W. Davis proposal for an adaptive TDMA access algorithm, to align with the “15.1 Reuse” concept
D. Skellern modified his MAC proposal to align with the 15.1 Reuse Concept and the Davis adaptive TDMA access algorithm.

## Slide 14: Results of the MAC Criteria Pugh Matrix Review Process continued...
The number of MAC proposals reduced from 6 to 4.
  Davis/Skellern
  Heberling
  Kinney
  Rios

## Slide 15: Results of the MAC Criteria Pugh Matrix Review Process continued...
Two of the proposals(Davis/Skellern & Heberling) advocate “Reuse of 15.1” and the addition of either
  the Heberling proposed adaptive TDMA access algorithm
  OR
  the R. Gubbi proposed adaptive TDMA access algorithm per the Davis/Skellern MAC proposal.

## Slide 16: Results of the MAC Criteria Pugh Matrix Review Process continued...
15.1Reuse MAC Architecture
802.15.1 Reuse
MAC Layer
PHY Layer
802.15.1
Reuse
L2CAP
802.15.1
Reuse MLME
w/
QoS extensions
Rx_signal
Tx_signal
802.15.1 Reuse Base band*
PLCP
PMD

## Slide 17: Results of the MAC Criteria Pugh Matrix Review Process continued...
Link Controller
ACL Process
802.15.1 TDMA
Algorithm
Heberling
or
Davis/Skellern/Gubbi
Adaptive TDMA
Algorithm
PMD
PLCP
Potential 802.15.1 BasebandReuse decomposition

## Slide 18: Results of the MAC Criteria Pugh Matrix Review Process continued...
The other two proposals(Kinney & Rios) advocate a dual MAC architecture in which 15.1 shares a MAC processor with either:
  an 802.11 “Like” MAC(Kinney)
  OR
  an 802.11 MAC(Rios) w/ TGe MAC enhancements

## Slide 19: Results of the MAC Criteria Pugh Matrix Review Process continued...
Kinney Dual MAC Architecture
L2CAP
802.15.1
MLME
Rx_signal
Tx_signal
802.15.1 BaseBand
PLCP
PMD
Kinney MLME
Kinney MAC
Data Service
Rx_signal
Tx_signal
802.11 Like DCF w/ CSMA
&
RTS/CTS signals
PLCP
PMD
Kinney
802.11Like
MAC

## Slide 20: Results of the MAC Criteria Pugh Matrix Review Process continued...
Rios Dual MAC Architecture
L2CAP
802.15.1
MLME
Rx_signal
Tx_signal
802.15.1 BaseBand
PLCP
PMD
802.11 MLME
802.11 MAC
Data Service
Rx_signal
Tx_signal
802.11DCF/PCF w Tge
Enhancements
PLCP
PMD
Rios
802.11 MAC

## Slide 22: Analysis of Results
MAC subcommittee still needs to clarify and evaluate these MAC criteria:
  Simple Network Join/Unjoin procedures
  Device registration
Pugh Matrix Summary indicates that all 4 proposals are close in their unweighted evaluations.

## Slide 23: Analysis of Results continued...
Pugh Matrix results indicate that distinctions among the 4 MAC proposals become apparent when the weighting factors are included.
  Heberling proposal lost 6 points for having a Power Management Type which was the same as 802.15.1

## Slide 24: Analysis of Results continued...
  Kinney proposal lost 5.5 weighted points for Data Transfer Types and 6.2 weighted points for not providing sufficient support for QoS.
  Rios proposal lost 8 weighted points for Unit Manufacturing Cost.

## Slide 25: Conclusions
The Pugh Matrix process provided a framework within which to:
  evaluate the submitted MAC proposals
  challenge each MAC proposer’s self evaluation criteria ratings
  identify criteria needing clarification
  identify criteria which are dependent upon MAC/PHY pairings

## Slide 26: Conclusions
The MAC proposals have been reduced to two classes:
an 802.15.1 Reuse with the addition of
  the Heberling proposed adaptive TDMA access algorithm
  OR
  the R. Gubbi proposed adaptive TDMA access algorithm per the Davis/Skellern MAC proposal.

## Slide 27: Conclusions
Dual MAC architecture in which 802.15.1 MAC shares MAC processor resources with either
  an 802.11 “Like” MAC
  OR
  an 802.11 MAC w/ TGe multi-media enhancements