## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Bluetooth PHY Model: Initial Results]
Date Submitted: [20 Sept 2000]
Source: [Josie Ammer, Jim Lansford] Company: [Mobilian Corporation]
Address: [7431 NE Evergreen Rd, Suite 220, Hillsboro, OR 97124]
Voice:[(405) 377-6170], FAX: [ (425) 671-6099], E-Mail:[jimlans@mobilian.com]
Re: [ ]
Abstract: [This presentation the initial results from the “Stage 0” model in TG2]
Purpose: [Provide a basis for evaluation of the coexistence mechanisms to be proposed in TG2]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: BT and 802.11 PHY Model (Stage 0)
M. Josie Ammer
9/19/00
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Introduction
PHY model call procedure
Multi-staged PHY modeling effort
Stage 0 (by Mobilian)
  SNIR computation:
    Frequency overlap
    Path loss
  BER computation based on SNIR (Signal to Noise and Interference Ratio)
    Q-function calculations
  Corrupt message based on BER
  Limitations
  Implementation

## Slide 4: PHY model call procedure
Spec set at La Jolla meeting (Beginning of July)
Called by MAC model in OPNET
Call PHY model for each period of stability (POS)
POS: period of time with same transmitters and receivers
Pass message segments for current POS
PHY model corrupts all message segments within POS
MAC layer combines message segments

## Slide 5: Build PHY model in 3 stages
Stage 0 (Mobilian)
  Use SNIR to calculate BER
  802.11b DS and BT only
Future stages use complex baseband models for higher fidelity
Stage I
  Look at 802.11b DS effect on BT
Stage II
  Look at BT effect on 802.11b DS
Stage III
  TBD (possibly, 802.11 FH, WB HomeRF, microwave oven interferer)

## Slide 6: SNIR computation
Frequency overlap
  Center frequency of transmission
  Transmit and receive masks
  Coding gain
Path loss
  Distance between nodes
  Transmit power

## Slide 7: Transmit and Receive Masks

## Slide 8: Coding gain
BT interference on WLAN11, WLAN55 decreased by 8dB due to CCK coding gain
  Represents “processing gain” of 802.11b

## Slide 9: Path loss model
For d<8m,
  40.2+20log d
For d>8m,
  58.5 + 33log(d/8)

## Slide 10: BER computation based on SNIR
BT
  Treat as non-coherent FSK
  BER = 0.5 e-SNIR/2
802.11b DS 1 Mb/s
  BER = Q(sqrt(11*2*SNIR/2))
802.11b DS 2 Mb/s
  BER = Q(sqrt(5.5*2*SNIR/2))
802.11b DS 5.5 and 11 Mb/s
  Treat as block code
  BER = Q(sqrt(2*SNIR*Rc*Wm))
  Rc = code rate
  Wm = codeword distance

## Slide 11: BER computation (cont.)
802.11b DS 5.5 Mb/s
  Codeword error probability: PEW
  PEW = 14 Q(sqrt(8 SNIR)) + Q(sqrt(16 SNIR));
  Each codeword encodes 4 bits, therefore
  BER = 1-(1-PEW)1/ 4
802.11b DS 11 Mb/s
  Codeword error probability: PEW
  PEW = 24 Q(sqrt(4 SNIR)) + 16 Q(sqrt(6 SNIR)) + 174 Q(sqrt(8 SNIR)) + 16 Q(sqrt(10 SNIR)) + 24 Q(sqrt(12 SNIR)) + Q(sqrt(16 SNIR));
  Each codeword encodes 8 bits, therefore
  BER = 1-(1-PEW)1/ 8

## Slide 12: BER computation (cont.)
BER curves used within certain limits: (for code efficiency)
  WLAN: -3dB < SNIR < 10dB
  BT: 1dB < SNIR < 20 dB

## Slide 13: BER vs. SNIR graph

## Slide 14: Corrupt messages based on BER
Probabilistic model:
  Each bit corrupted (flipped) independently
  Corruption based on Uniform distribution with BER as the mean

## Slide 15: Stage 0 limitations
Does not model WLAN to WLAN interference for WLANs with different center frequencies
  Therefore, within each simulation, all WLANs must be in same channel
  Supported in next Revision (9/30/00)
The 11Mb/s model has been validated (including 1Mb/s model, used for headers)

## Slide 16: Stage 0 Implementation
C++
mostly class-based
will be linked in with MAC code
550 lines of code

## Slide 17: Future of Stage 0 model
To be linked in with MAC model being developed in OPNET
Schedule for completion:
  Stage 0 (Mobilian):
    Version 1 delivered: 9/5/00
    Final version delivery: 9/30/00
  Stage I-III: ?
  MAC Layer: ?
Mobilian Stage 0 PHY model by:
  Josie Ammer
  Xudong Zhao
  Ron Nevo
  Ephi Zehavi
  Jim Lansford