## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
Structure of the IEEE 802.15.2 Coexistence Model

## Slide 2: Purpose of Presentation
Define the Inputs to the Coexistence Model
Describe the different sections of the Coexistence Model
Describe the information flow between sections of the Coexistence Model
Define the Outputs of the Coexistence Model.

## Slide 3: Comments on Terminology
In a given implementation of the Coexistence Model there are:
  Devices under Test
  Interfering Devices
For example, a set of several Bluetooth devices in a Piconet may be the devices under test. And a set 802.11 WLAN devices are the interfering devices.

## Slide 4: Inputs to the Coexistence Model
Physical Location of the Devices under Test and the Interfering Devices.
Power Levels of both the Devices under Test and the Interfering Devices.
Data Traffic Models for both the Devices under Test and the Interfering Devices.
Any Specific Parameters of either the Devices under Test or the Interfering Devices

## Slide 5: Sections of the Coexistence Model
Data Traffic Models
MAC Layer Models
  Network Traffic Data Analysis Node
Physical Layer Models
RF Channel Model

## Slide 6: Data Traffic Models
Statistical Descriptions of the Data Traffic Source into both the Devices under Test and the Interfering Devices.
Examples include:
  Periodic data source like voice in Bluetooth
  Poisson source of data
Input from the user - the selected parameters of data source.
Output to MAC Model - A Data source.

## Slide 7: MAC Layer Models
MAC Models of both the Devices under Test and the Interfering Devices
Input from Data Traffic Model - Data source.
Output to PHY Model - What are the interfering packets during desired packets, and at what frequency.
Calculate - Time overlap of desired packet and any interfering packets.

## Slide 8: MAC Layer Models
Input from PHY Model - Bit Error Statistics of data packet.
Calculate - Packet Errors
Network Traffic Data Analysis Node
  Convert Packet Errors into Performance Metrics

## Slide 9: Network Traffic Data Analysis Node
Input MAC Layer - Packet Errors
Performs Statistical Analysis on packet errors to produce Performance Metrics
  Throughput
  Latency
  Packet Error Rate
  etc.

## Slide 10: Physical Layer Models
Input from MAC Model - Parameters (e.g. frequency) of Data Packet being sent on Devices under Test.
Input from MAC Model - Parameters of (e.g. which interfering source at what frequency) any packets being sent by Interfering Devices during Data packet.

## Slide 11: Physical Layer Models
Input from Channel Model - Power levels, at receiver of device under test, of both desired signal and interfering signals.
Output to MAC Model - Bit Error Statistics of Data Packet.
  This may be a bit error rate (BER) or possibly more detailed statistics.

## Slide 12: RF Channel Model
Input from User - Parameters of Channel Model
  RF Propagation Model parameters.
  Fading Statistics
  Multipath delay spread parameters.
Input from User - Location of the devices under test and interfering devices

## Slide 13: RF Channel Model
Output to PHY Model - Power levels, at the receiver of the device under test, of desired signal and interfering signals.
Interaction with PHY Model - Fading and Multipath spread may need to be incorporated with PHY Model to calculate Bit Error Statistics.

## Slide 14
Data Traffic Source
(Device Under Test)
MAC Model
(Device Under Test)
Data with proper statistics
Desired Packet Parameters
Bit Error Statistics
Data Traffic Source
(Interfering Devices)
MAC Model
(Interfering Devices)
Data with proper statistics
Interfering Packet Parameters
PHY Models
Channel Model
Power Levels of Desired and Interfering Signals

## Slide 15: Conclusions
All the sections of the Coexistence Model have been briefly described.
The interfaces between the sections of the Coexistence Model have been described.
The details of each of the sections of the Coexistence Model are covered in other presentations.