## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 16 September 2000 ]
Source: [ T O’Farrell & L.E. Aguado] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332004 ], FAX: [ +44 113 2332032 ], E-Mail:[ enrique@supergold.com ]
Re: [ Physical layer modulation proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution presents a coded modulation proposal for the physical layer part of the High Rate WPAN standard. This scheme is evaluated based on the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Supergold Communication
Supergold Communication is a campus start up company that specialises in solutions for wireless communications:
  Sequence Coded Modulation
  Sequence/Code Design
  Synchronisation
By efficiently exploiting the distance properties of sequences/codes, Supergold’s solutions balance the trade-off between bandwidth efficiency, BER performance and complexity.
Supergold’s solutions can be beneficially applied in
  WPAN
  WLAN
  Wireless Infrared
  Cellular Mobile

## Slide 3: Sequence Coded Modulation for High Rate WPAN PHY
M-ary symbol modulation — QPSK / OQPSK chip modulation
  constant amplitude
  no PA back-off, low power consumption
  robust in multipath fading up to 30 ns rms delay spread
Single-error-correcting concatenated RS(127,125) code
  RS code matched to M-ary modulation
  very simple Berlekamp-Massey hard-decision decoding
  very high rate (0.98)
> 3 dB coding gain over QPSK @ 10-6 BER
High spectral efficiency: 22 Mbit/s data rate in 22MHz

## Slide 4: Properties of the sequence coded modulation (cont.)
Based on pre-existing technology
  Feasible solution
  Short Development time
  Dual mode 802.15.1 / 802.15.3 using common RF blocks
Works in the 2.4 GHz ISM band with 802.11 channelisation
  Cost effective
  Allows for 802.11b - 802.15.1 and 802.15.3 co-existence
  Can operate in 5 GHz band
Very low baseband complexity
CCA as in 802.11b

## Slide 5: Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts]
Rx Noise Figure: 15 dB (inexpensive implementation)
Rx Noise Bandwidth: 22 MHz
Rx Noise Floor: -174+10*log(22*106)+15 = -85.6 dBm
Implementation Loss Margin: 5 dB
Antenna Gain: 0 dB

## Slide 6: Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Refflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6 = 70.9 dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2*0 + 5 = 75.9 dB
Operating SNR is 10 dB for 10 -6 BER
Tx Power: Noise Floor + SNR + Loss = -85.6 dBm + 10 dB + 75.9 dB
Tx Power  0 dBm

## Slide 7: PHY Block Diagram

## Slide 8
Baseband Processor — M-ary Sequence coded modem
Fast Transform Correlator
Maximum Likelyhood Detector
RS Decoder
Select 1 of 128 Sequences
RS Encoder
DATA IN
1
d
c
7
xI
xQ
8
8
I OUT
Q OUT
8
8
7
1
1
1
Rx I IN
Rx Q IN
rI
rQ
c’
DATA OUT
y

## Slide 9
RF Functionality
  All RF blocks shared between 802.15.1 and 802.15.3 modes. No blocks repeated.
  Transmit power = 0dBm
  No RFPA back-off
  CMOS
BB Functionality
  3-bit Rx ADCs - 50 Msample/s speed
  6-bit Tx DACs - 50 Msample/s speed
  6-bit AGC ADC
  16-tap digital raised-cosine pulse shape filter
  ~30K gates for BB processor
  0.18u CMOS process
1 chip implementation, 1 crystal, 2 filters (front-end, SAW IF)

## Slide 10
Characteristic of pulse shape digital raised-cosine filter

## Slide 11: General Solution Criteria
2.1. Unit Manufacturing Cost
Similar to 802.15.1 equivalent UMC at 2H 2000
  Similar architecture to IEEE 802.11b
  Much simpler baseband processing than 802.11b (~30K gates)
  Low power PA (0 dBm Tx Power)
  Shared RF architecture for 802.15.1 and 802.15.3 modes
  1 Chip RF / BB implementation

## Slide 12: General Solution Criteria
2.2. Signal Robustness
2.2.2. Interference and Susceptibility
  BER criterion = 10-3  3dB loss of required sensitivity for:
    J/S (MAI) = -6 dB co-channel
    J/S (CW) = -7 dB co-channel
  Adjacent+1 channel power atenuation > 50 dBc min.
   In-band interference protection > 40 dBc
  Out-of-band attenuation > 80 dBc
   Complies with BT1.0b out-of-band blocking

## Slide 13: General Solution Criteria
2.2.2. Interference and Susceptibility (cont.)
System performance in the presence of interference

## Slide 14: General Solution Criteria
2.2.3. Intermodulation Resistance:
  The receiver can tolerate an intermodulating signal of up to -21dBm whilst retaining a BER=10-3 with 3dB Eb/N0 loss.
  The LNA parameters are:
  LNA input IP3 = -10dBm
  LNA gain = 16.2dB
  LNA P1D = -5dBm
  IM produced by one -35dBm tone = -106dBm

## Slide 15: General Solution Criteria
2.2.4. Jamming Resistance
  1. Microwave oven interference:
  Interference bandwidth = 25MHz  at least 1 free channel CCA would detect jammer and select clear channel.
  2-3. 802.15.1 piconet
  802.15.1 randomly hops over 78 1MHz-bands. It will jam 802.15.3 if it hops within 20MHz-jamming sensitive area  probability of jamming: 20 / 78  26%.
  4. 802.15.3 transmitting MPG2-DVD
  Data stream takes  26% of channel throughput. If 2 un-coordinated WPANs share the 1 channel with CCA-deferred access >50% throughput expected.
  Otherwise CCA in subject WPAN would select clear channel.
  5. 802.11a network
  Working on a disjoint frequency band  no jamming.
  6. 802.11b network
  CCA in subject WPAN would select clear channel.

## Slide 16: General Solution Criteria
2.2.5. Multiple Access
  22 Mbit/s bit rate  Throughput in [17.5, 20] Mbit/s range.
  Coordinated time-multiplexing used for multiple access to shared channel.
  No constraint when multiplexing an MPEG2 stream (4.5 Mbit/s) with 512-byte asynchronous packets (max. 234s).
    CASE 1: three MPEG2 streams (at 4.5Mbit/s) share the total throughput (min.) 17.5Mbit/s.
    CASE 2 and 3: one MPEG2 stream takes 4.5 Mbit/s whilst the asynchronous services share the remaining throughput in a time-multiplexing manner.

## Slide 17: General Solution Criteria
2.2.6. Coexistence
  IC1 & IC2 - 802.15.1 piconet:
A1
A2
B2
B1
3m
3m
10m
Physical Layout
802.15.3
802.15.1
A1 and A2 will not interfere with B2:
- A2 Tx Pwr = 0dBm; Pahtloss(A2-B2) ~62.4dB; A2 Rx Pwr at B2 ~ -62.4dBm over 12.5MHz (Nyquist frequency)  ~ -73.4dBm over 1MHz
- B1 Tx Pwr = 0dBm; Pathloss(B1-B2) ~60dB B2 Rx Pwr ~ -60dB
 C/I(B2) ~ -60 - (-73.4) ~ 13.4dB  no jamming
Interference on B1: Probability of 802.15.1 hopping on 802.15.3 interfering BW (< 20MHz), P(interf.) < 20 / 78 < 26%  802.15.1 throughput > 74%
Work in 802.15.2 would be applicable to 802.15.3

## Slide 18: General Solution Criteria
2.2.6. Coexistence
  IC3 & IC5 - 802.11b network:
  Different channels would be selected for each network via CCA
  IC4 - 802.11a network
  802.15.3 and 802.11a use different frequency bands and would be able to co-exist without interfering to each other.
2.3. Interoperability
  The 802.15.3 WPAN implements a dual mode radio with shared RF blocks for interoperability with 802.15.1.

## Slide 19: General Solution Criteria
2.4. Technical Feasibility
2.4.1. Manufactureability
  System architecture utilises pre-existing 802.11b and 802.15.1 technology.
  Baseband processing functionality similar to existing applications.
2.4.2. Time to Market
  Pre-existence of technology will ensure short development cycle
  Only PHY part proposed
  Available earlier than 1Q2002

## Slide 20: General Solution Criteria
2.4.3. Regulatory Impact
  The proposed scheme is compliant with regulatory standards FCC(25.249) and ETSI 300-328
2.4.4. Maturity of Solution
  The system utilises existing 802.11b and 802.15.1 technology
  Underlying modulation is constant amplitude QPSK
  Baseband processing less complicated than CCK
  Baseband scheme tested in a general purpose hardware demonstrator

## Slide 21: General Solution Criteria
2.5. Scalability
2.5.1.1. Power Consumption
  Transmit power can be changed with impact on either range or throughput (through change in coding rate).
2.5.1.2. Data Rate
  Coding level can be adjusted to fit power and channel conditions.
2.5.1.3. Frequency Band of Operation
  This modulation scheme can be applied at both 2.4 GHz and 5 GHz
2.5.1.4. Cost
  Changing the level of coding or power would not significantly affect the unit cost.
2.5.1.5. Function
  Equalisation can be introduced into the scheme inorder to enhance resistance to time dispersive channels with large delay spreads.

## Slide 22: PHY Layer Criteria
4.1. Size and Form Factor
  Dual mode RF / BB parts integrated in one PHY chip.
  Three external components: crystal oscillator, front-end filter and SAW IF filter.
  One chip for dual mode 802.15.1 / 802.15.3 MAC.
  Size smaller than a Compact Flash Type 1 card.

## Slide 23: PHY Layer Criteria
4.2. MAC/PHY Throughput
4.2.1. Minimum MAC/PHY Throughput
  Offered data rate: 22 Mbit/s, 21.65 Mbit/s with coding PHY overhead
4.2.2. High End MAC/PHY Throughput
  One throughput level is offered

## Slide 24: PHY Layer Criteria
4.3. Frequency Band
  This proposal is aimed at the 2.4 GHz ISM band, but is also be applicable to the 5GHz ISM band.
4.4. Number of Simultaneously Operating Full Throughput PANs
  The IEEE 802.11b channelisation is adopted
  Up to 3 co-located networks could share the 2.4 GHz ISM band with no co-channel interference
  Up to 5 co-located networks could share the 5 GHz ISM band with no co-channel interference
4.6. Range
  For 0 dBm Tx. Power, range > 10 m (for link budget presented)

## Slide 25: PHY Layer Criteria
4.7. Sensitivity
BER v. Eb/N0 Performance in the AWGN channel

## Slide 26: PHY Layer Criteria
4.7. Sensitivity
BER v. SNR Performance in the AWGN channel

## Slide 27: PHY Layer Criteria
4.7. Sensitivity
PER v. SNR Performance in the AWGN channel

## Slide 28: PHY Layer Criteria
4.8.2. Delay Spread Tolerance
System Performance in the multipath channel for TRMS = 25 ns

## Slide 29: PHY Layer Criteria
4.8.2. Delay Spread Tolerance
  The BER criterion = 10-3 is met for TRMS = 25 ns with no equalisation
  A delay spread of 30ns is tolerated for more than 90% of the channels with FER < 1% at Eb/N0 = 17.5 dB
  No equalisation required

## Slide 30: PHY Layer Criteria
4.9. Power Consumption
  0 dBm transmitted power
  Constant amplitude  No RFPA back-off.
  Low baseband processor complexity
    very low complexity FEC
    no equaliser
    small BB processor gate count
 Power consumption below 200 mW peak.

## Slide 31: Pugh Matrix - General Solution Criteria

## Slide 32: Pugh Matrix - General Solution Criteria

## Slide 33: Pugh Matrix - PHY Layer Criteria

## Slide 34: Pugh Matrix - PHY Layer Criteria