## Slide 1: Regulatory Ad Hoc Group Report
Scottsdale, AZ, USA
September 2000

## Slide 2: UWB Update
NPRM is released 98-153
    Comments closed Sept 12, 2000
    Reply comments will close Oct 12, 2000
Commission proposes to allow:
    Intentional emissions at Class B limit > 2GHz
    12dB below Class B limit < 2GHz
UWB technology promises to:
    enable new class of communications products
    extremely high rate, low power, short range
    other non-communication apps (radar)

## Slide 3: 5 GHz WLAN I.A.G.
Objective: 1 Global 5 GHz WLAN Std.
    Initiated by Compaq, Intel, Microsoft
Alternatives:
        Make a new standard
        Pick one
        Drive Convergence
        Pick one for early adoption
Liaisons established w/ IEEE and ETSI BRAN
Next meeting 10/20/00 in Houston

## Slide 4: IEEE 802.11a in Europe
IEEE 802.11 / ETSI BRAN Corresponding
RAH drafted response to ETSI BRAN Letter of May 2, 2000
  Clarifications requested on:
    impact on users of existing equipment
    coexistence of HiperLAN and 802.11a
    TPC and DFS
    IP
RAH draft forwarded to plenary for approval

## Slide 5: NPRM 99-231
Proceeding has been bifurcated
  R & O issued on WBFH
  DSSS Processing Gain Test issue remains active
Commission authorizes WBFH
  Modifies Part 15 rules for FHSS
    125 mW power limit
    >15 non-overlapping channels spanning 75 MHz
    2.5 Hz hop rate
DSSS Processing Gain issue not decided
    RAH Group passed resolution to contact FCC in November
    Forwarded motion to 802.11b HR SG for joint action

## Slide 6: World Radiocomm. Conference (WRC)
WRC expected US proposal for global allocation of upper UNII band for RLAN apps
    current world allocation: 5.15 - 5.725 GHz
    does not include ISM band at 5.725 - 5.825 GHz
But…US had no proposal
    US needs to make request for inclusion of 5.725 - 5.825 GHz band into global allocation for RLAN
Needs to be included in agenda for next meeting
    2003
    proposals from industry are needed!
More info: http:\\www.ero.dk