## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Frequency Hopping Multi-Mode QAM Physical Layer Proposal for High Rate WPANs
Date Submitted: 7 July 2000
Source: Dr. Jeyhan Karaoguz
Address: Broadcom Corporation, 16215 Alton Parkway, Irvine, CA 92619
Voice: 949 585 6168
E-Mail: jeyhan@broadcom.com
Contributors: Jeyhan Karaoguz, Christopher Hansen, Brima Ibrahim, Reza Rofougaran, Nambi Seshadri, Broadcom Corporation
Re: Call for Proposals for IEEE P802.15.3 High Rate Task Group
Abstract: This proposal describes a 5 MHz frequency hopping physical layer operating in the unlicensed 2.4 and 5 GHz bands. The proposed system provides adaptive data rates of 8, 12, 16, and 20 Mbit/sec depending on the channel and noise conditions.
Purpose: To be considered as a candidate PHY layer technology for IEEE P802.15.3 specification
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Physical Layer Summary
5 MHz Frequency Hopping (FH) transmission system operating in the 2.4 GHz unlicensed radio spectrum
Multi-mode adaptive Quadrature Amplitude Modulation (8-PSK, 16/32/64 QAM) with Trellis Coding supporting 8, 12, 16, 20 Mbit/sec
Adjustable transmit power 0 to 20 dBm if desired for range
Minimum Mean Squared Error Decision Feedback Equalization (MMSE-DFE) receiver to combat delay spread
Variable length coded frame size (suitable due to TCM)
Will support existing 802.15 devices in dual mode
PHY layer design based on extensive field test results (up to 17 m indoor coverage) conducted by UCLA Electrical Engineering Department

## Slide 3: Modulation Characteristics
Frequency hopping (1600 Hops/sec) for backward compatibility (w.r.t network synchronization) with the 802.15.1 specification
Multi-Mode QAM PHY layer operates at a modulation rate of 4 MBaud with a 20 dB signal bandwidth of 5 MHz
25% excess bandwidth to achieve low Peak-to-Average-Ratio (PAR)
Simple 8-State/2-D TCM applied to 8-PSK, 16/32/64 QAM signal constellations (spectral efficiencies of 2/3/4/5 bits/symbol)
Adaptive data rates of 8, 12, 16, 20 Mbit/sec
MMSE-DFE equalization at the receiver to combat delay spread
Signal acquisition and equalization are both based on a short preamble

## Slide 4: Considerations for 5 MHz FH System
FCC 15.247 rules permit 5 MHz bandwidth FH systems with up to 21 dBm transmit power in the 2.4 GHz band (as of August 22, 2000)
Extensive field tests (3600 experiments) conducted by UCLA Electrical Engineering Department showed good performance within 17 m radius for uncoded 5 MHz multi-mode QAM systems supporting 20+ Mbps
5 MHz frequency hopping systems require less power compared to wideband non-hopping systems
Higher SNR and front-end linearity required by multi-level QAM modulation can be offset by simple 8-State TCM, which achieves ~3.5 dB coding gain
Frequency hopping is effective in dealing with narrowband interference

## Slide 5: Signal Constellations
16-QAM TCM (12 Mbit/s)
32-QAM TCM (16 Mbit/s)
64-QAM TCM (20 Mbit/s)
8-PSK TCM (8 Mbit/s)

## Slide 6: 8-State Multi-Mode TCM Encoder
T
+
T
T
+
8-PSK
Encoder
16-QAM
32-QAM
64-QAM
2-D Output
to Pulse Shaping
Filter
C
bo
b1
b2
b3
b4
2,3,4,5
bits/symbol
8/16/32/64 QAM TCM
Mode Selection

## Slide 7: 8-State/ 2D Trellis Coded Modulation
D0
D4
D2
D6
D1
D5
D3
D7
D4
D0
D6
D2
D5
D1
D7
D3
D2
D6
D0
D4
D3
D7
D1
D5
D6
D2
D4
D0
D7
D3
D5
D1
D0
D4
D2
D6
16-QAM Set Partitioning
D0
D4
D2
D6
D1
D5
D7
D3
C0
C2
C1
C3
B1
B0
8-State Trellis Diagram

## Slide 8: Coding Gains for 8-State QAM TCM

## Slide 9: Variable Length Frame Format
Preamble
CRC
Tail
Message Body
3 T
12-18 T
Hopping Boundaries
Preamble: Low overhead preamble for fast packet-by-packet MMSE-DFE equalization
Tail: Beneficial for reaching a known TCM state at the end of a burst transmission

## Slide 10
Simulations for Multipath Immunity
Exponential decaying Rayleigh fading channel
25 ns RMS delay spread
-73 dBm received signal level
  3 dB higher than minimum required sensitivity
Monte Carlo simulation used to evaluate MMSE-DFE performance
  2000 random channels evaluated on two equalizers
  4 Feed-Forward and 4 Feed-Back taps
  8 Feed-Forward and 4 Feed-Back taps
SNR at slicer is sufficient for operation under worst case conditions
  At 99.9 percentile, SNRs of 14.7 dB (4 FF taps) and 17.0 dB (8 FF taps) is achieved
  This corresponds to 12 Mbps and 16 Mbps
  20 Mbps can be achieved at 98th percentile with 8 FF Taps

## Slide 11
Multipath Immunity & Equalizer Performance

## Slide 12: Multi-Mode QAM TCM Transmitter
Randomizer
and CRC
Generator
Preamble
Generator
TCM
Encoder
Transmit Control
I/Q Modulator
DACs and LPFs
Inter-
polator
X 2n
Pulse
Shaping
Filter
X 2n
Data
Control
IF and RF Stages

## Slide 13: High-Speed Wireless Indoor Prototype System
2.4 GHz 5 Mbaud multi-mode QAM (4, 16, 64-QAM) built by UCLA researchers
System implementation and distortion issues such as real-time adaptive equalization, timing and carrier recovery, inter-modulation distortion, and phase noise are reflected in the measurements
Prototype system description and results are published in the IEEE Journal on Selected Areas in Communications, March 2000, “Field Trial Results for High-Speed Wireless Indoor Data Communications” by J.F. Frigon, B. Daneshrad, J. Putnam, E. Berg. R. Kim, T. Sun and H. Samueli.
IF to RF
Up-Converter
RF to IF
Down-Converter
IF to Baseband
Converter
Baseband
to IF Converter
Low IF
Out
Data
CLK
BER
Tester
Out
In
Low IF
In
Data
CLK
Baseband QAM Modulator
Baseband QAM Demodulator
NF = 6.5 dB
IP3 = -36.5 dB
Laptop
PC
fc = 2.44 GHz
BW3dB = 5 MHz

## Slide 14: Field Test Results
Field test environment
  UCLA Engineering building 5th floor laboratories
  Modern construction with reinforced concrete with metal support structures
  Rooms contain a set of lab benches with equipment (square rooms with 9.7 m2 area)
Total of 3600 experiments carried out
  1200 measurements within one room (24.8 ns rms delay spread)
  1200 measurements between rooms (35.4 ns rms delay spread)
  1200 measurements between a room and hallway (31.2 ns rms delay spread)
0 dBm transmit power used for measurement within one room
  -43.5 dBm of measured average received power
  24 dB of measured average SNR (with MMSE-DFE)
  SNR > 14.5 dB for %90 of the time (with MMSE-DFE)
  SNR > 10 dB for %95 of the time (with MMSE-DFE)
  As much as 14 dB SNR degradation observed without an MMSE-DFE in the receiver
Results showed that MMSE-DFE equalized system is not ISI but noise limited
  5 dBm transmit power would guarantee 20 Mbps transmission over 90% of the channels encountered (requires 19.5 dB SNR)

## Slide 15: Designed System Performance
BER and PER (512 Bytes)
  10-5 (BER) and 4 x 10-2 (PER)
  19.5 dB SNR requires for 64 QAM TCM
Receiver Sensitivity (AWGN5 MHz BW + Noise Figure + SNR10-5 BER)
  -76 dBm for 64-QAM TCM, 20 Mbit/sec
  -79 dBm for 32-QAM TCM, 16 Mbit/sec
  -82 dBm for 16-QAM TCM, 12 Mbit/sec
  -85 dBm for 8 -PSK TCM, 8 Mbit/sec
Inter-modulation Performance
  -35 dBm to -45 dBm inter-modulating signals while receiving at 3 dB above sensitivity level
  Results in input IP3 from -6.5 dBm to -21.5 dBm
Spurious Noise
  -45 dB below carrier power (out of band spurious)
Phase Noise
  -40 dBc (total integrated over 5 MHz signal bandwidth), -85 dBc/Hz @ 50 kHz

## Slide 16: Regulatory Update
As of August 22, 2000, FCC amended the Part 15 rules to allow for frequency hopping spread spectrum transmitters use 5 MHz wide channels (15 hopping channels in the 2400 - 2483.5 MHz band)
  With the new rule change, from a scalability point of view, our 5 MHz bandwidth frequency hopping multi-mode QAM proposal has the ability to transmit up to 21 dBm power for extended range beyond 10 meters

## Slide 17: Transmitter Complexity
Digital Baseband Processing
  Randomizer
  Preamble generator
  TCM encoder
  Pulse shaping filter
  Total digital gate complexity: 10K gates
Analog Front-end
  Dual 8-bit DACs (8 Msamples/sec)
  Baseband to RF up-conversion
  0 dBm output on-chip PA (5 dB back-off from 1 dB compression point)
  RF synthesizer block (VCO, PLL, etc) shared with receive section
Power Consumption (Analog + Digital) (0 dBm)
  ~67 mW for .18u technology

## Slide 18: Receiver Complexity
Digital Baseband Processing
  Square-Root-Raised-Cosine Filter: 25% excess bandwidth
  Feed-forward equalizer: 8 symbol interval span
  Decision feedback sequence estimation (4 taps for the feedback filter)
  Signal acquisition block
  8-State 2-D Viterbi decoder
  Total digital gate complexity: 75K gates
Analog Front-end
  Dual 8-bit A/D converter (8 Msamples/sec)
  AGC
  RF-to-IF down conversion block
  IF-to-baseband down conversion
  RF synthesizer block (VCO, PLL etc.) shared with transmit section
Power Consumption (Analog + Digital)
  ~108 mW for .18u technology

## Slide 19
Dual Mode 802.15.1/3 Radio Architecture
Due to frequency hopping (1600 hops/sec) nature of the proposed high rate WPAN proposal, only RF filters need to be programmable while the rest of the blocks are shared between 802.15.1 and 802.15.3 modes
LNA
PA
Mixer
BPF
IF to Baseband
Conversion
PGA
Mixer
LPF
1/5 MHz
Programmable
LO
Generation
Control
Channel
Select
PLL
To Baseband
Processor
From Baseband
Modulator
Control
interface
Dual-mode 802.15.1/3 Radio Chip
TDD
switch
1/5 MHz
Programmable
.
IF BW
Programmable
.

## Slide 20
Dual Mode 802.15.1/3 Overall System Architecture
Flash
Program
Memory
(32K)
Mixed Signal Baseband Core (Mod/Demod)
8-bit Dual DAC
8-bit Dual ADC
TX/RX square-root-raised-cosine filters
TCM encoder
Signal acquisition
Channel estimation
Feed-forward equalizer
Decision-feedback sequence estimator
Total Digital Gate Count: 85K
MAC Controller
Dual mode 802.15.1/3 MAC
Integrated micro-processor
Integrated SRAM
Data buffers
External memory interface
Host interfaces
Dual-mode
802.15.1/3
Radio
Crystal
.
0.18u CMOS
16 mm2
Total chip area
(including MAC)
0.18u CMOS
23 mm2
UART, USB,
PCI, etc.
Overall System Components
1. Dual-mode radio chip
2. Baseband PHY/MAC chip
3. Flash program memory
4. Crystal

## Slide 21: General Solution Criteria
Unit Manufacturing Cost
  Estimated cost of the proposed solution is less than 1.5 x equivalent Bluetooth 1 cost specified in the evaluation criteria
Interference and Susceptibility
  Based on the design of front-end and baseband filters reflected in the presented system cost and complexity, proposed system achieves the following interference blocking performance:
  “Out-of-Band” blocking performance (interfering signal power level while the wanted signal is at -73 dBm)
    30 MHz - 2000 MHz: -10 dBm
    2000 MHz - 2399 MHz: -27 dBm
    2498 MHz - 3000 MHz: -27 dBm
    3000 MHz - 12.75 GHz: -10 dBm
  “In-Band” blocking performance (excluding co-channel and adjacent channel and first channel)
    Interference protection is greater than 35 dB
Inter-modulation Performance
  -35 dBm to -45 dBm inter-modulating signals while receiving at 3 dB above sensitivity level
  Results in input IP3 from -6.5 dBm to -21

## Slide 22: General Solution Criteria
Jamming resistance
  defined as the ability of the proposed system to maintain greater than 50% throughput in the presence of other uncoordinated in-band interferers
  As shown below, the proposed system achieves much better than 50% throughput for the jamming scenarios given in the evaluation document
  With respect to microwave oven interference:
    Two factors are important to consider when evaluating microwave interference performance: (1) interference bandwidth is limited to 25 MHz, (2) interference has a duty cycle of 50% (being on for 8.3 msec out of a 1/(60 Hz) cycle)
    Proposed system hops 1600 times/sec using 15 distinct channels each 5 MHz wide, therefore, in the worst case situation only 6 out of 15 hops get affected by the microwave oven interference
    Since the microwave oven interference has a duty cycle of 50%, the proposed system achieves 100*(1 - 6/15*1/2) = 80% throughput on average
  With respect to an 802.15.1 piconet transmitting HV1 voice packets
    Both the 802.15.1 piconet and the proposed system hop at the same rate (1600 hops/sec) in an uncoordinated fashion
    Probability of that an 802.15.1 hop frequency coincides with the proposed system hop frequency is 15*(1/15*5/75), which results in a propose system throughput of 93%

## Slide 23: General Solution Criteria
Jamming resistance (continued)
  With respect to an 802.15.1 piconet transmitting DH5 voice packets
    In this mode, an 802.15.1 piconet is effectively hopping 5 times slower (320 hops/sec) than the proposed system while using all of the 75 available channels
    Since the hops between two systems are uncoordinated, the probability that the proposed system hop frequency coincides with the 802.15.1 piconet hop frequency is still approximately 1/15 resulting in a throughput of ~93% for the proposed system
  With respect to an 802.15.3 data connection operating in an uncoordinated manner transferring a DVD video stream compressed with MPEG2
    In this case, the probability that two uncoordinated proposed system hop frequencies coincide is 15*(1/15*1/15) resulting in a throughput of 93%
  With respect to an 802.11a piconet
    Proposed system achieves 100% throughput since the frequency band of operation can be 2.5 GHz band
  With respect to an 802.11b piconet transmitting DVD video stream compressed with MPEG2
    Since the 802.11b piconet occupies 5 of the proposed system hopping channels, the proposed system in the worst case achieves a throughput of 100*(1-5/15) = 67%

## Slide 24: General Solution Criteria
Multiple Access
  Multiple access is the ability of the coordinated systems to simultaneously share the medium
  As shown below, the proposed system can handle all three multiple access scenarios given in the evaluation criteria document
  With respect to three systems (each containing 2 nodes) where all three systems transmitting a DVD video stream compressed with MPEG2
    In this case, each system can simultaneously achieve the required 4.5 Mbps in a time-division multiplexed manner since the total system throughput is 20 Mbps
  With respect to the desired system transferring a DVD video stream compressed with MPEG2 as the other two transferring asynchronous data with a payload of 512 bytes
    In this case, the desired system would use 4.5 Mbps bandwidth while the remaining two systems transfer asynchronous data with the remaining 15.5 Mbps data rate all in a time-division-multiplexed manner
  With respect to the desired system and one other system transferring asynchronous data with a payload size of 512 bytes while the third system transferring a DVD video stream compressed with MPEG2
    Similar to the second scenario given above, two systems can utilize up to 15.5 Mbps data bandwidth whereas the DVD video transfer can take place at a 4.5 Mbps rate in a time-division-multiplexed manner

## Slide 25: General Solution Criteria
Coexistence
  Coexistence is defined as the net throughput of an alternate system in the presence of the proposed system divided by the net throughput of the alternate system with no other interferers or systems present
  To evaluate the coexistence performance of the proposed system with alternate systems, we rely on the results presented in the jamming performance section
  As shown below, the coexistence performance of the proposed system is more than adequate
  With respect to an 802.15.1 piconet with one HV1 voice transmission active
    Considering the worst case scenario of transmissions by the proposed system completely jamming the 802.15.1 HV1 transmissions when their hopping frequencies coincide, the throughput of the 802.15.1 system would still be 93% (see the jamming performance section), which results in a better than 60% throughput for the 802.15.1 system
    Thus, IC1=1
  With respect to an 802.15.1 system transferring data with DH5 packets bi-directionally
    Since the hops between two systems are uncoordinated, the probability that the proposed system hop frequency coincides with the 802.15.1 piconet hop frequency is approximately 1/15 (see the jamming performance section), which results in a better than %60 throughput for the 802.15.1 system
    Thus, IC2=1

## Slide 26: General Solution Criteria
Coexistence (continued)
  With respect to an 802.11b network transferring data with 500 byte packets bi-directionally
    Since the duration for an 802.11b device to transmit a 500 byte packet is in the same order as the hop-dwell time of the proposed system, approximately 33% of the 801.11b transmissions will fail in the worst case scenario, which results in a better than 60% throughput
    Thus, IC3=1
  With respect to an 802.11a data connection transferring a MPEG2 DVD video stream
    Considering that the proposed system can operate in the 2.4 GHz band, the 802.11a system can achieve a throughput of 100%
    Thus, IC4=1
  With respect to an 802.11b network transferring an MPEG2 DVD video stream
    Similar to the 802.11b scenario given above, the 802.11b network will still achieve a throughput better than 60%
    Thus, IC5=1
  Consequently, the total value for coexistence evaluation: 2*IC1 + 2*IC2 + IC3 + IC4 + IC5 = 7
Interoperability
  Proposed solution (1600 Hops/sec) will be interoperable with Bluetooth 1 solution

## Slide 27: General Solution Criteria
Manufacturability
  Proposed solution is based on proven frequency hopping and QAM technologies (similar ICs already exist)
Time-to-Market
  Chips for the proposed solution would be available well before 1Q2002
Regulatory Impact
  Proposed solution (o dBm) is already compliant with the FCC 15.249 rule
Maturity of Solution
  A prototype consisting of similar chips already exists
Scalability
  Proposed solution provides scalability in all of the following areas: (1) power consumption (1, 10, 100 mW), (2) data rate (8,12,16,20 Mbps, or above), (3) frequency band of operation (can operate both in 2.4 or 5 GHz bands), (4) cost, and (5) function

## Slide 28: Physical Layer Solution Criteria
Size and Form Factor
  Die and package size for the solution is estimated to fit in a form factor smaller than a compact flash
Minimum MAC/PHY Throughput
  Proposed solution achieves 20 Mbps data rate
High End MAC/PHY throughput
  Proposed solution may achieve greater than 20 Mbps data rate with higher order QAM (>64-QAM) or wider signal bandwidth (for example, 7.5 MHz instead of 5 MHz)
Frequency Band
  Can operate both in 2.4 or 5 GHz bands
Number of Simultaneously Operating Full-Throughput PANs
  As the number of independent PANs increase, full throughput gracefully degrades due to frequency hopping spread spectrum
  Thus, the number of simultaneously operating full-throughput PANs is less than 4

## Slide 29: Physical Layer Solution Criteria
Signal Acquisition Method
  Preamble based
Range
  Covers 10m radius with 0 dBm transmit power
  Larger coverage possible with > 0 dBm transmit power
Sensitivity
  -76 dBm
Delay Spread Tolerance
  Can easily handle 25 ns RMS delay spread
Power Consumption
  Total power consumed by the proposed PHY solution during transmit: 67 mW (.18u technology)
  Total power consumed by the proposed PHY solution during receive: 110 mW (.18u technology)

## Slide 30
General Solution Evaluation Matrix
Note: Evaluation of the proposed solution is highlighted

## Slide 31
General Solution Evaluation Matrix (Cont.)
Note: Evaluation of the proposed solution is highlighted

## Slide 32
PHY Solution Evaluation Matrix
Note: Evaluation of the proposed solution is highlighted