## Slide 1
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Thoughts on Broken, Missing and Misplaced 802.15.3 Criteria ]
Date Submitted: [17 September 2000]
Source: Name [Carlos Rios ] Company [LinCom Wireless, Inc.]
Address [5120 W Goldleaf Circle, Ste 400, Los Angeles, CA 90056]
Voice:[408 202 6294], FAX: [408 399 9704], E-Mail:[riosc@lincom.com]
Re: [Documents 110r12 and 245r8 and successors ]
Abstract: [Ideas on improving 802.15.3 selection criteria]
Purpose: [Achieve 802.15.3 consensus sooner]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.

## Slide 2: Thoughts on Broken, Missing and Misplaced 802.15.3 Selection Criteria

## Slide 3: Background
Since September quite a few dedicated, talented folks have been stealing considerable time from their real jobs to evaluate the 802.15.3 PHY and MAC proposals
The task was quite formidable, and we didn’t finish
Unfortunately, along the way we found some of our marching orders (i.e., the selection criteria of doc 110rxx) less than perfect
However, to a greater or lesser degree we tried to compensate as we went along and patch things

## Slide 4: But, I think we need major surgery
Key evaluations could not be performed because of incomplete or “broken” criteria
  PHY+MAC size and form factor
  PHY+MAC power consumption
  PHY+MAC Minimum Throughput
  PHY+MAC High End Throughput
  Sensitivity
  Delay Spread Tolerance
  Network Join, Unjoin
  Registration
  Authentication
  Privacy

## Slide 5: Methinks we need to add stuff
More information from proposers so the committee can comprehensively evaluate and recommend
  PHYs are very distinct and complex, featuring advanced modulation, coding and equalization
  MACs are also very distinct and sophisticated
  Difficult to understand exactly how they work, much less how they compare with each other
New criteria
  PHY, MAC time delays
  Additional, “stricter” coexistence
  User transparent security

## Slide 6: And, on a procedural note
The committee should issue strong, well reasoned selection recommendations to the membership
  Extremely hard for voters to decide on tech merit
  Don’t want a popularity contest
  Don’t want voters to spin the bottle or flip nickels
  Yet no one wants to get voted off the island
We are not prepared to issue such a recommendation at this time
That means we have a lot of work ahead of us

## Slide 7: Proposed PHY Criteria Mods

## Slide 8: Proposed New PHY Criteria
PHY Overhead
  Informational submission to assist SYS Overhead calculations
  “Added bits” due to preamble, coding rate expansion, code blocking (pad/tail bits), recursive coding/interleaving, etc
  Plus interpacket spacing, ACKs
  Express in terms of time units
PHY Latency
  Informational submission to assist SYS Latency calculations
  PHY contribution to time needed to transfer a data payload from transmitter to receiver and ensure no retransmission
  Propagation, coding/interleaving, decoding/deinterleaving
  Also expressed in time units

## Slide 9: Proposed Relocated PHY Criteria
Interference and Susceptibility
  Interference and susceptibility mechanisms are purely PHY issues, are best discussed in PHY forum
  No modifications proposed to criteria as is
Intermodulation Resistance
  Intermodulation mechanism is a purely PHY issue, is best discussed in PHY forum
  No modifications proposed to criteria as is

## Slide 10: Broken PHY Criteria
Delay Spread Mitigation
  “The delay spread tolerance is the value of T_RMS for which a maximum FER of 1% is met for 90% of the channels generated using the channel model…”
  What about the other 10% of the channels???
  I think we goofed, or maybe are not answering the right questions
  We need to evaluate PHY performance (modulation, equalization, coding) in 100% of the channels
    Useful to compare with unequalized, uncoded PHY
    Ditto equalized, uncoded PHY
    And coded, uncoded PHY in AWGN

## Slide 11: Performance of 11 MSps QPSK (22 MHz BW) in AWGN and 50ns DS Multipath

## Slide 12: Proposed MAC Criteria Mods

## Slide 13: Proposed New MAC Criteria
Multiple Access Type
  Informational submission to assist SYS Overhead and Latency calculations
  Advise if TDMA, FDMA, CDMA, CSMA/CA, Poll/ Response, ACK/NACK, Superframe, ARQ method, etc.
MAC Overhead
  Informational submission to assist SYS Overhead calculations
  Header “added bits” (Source, destination address, etc)
  ARQ packets and corresponding ACKs/NACKs
  Superframe overhead
  Evaluate 2 distinct scenarios
    “Single Access”, point to point link
    “Multiple Access”, single point to two points, two independent co channel links

## Slide 14: Proposed New MAC Criteria
MAC Latency
  Informational submission to assist SYS Latency calculations
  MAC contribution to time needed to transfer a data payload from transmitter to receiver and ensure no further retransmissions are needed
  CRC, ERC, FCS processing and ARQ request
  Delays associated with all retransmissions, ACKs/ NACKs and further ARQ requests
  Evaluate 2 distinct scenarios
    “Single Access”, point to point link
    “Multiple Access”, single point to two points, two independent co channel links
Authentication, Privacy Key Management
  “Extra Credit” criteria
  “User transparent” authentication and privacy enabling
  No need for PIN numbers, manual key entry, etc

## Slide 15: Broken MAC Criteria
Simple Network Join/Unjoin
  Criteria is comparison with 802.15.1
  Extremely subjective to gauge whether a different implementation is better or worse
Device Registration
  Criteria is comparison with 802.15.1
  Extremely subjective to gauge whether a different implementation is better or worse
Authentication
  Criteria is comparison with 802.15.1
  Extremely subjective to gauge whether a different implementation is better or worse
Privacy
  Criteria is comparison with 802.15.1
  Extremely subjective to gauge whether a different implementation is better or worse

## Slide 16: Proposed System Criteria Mods

## Slide 17: Relocated and Broken PHY Criteria
Size and Form Factor
  Discussed separately in MAC and PHY subcommittees
  Limited utility in discussing them independently
Power Consumption
  Discussed separately in MAC and PHY subcommittees
  Limited utility in discussing them independently
Min MAC/PHY Throughput
  Suggest combining new MAC, PHY overhead numbers to arrive at consistent Minimum Throughput calculations
High End MAC/PHY Throughput
  Suggest combining new MAC, PHY overhead numbers to arrive at consistent High End Throughput calculations

## Slide 18: New PHY Criteria
MAC + PHY Latency
  Calculation of time delays inherent to a combined MAC/ PHY
Harmony
  “Stricter” level of coexistence with devices of other standards
  Present coexistence is a “survival” criterion
    Devices can jam each other if only reduce throughput by 50%, max
  Propose a level of coexistence wh devices do not interoperate, but can identify and defer to each other’s transmissions
    802.15.3 and 802.11b defer to each other if at 2.4 GHz
    802.15.3 and 802.11a defer to each other if at 5 GHz

## Slide 19: Proposed Process Modification
Modify, add and relocate criteria as necessary to achieve the “best and final” set this week
Formulate all modified, new criteria as informational only
Provide for a last stage of proposal updates
  Reflect the best and final criteria
  Complete within maybe 2 weeks after this meeting ends
Defer first stage selection process until November
  Don’t throw anyone off the island yet!
Apply the modified criteria to the updated proposals over the next 2 months and refine the evaluations
Come November
  Present all the final proposals to the membership
  Present the final subcommittee evaluation recommendations
  Have the bakeoff to the single solution over a set of votes that week