## Slide 1
Slide <number>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Kodak - High Rate PHY Proposal]
Date Submitted: [11July2000]
Source: [James D. Allen] Company: [Eastman Kodak Co.]
Address: [1669 Eastman Ave. Rochester, NY, 14650-2015]
Voice:[(716) 588-1906], FAX: [(716) 722-9053], E-Mail:[james.d.allen@kodak.com, grantbc@earthlink.net]
Re: [802.15.3 final Call for Proposals]
Abstract: [This presentation outlines Kodak’s PHY proposal to 802.15.3 High Rate Task Group]
Purpose: [To communicate the proposal for consideration by the standards team]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Kodak’s High Rate PHY Proposal to IEEE 802.15.3
Presented by Jim Allen

## Slide 3: Summary
22 Mbps Maximum Data Rate
2FSK , Bi-directional Half Duplex
Low Cost - Comparable to 802.15.1 (Bluetooth) Class of Devices
2.4 - 2.5 GHz ISM Band (International)
  for International Acceptance
  for Interoperability with BT infrastructure and applications
Minimum 3 Channels
Low RF Power Operation ( approx. 0dBm)
Range and Power Consumption similar to 802.15.1

## Slide 4: Summary
Interoperable with IEEE 802.15.1 WPAN Devices (same modulation scheme and index)
Presence Detection Capability for 802.15.1 Signals
Coexistence with IEEE 802.11 (2.4GHz) WLANs
Position for Low Cost sharing Majority of IEEE 802.15.1 Software and Hardware components.
Reference Support Document 00215r0P802.15_TG3_Eastman-Kodak-Support-Documents-for-PHY-Proposal

## Slide 5: Comparative Comments
Same Scheme as 802.15.1 but:
  Doesn’t hop
  Faster MAC
  Wider BW
  Different Base-Band Signal

## Slide 6: Unit Manufacturing Cost
Due to Similarities with BT
  Same IC Processes are applicable
  Cost about $1 more for External Components.
  Slightly More Cost for Antenna System (Stearable Array)
Potentially Less Expensive than 5GHz Solutions.

## Slide 7: Coexistence
802.15.1 Hops into Receiver Bandwidth
Discriminator Can Detect BT 1 Mbps Symbol Rate
Rules for Coexistence could be Determined with 802.15.1
Channel structure should be close to 802.11 to better co-exist with DSSS systems

## Slide 9: Interoperability
2FSK Modulation Scheme is same as 802.15.1
PHY layer has FH capability and follows 802.15.1 rules
MAC controls PHY Mode
Is not interoperable with 802.11
.1 and .3 modes can not operate in the same Frame

## Slide 10: Time to Market
Standard technologies
No New Inventions Required
No New Agency Regulations Required

## Slide 11: Scalability
Power Consumption
  Similar to 802.15.1
  Two RF power modes
  Power Management
Data Rate
  Maximum 22 Mbps
  802.15.1 Modes

## Slide 12: Scalability
Cost
  TBD - Depends on implementation
Functions
  Can be implemented as 802.15:
    .1 only
    .1 and .3
    .3 only

## Slide 13: Form and Size Factor
Similar to 802.15.1 class designs
Compatible with Compact Flash Cards

## Slide 14: Maturity
Prototypes
  Built from Discrete Components
  Tested in Open Range

## Slide 15: Range
Range of 10 meters or greater
  at a receiver sensitivity of -70dBm
  with a corresponding BER of 1E-03 or -04
  permits more than 10 meters range inside residential house with 0dbm xmtr.

## Slide 16: Number of Simultaneously Operating Full Throughput PAN
22 MHz wide RF Channel allows 3 full Channels
Approximates 802.11 three non-overlapping channels
Can support more than 4 channels with proportional reduction in data rate

## Slide 17: Self Evaluation - General

## Slide 18: Self Evaluation - General

## Slide 19: Self Evaluation - General

## Slide 20: Self Evaluation - PHY

## Slide 21: Self Evaluation - PHY

## Slide 22: Conclusion
This Simple Proposal Provides a Good Combination of:
  Cost
  Speed
  Coexistence/Commonality with 802.15.1
  Time to Market
  Minimum Risks

## Slide 23: Criteria Changes
Propose PHY Criteria is Data Rate, and listed Independent of MAC.
Propose Max. 2.4GHz channel bandwidth is limited to 22MHz to support 802.11 channel plan

## Slide 24: Appendix I - Criteria Ranking Comments
This appendix addresses the issues brought up in the various committee discussions, in order to make the feedback official.

## Slide 25: Appendix I
PHY issues for September 12th.
  Section 2.5 Rating “0” Request “+1”
    This factor requires 3 or more scaleable factors to justify a "+1 rating. We already proposed Data rate (1Mbps BT and 22 Mbps high rate), and Range (0dbm and lower power for Kiosk work at less than one meter) This lower range also implies one of the several power saving modes. Our architecture provides many ways to power only necessary systems functions. In Addition, this architecture is compatible with 2.4 or 5GHz bands, although we recommend its uses only at 2.4GHz for cost and performance reasons. This provides a count of 4. In addition, one of the original functions of our architecture and implementation included an IF capable of receiving control, or low bandwidth signals from the ~400MHz band even without the RF Rcvr or Xmtr sections being powered. Although not currently in our plans, this architecture still has that potential for this function and should be considered a feature for this body of experts to consider.

## Slide 26: Appendix I
  Section 4.6 Rated “?”, Request “0”
    In version two of this submission we requested a change from a "?" to a "0". It may not have been noticed. Our prototype was tested in an open range to over 300 feet, at BERs of 10-6 as charted in previous submissions. Structural testing indicated ranges in excess of 10 meters. This configuration met FCC and ETSI rules for low power devices, and did have a patch antenna configuration.

## Slide 27: Appendix I
  Section 4.8.2 Rated “0”, Request “+1”
    The capture effect of 2 and 4 FSK systems, tend to reduce the multi-path affects when the incident signal strength exceeds any reflected signal by about 6 db. Consequently, this criteria should include magnitude aspects in addition to time. Walt Davis has volunteered to present simulation data to support the field and lab results we observed in our prototypes. It is being planed for the September meeting. Since this affect simplifies the architecture for a given price/performance point, I would like to argue for a +1 rating.