## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Evaluation of Coexistence Performance
Date Submitted: January 16, 2001
Source: Oren Eliezer Company: Texas Instruments Israel
Address: POB 5133, Kfar-Saba 44150, Israel
Phone: +972-9-7476962, Fax: +972-9-7430951, E-Mail: OrenE@ti.com
Re: Proposed approach for the evaluation of coexistence performance
Abstract: The two aspects of coexistence performance are discussed (interference suffered and interference caused). Coexistence performance is claimed to be a function of various factors relating to to all layers of a the communication protocol of the coexisting systems. Guidelines for the evaluation of coexistence performance are proposed (system approach, with application dependent performance measures).
Purpose: The purpose of this is to ensure that coexistence performance is evaluated properly by considering the realistic likelihood and user-perceived performance degradation in the scenarios examined.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE 802.15 TG2 Evaluation of Coexistence Performance Monterey January 16, 2001
Oren Eliezer
Texas Instruments Israel
OrenE@ti.com
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 3: Outline
1. The Two Aspects of Coexistence Performance 2. Factors Determining the Coexistence Performance 3. Proposed Guidelines for Evaluation

## Slide 4: Coexistence Performance Aspects
Both aspects of interference are of interest and should be examined:
Interference Susceptibility of our System
  What interfering signals are likely to be present?
  What are their probabilities (statistical distribution)?
  What properties and/or mechanisms of our system make it less susceptible to these interferers?
Potential Interference Caused by our System
  What systems are likely to suffer interference from our system?
  What is the likelihood of each type of system being present?
  What are their susceptibilities to such interference?
  What properties and/or mechanisms of the system allow it to minimize the interference it causes?

## Slide 5: Factors Determining the Coexistence Performance
Coexistence performance is a function of the structure and parameters of all layers of the communications protocol (up to application layer) and not just PHY.
The application is actually the most dominant factor in determining both aspects of coexistence performance.
Good radio performance is necessary (dynamic range, selectivity…) but cannot compensate for a MAC’s vulnerability to interference.
A system may employ both passive and active means for enhancement of its coexistence performance.

## Slide 6: Proposed Guidelines for Evaluation
Specific realistic usage scenarios should be examined.
Different environments are characterized by different typical coexistence scenarios (home, office, outdoors).
The probability and importance of each of the usage scenarios should be considered (prioritized and weighted accordingly).
User-perceived performance degradation is most important, so the coexistence performance measure should reflect that (e.g. latencies, throughputs, distortion measures for image/sound).

## Slide 7: Proposed Guidelines for Evaluation (cont.)
Realistic application-based parameters must be assumed both for the system under examination and for the interfering or interfered system/s surrounding it. Among these are:
  transmission power levels
  relative distances (typical ranges and system layouts)
  system loads (duty cycles)
  transmission durations (packets and entire messages)
  data rates
  instantaneous spectral occupancy (bandwidth and shaping)
  types of data sent (asynchronous, isochronous)
  vulnerability of application to interference