## Slide 1: IEEE P802.15 Working Group for Wireless Personal Area Networks
Power Control and Packet Scheduling for Bluetooth to Avoid 802.11 Direct Sequence Interference
Nada Golmie and Nicolas Chevrollier
National Institute of Standards and Technology
Gaithersburg, MD 20899
USA

## Slide 2: Outline
Non - Collaborative technique to improve Bluetooth data traffic performance
  Part I: Power control
  Part II: Efficient frequency use
Simulation Experiment Setup
  Topology, parameters and traffic model used
Results
Summary

## Slide 3: Part I: Power Control
Update the power of the transmitter, based on the receiver Carrier to Interference Ratio (CIR):
where and , are the transmitted power during update intervals t+1 and t respectively, and is the CIR measured during interval t.

## Slide 4: Part II: Frequency Use
Construct a table of the available frequencies based on the BER measurement at the receiver.
Master checks both its available frequencies and the slave’s available frequencies before sending a packet to the slave.
Frequency Offset
...
0
1
78
Master BER
Master Available Freq.
0
1
0
Master Frequency Use Table
Slave Available Freq.
0
1
1
Slave Sends to Master Updates on its Available Receive Frequencies
10^-2 <
10^-2 <
< 10^-3

## Slide 5: Simulation Parameters
Length of Simulation Run
Bluetooth Parameters
30 seconds
WLAN Parameters
DM1 Packet Interarrival Time
Load
Transmitted Power
1.25 ms
Packet Interarrival Time
Load
1.86ms
50%
50%
1mW
25 mW
Transmitted Power
Slave Coordinates
(0,0)
(1,0)
Master Coordinates
AP Coordinates (Sink)
Mobile Coordinates (Source)
(0,15)
(0,d)
Packet Header
224 bits
Slot Time
SIFS
DIFS
CW_min
CW_max
RTS
20 us
10 us
50 us
31
1023
None
Update Interval
300 packets
DM1 Packet Interarrival Time
Load
2.91 ms
30%

## Slide 6: Topology

## Slide 7: Traffic Model

## Slide 8: Performance Measurements
Measurements are performed at the Baseband:
  Probability of packet loss
  Normalized and mean access delay
  Bluetooth transmitted power

## Slide 9: Error Occurrences and Packet Acceptance Decisions
Error Location
Action Taken
Error Correction
Access Code
Packet Header
DM1 payload
Hamming distance, d=14
1/3 FEC
2/3 FEC
Drop
Drop
Drop

## Slide 10: Packet Loss at Bluetooth Slave

## Slide 11: Bluetooth Master Power Transmitted

## Slide 12: Mean Access Delay for Bluetooth Slave

## Slide 13: Normalized Mean Access Delay for Bluetooth Slave

## Slide 14
Simple non-collaborative techniques can improve the performance of Bluetooth and IEEE 802.11:
  control of Bluetooth transmitted power has limited advantage (decreases packet loss for interference distance > 1 m) but at the cost of increasing the interference on the other devices.
  scheduling of Bluetooth LAN traffic to use non-interfering frequencies (available) eliminates packet loss and increases access delay by ~ 625 us.
Conclusions

## Slide 15
Evaluate the same technique for other DM packet sizes.
Devise other techniques to deal with Bluetooth voice traffic, WLAN Frequency hopping systems.
Future Work