## Slide 1
IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Miscellaneous Coexistence Ideas
Date Submitted: January 16, 2001
Source: Steve Shellhammer Company: Symbol Technology, Inc.
Address: One Symbol Plaza, Holtsville NY 11742
Voice: (631) 738-4302, FAX: (631) 738-4618, E-Mail: shell@symbol.com
Re: Submission of a Coexistence Mechanism in response to IEEE 802.15-00/009r4
Abstract: This is a submission to P802.15.2 of miscellaneous coexistence mechanism ideas
Purpose: To present ideas to IEEE 802.15.2 to be considered as part of the Recommended Practice.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
Miscellaneous Coexistence Ideas

## Slide 3: Purpose of This Submission
This submission is not a standalone Coexistence Mechanism
These are a combination of ideas that may be useful in combination with a coexistence mechanism
It is not my intent for this submission to be voted on.
TG2 can select any of these ideas to supplement a Coexistence Mechanism

## Slide 4: Preferred 802.11b Data Rate
There are four data rates in 802.11b
  1, 2, 5.5 and 11 Mbps
The higher the data rate the lower processing gain
  This implies lower data rate is better
The higher the data rate the shorter the duration of the packet
  This implies higher data rate is better

## Slide 5: Preferred 802.11b Data Rate
These two observations are in opposition
It has been observed that the benefits of having shorter packets more than offsets the decrease in processing gain, by going to higher rates
IT IS BEST TO USE THE HIGHEST DATA RATE IN 802.11B

## Slide 6: Data Rate Scaling in 802.11b
IEEE 802.11b allows for automatic data rate scaling
How data rate scaling is implemented is not specified in the IEEE Standard
The intent of automatic data rate scaling is to increase the range of the network at the expense of data rate
Detect edge-of-range and then rate scale

## Slide 7: Data Rate Scaling in 802.11b
Since the rate scaling algorithm is not in the standard we cannot make too broad a statement about the effect of interference
It is possible for Bluetooth interference to fool the rate scaling algorithm to believe it needs to decrease the data rate.

## Slide 8: Data Rate Scaling in 802.11b
If Bluetooth interference causes the rate scaling algorithm to decrease the 802.11b data rate.
Since decreasing the data rate increases the effect of interference, we have Positive Feedback, resulting in a quick drop to 1 Mbps.

## Slide 9: Data Rate Scaling in 802.11b
IF THE DATA RATE SCALING ALGORITHM IS FOOLED BY BLUETOOTH INTERFERENCE THEN DISABLE IT AND FIX THE DATA RATE AS HIGH AS POSSIBLE

## Slide 10: Bluetooth SCO Link
The Bluetooth SCO Link is a periodic transmission every six Bluetooth slots
  2 out of 6 slots used (No FEC)
  4 out of 6 slots used (2/3-rate FEC)
  6 out of 6 slots used (1/3-rate FEC)
The SCO packets do not include a CRC and retransmission is not included.

## Slide 11: Bluetooth SCO Link
The SCO Link, as an interferer, represents periodic interference with a short period (3.75 ms).
If the Bluetooth power level at the 802.11 receiver is too high, then this periodic interferer is potentially a worse interferer than an ACL Link.

## Slide 12: Bluetooth SCO Link
The SCO Link is more susceptible to 802.11 interference than an ACL Link
  Under interference it is more likely to cause full packet errors, not a few bit errors
  The FEC does very little to mitigate the effect of interference
  The SCO link does not support Packet Retransmission, which is what is needed in an interference environment

## Slide 13: Bluetooth SCO Link
THE SCO LINK IS WEAK IN AN INTERFERENCE ENVIRONMENT
RECOMMENDATION:
  ELIMINATE 1/2-RATE AND 1/3-RATE FEC
  REPLACE IT WITH A NEW SCO LINK WITH UP TO TWO RETRANSMISSIONS
  NEED TO ADD CRC TO SCO

## Slide 14: Look-Ahead CCA in Bluetooth
Currently Bluetooth does not include Clear Channel Assessment
To make CCA useful in Bluetooth it would need to detect other wireless systems, not just Bluetooth devices
Use Receive Signal Strength Indicator to detect other wireless systems

## Slide 15: Look-Ahead CCA in Bluetooth
Since for ACL Link the Slaves can only transmit if the Master sent a packet in the previous slot
For ACL link you could add CCA only to the Master and have it check the current and next frequency.
Look ahead one frequency.

## Slide 16: Look-Ahead CCA in Bluetooth
Bluetooth allocates about 220 s for the frequency synthesizer to tune to the next frequency.
This is quite long and it is possible to design a synthesizer that tunes to a different frequency faster at a reasonable cost.
So look ahead to the next frequency and check for a clear channel.

## Slide 17: Look-Ahead CCA in Bluetooth
BT
220 s
405 s
Tune to fn
Transmission Time
BT
with
CCA
80 s
80 s
60 s
Tune to fn+1
Tune to fn
CCA

## Slide 18: Summary
Presented several observations about Bluetooth and 802.11 Coexistence
  Impact of 802.11b Data Rates
  Impact of 802.11b Rate Scaling Algorithm
  Weakness of the Bluetooth SCO Link
  Look-ahead CCA in Bluetooth