## Slide 1: Proposal for Non-collaborative 802.11 MAC Mechanisms for Enhancing Coexistence: Adaptive Fragmentation
Matthew B. Shoemake, Ph.D.
shoemake@ti.com

## Slide 2: Overview
Fragmentation limits the length of packets on the network
Each packet has a finite amount of overhead
If there is no interference, fragmentation reduced the throughput
If there is interference, fragmentation may increased the throughput
This leads to the question: Under what circumstances should fragmentation be enabled and what should the fragmentation level be set to?

## Slide 3: Interference Detection
Many IEEE 802.11b solutions estimate the SNR and SINR in the header of each packet
Let G be the set of (SNR, SINR) tuples such that for all (x,y) in G, the probability of having a packet error is small, e.g. p << 1
Estimate the PER on all packets with (x,y) in G
If the packet error rate is significantly above p, then there must be an interferer in the area that is interfering with the MPDU of the packet
System can then implement mitigation, e.g. fragmentation

## Slide 4: Adaptive Fragmentation
Should adjust length of packet in time to optimize throughput on 802.11b networks.
Let
  tp be the time taken to transmit a packet
  to be the overhead between packets
IEEE 802.11 Packet
tp
to

## Slide 5: Throughput
Assume when a collision occurs, there is a packet error. Throughput for a given rate is:
Where tH is the time for header of the packet, tD is the time for the data part of the packet, r is the rate of data transmission in the data part of the packet, p is the probability of a packet error, and tP = tH + tD
R =
tD x r
tH + tD + tO
x (1 – p)

## Slide 6: Throughput
The flowing values are constant in the BSS:
  to is fixed, e.g. at the minimum spacing between frames
  tH is fixed, e.g. long preamble or short preamble plus header
Packet error rate is a function of the length of the packet on the air, so q(tp) can be written

## Slide 7: Throughput Plot
For a given data rate and a fixed q(tp), the throughput, R, as a function of tp is well defined

## Slide 8: Optimal Fragmentation
To find the optimal length of each packet analytically, the derivative of R with respect to tp or q(tp) can be taken and set to zero.
Either way the value of dtp/dq or its inverse must be known, and the only way to know this value is to know the function q(tp)
The function q(tp) varies and is not likely to be available in closed form
This implies an adaptive algorithm should be used!

## Slide 9: Adaptive Packet Length Calculation
Let q’ be an estimate of the probability of packet success. This can be measure over some period of time
tp,k+1 = tp,k + 
Where
  Fk = q’(tk) x (tp,k – tH) / (tp,k + to)
   = Fk – Fk-1

## Slide 10: Performance of Adaptive Scheme
Adaptive algorithm find the optimal packet length to optimize throughput after approximately 15 PER estimates. Compare packet length determination with plot on Slide 7

## Slide 11: Summary
A mechanisms for IEEE 802.11b devices to perform adaptive fragmentation calculations is provided.
The optimal fragmentation by the network is determined by the AP via this adaptive algorithm, and the optimal setting is set on the BSS
This algorithm allows for maximization of throughput with by monitoring PER only
This algorithm is compatible with the joint rate shift/power control algorithm proposed in document number TBD.