## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 802.11b Deterministic Frequency Nulling
Date Submitted: 18 January, 2001
Source: Robert E. Van Dyck Company: National Institute of Standards and Technology
Address: 100 Bureau Drive, Mail Stop 8920, Gaithersburg, Maryland, U.S.A.
Voice: 301 975-2923, FAX: 301 590-0932, E-Mail: vandyck@antd.nist.gov
Re: 0
Abstract: In this presentation, we suggest using deterministic frequency nulling to mitigate the effect of Bluetooth interference on 802.11b. Because of the relatively narrow band of the Bluetooth signal, it may be possible to put a null in the frequency spectrum of the 802.11b receiver. However, since Bluetooth is hopping to a new frequency for each transmission, the 802.11b receiver needs to now the frequency hopping pattern. Knowledge of the pattern is obtained by using a bluetooth receiver. Thus, this is a non-collocated, collaborative method.
Purpose: The information in this document should be used to further TG 2 coexistence studies.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.11b Deterministic Frequency Nulling to Mitigate Bluetooth Interference
Robert E. Van Dyck
NIST
Gaithersburg, Maryland
January 2001

## Slide 3: Problem Definition
Some BT traffic have high time utilization
  e.g. SCO traffic with HV1 packets
  A long file transfer using ACL
Bluetooth is narrowband interference to 802.11
  Can cause serious packet loss
  Retransmissions may lead to extensive delay
Do not want to significantly reduce BT throughput

## Slide 4: Deterministic Frequency Nulling
Basic Idea:
  Put a null at the frequency of the BT signal in the 802.11 receiver
Not enough time to adaptively null
  Need to obtain packet’s access code
Determine the BT frequency a priori
  Need Bluetooth receiver
Use a transversal filter

## Slide 5: Combined Solutions
Primarily a PHY level solution
Nulling can be used with other mechanisms:
Adaptive Power Control
Scheduling
Adaptive Frequency Hopping