## Slide 1: ‘RF-Lite’ a solution for Low Data Rate Application
Benno Ritter
Philips Semiconductors

## Slide 2: Contents
Introduction
  Target Markets & Application Scenarios
PURL Protocol
Air Interface Physical Layer
Application Scenarios
System Realisation
Demonstration

## Slide 3: Preface
Based on work performed in RF-Lite (Firefly) committee (http://12.5.139.199)
20 companies are members and growing
MRD V0.91
TRD V0.9
Current revision of the spec V0.8
Spec V1.0 to be finalized in Q2/01

## Slide 4: Introduction
Success Factors
Target Markets
Applications & Environment
Market Sizes

## Slide 5: Success Factors
Low cost
Data type support
Unlicensed band
Unrestricted geographical use
Global implementation
Governmental regulations

## Slide 6: Low Cost
The added cost of the RF communication capability must be at or below existing consumer price points for end user solutions currently servicing these markets. (interactive wireless joystick would be expected to cost the same as an existing IR or wired joystick)
In Home Automation systems, the added cost needs to be comparable to the most efficient cost of installing a wire to a specific device.

## Slide 7: Data Type Requirements
An aggregate data link service of at least 115 kbps is needed to support the following data types:
  One asynchronous data link at a rate up to 115.2 kbps (RS232)
  Voice recognition at a peak aggregate rate of up to 64 kbps
  Text-to-speech (TTS)
  Critical latency applications, such as, interactive gaming
  USB packets excluding isochronous transfer types
  Any combination of the above data types subject to aggregate capacity limitations

## Slide 8: Unlicensed Band & Unrestricted Geographical Use
Unlicensed Band
  The user is not required to apply for any licenses to operate the product implementing this specification.
Unrestricted Geographical Use
  Within a geographical (or political) region, there should not be any restrictions on its use.
  Users would expect to be able to purchase the device implementing this RF technology at one part of the geographic region and use it in another part.
  The geographic region can be as localized as a country (e.g. USA or Japan) or a geo-political area such as European Union where the standards are uniform.

## Slide 9: Global Implementation & Governmental Regulations
Global Implementation
  A desirable consideration is to have one specification (and implementation) that can be sold and used internationally with minimum product variation.
Governmental Regulations
  The specification will need to comply with the appropriate regulations in force at the time for the geographical or political region (includes regulations relating to safety, energy, radiation, etc.)

## Slide 10: Target Markets
Consumer
Electronics
Low-End Radio
Devices
PC
Peripherals
Home
Automation
Toys &
Games
Personal
Healthcare

TV

VCR

DVD

CD

Remote

…

Mouse

Keyboard

Joystick

Gamepad

…

Security

HVAC

Lighting

Closures

…

PETs

Gameboys

Educational

…

Monitors

Diagnostics

Sensors

…

## Slide 11: Applications & Environment
Human Input Devices (HID)
Home Automation & Control
Home Security & Interactive Toys

## Slide 12: Human Input Devices (HID) 1
  Keyboard
      Communication is typically uni-directional
      Expected throughput: 1.0 kbps
      Expected response time: < 50 msec.
      Expected Battery Life: 6 months min. with typical use (defined as 10 keystrokes/second for 3 hours/day)
  Mouse / Pointing Device
      Communication is typically uni-directional
      Expected throughput: 3.0 kbps
      Expected response time: < 25 msec.
      Expected Battery Life: 6 months min. with typical use (defined as updating the screen 5 times/second for 3 hours/day)
  Remote Controls (controls for audio & video equipment)
      Communication is uni- and/or bi-directional
      Expected throughput: 3.0 kbps
      Expected response time: < 25 msec.
      Expected Battery Life: 6 months min. with typical use (defined as updating the screen 5 times/second for 3 hours/day)

## Slide 13: Human Input Devices (HID) 2
  Gaming Device
  Double Joystick
      Communication is typically bi-directional for feedback controllers
      Expected throughput: 6.0 kbps
      Expected response time: < 16.7 msec.
      Expected Battery Life: 6 months min. with typical use (defined as updating the screen 5 times/second for 3 hours/day)
  Game Pad for DirectX
      Communication is typically bi-directional for feedback controllers
      Expected throughput: 9.0 kbps
      Expected response time: < 16.7 msec.
      Expected Battery Life: 6 months min. with typical use (defined as updating the screen 5 times/second for 3 hours/day)

## Slide 14: Home Automation & Control
Automated lighting, temperature control, maintenance, and amenities
Interaction with a controller for updates and supervisory functions
  Automation Devices
    Communication is uni- and/or bi-directional
    Expected data rates: <10 kbps to 64 kbps (aggregate)
    Expected Response Times: 100 msec.
    Expected battery life >2 years operating on 2AA batteries
    Very low power consumption
    High density of units, up to 128
  Control Devices
    Communication is uni- and/or bi-directional
    Expected data rates from <10kbps (aggregate)
    Expected Response Times: 100 msec.
    Battery life >2 years operating on 2AA batteries
    Very low power consumption
    Medium density of units, up to 64

## Slide 15: Home Security & Interactive Toys
Home Security
    Communication is uni- and/or bi-directional
    Expected data rates: <10 kbps to 64 kbps (aggregate)
    Expected battery life: >2 years operating on 2AA batteries
    Very low power consumption
    High density of units, up to 128
Interactive Toys
    In-room interaction with TV or PC program
    Home+yard coverage for mobile robots and multi-user gaming
    Support for voice recognition and TTS desired
    Communication link must support bi-directional communication
    Some applications may need to support packetized audio at 32 kbps with latencies on the order of 100 msec.
    Expected bandwidth: 115.2 kbps
    Must support four (4) simultaneous links
    Use the “Alkaline Battery Model” – throw away after use
      Expected battery life: > 3 months with typical use (Low data rate toys)
      Expected battery life: > 30 days with typical use (Medium data rate toys)
      Typical use is defined as 4 hours/day

## Slide 16: Estimated Market Size for Home Applications
Including
  White goods
  Home security
  HVAC
  PC peripherals
Excluding
  Industrial control
  Medical equipment
  Remote controls
Rough estimation based on forecast for goods only, wireless link penetration estimated
So far no overall market numbers are existent
Philips analysis based on reports from Gartner and Instat 1999

## Slide 17: Market Drivers
Extremely low cost
Ease of installation
Reliable data transfer
Short range operation
Reasonable battery life

## Slide 18: Philips Solution
Protocol specification (“PURL”)
Software design and implementation
Air interface design
Baseband and radio IC implementation

## Slide 19: PURL Protocol for Universal Radio Links

## Slide 20: Contents
Lite Overview
PURL Flavours
Data Transfer
Network Management

## Slide 21: RF-Lite Overview

## Slide 22: PURL Features
Master/slave topology
Automatic network configuration
Dynamic slave device addressing
Virtual peer-to-peer links (pairing)
Full handshaking for packet transfers
Power management features
Up to 254 (+ master) network nodes

## Slide 23: PURL Features Cont...
CSMA-CA channel access mechanism
15ms frame structure
TDMA slots can be allocated
12kbps & 115kbps (actual) data throughput
Service discovery
Low impact internet capability
Extended sleep periods for slave devices (programmable through application SW)

## Slide 24: PURL Flavors

## Slide 25: PURL Slave Node
PURL On-air Protocol Stack
PURL PHY
Radio
PURL Slave Node
PURL API
PURL MAC
PD-SAP
PM-SAP
MD-SAP
MM-SAP
User Interface
Slave APL
PURL DLC
Notes: The important thing here is the modular OSI layered approach. The PURL on-air protocol stack (PHY+MAC+DLC) will probably be included on the final chip. Any extra layers will need to be implemented off-chip, i.e. to implement a master node, as in the next slide.
The PURL API is a very simple interface (discussed later) which is common over all the architectures.

## Slide 26: PURL Host Enabled Master Node
PURL On-air Protocol Stack
PURL PHY
Radio
PURL Master Node
PURL API
PURL MAC
PURL DLC
PD-SAP
PM-SAP
MD-SAP
MM-SAP
DD-SAP
DM-SAP
Host Transport
Host Interface PHY
Host Stack
PURL Transport
PURL Interface PHY
Host Application
Host User Interface
Host
Local User Interface
Master APL
PURL NWK
Notes: The architecture here illustrates that, if desired, the master can be attached to a host (PC or STB). In this case the master node would need to implement some bridging protocol with which to transfer PURL API commands across another, probably wired, connection technology, such as USB or RS232.

## Slide 27: Data Transfer

## Slide 28: Frame Structure
Time, ms
t + tf
t
Basic frame:
Network beacon
Contention period
Time, ms
t
t + tf
Slotted frame:
Allocated slot
Notes: The basic frame shows the contention period during which devices must utilise the CSMA-CA mechanism before transmitting.
The slotted frame still has some portion of contention for those devices which do not have an allocated slot.

## Slide 29: Data Packet Structure
APL
DATA
8n
DSN
DFL
APDU
DLC
8n
8
8
ADD
NID
MPC
MFL
DPDU
MAC
8
8
8
8/16
16+8n
PLG
MPDU
PHY
8
40+8n+8/16
SOP
PRE
PPDU
8
16
48+8n+8/16
Notes: The key thing here is the simplicity of the packet structure. The data is appended at the DLC with a Data Sequence Number (DSN), network (NID) and device (ADD) addressing information is added at the MAC along with a checksum (MPC). The PHY adds a packet length (PLG) and the packet is transmitted with a preamble sequence (PRE) and start of packet marker (SOP).
The DSN is used to tie the handshake packet to the data packet, as on the next slide.

## Slide 30: Data Transfer Model
Master
Slave
Default control pipe
Function pipes
Control
endpoint
Function
endpoints
Notes: Each slave device can define one or more endpoints which are individually addressable parts of the slave. Virtual pipes are then created between the master and the slave. PURL reserves a pipe, known as the default control pipe, to pass configuration and control information to the device.

## Slide 31: Network Management

## Slide 32: Network Initiation
Master capable devices only
Listens for network beacons
Attempts to invoke network beacons
Assumes unique network identifier
Starts master operation

## Slide 33: Network Topology
Control flow
Remote
TV
Curtains
DVD
Lamp
STB
Master node
Slave node
Communications flow
Notes: An example network topology in the area of home (living room) control. A set-top-box is acting as the master with a remote, TV, DVD, lamp and curtains enumerated on the network. This has no functionality since the slaves can only talk to the master. What the consumer actually wants is to be able to control the TV, DVD, lamp and curtains using the remote. In this case there needs to be some virtual peer-to-peer links between the remote and the other devices on the network. The mechanism of creating these links is known as pairing.

## Slide 34: Air Interface Physical Layer

## Slide 35: Frequency Bands
2.4GHz ISM band
  Channel spacing: 3MHz
  F = 2404 + 3k MHz with k = 0, 1, …, 25
  Common band:
    USA, Europe including France and Spain
    2.449MHz – 2.470MHZ
    k = 15, …, 22; equals 8 channels
915MHz ISM band
  USA only

## Slide 36: Direct Sequence
Spread spectrum regulations allow higher transmit power
  Longer range
  Transmit power: -4 to +20dBm
Direct sequence
  Faster acquisition than frequency hopping
  Complexity in digital domain (cheaper)

## Slide 37: Direct Sequence
Spread using length 11 Barker sequence
  Optimal autocorrelation properties
  Short sequence gives fast acquisition
  Used in IEEE802.11
‘1’ sent as: 10110111000
2.2Mchips/sec
Processing gain of 10.4dB

## Slide 38: Modulation
GFSK
  Constant envelope  (cheap) non-linear PA
  Spectral efficiency
  Modulation index; h = 0.5
  Pre-modulation filter; BT = 0.5

## Slide 39: Bit Rates
200kbps (raw)
21.875kbps low bit rate option:
  Trade data rate for extra range via coding
  Over air bit rate remains 200kbps
  Hadamard Error Correction Coding
    achieves reliable link at low SNR
  Longer preamble and SOP
    reliable synchronisation at low SNR

## Slide 40: Range Estimation
Using Firefly TRD/RSI propagation model
Approx. x2

## Slide 41: Air Interface Summary
Direct Sequence 2.2Mchips/sec
2.4GHz band (and 915MHz)
200kbps
-4 to +20dBm
GFSK, h = 0.5, BT = 0.5
Low data rate option: 21.875kbps

## Slide 42: Application Scenarios and System Realisation

## Slide 43: Applications :- Slave Device
Light Switch
Thermostat
Accessory Control
Security Sensor
Computer Keyboard

## Slide 44: RF-Lite Block Diagram
RF IC
Control
Transmit Data
Receive Data
BASEBAND
Application

## Slide 45: Development Platform

## Slide 46: RF-Lite Protocol Demonstration

## Slide 47: Current Demonstration
STB
Auto dialler
Fan
Switch
Notes: In May we will have this demonstration which will use a STB, possibly acting as the master, along with our current demonstration devices. The STB will also implement a web server, allowing us to remotely access and control the devices connected to it. The TV can also be used to display status, such as whether the curtains are opened or closed, etc.

## Slide 48: Thanks

## Slide 49: Target Applications 1
Desktop PCs and Home Entertainment Systems (Home Theatre TV)
  Computer peripherals;
  HID devices
Video conference equipment
  Remote control
Video gaming equipment
  Multi-player PC & video games
  Playing a PC DVD game in front of a TV monitor
Remote controls for audio and video equipment
PC Enhanced & stand alone toys
  In-room coverage
  Home+yard coverage

## Slide 50: Target Applications 2
Home appliances and general consumer electronic devices
  Existing home security systems, electrical & heating systems
  Wireless door and opening monitoring, system control
  Glass breakage monitoring (sensors)
  Wireless Keypads
  Child Monitor
  Smoke and flame detectors
  Fire Pull stations
  Personal transponders
  Lighting and remote control of appliances in the home;
    Blinds
    Shades
    Fireplaces
    Pool/Spa equipment
    Garage door openers
  Voice Control
  Home Comfort Control
New device categories that have not yet been developed, such as news tablets, and keyboards with built-in displays

## Slide 51: Modulation
Transmitted spectrum:

## Slide 52: Simulated Performance

## Slide 53: Link Budget
Propagation models:
  Firefly-TRD/RSI
    Attenuation = 50.2 + 28log(d) dB
  IEEE 802.15
    Attenuation = 40.0 + 20log(d) dB (d<8m)
    = 58.5 + 33log(d/8) dB (d8m)

## Slide 54: Range Estimation