## Slide 1
<number>
Project: IEEE 802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IEEE 802.15 Report at BT Decvon]
Date Submitted: [09july00]
Source: [John Barr] Company [Motorola]
Address [1750 E. Golf Road, Schuamburg, IL 60173]
Voice:[+1 847 576-8706], FAX: [+1 847 538-4253], E-Mail:[John.Barr@Motorola.com]
Re: [00389R0P802-15_IEEE-802.15-Report-at-BT-Devcon.ppt]
Abstract: [IEEE 802.15 WG Presentation to Bluetooth Developers Conference – 7Dec2000]
Purpose: [Document IEEE 802.15 Presentation Given at Bluetooth Developers Conference]
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Bluetooth SIG and IEEE 805.15
John R. Barr, PhD
Chair, IEEE 802.15 Task Group 3
Director, Architecture & Technology Strategy
Motorola Personal Area Networks
December 7, 2000

## Slide 3: Objectives of IEEE 802
To develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of standards making:
  Due process
  Consensus
  Openness
  Balance
  Rights of appeal
Publish LAN/MAN Standards in electronic format

## Slide 4: IEEE 802 Architecture

## Slide 5: IEEE 802.15 Charter
Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks
  Communication of devices within a Personal Operating Space

## Slide 6: IEEE 802.15 Working Group Activities
802.15.1 (Standardization Task Group)
  IEEE Standard of Bluetooth™ Specification
802.15.2 (Recommended Practice)
  Model and Facilitate Coexistence of WPAN & WLAN devices
802.15.3 (High Rate WPAN Standard Task Group)
  A High-Rate (> 20 Mbps) WPAN
802.15.4 (Low Rate WPAN Standard Task Group)
  Raw Data Rate = 2Kb/sec to 200Kb/sec
Radio2 Study Group (suspended)
  Track Bluetooth2 and recommend an action.

## Slide 7: IEEE 802.15.1

## Slide 8: IEEE 802.15 Task Group 1
IEEE 802.15 Task Group 1 is converting the Bluetooth Specification into an IEEE Standard
  Convert to IEEE Format
  Add
    Introductory material
    Specification and Description Language (SDL)
    LLC interface
  Letter Ballots, Comments, and Comment Resolution.

## Slide 9: IEEE 802.15.1 and Bluetooth

## Slide 10: Bluetooth SIG Role
Only responder to original Call For Proposals (CFP)
Copyright agreement with IEEE for use of text
Advise on IEEE additions
Informal acceptance of Comments as Errata
Promotion of IEEE connection

## Slide 11: Current Draft Planning
D0.7.1
(v1.0B)
+-99/173r6
C1-11
Annex
+SDLs
+PICS
D0.8
(v1.1)
+-00/159r16
*24May00
Letter Ballot #(7)
10-15 Day LB
~24Nov00
v1.1
via errata
1Jan01
*8May00
D0.7.2
(v1.0B)
+-99/173r6
C1-11
Annex
+Informal
comments
*18Sep00
*Note: Date released by Editor-in-Chief
~Note: Based on an IEEE estimate for planning purposes; not confirmed by BSIG
D0.7.3
(v1.0B)
Smoothed
*27Dec00
Available one (1) week before ballot starts.
14Jan01

## Slide 12: More Information
http://standards.ieee.org/catalog/ordering.html
  Tom Siep, How to Find What You Need in the Bluetooth™ Spec, IEEE Press, November 2000
  Bob O’Hara and Al Petrick, The IEEE 802.11 Handbook: A Designers Companion, IEEE Press, 1999.
http://www.ieee802.org/11
http://www.ieee802.org/15

## Slide 13: Contact Data
Website: http://www.ieee802.org/15/pub/TG1.html
Chair: giffordi@ieee.org
Vice Chair: bisdik@us.ibm.com
Technical Editor: siep@ti.com
Secretary: kinneypw@norand.com
Public List Server: stds-802-wpan@ieee.org
http://standards.ieee.org/catalog/ordering.html
  Tom Siep, How to Find What You Need in the Bluetooth™ Spec, IEEE Press, November 2000

## Slide 14: IEEE 802.15.2

## Slide 15: Mutual Interference
Problem: Both IEEE 802.11 and Bluetooth operate in the same 2.4 GHz ISM Band.
Problem: Bluetooth enabled devices will likely be portable and will need to operate in an IEEE 802.11 WLAN environment.
Problem: There will be some level of mutual interference

## Slide 16: Task Group 2 Deliverables
Coexistence Model
  Model quantifying the effect of the mutual interference of WLAN and WPAN upon one another.
Coexistence Mechanisms
  Mechanisms or techniques to facilitate coexistence of WLAN and WPAN devices.
Both to be documented in an IEEE Recommended Practice

## Slide 17: Coexistence Model
The purpose of this Coexistence Model is:
  To quantity the effect of the mutual interference under varied circumstances.
    WLAN in Laptop and Bluetooth in nearby PDA
    WLAN and Bluetooth in the same Laptop
  To demonstrate the effectiveness of the adopted Coexistence Mechanism.

## Slide 18: Coexistence Model
The Coexistence Model consist of four sections,
  Physical Layer Models of the 802.11 and Bluetooth Radios (802.15.1)
  MAC Layer Models of both 802.11 and Bluetooth
  RF Channel Model of the Radio Channel
  Data Traffic Models of the traffic over both 802.11 and Bluetooth networks.

## Slide 19: Coexistence Model
Input to the Model
  Location of 802.11 and Bluetooth devices
  Type of Data Traffic flowing over both 802.11 and Bluetooth networks.
Output of the Model
  Reduction of Network Throughput, for both 802.11 and Bluetooth.
  Increase in Network Latency, for both 802.11 and Bluetooth.

## Slide 20: Coexistence Mechanisms
Coexistence Mechanisms Facilitate Coexistence of WPAN & WLAN devices
We sent out a Call for Submission of Coexistence Mechanisms in September 2000.
Presentations are planned for
  November 2000 meeting (last month)
  January 2001 meeting in Monterey

## Slide 21: Coexistence Mechanisms
Collaborative Mechanisms
  Some form of communication between the WLAN and WPAN exists.
  Use this link to provide fair sharing of medium.
Non-Collaborative Mechanisms
  No communication between WLAN and WPAN exists.
  Techniques to minimize the effects of the mutual interference

## Slide 22: Task Group 2 Current Status
First-order models of 802.11 and Bluetooth Physical Layers are complete.
MAC Layer model for 802.11 was available. We have added Bluetooth MAC Layer model.
We are currently integrating the PHY and MAC Layer Models.

## Slide 23: Task Group 2 Current Status
We have received letters of intent from a number of companies to submit their Coexistence Mechanisms.
We plan to hear those submissions at the January 2001 IEEE meeting in Monterey.
We will then evaluate and select a Coexistence Mechanism.

## Slide 24: Task Group 2 Future Work
Ensure proper coexistence of the High-Rate WPAN with both Bluetooth and 802.11
Issue subsequent releases of IEEE 802.15.2 with additional models to include High-Rate WPAN and possibly other wireless devices in the ISM bands

## Slide 25: Contact Data
Website: http://www.ieee802.org/15/pub/TG2.html
Chair: shell@symbol.com
Vice Chair: nada@nist.gov
Technical Editor: kevin.marquess@hyperinterop.com
BSIG Liaison: todsizer@lucent.com
Secretary: kinneypw@norand.com
PHY Chairman: jimlans@mobilian.com
MAC Chairman: nada@nist.gov
Public List Server: stds-802-wpan@ieee.org

## Slide 26: IEEE 802.15.3

## Slide 27: Application Summary
Fast file transfers between consumer devices.
Visit applications on Web site.
Local video distribution and control
DCT-2000

## Slide 28: TG3 Application Needs
Consumer Market, Environment and Interfaces and Co-existence
Throughputs above 8 Mbps are needed, which imply >20 Mbps for Multimedia applications
Cost is a KEY factor
Standard has to happen quickly
Needs to support Quality of Service

## Slide 29: Project Description
Wireless Medium Access Control (MAC) and Physical Layer (PHY) Specifications for High Rate Wireless Personal Area Networks (WPAN)
  … wireless connectivity with fixed, portable and moving devices within or entering a Personal Operating Space (POS) (up to 10 meters in all directions enveloping a person)
  … interoperability or coexistence with other 802.15 TGs
  … coexistence with other wireless devices in conjunction with Coexistence Task Groups such as 802.15.2
  … low complexity, low cost, low power
  … >20Mbps to satisfy a set of consumer multi-media industry needs for WPAN communications.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Submitted Proposals
MAC
  4 Proposals
    TG1 Reuse with M/M slot cycle TDMA
    Adaptive TDMA with M/M QoS policies
    CSMA with Real-Time features
    802.11 with point coordination function for isochronous
PHY
  8 Proposals
  2FSK, 4FSK, QPSK, OFDM, nQAM
  2.4 GHz, 5GHz, UWB
  Rates up to 50Mbps
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: Status
MAC selected as a result of a compromise between leading candidates:
  Scheduled TDMA for delivery of multi-media content (Kodak)
  Multi-media QoS policies (Sharewave/Motorola/Radiata)
  CSMA section for real-time response and channel allocation
  No 802.15.1 compatibility mode required (implementation specific)
PHY selected to reuse 802.11 single carrier model with variable coding:
  OQPSK for base mode 22 Mbps
  16,32,64QAM with TBD coding methods for higher data rates:
    33, 44, and 55 Mbps

## Slide 32: MAC Features
From Kinney Proposal:
  Proven support for mobile wireless PANs
  Wired infrastructure access point interaction
  Temporary sub-net separation and recombination procedure
  Protocol support for efficient power management policies
From Parks/Davis Proposal:
  Redundant master controllers
  Repeater service
  Virtual data streams (Asynchronous and Isochronous)
  Negotiation of QoS parameters
  Dynamic channel selection and/or migration
  Adaptive FEC and selective retransmission ARQs

## Slide 33: MAC Features (cont.)
From Heberling Proposal:
  Efficient Slot Cycle TDMA algorithm for accessing the RF medium
  Support for Isochronous and Asynchronous data streams
  Bounded latencies
  Negotiation of channel bandwidth allocation

## Slide 34: MAC Protocol Superframe
Maintain station synchronization
coordinate sleep cycles
FH coordination (if necessary)
Asynchronous slot/cycle assignments
Isochronous slot/cycle assignments
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period

## Slide 35: MAC Protocol: Contention Access Period
All control messages such as:
attachment requests
authentication responses
slot cycle requests
In addition short data frames could be sent in this period
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period

## Slide 36: PHY Features
Unlicensed 2.4 GHz band with a minimum raw data rate of 22 Mb/s with optional modes to go as high as 66 Mb/s.
  Frequency: 2.4-2.4835 GHz
  Symbol rate: 11 Msymbols/s
  Base Modulation: O-QPSK
  RF Bandwidth: <22 MHz
  Number of channels: 4 (3 in 802.11 compatible mode)
  Transmit power: 0 to 8 dBm
  Range: > 10m
Regulatory Compliance:
  US: FCC 47CFR15.249 (aka low power rules)
  European Community: ETS 300-328
  Japan: ARIB STD-T66

## Slide 37: PHY Features (cont.)
Modulation | Coding | Data rates | 
OQPSK | None | 22 Mb/s | Mandatory
16 QAM | TBD | 22-33 Mb/s | Optional
32 QAM | TBD | 33-55 Mb/s | Optional
64 QAM | TBD | 44-66 Mb/s | Optional

## Slide 38: Status and Plans for TG3
May 2001 - Complete Initial Draft (PHY and Data Link layers)
November, 2001 - Sponsor Ballot
Standard by the end of 2001 or early 2002
Archive documents
  00127 - TG3_High-Rate_Project-Plan-Proposal
  00180 - TG3 Evaluation Process Flow Chart
Notes: <number>
<footer>
<header>
<date/time>

## Slide 39: Contact Data
Website: http://www.ieee802.org/15/pub/TG3.html
Chair: john.barr@motorola.com
Vice Chair: james.d.allen@kodak.com
Secretary: kinneypw@norand.com
PHY Comm. Chair: jgilb@mobilian.com
MAC Comm. Chair: allen.heberling@kodak.com
SYS Comm. Chair: m-duval@ti.com
Public List Server: stds-802-wpan@ieee.org
Bluetooth Radio-2 Liaison: carlstevenson@lucent.com

## Slide 40: IEEE 802.15.4

## Slide 41: Low Rate PAR
To provide a standard for ultra low complexity, ultra low cost, ultra low power consumption and low data rate wireless connectivity among inexpensive devices. The raw data rate will be high enough (maximum of 200kbs) to satisfy a set of simple needs such as interactive toys, but scaleable down to the needs of sensor and automation needs for wireless communications.
The project may also address the location tracking capabilities required to support uses of smart tags and badges.

## Slide 42: Contacts
Due to the recent establishment of this task group, full contact information is not available.
See the IEEE 802.15 web site for the most recent information: http://ieee802.org/15/
Acting Chair – Bob Heile – bheile@bbn.com

## Slide 43: Questions?
Contact Information:
  John R. Barr
  Director, Architecture & Technology Strategy
  Motorola Personal Area Networks
  1750 E. Algonquin Road, 6th Floor
  Schaumburg, IL 60173
  Office: (847) 576-8706
  FAX: (847) 538-4253
  Email: John.Barr@Motorola.com