## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: 8-State Trellis Coded Modulated 16/32/64-QAM Proposal for High Rate WPANs
Date Submitted: 12 January 2001
Source: Jeyhan Karaoguz
Address: Broadcom Corporation, 16215 Alton Parkway, Irvine, CA 92619
Voice: 949 585 6168
E-Mail: jeyhan@broadcom.com
Re: Call for Proposals for IEEE P802.15.3 High Rate Task Group
Abstract: This proposal describes an 8-State Trellis Coded modulated 16/32/64-QAM physical layer operating in the unlicensed 2.4 band. The proposed system provides adaptive data rates from 33 Mbps to 55 Mbps depending on application requirements and channel conditions.
Purpose: To be considered as a candidate PHY layer technology for IEEE P802.15.3 specification
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Presentation Outline
16/32/64-QAM Signal Constellations
Description of Proposed Trellis Code
  16/32/64-QAM Set Partitioning
  8-state Trellis Code
  8-state Multi-Mode TCM Encoder
TCM Coding Gain
TCM Coded Frame Format
Performance Results with Rayleigh Fading Channel
Encoder/Decoder Characteristics
Conclusion
Notes: Let me draw your attention to the distinct features of our proposal compared to other proposals
First, we have proposed the only FH system achieving data rates up to 20 Mbps
FH systems brings major cost advantages for dual mode 802.15.1/3 devices since the RF front-end blocks are mostly re-used.
FH systems demonstrates great robustness wrt other wireless interferes due to hopping and low BW that is 5 MHz. This resutl is evident in our co-existence and jamming resistance numbers
The other distinction is that we have the smallest signal BW compared to other proposals. This feature gives us the best performance as accepted by the PHY subcommitte delay spread tolarance. Simulation result showing this will be shown shortly
Our proposal is the only one that takes advantage of the new FCC amendment that allows 5 MHz FH systems transmitting upto 21 dBm. Therefore, we can allow a longer range higher power mode just like BT systems do.

## Slide 3: Signal Constellations
16-QAM TCM (33 Mbit/s)
32-QAM TCM (44 Mbit/s)
64-QAM TCM (55 Mbit/s)

## Slide 4: 16/32/64-QAM Set Partitioning
S0
S0
S0
S2
S2
S2
S4
S4
S4
S6
S6
S6
S1
S1
S1
S3
S3
S3
S5
S5
S5
S7
S7
S7
64-QAM Set
Partitioning
32-QAM Set
Partitioning
16-QAM Set
Partitioning
d
d
d
d

## Slide 5: 8-State Trellis Code
S0 S2 S4 S6
S1 S3 S5 S7
S2 S0 S6 S4
S3 S1 S7 S5
S4 S6 S0 S2
S5 S7 S1 S3
S6 S4 S2 S0
S7 S5 S3 S1
Minimum distance error event occurs between code sequences S6-S4-S7-S2 and S2-S5-S7-S0
Squared Euclidean distance between these sequences: 2d2+d2+0+2d2 = 5d2
Approximate coding gain: 10log(5/2) = 4 dB

## Slide 6: 8-State Multi-Rate TCM Encoder
32-QAM
64-QAM
2-D Output
to Pulse Shaping
Filter
b2
b3
b4
3,4,5
bits/symbol
16/32/64 QAM TCM
Mode Selection
Subset
Selection
(S0,…,S7)
T
+
T
T
+
16-QAM
C
bo
b1
Symbol Selection
from Subsets

## Slide 7: Coding Gains for 8-State QAM TCM
Coding gain is measured at a BER of 10-5 in the presence of an AWGN channel

## Slide 8: Receiver Sensitivity
Receiver Sensitivity: AWGN14 MHz BW + Noise Figure (12 dB) + SNR10-5 BER
  -71 dBm for 64-QAM TCM, 55 Mbit/sec
  -74 dBm for 32-QAM TCM, 44 Mbit/sec
  -77 dBm for 16-QAM TCM, 33 Mbit/sec

## Slide 9: Variable Length Frame Format
Preamble: Low overhead preamble only needed for fast packet-by-packet MMSE-DFE equalization
Tail: Beneficial for reaching a known TCM state at the end of a burst transmission
Preamble
CRC
Tail
Message Body
3 T
160 T

## Slide 10
Delay Spread Performance
Exponential decaying Rayleigh fading channel
  Per IEEE P802.15-00/110r12 section 4.8.1
  Symbol time (inverse of modulation rate) = 90.91 ns, channel sampling time = 22.73 ns (1/4 of symbol time)
  Channel duration is 1 usec (44 samples)
Simulation Parameters
  I Carrier-frequency-offset | < 300 kHz, | Symbol-frequency-offset | < 25 ppm
  Feed-forward equalizer spans 8 symbol intervals, feedback filter spans 6 symbol intervals
  1000 random channels generated for each RMS delay spread simulated
  Various RMS delay spreads up to 90 nsec were simulated
  Frame Error Rate (FER) performance was evaluated against average received power
  Frame size is 8192 bits
Results
  Proposed PHY layer with 8-State TCM code outperforms the 25 nsec delay spread tolerance requirement
  Operating at 33 to 55 Mbit/s, better than 5% FER is achieved for greater than 95% of the channels simulated for up to 90 nsec RMS delay spread

## Slide 11
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 64-QAM/TCM in the presence of 10 ns RMS delay spread + AWGN
Receiver Sensitivity: -71 dBm

## Slide 12
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 64-QAM/TCM in the presence of 25 ns RMS delay spread + AWGN
Receiver Sensitivity: -71 dBm

## Slide 13
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 64-QAM/TCM in the presence of 90 ns RMS delay spread + AWGN
Receiver Sensitivity: -71 dBm

## Slide 14
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 32-QAM/TCM in the presence of 10 ns RMS delay spread + AWGN
Receiver Sensitivity: -74 dBm

## Slide 15
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 32-QAM/TCM in the presence of 25 ns RMS delay spread + AWGN
Receiver Sensitivity: -74 dBm

## Slide 16
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 32-QAM/TCM in the presence of 90 ns RMS delay spread + AWGN
Receiver Sensitivity: -74 dBm

## Slide 17
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 16-QAM/TCM in the presence of 10 ns RMS delay spread + AWGN
Receiver Sensitivity: -77 dBm

## Slide 18
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 16-QAM/TCM in the presence of 25 ns RMS delay spread + AWGN
Receiver Sensitivity: -77 dBm

## Slide 19
8-State TCM Receiver Performance
Frame Error Rate vs. Average Received Power: 8-State 16-QAM/TCM in the presence of 90 ns RMS delay spread + AWGN
Receiver Sensitivity: -77 dBm

## Slide 20: Multi-Rate QAM TCM Transmitter
Randomizer
and CRC
Generator
Preamble
Generator
TCM
Encoder
Transmit Control
I/Q Modulator
DACs and LPFs
Inter-
polator
X 2n
Pulse
Shaping
Filter
X 2n
Data
Control
IF and RF Stages

## Slide 21: 8-State TCM Characteristics
No PHY layer transmission overhead
  Coding redundancy achieved by constellation expansion rather than rate expansion
Low decoding delay
  Viterbi decoding delay is only 10 symbols, i.e., 910 nsec
TCM is suitable for variable length frame sizes or fragmented packets
Proposed TCM code is free of proprietary or patented intellectual property

## Slide 22: TCM Encoder Complexity
8-State TCM Encoder
  Requires an 8-State finite state machine
    Three 1-bit wide delay registers
    Two modulo-2 adders (each 1-bit)
    Negligible total gate count for the encoder
  Uses already required 16/32/64-QAM constellation mappers (bits to QAM symbols)
T
+
T
T
+
C

## Slide 23: TCM Decoder Complexity
TCM Decoder
  Viterbi decoder is used for 8-state decision-feedback sequence estimation
  6 feedback taps
  Symbol decision trellis relies on a past history of 10-symbols
Chip Area and Gate Count
  Chip area required for 8-state decision-feedback sequence estimation circuit is 450 um x 300 um, 0.135 mm2 in 0.13u CMOS technology
  25K Gates in 0.13u CMOS techology
Power Consumption
  ~5 mW power consumption in 0.13u CMOS technology

## Slide 24: Evaluation Criteria
Unit Manufacturing Cost
  Total gate count for the 8-state TCM encoder and decoder implementation in 0.13u CMOS is 25K gates including all logic and memory
Delay Spread Resistance
  Proposed PHY layer with 8-state TCM code easily outperforms the 25 nsec delay spread tolerance requirement
  Operating at 33 to 55 Mbps, better than 5% frame error rate is achieved for greater than 95% of the channels simulated for up to 90 nsec RMS delay spread
Delivered Data Throughput
  Proposed coding has no PHY layer overhead
  No throughput loss due to coding
  16-QAM/TCM: 33 Mbps
  32-QAM/TCM: 44 Mbps
  64-QAM/TCM: 55 Mbps

## Slide 25: Evaluation Criteria
Receiver Sensitivity (AWGN14 MHz BW + Noise Figure (12 dB) + SNR10-5 BER)
  -71 dBm for 64-QAM TCM, 55 Mbit/sec
  -74 dBm for 32-QAM TCM, 44 Mbit/sec
  -77 dBm for 16-QAM TCM, 33 Mbit/sec
Power Consumption
  Total power consumption for the 8-state TCM encoder and decoder implementation in 0.13u CMOS technology is 5 mW or 0.018 mW/MHz/KGates (less than 5% of the total receiver power)
Latency
  TX or encoding latency
    No latency
  RX or decoder latency
    910 nsec
Free of proprietary or patented intellectual property

## Slide 26: Conclusions
No PHY or MAC layer transmission overhead
Low decoding delay (less than 1 usec)
Low complexity
Free of proprietary or patented intellectual property
Well proven and mature technology

## Slide 27: References
“Delayed Decision-Feedback Equalization”, Heegard, et. al., IEEE Transactions on Communications, May 1989
“Reduced State Sequence Estimation with Decision Feedback and Set Partitioning”, Eyuboglu, et. al., IEEE Transactions on Communications, January 1988
“Detection of Coded Modulation Signals on Severely Distorted Channels Using Decision Feedback Noise Prediction ...”, Eyuboglu, et. al., IEEE Transactions on Communications, April 1988