## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE 802.15.3 High Rate WPAN PHY Layer Preamble definition for Rapid Signal Acquisition
Date Submitted: 11 January 2001
Source: Jeyhan Karaoguz
Address: Broadcom Corporation, 16215 Alton Parkway, Irvine, CA 92619
Voice: 949 585 6168
E-Mail: jeyhan@broadcom.com
Contributors: Anand Dabak, Texas Instruments
Abstract: This proposal describes a PHY layer preamble for rapid signal acquisition including channel equalization, frequency-offset estimation, and gain adjustment
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15

## Slide 2: Considerations for Preamble Definition
11 Msym/sec O-QPSK, 16/32/64-QAM require equalization to achieve required FER
Burst-by-burst signal acquisition may involve
  Gain adjustment
  Carrier-frequency offset compensation
  Symbol timing adjustment
  Calculation of equalizer coefficients
Signal acquisition must be completed during the preamble
Periodic preamble sequences with certain auto-correlation properties greatly aid the process of rapid signal acquisition
Preamble length and periodicity thereof depend on the length of the overall symbol response
Notes: Let me draw your attention to the distinct features of our proposal compared to other proposals
First, we have proposed the only FH system achieving data rates up to 20 Mbps
FH systems brings major cost advantages for dual mode 802.15.1/3 devices since the RF front-end blocks are mostly re-used.
FH systems demonstrates great robustness wrt other wireless interferes due to hopping and low BW that is 5 MHz. This resutl is evident in our co-existence and jamming resistance numbers
The other distinction is that we have the smallest signal BW compared to other proposals. This feature gives us the best performance as accepted by the PHY subcommitte delay spread tolarance. Simulation result showing this will be shown shortly
Our proposal is the only one that takes advantage of the new FCC amendment that allows 5 MHz FH systems transmitting upto 21 dBm. Therefore, we can allow a longer range higher power mode just like BT systems do.

## Slide 3: Periodic CAZAC Sequence
CAZAC sequences have “Constant Amplitude Zero Auto Correlation” properties that are useful for rapid signal acquisition
A 4-phase CAZAC sequence provides good signal acquisition performance even for low SNR conditions
A 4-phase CAZAC sequence {cn} of length 16 symbols can be determined by
By introducing a 45o phase rotation, CAZAC sequence can be transformed into a QPSK sequence

## Slide 4: PHY Layer Preamble Format
C0 C1 C2 C3, …, C15
C0 C1 C2 C3, …, C15
C0 C1 C2 C3, …, C15
C8 C9 C10 C11, …, C15
C0 C1 C2 C3 C4 C5 C6 C7 C8 C9 C10 C11 C12 C13 C14 C15
C8 C9 C10 C11 C12 C13 C14 C15 C0 C1 C2 C3 C4 C5 C6 C7
P0
P1
P8
E
“P0, P1, …, P8” are 9 identical copies of a QPSK-CAZAC (see page 3) sequence {C0,C1,…,C15}
9 repetitions of the CAZAC sequence are required for noise averaging and reliable signal acquisition
“E” represents the “end of preamble delimiter” sequence, which is a 8-symbol cyclic shift of the original CAZAC sequence
16-symbol period is sufficient to handle an overall symbol response (including delay-spread channel) of 1500 nsec