## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: IEEE802.15.3: A proposal for Clause 5
Date Submitted: 14 January, 2001
Source: Patrick Kinney Company: Intermec Technologies
Address: 550 Second St SE, Cedar Rapids, Iowa
Voice: +1.319.369.3593, FAX: +1.319.369.3299, E-Mail:pat.kinney@ieee.org
Re: A proposal for Clause 5 of the 802.15.3 standard
Abstract: Clause 5, an overview of the 802.15.3 standard
Purpose: To put the overview of the proposed standard in front of the Task Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Clause 5
An Overview of the 802.15.3 PAN

## Slide 3: General Description of the Architure
How wireless PAN systems are different from LANs
  very limited power, small size, short range
  Destination address does not equal destination location
  The medium impacts the design
    unreliable medium including interference
    dynamic topology
    no full connectivity
    time varying, asymmetric propagation

## Slide 4: Components of the IEEE 802.15.3 PAN
Personal Operating Space
  While defined as up to 10 meters the actual coverage boundaries are not well defined and could be time variant
STA A
STA B
Coor- dinator
Personal Service Set (PSS)

## Slide 5: Components of the IEEE 802.15.3 PAN
IEEE 802.15.3 PANs are Ad Hoc
  typically without preplanning
  no uniquely defined Access Point
Integration with other Networks
  Portal: the logical point at which external MSDUs enter the PAN, or vice versa
  any station, including the coordinator, may serve as a portal

## Slide 6: 802.15.3 PAN with portals
STA A
STA B
Coor- dinator
802.11 W-LAN
802.15.1 PAN
W-WAN

## Slide 7: Overview of Services
Coordination
  transmission of beacons containing timing and information describing the PAN
  allocation of bandwidth
Authentication
  stations wishing to join must first authenticate with the coordinator, then with each desired station
  Public Key exchange
    open or controlled

## Slide 8: Overview of Services
Data Transport: Three mechanisms
  Asynchronous in the Contention Access Period
  Asynchronous in the Contention Free Period
  Synchronous in the Contention Free Period
QoS
  coordinator manages bandwidth
  temporarily unused bandwidth is made available to other streams

## Slide 9: Overview of Services
Power Management
  stations can transmit data during the CAP, they need not use CFP
  stations not participating in CFP need not be active during CFP
  in CAP, RTS window is used to notify the station of a pending message

## Slide 10: Overview of Services
Transfer of Coordination
  coordinator can participate in this process actively or passively.
  Active: coordinator agrees with another station that the other station is better suited
  Passive: coordinator “disappears” ie gets turned off or is moved outside the POS

## Slide 11: Overview of Operation
Superframe
Overview of States

## Slide 12: Superframe
Beacon contains timing and information about the PAN
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period
RTS
Data

## Slide 13: Contention Access Period
CAP is used to send QoS requests/grants and some data as well as authentication requests/grants
RTS window is used to assist power management by requesting a station to stay awake during the data window
Data window is used for short data transfers, unicast requires an ACK
Contention
Access
Period
Beacon
Contention Free Period
RTS
Data

## Slide 14: Contention Free Period
CFP is composed of data streams with quality of service provisions
Stations may only use CFP if the coordinator has evaluated the current usage along with the request for new service and determines that sufficient bandwidth is available
Asynchronous slots
Isochronous slots
Contention
Access
Period
Beacon
Contention Free Period
RTS
Data

## Slide 15: CFP: Slots
Each slot may be composed of many cycles, each cycle assigned to a stream
All stations will count frames and use those slots and cycles that have been assigned to that station’s streams
A mini-slot occurs when a station doesn’t have data to send, the next stream may use this bandwidth
Cycles
Mini-slot

## Slide 16: Overview of States
Establishment of PAN
  establishes duration of superframe
  allocation between CAP and CFP
Joining
  station listens for beacon
  station attempts to authenticate with coordinator during CAP
  station will receive a secret key upon successful authentication
  station exchanges capability information with coordinator

## Slide 17: Overview of States
Stream Establishment
  station requests connection from coordinator during CAP
  coordinator will assign a slot/cylce identifier if required bandwidth is available
  station will use CFP at next superframe
  stream can be from any station to any station

## Slide 18: Overview of States
Data Exchange
  can occur in CAP or CFP
  CAP should be restricted to small transfers
  in CAP if destination is not known to be powered up, RTS window will be used with data transfer only if destination responds
  RTS/CTS can be used if hidden nodes are suspected
  data can be transferred from any station to any station (peer to peer)

## Slide 19: Overview of States
Coordination Transfer
  coordinator can transfer if another station is better suited or if coordinator cannot continue
Network Termination
  can be requested by a station or by coordinator’s management
  coordinator will broadcast termination command
  or you could just pop the batteries out

## Slide 20: ISSUES
Transfer of coordination: loss of service arrangements?
Do we authenticate with every station?
Do we have a mode of authenticating only with coordinator?
Do we then allow a single shared private key for network?
Multiple data rates within a PAN?