## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [IEEE 802.15.1 Tutorial]
Date Submitted: [11 July 2000]
Source: [Tom Siep] Company [Texas Instruments]
Address [12500 TI Blvd, m/s 8723, Dallas, TX 75243, USA]
Voice:[214.480.6786], FAX: [972.761.5581], E-Mail:[Siep@ti.com]
Re: [Original document.]
Abstract: [Tutorial on 802.15.1, including an explanation of SDL]
Purpose: [Inform WG voters about origin, form and content of Draft]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15.1 Tutorial
Tom Siep, Texas Instruments

## Slide 3: Topics
Introduction
History of IEEE  802  802.15 TG1
Specifications vs. Standards
Background on Bluetooth™
Bluetooth Architecture (Chatschik Bisdikian)
Construction of the Draft
SDL
Q&A

## Slide 4: Introduction
Tom Siep
  Chief Technical Editor, IEEE802.15
  Lead Technical Editor, IEEE802.15.1
  Bluetooth Specification Section Owner, L2CAP
  Editorial interface between BSIG and 802.15.1
  Author
    "An IEEE Guide: How to Find What You Need in the Bluetooth Spec"
    http://standards.ieee.org/catalog/press/index.html#Bluetooth

## Slide 5: IEEE: An Overview
Established in 1884 (AIEE & IRE)
Membership was 334,811 Dec98; 66% USA & 33% Non-USA
Produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
Holds annually more than 300 major conferences
Has more than 800 active standards with 700 under development.

## Slide 6: IEEE 802 Standards Principals
Due Process through established rules and procedures
Consensus highly desired, near unanimity is generally the rule
Openness where all individuals, world-wide, have access to the process
Balance maintained by having balloting group include both developers and users
Right to Appeal both procedural and technical issues at any time during the process

## Slide 7: IEEE Project 802 Local and Metropolitan Area Network Standards Committee
Accredited by ANSI, Sponsored by IEEE Computer Society
  Ethernet, Token Ring, Wireless, Cable Modem Standards
  Bridging, VLAN, Security Standards
Meets three times per year (400 individuals, 15% non-US)
Develops equivalent IEC/ISO JTC 1 standards
  JTC 1 series of equivalent standards are ISO 8802-nnn
IEEE URLs
  802 http://grouper.ieee.org/groups/802/
  802.15 http://grouper.ieee.org/groups/802/15/

## Slide 8: IEEE 802.15
Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks
  Communication of devices within a Personal Operating Space

## Slide 9: History of WG15/TG1
Predates public announcement of Bluetooth
Decided to become WG in Jan99
First WG meeting July99
Call for Response ended July99
  Many SIGs solicited
  Bluetooth was only respondent

## Slide 10: Specification versus Standard
versus
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 11: The Specification Artist
Helps people see the world in a new way.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 12: The Standards Engineer
Codifies well-understood phenomena and applies them to well-known problems
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 13: Specification vs. Standard
Starts with a blank canvas
Free format
Usually evolves
Often describes an implementation
Says many (perhaps different) things to many people
Sometimes “you had to be there”
Inspires
Starts with defined goal
Format dictated by Standard
Evolution by formal means
Implementation Independent
Unambiguous
All you need to know is right there (or in the references)
Communicates

## Slide 14: Background on Bluetooth™
Bluetooth Special Interest Group (BSIG)
  Formed May 1998
    Nine “Promoter” Companies
    ~100 Associate Companies
    ~2000 Adopter Companies
  Has been “Virtual”
  Becoming a not-for-profit entity
  Major purpose in life is Quality Control

## Slide 15: Bluetooth Wireless Technology
Operates in the 2.4 GHz band at a maximum user data rate of 720Kb/s. (1Mbit nominal)
Uses Frequency Hopping spread spectrum (FHSS)
Radio transceivers hop from one channel to another in a pseudo-random fashion, determined by the master.
Supports up to 8 devices in a piconet (1 master and 7 slaves).
Piconets can combine to form scatternets.

## Slide 16: Bluetooth Architecture Presentation
Chatschik Bisdikian
IBM Research

## Slide 17: What IEEE Project 802 Covers

## Slide 18: More Detail of IEEE P802 Structure

## Slide 19: How Does That Relate to Bluetooth?
Bluetooth
IEEE

## Slide 20: Real Structure of Bluetooth Protocol

## Slide 21: Constructing the Draft

## Slide 22: The Process of Creating a Standard
You are here

## Slide 23: SDL Primer
Definition
Why SDL was created
Overview of the various SDL symbols

## Slide 24: Specification and Description Language
Unambiguous graphical language used to specify and describe complex systems
Developed by CCITT (now ITU-T Z.100)
Specifically concerned with
  Behavior
  Structure
  Data
Can be Implementation Independent
Ability to analyze the correctness and completeness of specifications

## Slide 25: Why SDL was created
First defined 1976
  Informal until 1984 when structure and data added
  Grew through use
Common Telecommunications medium of understanding
Ability to analyze correctness and completeness of specifications
Suitability for the use of computer-based tools

## Slide 26: Overview of various SDL symbols
Block Types
Process Types
Procedures
Signal Paths
Signal Types (Input, Output)
Task Symbols
Create Processes

## Slide 27: Block Reference Symbol
Fundamental unit of lexical scope and structural hierarchy.
Each block contains
  Other blocks
  Processes
  Procedures
  Data declarations
Implicit or Explicit channels (signals) in the to/from the environment
Block_Z
Sync_sig

## Slide 28: Process Reference Symbol
Processes specify dynamic behavior using extended finite state machines.
Processes operate concurrently, communicating by means of signals and remote variables.
After the process name is the number of process instances at startup and the maximum number of instances.
For processes created dynamically, the dashed arrow connects the parent process to the offspring.
Process_A (1,1)
Out_sig
Parent_Sig

## Slide 29: Procedure Reference Symbol
A procedure is defined and called in the process where this symbol appears.
If declared "remote" the procedure may be imported for calling from other processes.
A value-returning procedure, callable in assignment statements, is defined using the "returns" keyword in the formal parameter list.
Procedure_Name

## Slide 30: Signal Paths

## Slide 31: Signal Types
Symbols
  Inputs
  Outputs
May face left or right
Input signal transition occurs upon receipt of named signal
Output signal transition is zero time, but receipt is non-deterministic
In_Signal
Out_Signal

## Slide 32: Task Symbols
Used to assign a new value to a variable
Part of a transition
X := 2.4

## Slide 33: Creating Processes
Processes either created at initialization or by other processes in the same block
When created, all variables of the process are also created
Initial value may be specified for variables

## Slide 34: 802.15.1 SDL

## Slide 35: 802.15.1 SDL Summary
Derived a picture of what the structure of the BT spec is in IEEE terms.
Helped to uncover holes in existing spec
Enables bench testing and validating of components
Provides a common language between the SIG and the IEEE
Generation of TTCN from SDL is possible

## Slide 36: Implications for the future of Standards
Normative SDL makes an unambiguous Standard
Working SDL models can be used to extend currently working Standards, minimizing the danger of breaking the protocol
SDL makes the relationship between Standards and Test Suites explicit

## Slide 37: Questions?
Tom Siep
Texas Instruments
Siep@ti.com