## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ Supergold Encoding for High Rate WPAN Physical Layer ]
Date Submitted: [ 12 January 2001 ]
Source: [ T. O’Farrell, L.E. Aguado & C. Caldwell] Company [Supergold Communication Ltd. ]
Address [ 2-3 Sandyford Village, Sandyford, Dublin 18, Ireland ]
Voice:[ +44 113 2332052 ], FAX: [ +44 113 2332032 ], E-Mail:[ tim.ofarrell@supergold.com ]
Re: [ Physical layer coding proposal for the IEEE P802.15.3 High Rate Wireless Personal Area Networks Standard.ref 00210P802.15]
Abstract: [ This contribution is a final presentation of Supergold’s sequence coded modulation proposal for the physical layer part of the High Rate WPAN standard as evaluated by the Pugh criteria. ]
Purpose: [ Proposal for PHY part of IEEE P802.15.3 standard.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Outline of the Presentation
Supergold’s approach
M-ary Bi-Code Keying
System Specifications
Performance Curves
Conclusions

## Slide 3: M-ary Bi-Code Keying
The critical principle behind Supergold’s solution for WPANs is to:
Meet the performance criteria by
A straight forward application of DSSS techniques + FEC
With low implementation complexity

## Slide 4: M-ary Bi-Code Keying
The PHY architecture evaluated is based on
A heterodyne radio architecture
Incorporating RF, IF and BB processing functions
And minimal external filtering functions
MBCK with equalisation and RS Coding are implemented in the BB processing unit

## Slide 5
RF
IF
PHY Architecture Evaluated
BB
BPF
BPF
BPF
LNA
IF
Amp
PA
RF
Synthesiser
IF
Synthesiser
0o / 90o
LPF
LPF
LPF
LPF
ADC
ADC
DAC
DAC
ADC
BB
Processing
AGC
Rx I
Rx Q
Tx Q
Tx I
RSSI
44 MHz
Oscillator
Band
Filter
Image
Reject
Filter
MAC
802.15.3 IF Filter
SAW

## Slide 6
M-ary Bi-Code Keying
This is an established principle:
DSSS for 802.11, M-ary Bi-Orthogonal Keying (MBOK) and CCK for 802.11b are schemes that
Benefit from processing gain and inherent coding gain that
Give robust performance in noisy channels, flat fading channels, and ISI channels
Code and Go

## Slide 7
M-ary Bi-Code Keying
M-ary Bi-Code Keying is a member of the family of direct sequence coding schemes that specifically
Addresses the issue of high data rates
By carrying more bits per symbol
But retains good distance properties between codewords
Hence robust performance in interference, flat fading and ISI channels

## Slide 8
Reed Solomon Coding
Supergold concatenate M-ary Bi-Code Keying with a Reed-Solomon code to:
Enhance the overall coding gain,
Protect against random and burst errors and
Provide rate adaptation – more coding gain at low data rates
Supergold use an RS(63,k) code, with k= 41 and 57, matched to the MBCK symbol set.

## Slide 9
MBCK-RS Encoding Chain
32-Correlator Bank
Greatest
Peak Detector
RS Decoder
6
1
1
1
Rx I IN
Rx Q IN
rI
rQ
c’
DATA OUT
y
64-ary Bi-Code Keying
Select 1 of 64 Sequences
RS Encoder
DATA IN
1
d
c
6
xI
xQ
8
I OUT
Q OUT
1
1
32 Sequences +
Complements

## Slide 10
The MBCK block code maps to a 16-QAM constellation
16-QAM

## Slide 11
Protocol Stack
MAC
30 Mbps
High Rate
Mode
16-QAM
MMSE Equaliser
MBCK
RS(63,57)
22 Mbps
Coded Base
Mode
16-QAM
MMSE Equaliser
MBCK
RS(63,41)

## Slide 12
PLCP Packet Format Evaluated
Sync
10*16 Chips
SFD
16 Chips
PSDU
PLCP Short Preamble
PLCP Header
Signal
4 bits
Service
4 bits
Length
16 bits
CRC
16 bits
PPDU
T1
11 Mchip/s QPSK
T2
22 Mb/s QAM
Tpsdu
22, 30 Mb/s
QAM
T1 = 176/11e6 = 16 us
T2 = 40/22e6 = 1.8 us
Length 16 CAZAC Sequences for preamble & SFD
PLCP Header uses RS(63,41) and decoded separately from payload

## Slide 13
Optional Channel Coding
A soft-decision (SD) metric can be derived for MBCK enabling the use of binary con-volutional codes and SD Viterbi decoding.
Extended MBCK symbol sets that map onto 16, 32 and 64 QAM exist giving uncoded data rates of 44, 55 and 66 Mb/s respectively
  Rate ½ and ¾ BCC can then be used

## Slide 14
PHY System Specification
Parameter | Symbol | Test Condition | Value | Units
Frequency band |  | 2400 – 2483.5 MHz ISM Band | 2.4 | GHz
Channel frequencies | fc | 2412, 2417, 2422, 2427, 2432, 2437, 2442, 2447 2452, 2457, 2462, 2467, 2472, 2483 |  | MHz
Channel spacing | f |  | 5 | MHz
Number of Channels | N |  | 14 | 
Channel bandwidth | B | Null-to-null, 25% root raised cosine filter | 14 | MHz
Chip rate | Rchip |  | 11 | Mchip/s
Data rates (Throughput) | R | Coded base mode Higher rate mode | 22 30 | Mb/s Mb/s
Delay Spread Tolerance | Trms | > 95% channels @ FER  1% 7 tap MMSE > 95% channels @ FER  1% 44 tap MMSE | 25 100 | ns ns
Sensitivity | S | 22 Mb/s coded base mode 30 Mb/s high rate mode | -79.5 -78.0 | dBm

## Slide 15
PHY Encoding Specification
Parameter | Symbol | Test Condition | Value | Units
Sequence coding | MBCK | 64-ary bi-code keying Quaternary sequences of length 4 chips |  | 
Coded bits/sequence | k |  | 6 | 
MBCK Detector Implementation |  | 32-correlator bank and greatest peak detector |  | 
FEC scheme |  | Reed Solomon RS(63,k) |  | 
Coding rates | r | Coded base mode High rate mode | 2/3 10/11 | 
Coding gain | g | Over 16-QAM at 10-6 BER, AWGN channel 22 Mb/s coded base mode 30 Mb/s high rate mode | 5.5 4 | dB dB
Encoding Latency | Tel | 1st bit in to 1st bit out | <4 | us
Decoding Latency | Tdl | 1st bit in to 1st bit out | <10 | us

## Slide 16
PHY RF Specification
Parameter | Symbol | Test Condition | Value | Units
Modulation |  |  | 16-QAM | 
PA back-off |  | From 1 dB compression point | 6-to-9 | dB
Carrier frequency accuracy |  | PER is not substantially degraded for frequency offsets caused by this inaccuracy | 25 | PPM
IF frequency | fIF |  | 280 | MHz
IF bandwidth | fIF |  | 17 | MHz
Jamming margin | J/S | FCC Jamming Test for PER 1% | 8 | dB
Adjacent channel rejection | ACR | 25 MHz separation between active channels | >50 | dBc
Spectral mask requirement | RF-mask | At 11 MHz At 22 MHz | -30 -50 | dBc dBc
Phase noise penalty | n | At 10% PER and 4o rms phase noise | 1 | dB

## Slide 17
PHY-BB Specification
Parameter | Symbol | Test Condition | Value | Units
Clock rates | clk bb | Master BB processing | 44 11 | MHz MHz
Samples/chip | Ts | To meet root raised cosine filter spec. | 4 | 
RRCF |  | Root raised cosine filter, 25% excess B/W | 22 | taps
ADC precision |  | 44 Msamples/s | 6 | bits
DAC precision |  | 44 Msamples/s | 6 | bits
RSSI ADC |  | 11 Msamples/s | 6 | bits

## Slide 18
PHY-BB Specification Cont.
Parameter | Symbol | Test Condition | Value | Units
BB processing |  | MBCK (implemented in a demonstrator) RS(63,41) Root raised cosine filter (22 tap) MMSE Equaliser (7 taps for 25 ns Trms) | 10 7 20 8 | kgates
Incremental cost $0.2 / 100k gates |  | MBCK + RS(63,41) MBCK + RS + RRC MBCK + RS + RRC + MMSE | 3.4 7.4 9.0 | Cents
Power Consumtion 0.018mW / MHz . Kgate (44 MHz Clock) |  | MBCK + RS(63,41) MBCK + RS + RRC MBCK + RS + RRC + MMSE | 13.46 29.30 35.64 | mW

## Slide 19
PHY-Throughput Evaluation
Parameter | Symbol | Test Condition | Value | Units
Uncoded Rate |  | 16 QAM | 44 | Mb/s
Coding Overhead |  | MBCK RS(63,41) RS(63,57) | 75.0 65.1 90.5 | % % %
Total Overhead |  | MBCK + RS(63,41) MBCK + RS(63,57) | ~50 ~68 | % %
Throughput |  | Coded base mode (44*0.5) Higher rate mode (44*.68) | 22 30 | Mb/s

## Slide 20
Performance Curves
PER performance versus AWGN with non-ideal power amplifier (criteria 17) requires rerun of simulation results

## Slide 21
BER v. Eb/N0 in the AWGN channel for 22Mbps and 30Mbps

## Slide 22
PER v. SNR in the AWGN channel for 22Mbps

## Slide 23
PER v. SNR in the AWGN channel for 30 Mbps

## Slide 24
PER v. SNR for the p = 2 Rapp PA model for 22 Mbps

## Slide 25
PER v. SNR for the p = 3 Rapp PA model for 22 Mbps

## Slide 26
11 Mchip/s rate
MBCK Signal (x4)
Root Raised Cosine Filter
Alpha = 0.25
fc = 7 MHz
Rapp PA (p=2)
7 dB Output Backoff
PA Non-linearity Effects

## Slide 27
Pulse Shaped-Waveform Power Spectrum Response at the Input of the PA
Frequency (Hz)

## Slide 28
Power Spectrum Response for 7dB RF PA Back-Off from saturation (p = 2)
Frequency (Hz)

## Slide 29
PER v. SNR in the flat fading channel for 22 Mbps

## Slide 30
PER v. SNR in the fading ISI multipath channel for 22 Mbps

## Slide 31
PER v. SNR in the fading ISI multipath channel for 30 Mbps

## Slide 32
PER v. Eb/N0 in the AWGN channel in the Presence of Phase Noise

## Slide 33
PER v. RMS Phase Noise in the AWGN channel for a range of Eb/N0

## Slide 34
Example of Link Budget for Two-Ray Model
[based on: IEEE 802.15-00/050r1, Rick Roberts]
Rx Noise Figure: 12 dB (inexpensive implementation)
Rx Noise Bandwidth: 14 MHz
Rx Noise Floor: -174+10*log(14*106)+12  -90.54 dBm
Implementation Loss Margin: 6 dB
Antenna Gain: 0 dB

## Slide 35
Example of Link Budget for Two-Ray Model (Cont.)
Maximum Second Ray Delay: 25 ns
Maximum Second Ray Reflection Coefficient: -6 dB
Required Direct Ray Range: 10 m
Loss Equation (dB): L = 32.5+20log(dmeters)+20log(FGHz)
At 2.4 GHz, assuming the direct ray is blocked, the loss of the reflected ray path (17.4 m) is:
L = 32.5+24.8+7.6+6  71dB (6 dB reflection coefficient)
Including antenna gain and implementation loss:
Total Loss Budget: L + 2x0 + 6 = 77 dB
SNR at 1% PER for 22 Mb/s coded base mode = 11 dB
SNR at 1% PER for 30 Mb/s higher rate mode = 12.5 dB
Rx Sensitivity at 22 Mb/s = Noise Floor + SNR = -79.5 dBm
Rx Sensitivity at 30 Mb/s = Noise Floor + SNR = -78.0 dBm

## Slide 36
IP Issues
Potential IP
Quaternary block code
Bit – to – codeword assignment
SG is willing to accept IEEE IP policy
MBCK principle has been in the open literature for > 20 years

## Slide 37
Conclusions
MBCK is a low complexity code that
Meets the WPAN robustness criteria
Is a mature concept based on MBOK
Can use Hard & Soft Decision Decoding
Is an inexpensive solution for WPANs