## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [TG3-PHY-Committee-Monterey-Report]
Date Submitted: [15 January 2001]
Source: [James P. K. Gilb] Company [Mobilian]
Address [11031 Via Frontera, Suite C, San Diego, CA 92127]
Voice:[1-858-451-3438], FAX: [1-858-451-3546], E-Mail:[gilb@ieee.org]
Re: []
Abstract: [A summary of the work accomplished by the PHY committee in conference calls and via email since the last meeting in Tampa.]
Purpose: [Document the work accomplished by the PHY committee.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Decisions Reached
Frequency accuracy +/-25 ppm
Packet size for RX sensitivity: 1024 bytes
RX sensitivity measured at 10-5 BER
TX power ramp up/down – same as 802.11b
Carrier suppression – same as 802.11b
TX filter, 0.3 <  < 0.8, exact value to be settled on later.
TX power measured radiated, no power control specified

## Slide 3: Jamming Test
Use 802.15.3 interferer, base modulation
Desired signal 10 dB higher
Numbers still TBD
Data Rate (Mbit/s)
Minimum sensitivity
Adjacent channel rejection (dB)
Next adjacent channel rejection (dB)
22
TBD
TBD (10 dB)
TBD (30 dB)
22 – 44
TBD
TBD (6 dB)
TBD (26 dB)
33 – 55
TBD
TBD (3 dB)
TBD (23 dB)
44 - 66
TBD
TBD (0 dB)
TBD (20 dB)

## Slide 4: PLCP Preamble
16 symbol Constant Amplitude Zero Auto-Correlation (CAZAC) sequence
Between 6 and 12 repetitions (8.7-17.45 s)
10 repetitions seems popular for some equalizers (~15 us)
Last sequence is shifted by 8 bits to act as the end of preamble delimiter or Start Frame Delimiter (SFD).
Karagouz will present preamble definition later

## Slide 5: Some Outstanding issues
Modulation accuracy test
Numbers for jamming
Intermodulation test
Sensitivity numbers
TX power and Power Spectral Density (PSD)
Coding method

## Slide 6: Agenda for 17 Jan. 01 Morning
PLCP preamble sequence presentation and vote – Jeyhan Karagouz
Channelization and TX PSD – Stan Ling
Issue Capture
Intermodulation
Modulation accuracy

## Slide 7: Intermodulation
Suggestion: Desired signal 3 dB above the reference sensitivity centered at fd, a static sine wave at f1 and an 802.15.3 modulated signal at f2, both signals 35 dB above the desired signal, the DUT shall meet the error rate criterion.
  |fd-f1| = channel spacing, |fd-f2| = 2*channel spacing
  fd for all supported channels
Resolution: Tabled, to be discussed on the conference calls if we need this specification

## Slide 8: Modulation Accuracy
OQPSK
  Suggestion: Adopt 802.11b with slight modifications
  Resolution: Table for conference calls, Wayne Music will submit proposal by 23 January 2001 for discussion on 25 January 2001 PHY Committee conference call.
16-QAM, 32-QAM, 64-QAM
  Suggestion: Adopt 802.11a with slight modifications
  Resolution: Same as above

## Slide 9: Error rate criterion
The error rate criterion shall be a PER of 8% with packet length of 1024 data bytes containing pseudo random data using a PN23 sequence as defined in ?.

## Slide 10: Reference Sensitivity
Suggestion: Reference sensitivity is measured at the antenna connector (50  input impedance or equivalent connection). With an 802.15.3 modulated signal input at a power level Psens, the DUT shall meet the error rate criterion.
Modulation | Psens (dBm)
OQPSK | 
16-QAM/TCM | 
32-QAM/TCM | 
64-QAM/TCM | 
Resolution: Jeyhan Karagouz will provide numbers by next conference call