## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Bluetooth and 802.11b Physical Layer Coexistence
Date Submitted: 18 January, 2001
Source: Robert E. Van Dyck Company: National Institute of Standards and Technology
Address: 100 Bureau Drive, Mail Stop 8920, Gaithersburg, Maryland, U.S.A.
Voice: 301 975-2923, FAX: 301 590-0932, E-Mail: vandyck@antd.nist.gov
Re: 1
Abstract: Baseband simulations are presented showing the effects of Bluetooth interference on Bluetooth, using an improved BER measurement methodology. Next, the performance of Bluetooth with the 1 Mb/s IEEE 802.11b WLAN as the interferer is shown. Additionally, results of Bluetooth interference on the 1 Mb/s and the 11 Mb/s 802.11b devices are given.
Purpose: The information in this document should be used to further TG 2 coexistence studies.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Further Bluetooth and 802.11b Physical Layer Coexistence Results
Amir Soltanian & Robert E. Van Dyck
National Institute of Standards
and Technology
Gaithersburg, Maryland
January 2001

## Slide 3: Outline
Bluetooth transmitter & receiver modeling
Bluetooth Performance with BT interference
  Co-channel Interference
  Adjacent Channel Interference
802.11b Transmitter Model
Bluetooth with 802.11b interference
802.11b Receivers
  1 Mb/s Direct Sequence Spread Spectrum
  11 Mb/s CCK Modulation
802.11b Performance with BT interference

## Slide 4: Simulations
Additive White Gaussian Noise Channel Model
Mainly Considering Coexistence Scenarios
Signal processing-based implementations
Bluetooth: Gaussian Frequency Shift Keying
IEEE 802.11b:
1 Mb/s with 11 Mchips/sec spreading
Direct Sequence DBPSK
11 Mb/s using CCK coding
Baseband Models at 44,000,000 samples/sec

## Slide 5: Baseband Model of Bluetooth GFSK

## Slide 6: Co-channel and Adjacent Channel Interference
Consider Bluetooth as an Interferer
for Bluetooth -- Multiple Piconets
Set Interference Power according to spec.
0 MHz --> 11 dB C/I ratio
1 MHz --> 0 dB
2 MHz --> -30 dB
>= 3 MHz --> -40 dB
Simple Limiter-Discriminator Receiver
Vary the IF Filter Bandwidth

## Slide 7: Bluetooth on Bluetooth Results
It seemed that the Bluetooth Linear- Discriminator Receiver could not meet adjacent channel specifications
Problem in first few bits of each packet
Solution:
  Change BER measurement methodology
  Do not use preamble in BER calculation
Next two viewgraphs for older approach
Third viewgraph for improved approach

## Slide 8: BER for Bluetooth Co- and Adjacent Channel Interference

## Slide 9: BER for Bluetooth Co- and Adjacent Channel Interference

## Slide 10: BER for Bluetooth Co- and Adjacent Channel Interference with Improved Receiver

## Slide 11: 1 Mb/s 802.11b Transmitter
Consider IEEE 802.11b as an Interferer
for Bluetooth – Coexistence Problem
Similar to broadband noise
Use roll-off factor a = 1
Meets transmitter power specification
Evaluate Co-channel and Adjacent
Channel Interference

## Slide 12: IEEE 802.11b Block Diagram

## Slide 13: Spectrum of DS-SS 801.11b Transmitter

## Slide 14: BER for Bluetooth with 802.11b Interference

## Slide 15: BER for Bluetooth with Adjacent Channel 802.11b Interference

## Slide 16: Integration with MAC Layer Model
Consider four node Scenario
Bluetooth transmitter and receiver
802.11b transmitter and receiver
Assume no frequency hopping
Bluetooth radio:
Transmitter power = 1 mW = 0 dBm
Distance = 7 meters
Receiver sensitivity = -80 dBm
802.11 transmitter power = 25 mW = 14 dBm
Distance = 1 meter (to BT receiver)

## Slide 17: BER for Scenario 1

## Slide 18: IEEE 802.11b Receiver
1 Mbit/sec mode
  Direct Sequence Spread Spectrum
with Differentially coherent
BPSK Modulation
  11 Chip Barker PN Sequence
11 Mbits/sec CCK mode
  Walsh-Hadamard Transform or
  Correlating against all 256 Code Words

## Slide 19: BER for 1 Mb/s SS-DBPSK 802.11b Receiver in AWGN

## Slide 20: Barker Code Sequence Power Sequence

## Slide 21: Direct Sequence Spread Spectrum with a Single Tone Jammer

## Slide 22: Direct Sequence Spread Spectrum with a Single Tone Jammer

## Slide 23: 1 Mb/s IEEE 802.11b with Bluetooth Co-channel Interference

## Slide 24: 1 Mb/s IEEE 802.11b with Bluetooth Adjacent Channel Interference

## Slide 25: 1 Mb/s 802.11b with Bluetooth Interference

## Slide 26: 11 Mb/s 802.11b CCK Modulation
The complementary codes in 802.11b are defined by a set of 256 8-chip code words.
where

## Slide 27: 11 Mb/s CCK Phase Encoding
Each code word has a complementary pair that is also a member of the set
8 bits transmitted per code words
(d0,d1) encodes 1 based on DQPSK
(d2,d3), (d4,d5), (d6,d7) encode 2, 3 and 4, respectively
(d0,d1) Even Symb D-Phase Odd D-Phase
  00 0 
  01 /2 3/2
  11 0
  10 3/2 /2

## Slide 28: Block Diagram of 11 Mb/s IEEE 802.11b

## Slide 29: BER Performance of 11 Mb/s IEEE 802.11b in AWGN Channel

## Slide 30: BER Performance of 11 Mb/s IEEE 802.11b with BT Interference

## Slide 31: References
M. K. Simon and C. C. Wang, “Differential vs. limiter-discriminator detection of narrow-band FM,” IEEE Trans. on Comm, pp. 1227-1234, Nov. 1983.
M. K. Simon and C. C. Wang, “Differential detection of Gaussian MSK in a mobile radio environment,” IEEE Trans. On Vehic. Tech., pp. 307-320, Nov. 1984.
P. Varshney and S. Kumar, “Performance of GMSK in a land mobile radio channel,” IEEE Trans. on Vehic. Tech., pp. 607-614, Aug. 1991

## Slide 32: References
J. Proakis, Digital Communications, McGraw-Hill.
Lee and L. Miller, CDMA Handbook.
T. Ekvetchavit and Z. Zvonar, “Performance of Phase-locked loop receiver in digital FM systems,” IEEE Int. Symp. on PIMRC , pp 381-385, 1998.
D. L. Schilling et al., “Optimization of the Processing Gain of an M-ary Direct Sequence Spread Spectrum Communication System,” IEEE Trans. on Comm., pp. 1389-1398, Aug. 1980.

## Slide 33: References
M. J. E. Golay, “Complementary Series,” IRE Trans. on Information Theory, vol. IT-7, pp. 82-87, April 1961.
C. C. Tseng and C. L. Liu, “Complementary Sets of Sequences,” IEEE Trans. on Information Theory, pp. 644-652, Sept. 1972.
R. Sivaswamy, “Multiphase Complementary Codes,” IEEE Trans. on Information Theory, pp. 546-552, Sept. 1978.

## Slide 34: References
R. L. Frank, “Polyphase Complementary Codes,” IEEE Trans. on Information Theory, pp. 641-647, Nov. 1980
R. D. J. Van Nee, “OFDM Codes for Peak-to-Average Power Reduction and Error Correction,” IEEE Global Telecom. Confence, vol. 1, pp. 740-744, 1996.