## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Selective Hopping for Hit Avoidance
Date Submitted: January 15, 2001
Source: KC Chen, HK Chen, CC Chao
Company: Integrated Programmable Communications, Inc.
Taiwan Laboratories Address: P.O. Box 4-2, Chupei, Hsinchu, Taiwan 302
TEL: +886 3 553 9128, FAX: +886 3 553 9153, E-Mail: {kc,hkchen,ccc}@inprocomm.com
Re: original document.
Abstract: Submission to Task Group 2 for consideration as the coexistence mechanism for 802.15.2
Purpose: Description of Proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Selective Hopping for Hit Avoidance
HK Chen, KC Chen, CC Chao
Integrated Programmable Communications, Inc.

## Slide 3: Scenarios
Co-existence of 802.15 and 802.11 DS
Frequency hopping still follows FCC’s regulations
Other co-existence scenarios are not considered in this document
  Other FH at 2.4G Hz band
  Other DS at 2.4G Hz ISM band
  Shall be considered later
    Principle is applied.
    Procedures need more definitions.

## Slide 4: Frequency Arrangement of IEEE 802.11b and 802.15
802.11b Channel Number | Central Frequency (MHz) | Range (MHz) | Corresponding Bluetooth Channel Numbers
1 | 2412 | 2400-2424 | 0-22
6 | 2437 | 2425-2449 | 23-47
11 | 2462 | 2450-2474 | 48-72

## Slide 5: Frequency Partition
Partition Number | Corresponding Bluetooth Channel Number | Total Channel in the Partition | Corresponding 802.11 Channel Number
1 | 0-22,75-77 | 26 | 1
2 | 23-47,78 | 26 | 6
3 | 48-72,73-74 | 27 | 11

## Slide 6: Two-Layer Hopping Sequences
In case 802.15 hopping channel is within the frequency range of a 802.11 DS transmission
  Select a set of partition sequences from 3 possible sets
  Original sequence is mapped into a new sequence according to the selected set of partition sequences

## Slide 7: Selective Hopping Avoidance System Architecture
Frequency Synthesizer
Multiplexer
Partition mapping re-mapping
Hopping sequence generation
Original/Mapped sequence selection
Partition sequence generation
Partition sequence selection procedure
RSSI (& 802.11b locking detection)
Demodulation with interference suppression
Error
Check
Interference identification
Traffic requirement
Hopping clock
RF input signal
Partition sequence change procedure
Packet target
Uniform channel usage requirement
Optional indicator
of 802.11 DS from
the 802.11-802.15
integrated device

## Slide 8: Interference Identification
It consists of
  Instantaneous interference detection: interference-free or not
    Checks of received packet and power level
    Utilization of channel silent duration between channel active time
  Hit ratio measurement
    Counting the interference ratio for each partition

## Slide 9: Partition Sequence Selection Under Uniform Channel Utilization
For partitions with interference hit ratios below threshold, corresponding hit ratios are set to be zero.
From the time slots reserved by the traffic requirements, calculate the partition usage vector for partition sequences.
Calculate the average hit probability H(p) for each type p of partition sequence
Select the partition sequences with minimal H(p)
If more than one in step 4, select the most evenly used one

## Slide 10: Partition Sequence Change Procedure
After the device decides to apply a new partition sequence, it starts to communicate with all its peers.
  Negotiate with peers to change to new hopping sequence
  In case no support of co-existence in peers, original sequence is still used.

## Slide 11: Original/Mapped Sequence Selection
Designed for backward compatibility
  Allowing original sequence and mapped sequence co-existing in a pico-net.
  Master selects an appropriate sequence based on the targeting receiver(s).
  A simple directory records
    Peers
    802.15.2 compliance or not
    Sequence used

## Slide 12: Partition Sequence Generation
One table contains all possible types of sequences.
To reduce implementation complexity, a small set of partition sequences, containing enough sequences to optimize hit probability for any combination of interference and traffic situations, is desired.
  For 802.15, SCO traffic has the highest priority need using partition sequences.
It can be generalized to all co-existing environments.

## Slide 13: Traffic Requirement
Traffic combinations
Bluetooth traffic parameters
Corresponding traffic parameters
1
One full-duplex SCO link,
Tsco=4, Dsco=0,1
Tstep=2, offset=0
2
One full-duplex SCO link,
Tsco=4, Dsco=2,3
Tstep=2, offset=1
3
One full-duplex SCO link,
Tsco=6, Dsco=0,1
Tstep=3, offset=0
4
One full-duplex SCO link,
Tsco=6, Dsco=2,3
Tstep=3, offset=1
5
One full-duplex SCO link,
Tsco=6, Dsco=4,5
Tstep=3, offset=2
7
Two full-duplex SCO link,
Tsco=6, Dsco=0,1,2,3
Tstep=3, offset=0,1
8
Two full-duplex SCO link,
Tsco=6, Dsco=0,1,4,5
Tstep=3, offset=0,2
9
Two full-duplex SCO link,
Tsco=6, Dsco=2,3,4,5
Tstep=3, offset=1,2

## Slide 14: Example of Partition Usage Vector
Traffic combination
Corresponding traffic parameters
1
Tstep=2, offset=0
1
0
2
2
Tstep=2, offset=1
1
2
0
3
Tstep=3, offset=0
2
0
0
4
Tstep=3, offset=1
0
1
1
5
Tstep=3, offset=2
0
1
1
6
Tstep=3, offset=0,1
2
1
1
7
Tstep=3, offset=0,2
2
1
1
8
Tstep=3, offset=1,2
0
2
2

## Slide 15: Partition Mapping
Mod Nj
Mapping table of P3
Channels in Pj
P1
P2
P3
Nj
Select one table among the three
Selected channel number of original hopping sequence
Partition sequence

## Slide 16: Rearrangement as an Alternative of Sequence Generation
Temporary re-arrangement of pre-determined N channels of hopping sequence
  Taking advantage of interference duty cycle
  Can also be used for smaller ISM bandwidth at certain countries.
  Algorithm:
    Determine coming hopping channel suffering interference of a 802.11 DS transmission.
    Create the segment of upcoming N elements in the hopping sequence. Initial suggestion: N=4-8.
    Move those in the interference band to the end of the segment. The rest of sequence is kept the same.
    Inform/negotiate peer(s) as our earlier procedure.

## Slide 17: Features of Selective Hopping Avoidance
Backward compatible (in function)
Meeting FCC regulations
  Global consideration
Traffic based
  Primarily SCO in 802.15
  Re-arrangement as an alternative
Just being extra module in implementation, that is, backward compatible in implementation
  Simple and no other new functions from 802.15/11
  Considering (802.11/802.15) integrated devices