## Slide 1
Slide <number>
Jie Liang, Texas Instruments
January 2001
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for Non-Collaborative BT Mechanisms for Enhanced Coexistence]
Date Submitted: [15Jan01]
Source: [Jie Liang] Company [Texas Instruments Incorporated]
Address [12500 TI Blvd. Dallas, Texas 75243]
Voice:[+1 214-480-4105], FAX: [?], E-Mail:[liang@ti.com]
Re: []
Abstract: [Proposal for Non-Collaborative BT Mechanisms for Enhanced Coexistence.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
NOTE: -01/026r0 WAS MODIFIED BY IANG TO ADD THIS TEMPLATE

## Slide 2: Proposal for Non-Collaborative BT Mechanisms for Enhanced Coexistence
Jie Liang
Texas Instruments Incorporated
12500 TI Blvd.
Dallas, Texas 75243
(ph) 214-480-4105
(email) liang@ti.com

## Slide 3: Key Ideas
Adaptive selection of link level and packet type configuration according to channel conditions
QoS-based traffic allocation and scheduling
Features:
    - Compliant with current BT specifications
    - Fully compatible with standard BT devices
    - Changes can be implemented through software-upgrades for most BT implementations

## Slide 4: Key Tools
Packet type (baseband):
        Single slot vs. multi slot,
        FEC (none, 2/3,1/3),
        CRC (yes, no)
Packet payload length (baseband + L2CAP)
Traffic Flow control (L2CAP)
Data rate setup (L2CAP)
Piconet setup (LMP)

## Slide 5: Premises
During collision periods, BT devices should reduce offered load, instead of increasing it:
  Repetitive re-transmission
It is more co-existence friendly to have BT transmit in bursts than transmit more frequently in small intervals
Voice data tolerates high random bit errors, and FEC do not help much in packet loss

## Slide 6: 802.11b Channel Access Timing
Busy Medium
DIFS
Back-off Window
Medium Idle
New Frame
ACK
Frame Exchange Sequences
Tcp
SIFS
Tbf
SIF= 10us DIF = 50us aSlot_time = 20us
Tbf = N x aSlot
Tf=PLCP Preamble + Header = 192us
Minimum Time Needed (no back-off and payload):
Tm= DIFS+Tf+SIFS+Tf=50+192+10=252us
500bytes Payload (add back-off and Payload at 11Mbps):
T=16xaSlot+Tm+400=972us
Note: needs 1.5 BT Slot time for transmitting one average packet
for 11Mbps 802.11b (a block of time is needed by 802.11b)

## Slide 7: Channel Condition Assessment
key for the proposed method
Channels need to be continuously monitored
    PER, BER
Tools for channel assessment:
    CRC, HEC, RSSI, Channel Assessment Packet (like a probe)
The same tool needed in Adaptive Frequency Hopping (AFP) methods, but used for different purposes:
    No changes in hopping sequence
    Used for link level and packet type configuration and traffic scheduling

## Slide 8: Adaptive Packet Configuration – ACL Links
Packet type selection:
    Contiguous good channels -> use of multi-slot packet types
    (DM3, DH3, DM5,DH5)
    When hopping into noisy channels -> single slot packet (DM1)
    NULL packet, silence
    When hopping into noisy channels -> use of FEC (DM1,DM3,DM5)
    Good channels -> may omit FEC (DH1,DH3,DH5)
Payload length:
    Channel BER up -> payload length down (fragmentation)

## Slide 9: Adaptive Link Configuration – ACL Links
Rate Selection:
    Lower data rate during collision by monitoring
    re-transmission counts and throughput
    (Note: apply when interference is stationary)
Flow control:
    When a contiguous block of heavily noisy channels coming up, put the traffic on HOLD using flow control procedures

## Slide 10: Adaptive SCO Link Configuration
QoS requirement of voice payload:
  PCM coding: 10-4 (random errors) good quality is retained
    10-3 start to notice artifacts, but still acceptable
  CVSD coding: 10-3 good quality is retained
    10-2 start to notice artifacts, but still acceptable
  Perceptible errors mostly come from collisions (really high BER or fail to decode the BT packet header)
HV1 vs. HV2 vs. HV3
  Tsco = 2, 4, 6
  FEC 1/3, 2/3, none
  Payload different (1.5ms, 3ms, 4.5ms)

## Slide 11: Adaptive SCO Link Configuration
Proposal: Use HV3 packet as default (more co-existence friendly)
Leave more time for 802.11 transmissions
Lack of FEC in HV3 is not problem
  high tolerance of random BER
  FEC does not help during collision
Transmit less often – good for saving power
HV1 Traffic
HV3 Traffic

## Slide 12: ACL-AUX1 Packet for Voice Payload
AUX1 packet:
  No CRC, no FEC
  Through ACL link
Proposal: transmit voice payload with AUX1 packet with proper setup of Npoll to restrict delay
Why:
  Flexible in traffic scheduling to avoid collisions (no fixed intervals)
  No need for the mandatory ARQ (voice do not require data integrity)
  Best of both worlds!

## Slide 13: Summary of Tools Proposed
Data:
Adaptive packet type selection considering slot time, FEC, CRC:
DM1, DM3, DM5, DH1, DH3, DH5
Adaptive packet payload length selection: fragmentation
Adaptive link configuration: flow control, rate control
Voice:
Selecting HV3 as default SCO setup
Use AUX1 packet for voice in ACL link with restrictions on Npoll.

## Slide 14: Conclusions (1)
Proposed use of existing tools in BT MAC for co-existence
No changes to the current BT specs, just new usages
Easy implementation through software upgrades

## Slide 15: Conclusions (2) Evaluation Questionnaires
Non-Collaborative
Impact on Standards:
  No change in Specs, implementation issue
Regulatory Impact:
  None
Complexity:
  Software upgrade for most implementations
Interoperability with Non-coexistence Devices:
  Fully compatible (all proposed methods use existing tools)

## Slide 16: Conclusions (3) Evaluation Questionnaires
Classes of Operations:
  Both PCF and DCF for 802.11b
  All profiles in BT
Voice and Data Support:
  Both
Impact on higher layer:
  Mostly none
  Rate changes should be done in coordination with higher layer (e.g. TCP/IP)
Impact on Power Management:
  None