## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for Intelligent BT Frequency Hopping for Enhanced Coexistence]
Date Submitted: [15Jan01]
Source: [Anuj Batra, Jin-Meng Ho, and Kofi Anim-Appiah] Company [Texas Instruments Incorporated]
Address [12500 TI Blvd, MS 8653 Dallas, TX 75243]
Voice:[+1 214.480.4220], FAX: [?], E-Mail:[batra@ti.com]
Re: []
Abstract: [Proposal for Intelligent BT Frequency Hopping for Enhanced Coexistence.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
NOTE: -01/082r0 WAS MODIFIED BY IANG TO ADD THIS TEMPLATE

## Slide 2
Proposal for Intelligent BT Frequency Hopping for Enhanced Coexistence
Anuj Batra, Jin-Meng Ho, and Kofi Anim-Appiah
Texas Instruments
12500 TI Blvd, MS 8653
Dallas, TX 75243
214.480.4220
batra@ti.com

## Slide 3: Outline of Talk
Background
Possible solutions
Motivation for Intelligent Frequency Hopping
Description of algorithm
Conclusions

## Slide 4: Background
BT is an interference-limited system
Sources of interference in 2.4 GHz band include:
  802.11b networks
  microwave ovens
  cordless phones
When interference is present, the throughput for BT drops and the PER increases (see previous TI slides)
To increase throughput in interference-limited environments, BT device must use some kind of coexistence mechanism
  example: change the hopping sequence

## Slide 5: Possible Solutions
A simple, effective idea is to avoid the interference altogether:
  find a subset of channels that are free from interference
  use only these channels in the new HS (reduced HS)
  problem: requires an FCC clarification or a rules change
Q: if we are forced to use all 79 channels and know where the interference is located, can we adaptively design a HS that minimizes the effects of the interference?
A: design an (intelligent) HS that exploits knowledge of the location of the interference:
  the goal of the new sequence would be to minimize packet loss
  new sequence would also be friendly to 802.11b networks
  new sequence would comply with the current FCC regulations

## Slide 6: Motivation for Algorithm: Example 1
Observations:
  2 Good channels (f2 and f3) are required to transmit DM1
  1 Bad channel (in either f0 or f1) can affect 2 slots
Idea:
  Group Good channels in pairs
  Group Bad channels in pair as well

## Slide 7: Motivation for Algorithm: Example 2
Observations:
  2 Good channels (f0 and f3) are required to transmit DM3, DM1
  1 Bad channel (in either f0 or f3) now affect 4 slots
Idea:
  Group Good channels in quartets
  Group Bad channels in quartets

## Slide 8: Grouping of Channels
ACL links:
  packet loss is reduced by grouping good and bad channels
  ARQ protocol ensures that data packets arrive correctly
SCO Links:
  grouping of bad channels ensures an even distribution of bad channels on M  S and S  M
  both directions of the link are affected equally likely
  distribution of bad channels should be uniform so that voice packets are lost every so often (level of QoS)
Grouping of channels is beneficial to 802.11b networks
  reduces interference (slave does not transmit)
  interference from BT occurs over longer period of time
  interference affects only a few packets (maybe repeatedly due to ARQ)
  802.11b networks can maintain large number of packets/seconds

## Slide 9: Idea for New HS
Define a new hopping sequence, where the good and bad channels are grouped together:
where m  {1, 2, 3, 4, 5}. Actual value depends on traffic type.
Length of window for good channels determines the traffic type that can be supported for that particular environment

## Slide 10: Actual Implementation: Example
Example:
  Suppose BT device only had to hop over 16 channels
  Ratio of Good to Bad channels = 3 / 1
  Traffic type: DM1 (M  S), DM1 (S  M)
  Length of Good window = 6, Length of Bad window = 2
Channels: 01, 02, 03, 04, 05, 06, 07, 08, 09, 10, 11, 12, 13, 14, 15, 16
Original HS: 12, 11, 07, 05, 02, 03, 14, 08, 07, 04, 15, 05, 01, 08, 05, 03, …
New HS
  GW:
  BW:
  GW:
12,
11,
05,
02,
03,
14,
08,
07,
04,
15,
05,
01,
05,
03,

## Slide 11: Actual Implementation: Summary
For the Good Window:
  look ahead in the original hopping sequence until a good channel is found; this is done by comparing the channels produced by the original hopping sequence with the list of good and band channels
  use this frequency in the next slot interval
  repeat this process until the good window has been exhausted
For the Bad Window:
  look ahead in the original hopping sequence until a bad channel is found; this is done by comparing the channels produced by the original hopping sequence with the list of good and band channels
  use this frequency in the next slot interval
  repeat this process until the bad window has been exhausted

## Slide 12: Implementation Issues
In this scheme, the master must:
  compile a list of good channels bad channels
  determine length of good and bad windows (function of traffic type)
  transmit this information to the slaves in the piconet
If every device in the piconet has the same list of good and bad channels, then synchronization can be maintained.
In case synchronization is lost: can have a period where the intelligent hopping sequence is used and then revert back to original hopping sequence to make sure everyone has the correct list. Then, start the intelligent hopping sequence again.

## Slide 13: Conclusions
Non-collaborative Coexistence Mechanism
Proposed a new intelligent frequency hopping scheme
Minimizes BT packet loss by grouping good and bad channels
Implementation is straightforward and easy: requires an estimate of the good and bad channels within band
New hopping sequence is very friendly towards 802.11b networks: improves throughput in terms of packets/second