## Slide 1
Slide <number>
Shoemake, Texas Instruments
January 2001
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for Power Control For Enhanced Coexistence]
Date Submitted: [15Jan01]
Source: [Matthew B. Shoemake] Company [Texas Instruments Incorporated]
Address [?]
Voice:[?], FAX: [?], E-Mail:[shoemake@ti.com]
Re: []
Abstract: [Proposal for Power Control For Enhanced Coexistence.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
NOTE: -01/081r0 WAS MODIFIED BY IANG TO ADD THIS TEMPLATE

## Slide 2: Proposal for Power Control For Enhanced Coexistence
Matthew B. Shoemake
shoemake@ti.com

## Slide 3: Abstract
This document describes non-coordinated methods to improve performance of coexisting IEEE 802.15.1 and IEEE 802.11b devices. The fundamental idea idea of this document is that to better coexist, IEEE 802.11b and IEEE 802.15.1 devices should both limit their transmit power to the minimum levels required to obtain satisfactory performance in a given environment. This document presents a power control mechanism for IEEE 802.11b devices.

## Slide 4: Power Control Premises
Coexistence becomes a problem in the 2.4GHz band when devices receive undesired signal and noise that exceed the threshold above which the desired signal, IEEE 802.15.1 or IEEE 802.11b, can no longer be successfully decoded.
It follows that one way to improve coexistence is to limit the amount of undesired signal energy being received.

## Slide 5: Power Control Premises (Cont’d.)
If IEEE 802.11b and IEEE 802.15.1 systems alike would determine the amount of transmitted energy required to achieve good performance and transmit at or near that amount of power without significantly exceeding it:
  Other IEEE 802.15.1 and IEEE 802.11b devices in the area would experienced a reduced level of interference
  The overall capacity in the area would be increased due to frequency reuse

## Slide 6: Power Control Mechanism for IEEE 802.11b Devices
To implement power control, a transmit power control mechanism must be implemented
All IEEE 802.11b devices currently support multiple transmit rates, i.e. 1, 2, 5.5 and 11Mbps.
  As a results, all IEEE 802.11b devices currently implement a rate shifting/control algorithm

## Slide 7: Rate Control Curves

## Slide 8: Rate Control
Systems monitor SNR, SINR, PER, etc. to determine which rate should be used.
The maximum rate is always desired
Rate is shifted down when packets can not be successfully decoded at current rate

## Slide 9: Proposed IEEE 802.11b Joint Rate Shift and Power Control Mechanism
The rate control algorithm of IEEE 802.11b devices can be extended to incorporate the highest mandatory rate at lower transmit powers.
The rate shift algorithm would shift from the highest possible rate to the highest possible rate with lower transmit power, when possible

## Slide 10: Joint Rate Shift and Power Control Curves
For algorithm to be effective in limiting the transmitted power, the joint rate shift and power control algorithm must attempt to move to the modulation/power level requiring the maximum SNR on the rate/power shift curves on the left.
PTX=Pmax-20db
PTX=Pmax-5db

## Slide 11: Joint Rate Shift and Power Control
Following the curves on the previous page results in a joint rate shift and power control function.
There is no need for additional logic to control the power; the only need is to add additional operational points at lower power levels to the shifting algorithm
These new points are at the same rate as the maximum rate the 802.11b system can transmit at; however, they are at reduced transmit power levels, thus in effect, they require more SNR

## Slide 12: Old Rate Shift Mechanism
Rate
Determination
Algorithm
PER
SNR
SINR
TX Rate
Rate determination algorithms vary among manufactures.

## Slide 13: New Joint Rate Shift/Power Control Mechanism
Rate and Power
Determination
Algorithm
PER
SNR
SINR
TX Rate
Rate determination algorithm may still vary among manufactures. Same algorithm may be used with more effective rates.
TX Power

## Slide 14: Minimum Transmit Power Requirement
Power control mechanism will not be effective if IEEE 802.11b and IEEE 802.15.1 devices are not capable of limiting there transmit powers to near the threshold required transmit power to obtain good performance
Therefore, mandatory minimum transmit power of –10dBm is suggested as a mandatory minimum transmit power to comply with this portion of the 802.15.2 standard (if adopted)

## Slide 15: Power Control Levels Requirement
In addition to a minimum transmit power requirement, it is also suggested that devices should have a sufficient number of transmit power levels to produce a resolution that is not too coarse
It is recommended that IEEE 802.15.1 and IEEE 802.11b devices comply with the following table.
If Maximum Transmit Power is less than or equal to | Then Minimum Number of Levels is
1mW | 2
10mW | 4
100mW | 6
1000mW | 8