## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Some Coexistence Issues in 802.11g proposals: Bluetooth Impacts
Date Submitted: January 2001
Source: Ephi Zehavi, Rob Roy, Jim Lansford; Company: Mobilian Corporation
Address: 7431 NW Evergreen Pkwy, Suite 220, Hillsboro, OR 97124
Voice:+1.405.377.6170 , FAX: +1 426 671 6099, E-Mail:Jim.Lansford@mobilian.com
Re:
Abstract: Some Coexistence Issues in 802.11g proposals: Bluetooth Impacts
Purpose: More input.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
NOTE: -01/066r0 WAS MODIFIED BY IANG TO ADD THIS TEMPLATE

## Slide 2: Some Coexistence Issues in 802.11g proposals: Bluetooth Impacts
Ephi Zehavi, Rob Roy, Jim Lansford
Mobilian Corporation
ephi@mobilian.com,
robroy@mobilian.com
jim.lansford@mobilian.com

## Slide 3: Motivation
Should we worry about 802.11g/BT interference?
  Yes, of course!
  BT can significantly erode performance
    Effects have not been studied in depth
    Fix it now or fix it later
  Relief from 802.15.2 is some time away
    Current efforts have focused on 802.11b
    802.11g proposals should be examined
802.11/15/16 are forming a joint coexistence task force to address exactly this issue - coexistence of new specs

## Slide 4: Interference Problem: Overview
Collocated scenarios
  Closely collocated vs. far-spaced
Large body of work on BT – 802.11b interference
  Numerous 802.15.2 documents
  Whitepaper at http://www.mobilian.com
Strong BT/11b interference demonstrated by
  Simulation
  Experimental measurements
Higher rate proposals pose the potential for reduced interference immunity

## Slide 5: Simulation & Experimental Data
Simulations and measurements indicate Bluetooth is a significant interferer to 802.11b

## Slide 6: Review of 802.15.2 Mission
The goal will be to address coexistence of:
  Any 802.15 WPAN with any 802.11 WLAN
  Any 802.15 WPAN with any other 802.15 WPAN (assuming there will be more than one)
  Any 802.15 WPAN with selected other devices in the same band (e.g. HomeRF).
Goal: “Recommended Practices” document
Letter ballot in Aug-Sep ‘01

## Slide 7: Overview of 802.15.2 Proposals
MEHTA, Adaptive Hopping, TDMA of BT and 802.11b
No solution solves the problem for all possible situations
Some require spec changes, regulatory changes, or both
  At least one requires neither
None have addressed 802.11g

## Slide 8: What are the 802.11g Requirements?
Provide variable data rate of at least 20 Mbps
Backward compatibility with 802.11b
Satisfy FCC regulations
Provide flexible power and spectrum allocation
  Efficient modulation and coding to increase coverage area and total throughput
Desired goal: Immunity against other wireless systems sharing the 2.4 GHz band (such as Bluetooth)

## Slide 9: The Interference Link Budget major parameters
Power margin- Signal power vs. Jammer power: Ps/Pj
  WLAN have Power margin of 23-13 dB over Bluetooth
Coding gain- the reduction of the received Energy per symbol of a coded system relative to Energy per symbol of uncoded system operating with the same information rate over the same channel and the same interference model
  8PSK with rate 2/3 relative to uncoded QPSK has a coding gain of 5.5 dB AWGN.
  Coding gain depends on the channel model (AWGN/Fading) and the interference model.
Processing Gain- Effective interference power reduction due to signal shaping, interleaving and coding e
  Processing Gain is not unique number it depends on the interference model and the channel model

## Slide 10: The interference Link Budget major parameters (2)
Distance Margin- The relative distance between the Jammer and the receiver vs. the distance between the transmitter and the receiver
Eb/No- The minimum amount of bit energy to noise that is needed for a given performance level
Propagation model- Signal attenuation and signal distortion as a function of the media between transmitter and receiver
Jammer model- Statistical or/and deterministic description of the Jammer
  Examples: Tone Jammer, Partial band jamer, multitone jammer
  Different systems behave differently to the same jammer

## Slide 11: Type of Interference
Wide Band jammers
  multi tone jammer-multi narrow band modems distributed randomly over the frequency band and operating simultaneously
  White Noise/Colored noise- multi wide band modems sharing the same frequency band and operating simultaneously
Narrow Band Jammers
  Single tone jammer- single narrow band modem sharing the same frequency band and operating simultaneously
  Partial band Jammer- multiple Narrow band modems sharing the same frequency band and operating simultaneously but are restricted to operate in part of the receiver bandwidth
multi tone
single tone

## Slide 12: The Bluetooth interference Model (1)
GFSK modulation, 1 Msps
FH system 1600 hops/sec
For 8 PSK system it behaves like a random tone jammer with random phase. The phase changes every μsec.
For OFDM system it behaves like a partial band jammer

## Slide 13: The Bluetooth interference Model (2)
For high data rate system based on single carrier without M-ary Modulation, Bluetooth interference behaves like single tone jammer
The Power margin is about 23-13 dB
The change in BT phase is very small during the observation time of 1/11 microsec.
Wide band filtering causes minor reduction of the interference
Adaptive Notch filtering requires fast adaptation and causes a transit effect-burst of errors

## Slide 14: 8PSK Proposal
Single Carrier 8 PSK Modulation
Cover sequences
FEC-Trellis coding Technique
  Rate code ½-11 Mbps; Rate 2/3-22 Mbps
Direct Mapping of Encoder output to 8PSK symbol
No intereleaver operation
Coding gain relative to uncoded QPSK system
5.5 dB=10 *log(352/98) for AWGN channel
Burst of four symbol failures causes unrecoverable frame error

## Slide 15: Coding for 11 Mbps-QPSK modulation
Reduced code diversity compared to standard NASA code (dfree=9 vs. 10)
Non-interleaved scheme
  Not immune against transit effect
  Burst of six symbol failures causes unrecoverable frame error

## Slide 16: 8 PSK modulation signal constellation with no Jammer

## Slide 17: 8 PSK with Bluetooth Jammer
Bluetooth Interference causes a displacement of the signal constellation by a fixed vector with random phase
The receiver matched filter reduces slightly the interference power before decoding

## Slide 18: Effect of BT interference on OFDM
FFT Outputs
Energy of BT after FFT RX of 64 OFDM

## Slide 19: Operating Scenario for Simulation

## Slide 20: Single Tone Impact on the throughput of 8PSK and OFDM proposals
Simulation Parameters
  Single tone TX- WLAN RX : 1 m
  Single tone Power – 0 dBm
  WLAN Power – 13 dBm

## Slide 21: Conclusions
8PSK proposal has better error performance over OFDM scheme for AWGN channel (2 dB)
The usage of traditional trellis code, based on maximizing Euclidian distance, reduces dramatically the immunity against transit effects of jammers
8PSK proposal is not immune against strong jammer
Single tone jammers (like Bluetooth) cause major hit in 8PSK throughput
  OFDM is more immune to single tone jammers

## Slide 22: Summary
Coexistence is extremely important
Both proposals
  potentially suffer from BT interference
  can benefit from 802.15.2 techniques, when available and adapted for 802.11g
OFDM needs more study, but 8PSK proposal appears to have Bluetooth coexistence issues.