## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Slot Cycle TDMA Overview
Date Submitted: [16 January 2001]
Source: [Mark E. Schrader] Company [Eastman Kodak Company]
Address [4545 East River Road, Rochester, New York 14650-0898]
Voice:[716-781-9651], FAX: [716-781-9733], E-Mail:[mark.e.schrader@kodak.com]
Re: []
Abstract: An access method based on TDMA is shown that manages access to a WPAN through cycles of time slots that are self timed by the joined stations. The method uses a Coordinator for join and periodic resynchronization via a beacon. The method uses minslots and variable length data slots, whose quantized size is specified in the PLCP header. The system is straight forward, efficient, and adaptable to various hidden node mitigation techniques.
Purpose: This is presented as basis for understanding the SC-TDMA protocol and a basis for writing the full WPAN specification Clause 9,
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.3 MAC Clause 9
Sub-clause: Slot cycle TDMA

## Slide 3: Outline
Overview of Slot Cycle TDMA
Comparison to standard TDMA with respect to QoS
Message structure differences
Example sequences
Self timing methodologys
Hidden node problem issues

## Slide 4: Slot Cycle TDMA Overview
It is a Time Division Multiple Access method.
Primary mode is peer-to-peer.
One station at any one time is a coordinator.
Join & Unjoin are via the coordinator.
The coordinator assigns time slot cycles based on requested QoS.

## Slide 5: Slot Cycle TDMA Overview continued...
Time slots are timed by each joined station simultaneously, with the coordinator serving as beacon generator/synchronizer.
Each station transmits during its assigned slot cycle (or cycles).
Stations listen before transmitting in their slot cycle.
An unused slot cycle, minislot, has minimal length.

## Slide 6: Slot Cycle TDMA Overview continued...
A utilized slot cycle is variable length, depending on the message sent and the ACK/reply required.
The coordinator broadcasts a periodic beacon.
Beacon signals the contention period for a join request or small peer-to-peer transmission.

## Slide 7: Join Process & Timing
Unjoined station responds to beacon with a request to join.
Coordinator will ack, otherwise unjoined station uses random backoff and retry to re-request.
Coordinator responds in its next beacon with the slot cycle data for join accept, or a join decline if the requested QoS is not available.

## Slide 8: Join Process & Timing continued...
Joined station uses: total slots per cycle, total cycles in assigned slot, and time quantization value, Tq, to time the minislots, utilized slots (Async. or Isoc. data), and the beacon.
Tq is an integer number of symbol periods.

## Slide 9: Compare Slot Cycles with Standard TDMA

## Slide 10: QoS With Standard TDMA

## Slide 11: QoS With Standard TDMA continued...
Summary:
As new stations are added to a fixed TDMA system, existing isochronous mode stations must be assigned additional slots in order to have their QoS requirements met.

## Slide 12: Slot Cycle TDMA
Cycles
Slots

## Slide 13: Slot Cycle TDMA
Cycles
Slots

## Slide 14: Primary Slot Cycle Types
BEACON: Not a slot cycle. A broadcast by the master at fixed intervals, superceding all slots.
MINISLOT: An unutilized slot cycle. It is only about 3% to 6% as long as a slot in which data is sent. Also called an access window.
ISOCHRONOUS DATA SLOT: Always has a QoS constraint and may or may not require an ACK.

## Slide 15: Primary Slot Cycle Types continued...
ASYNCHRONOUS DATA SLOT: Signifies a slot cycle with time for an ACK from the recipient. QoS is assumed not as critical as isochronous.

## Slide 16
PLCP
RxTx
ACK
PLCP
SIFS
Payload
PLCP
RxTx
SIFS
PLCP
JREQ or CPData
Asynchronous
Isochronous
Beacon
PLCP
RxTx
SYNC
HNT
Mslot
Minislot
ACK
PLCP
Message Structures
Payload
Notes: PLCP is PLCP preamble + PLCP header HNT is time to DIT/CSO for hidden nodes, CPData is small, fixed size payload.
HNT
HNT

## Slide 17: Example Slot Cycle Sequence
3
1
2
Cycle 4
3
1
2
Cycle 5
1
2
3
1
2
3
1
2
3
1
2
3
1
1
2
3
Cycle 6
Join
Beacon
Minislot
Payload
Isoc. Payload
Cycle 10
Cycle 7
Cycle 9
Cycle 1
Payload
Cycle 8
Preamble
1
3
2
2
3
2
2
1
1
1
Cycle 1
Cycle 2
3
Cycle 3
3

## Slide 18: Self Timing Overview
Time is quantized. The basic unit of time, Tq, is symbol clock divided by a power of 2 (TBD).
The interval from Beacon to the first access window is a constant multiple of Tq, used by all joined stations for synchronization.
The Minislot width, Taw, is a constant known to all stations. Taw is counted modulo Nslots.

## Slide 19: Self Timing continued...
Each station assigned a slot, k, counts occurrences of slot k modulo Mk, the total number of cycles assigned to that slot by the coordinator.
The multiple of Tq received in the PLCP header is used to time the duration of the current slot cycle to the beginning of the next access window.
Each beacon, Minislot, Isoc. message time or Async. message time is an integer multiple of Tq.

## Slide 20
Elements Related to Self Timing
3
3
2
2
2
1
1
1
Cycle 1
Cycle 2
3
Cycle 3
1
2
Cycle 4
3
3
1
2
Cycle 5
1
2
3
1
2
3
1
2
3
1
2
3
1
1
2
3
Cycle 6
Join
SYNC
Minislot
Payload
Cycle 10
Cycle 7
Cycle 9
Cycle 1
Cycle 8
PLCP
1
2
3

## Slide 21: Slot Cycle Required PLCP Header Fields
Source and destination ID numbers, or addresses (TBD).
Current slot and cycle number (TBD).
Delay time (in Tq) from PLCP header to the next access window.

## Slide 22: Hidden Nodes
Two joined stations that cannot hear each other are “hidden nodes”.
Not hearing the message will corrupt self timing because the PLCP of the sender will not be heard by nodes hidden from it.
A station may try to transmit at the wrong time interfering with others.

## Slide 23: Hidden Nodes continued...
Listen before send will minimize the probability of interference in well utilized networks because the Taw is very small compared to data transmission time. The network is mostly busy.

## Slide 24: In Search of Sync.
Synchronization can be regained
via the beacon
the sequence of slot cycle values in the message headers,
or an exchange with the coordinator that can be added at the beginning of the access time.

## Slide 25: DIT (RTS) - CSO (CTS)
Joined station sends “Declare Intent to Transmit”, DIT, containing source and destination ID, and delay time for self timing
Coordinator replies with “Confirm Slot Ownership”, CSO echoing the source and destination ID, delay time.
Joined stations time the slot using the coordinator’s CSO transmission.