## Slide 1
Slide <number>
<footer>
<date/time>
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [WG Comdex Presentations, November 2000]
Date Submitted: [14 November 2000]
Source: [Bruce Kraemer] Company [Intersil Corporation]
Address [2401 Palm Bay Road NE M/S 62A/024 Palm Bay FL 32905 USA]
Voice:[+1 322 729 5683], FAX: [+1 322 724 7886], E-Mail:[bkraemer@intersil.com]
Source: [Dr. Stephen J. Shellhammer] Company [Symbol Technologies, Inc.]
Address [One Symbol Plaza, MS B-2 Holtsville, NY 11742-1300 USA]
Voice:[+1 631 738 4302], FAX: [+1 631 738 4618], E-Mail:[shell@symbol.com]
Source: [James Allen] Company [Eastman Kodak, Co]
Address [4545 East River Road Rochester, NY 14640-0898 USA]
Voice:[+1 716 781 9025], FAX: [+1 716 722 9052], E-Mail:[james.d.allen@kodak.com]
Source: [Tom Siep] Company [Texas Instruments]
Address [8505 Forest Lane M/S 8723 Dallas, TX 75243 USA]
Voice:[+1 972 480 6786], FAX: [+1 972 480 6552], E-Mail:[siep@ti.com]
Re: [four presentations relating to 802.15]
Abstract: [COMDEX Fall 2000, E-Mobility Program, EM I-1: IEEE WPAN Projects Update. Panel presentation held 9:00 a.m.on Tuesday, 14 November in Las Vegas.]
Purpose: [Description of what the author wants P802.15 to do with the information in the document.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Bruce Kraemer
Marketing Chair of IEEE 802.15
Intersil
Palm Bay, FL 32902
(321) 729-5683
bkraemer@intersil.com
Wireless Personal Area Networks™

## Slide 3: IEEE
IEEE Established in 1884 (AIEE & IRE)
IEEE December 1999 Membership was 360,000; 66% USA & 33% Non-USA
IEEE produces 30 percent of the world's published literature in electrical engineering, computers and control technology,
IEEE holds annually more than 300 major conferences and
IEEE has more than 800 active standards with 700 under development.
Institute of Electrical and Electronic Engineers

## Slide 4: Objectives of IEEE 802
To develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of standards making:
  Due process
  Consensus
  Openness
  Balance
  Rights of appeal
Publish LAN/MAN Standards in electronic format

## Slide 5: IEEE 802 Architecture

## Slide 6: IEEE Structure
802.10 SECURITY
*802 OVERVIEW & ARCHITECTURE
802.1 MANAGEMENT
802.2 LOGICAL LINK CONTROL
802.1 BRIDGING
802.9
MAC
802.9
PHY
802.11
MAC
802.11
PHY
802.12
MAC
802.12
PHY
802.14
MAC
802.14
PHY
802.15
MAC
802.15
PHY
802.3
MAC
802.3
PHY
802.4
MAC
802.4
PHY
802.5
MAC
802.5
PHY
802.6
MAC
802.6
PHY
DATA
LINK
LAYER
PHY
LAYER
802.16
MAC
802.16
PHY
Source: IEEE Std P802.15.1 D0.7.2

## Slide 7: Current IEEE 802.11 Standard
Wireless Local Area Networks (WLAN)
Medium Access Control (MAC) Layer
Currently includes five Physical (PHY) Layers
  Frequency Hopping Spread Spectrum
  Direct Sequence Spread Spectrum
  Infrared
  11 Mbps in 2.4 GHz
  54 Mbps in 5 GHz

## Slide 8: IEEE 802.15
Jim Allen, Vice Chair
Ian GIfford, Vice Chair
Tom Siep, Technical Editor
Pat Kinney, Secretary
MAC Sublayer
PHY Layer
Standard/P802.15.1
Task Group 1 (TG1)
WPAN(TM)/Bluetooth 1
Ian Gifford, Chair
Sub Task Group 1
MAC Model Team
Jim Lansford, Chair
Sub Task Group 2
PHY Model Team
Nada Golmie, Chair
Std Practice/P802.15.2
Task Group 2 (TG2)
Coexistence
Steve Shellhammer, Chair
MAC Sublayer
PHY Layer
Standard/P802.15.3
Task Group 3 (TG3)
High Rate
John Barr, Chair
Task Groups
Marketing Committee (MC)
Bruce Kraemer, Chair
Radio2 Study Group (R2SG)
Tom Siep, Chair
Low Rate Study Group (LRSG)
Sean Middleton, Chair
Study Groups
Working Group
IEEE 802.15 WPAN(TM)
Bob Heile, Chair
Sponsor
IEEE802 LMSC
Jim Carlo, Chair
Mike McInnis, Assistant
Mike McInnis, Assistant

## Slide 9: IEEE 802.15
Standards for Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks (e.g. 8-16 nodes)
  Communication of devices within a Personal Operating Space (POS) of 10 meters

## Slide 10: IEEE 802.15 Activities Summary
802.15.1 (Standard)
  IEEE Standard of Bluetooth™ Specification
802.15.2 (Recommended Practice)
  Model and Facilitate Coexistence of WPAN & WLAN devices
802.15.3 (Standard)
  A High-Rate (> 20 Mbps) WPAN
Radio2 Study Group
  Track Bluetooth2 and recommend an action.
Low Rate Study Group
  Raw Data Rate = 2Kb/sec to 200Kb/sec

## Slide 11: IEEE 802.15 Process Status
Idea for standard
Find Sponsor
Submit PAR
Approve PAR
Organize Task Group
Develop draft standard
Ballot draft standard
Approve draft standard
Publish approved standard
Radio2 SG
Low Rate SG
Task Group 3
Task Group 2
Task Group 1

## Slide 12: IEEE 802.15 Task Group 1
Converting the Bluetooth Specification into an IEEE Standard
  Convert to IEEE Format
  Adding System Description Language (SDL) diagrams
  IEEE Std 802.15.1-2001 June 2001
  Bluetooth™ Pocket Guide December 2000 via IEEE-Press
  IEEE 802.15 Handbook: A Designer's Companion June 2001

## Slide 13: IEEE 802.15 Task Group 2
IEEE 802.11 and Bluetooth occupy same 2.4 GHz ISM Band and same locations
  There will be some mutual interference
Developing Recommended Practice regarding how to minimize impact
Coexistence Model
  Model describing the mutual interference of WLAN and WPAN upon one another.
Coexistence Mechanisms
  Mechanisms or techniques to facilitate coexistence of WLAN and WPAN devices.

## Slide 14: IEEE 802.15 Task Group 3
Provide a standard for low complexity, low cost, low power consumption, high data rate wireless connectivity with data rates of at least 20 Mbps
Satisfy a set of multimedia needs for services such as video or digital still imaging communications including Quality of Service
Coexist with 802.11 and Bluetooth

## Slide 15: IEEE 802.15 Low-Rate Study Group
Less than 200 kbps
Support at least 16 nodes in a network
10 meters range
No battery or battery life of months to infinite
Low cost relative to target device
Status: Progressing to Task Group
Applications
  Sensors & Actuators, Toys, Smart Badges, Health Monitoring, Computer Peripherals, Remote Control, Home Automation, Automatic Meter Reading

## Slide 16
Steve Shellhammer
Chairman of IEEE 802.15.2
Symbol Technologies, Inc.
One Symbol Plaza
Holtsville, NY 11742
(631) 738-4302
shell@symbol.com
IEEE 802.15.2 Coexistence of WLAN and WPAN

## Slide 17: Mutual Interference
Problem: Both IEEE 802.11 and Bluetooth operate in the same 2.4 GHz ISM Band.
Problem: Bluetooth enabled devices will likely be portable and will need to operate in an IEEE 802.11 WLAN environment.
Problem: There will be some level of mutual interference.

## Slide 18: Deliverables
Coexistence Model
  Quantify the effect of the mutual interference of WLAN (e.g. 802.11) and WPAN (e.g. Bluetooth) upon one another.
Coexistence Mechanisms
  Mechanisms or techniques to facilitate coexistence of WLAN and WPAN devices.
Both to be documented in an IEEE Recommended Practice

## Slide 19: Coexistence Model
The purpose of this Coexistence Model is:
  To quantify the effect of the mutual interference under varied circumstances.
    WLAN in Laptop and Bluetooth in nearby PDA
    WLAN and Bluetooth in the same Laptop
  To demonstrate the effectiveness of the adopted Coexistence Mechanism.

## Slide 20: Coexistence Model
The Coexistence Model consist of four sections,
  Physical Layer Models of the 802.11 and Bluetooth Radios
  MAC Layer Models of both 802.11 and Bluetooth
  RF Channel Model of the Radio Channel
  Data Traffic Models of the traffic over both 802.11 and Bluetooth networks.

## Slide 21: Coexistence Model
Input to the Model
  Location of 802.11 and Bluetooth devices
  Type of Data Traffic flowing over both the 802.11 and Bluetooth networks.
Output of the Model
  Network Throughput, for both 802.11 and Bluetooth.
  Network Latency, for both 802.11 and Bluetooth.
  Packet Error rate for voice link

## Slide 22: Coexistence Mechanisms
Coexistence Mechanisms Facilitate Coexistence of WPAN & WLAN devices
Sent out a Call for Submission of Coexistence Mechanisms in September.
Presentations are scheduled for
  November 2000 (last week)
  January 2001 meeting (Monterey)

## Slide 23: Coexistence Mechanisms
Collaborative Mechanisms
  Some form of communication exists between the WLAN and WPAN.
  Use this link to provide fair sharing of medium (i.e. air waves)
Non-Collaborative Mechanisms
  No communication between WLAN and WPAN exists.
  Techniques to minimize the effects of the mutual interference

## Slide 24: Current Status
First-order models of 802.11 and Bluetooth Physical Layers are complete.
MAC Layer model for 802.11 was available. We have added Bluetooth MAC Layer model.
We are currently integrating the PHY and MAC Layer Models.

## Slide 25: Current Status
Presentation last week on impact of 802.11 on Bluetooth SCO link (voice).
  Included Physical Layer models for both 802.11 and Bluetooth
  Integrated with MAC model for both
  Plotted SCO Packet Error Rate as a function of Bluetooth 802.11 separation.

## Slide 26: Current Status
We have received 8 letters of intent to submit Coexistence Mechanisms.
We received two submissions last week.
The remaining submissions will be given at the January 2001
We will then begin the selection process.

## Slide 27: Future Work
Ensure proper coexistence of the High-Rate WPAN with both Bluetooth and 802.11
Issue subsequent releases of IEEE 802.15.2 with additional models to include High-Rate WPAN and possibly other wireless systems (e.g. higher rate 802.11 versions).

## Slide 28: IEEE 802.15 Web Site
For more information see the IEEE 802.15 web site (TG2)
www.ieee802.org/15/

## Slide 29
James D. Allen - PE
Vice Chairman of IEEE 802.15 Task Group 3
Eastman Kodak Co.
4545 East River Road
Rochester, NY 14650-0898
(716) - 781- 9025
james.d.allen@Kodak.com
IEEE 802.15.3 High Rate WPAN
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 30: IEEE 802.15 Org chart
You
are
Here
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 31: Application Summary
Multimedia and large file transfers between consumer devices.
Visit application presentations on our Web site.
DCT-2000
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 32: TG3 Application Needs
Consumer Market - Indoor/Outdoor
Simple to use
Cost is a KEY factor
Throughputs above 8 Mbps are needed for Multimedia applications, which imply >20 Mbps (ovens, protocol overhead)
Standard has to happen quickly
Needs simple Quality of Service algorithm
Co-existence is important
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 33: Project Description
Standardize Wireless Medium Access Control (MAC) and Physical Layer (PHY) Specifications for High Rate Wireless Personal Area Networks (WPANtm)
  … wireless connectivity with fixed, portable and moving devices within or entering a Personal Operating Space (POS) (up to 10 meters in all directions enveloping a person)

## Slide 34: Project Description-continued
  … interoperability or coexistence with other 802.15 standards
  … coexistence with other wireless devices in conjunction with Coexistence Task Groups such as 802.15.2
  … low complexity, low cost, low power
  … >20Mbps to satisfy a set of consumer multi-media industry needs for WPANtm communications.
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 35: Proposals
MAC Layer (Protocol)
  4 Proposals
    TG1 Reuse with M/M Slot cycle TDMA
    Adaptive TDMA w/ M/M QoS Policies
    CSMA with real time features
    802.11 with point coordination function for isochronous
PHY Layer (Radio)
  8 Proposals
    2FSK, 4FSK, QPSK, OFDM, nQAM, UWB...
    2.4 GHz, 5 GHz
    Rates up to 50 Mbps (bits per second)
M/M=Multimedia
QoS=Quality of Service

## Slide 36: Results & Features
MAC - Combination of:
  Adaptive TDMA w/ M/M QoS Policies and
  ….CSMA with real time features
    Quick response, Power management
    Low complexity
    Point to mulit-point personal area network
    M/M QoS by a negotiated time slot cycle TDMA mechanism
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 37: Results & Features
PHY (Starting Point)
  2.5GHz, Single Carrier, OQPSK, nQAM
    Scaleable costs & rates
    Consumer oriented
    Embeddable
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 38: Status and Plans for TG3
November 2000 - Reduction of Proposals to 1PHY/1MAC
May 2001 - Complete Initial Draft (PHY and Data Link layers)
November, 2001 - Sponsor Ballot
Standard by the end of 2001 or early 2002
Archive documents
  00127 - TG3_High-Rate_Project-Plan-Proposal
  00180 - TG3 Evaluation Process Flow Chart

## Slide 39: Participation is
Meeting Size
  November 47 (Bold = Plenary
  January 30 Meetings)
  March 88
  May 73
  July 145
  September 120 50 voters
  November 113 74 voters
Growing
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 40: Contact Data
Website: http://www.ieee802.org/15/pub/TG3.html
Chair: john.barr@motorola.com
Vice Chair: james.d.allen@kodak.com
Secretary: kinneypw@norand.com
PHY Comm. Chair: jgilb@mobilian.com
MAC Comm. Chair: allen.heberling@kodak.com
SYS Comm. Chair: m-duval@ti.com
Public List Server: stds-802-wpan@ieee.org
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 41: Overview of IEEE 802.15 / Bluetooth™ Presented at COMDEX Fall November 14, 2000 Las Vegas, Nevada

## Slide 42: Agenda
The Basic Technologies
  IEEE 802.15.1 Standards Activities
  Bluetooth™ Special Interest Group
Where These Technologies Play
Questions and Answers

## Slide 43: Objectives of IEEE 802
To develop consensus standards that benefits the World Wide Networked Society.
Maintain the imperative principals of standards making:
  Due process
  Consensus
  Openness
  Balance
  Rights of appeal
Publish LAN/MAN Standards in electronic format

## Slide 44: IEEE 802 Architecture

## Slide 45: IEEE 802.15
Wireless Personal Area Networks (WPANsTM)
  Short-range
  Low Power
  Low Cost
  Small networks
  Communication of devices within a Personal Operating Space

## Slide 46: IEEE 802.15 Task Group 1
IEEE 802.15 Task Group 1 is converting the Bluetooth Specification into an IEEE Standard
  Convert to IEEE Format
  Add
    Introductory material
    Specification and Description Language (SDL)
    LLC interface
  Letter Ballots, Comments, and Comment Resolution.

## Slide 47: Bluetooth Wireless Technology
Operates in the 2.4 GHz band at a maximum user data rate of 720Kb/s. (1Mbit nominal)
Uses Frequency Hopping spread spectrum (FHSS)
Radio transceivers hop from one channel to another in a pseudo-random fashion, determined by the master.
Supports up to 8 devices in a piconet (1 master and 7 slaves).
Piconets can combine to form scatternets.

## Slide 48: IEEE 802.15.1 and Bluetooth

## Slide 49: When to Use a WPAN
Access just to devices being carried
The IT people don’t care
No physical access to wired network
Moderate data rate needed

## Slide 50: The WPAN™ in Action

## Slide 51: More Information
Tom Siep, How to Find What You Need in the Bluetooth™ Specification, IEEE Press, estimated publication November 2000
www.amazon.com/exec/obidos/ASIN/0738126357/
Book signing: Digital Guru, Wednesday, Noon
www.ieee802.org/15/
www.bluetooth.com

## Slide 52: Questions?
Tom Siep
Texas Instruments
Siep@ti.com

## Slide 53: Backups
(possibly not be presented)

## Slide 54: WLANs verses WPANs (WARNING:gross simplifications)
WLAN is outwardly looking
  Interacts with wired infrastructure (LANs)
  Network timeframe hours to days
  Portable devices
  “Wires are expensive”
WPAN is inwardly looking
  Interacts with personal objects
  Network timeframe seconds to hours
  Highly mobile devices
  “Wires get in the way”

## Slide 55: When to Use a WLAN
Access to BMITS (Big Machine In The Sky)
The Information Technology (IT) people need to be involved
  Network addresses
  High level of Network Security
  Physical access to wired network
High data rate needed

## Slide 56: The WLAN in Action

## Slide 57: IEEE 802.15
802.15.1 (Standard)
  IEEE Standard of Bluetooth™ Specification
802.15.2 (Recommended Practice)
  Model and Facilitate Coexistence of WPAN & WLAN devices
802.15.3 (Standard)
  A High-Rate (> 20 Mbps) WPAN
Radio2 Study Group
  Track Bluetooth2 and recommend an action.
Low Rate Study Group
  Raw Data Rate = 2Kb/sec to 200Kb/sec