## Slide 1: Texas Instruments Responses to TG4 CFA
Classroom Network
Low Data Rate Computer Peripherals

## Slide 2: Classroom Network
What are the types of devices in that application
  Graphing calculators
  Teacher workstation
  Printer (may be attached to workstation)

## Slide 3: Classroom Network
How many devices are in this low rate network?
  Range 10 to 64
  Typically 30

## Slide 4: Classroom Network
Describe how the network is initiated
  Students arrive at classroom
  Teacher initiates communications with “known” units
  Students turn on calculators are are automatically registered with the correct teacher’s network

## Slide 5: Classroom Network
How do devices attach and detach from the network
  Auto-attach, based on configuration
    Beginning of semester units identified with student/class
    Teacher can alter configuration at workstation
  Detach is power-down
Is human intervention required?
  Initial setup
  Power-up

## Slide 6: Classroom Network
Describe the traffic flow of the data
  Bursty interaction
    Problem download
    Solution upload
    Printing
  Most times data channel is idle

## Slide 7: Classroom Network
Describe the type of data that flows in each branch of the network.
  Fairly uniform data types for all students and teacher
  Multicast useful from workstation, but subsequent verification of complete downloads necessary

## Slide 8: Classroom Network
How much data is typically in each message?
  Typical payload of 100 to 500 bytes
  Ability to handle a bitmap of 2K is a plus
    Infrequent
    No other activity on net at time

## Slide 9: Classroom Network
How often are messages sent?
  Several times per hour per student

## Slide 10: Classroom Network
How much latency in the message transfer is acceptable?
  1 to 3 seconds typical, 5 seconds max

## Slide 11: Classroom Network
Describe the network topology
  Master/slave
  Peer to peer not allowed (no cheating!)

## Slide 12: Classroom Network
Is there a master node? Where do data flows originate and terminate? Are the devices peer to peer or master/slave?

## Slide 13: Classroom Network
Does this network have to interface to another network?
  Yes
If so, how should these two networks be connected?
  Through the workstation LAN connection

## Slide 14: Classroom Network
If two low-rate networks are in range of one another, should they interact?
  Unlikely
If yes, how?
  If >64 students (e.g. a lecture hall) then may have to have several networks all connected to the main workstation

## Slide 15: Classroom Network
Do the devices support authentication and security?
  Authentication is important
  Security less important

## Slide 16: Classroom Network
What is the data traffic type?
  Asynchronous

## Slide 17: Classroom Network
What are the battery life requirements?
  Minimum: 1 week
  Desired: 1 semester
  Rechargeable in place also desirable

## Slide 18: Classroom Network
What is the physical size of the low-rate transceiver?
  Calculator: ~ compact flash card
  Workstation: don’t care

## Slide 19: Classroom Network
What is the range requirement of the application?
  10 Meters
    In same room
    Through human bodies
    Around metal desks, tables, chairs
    Desirable if does not go through walls

## Slide 20: Classroom Network
What is the estimate market size (units) of the proposed application?
  Population of grades 6-12
  Estimated 3 year lifetime of device

## Slide 21: Classroom Network
Will this application benefit from location awareness?
  no

## Slide 22: Low Data Rate Computer Peripherals
How many devices are in this low rate network?
  2 to 5

## Slide 23: Low Data Rate Computer Peripherals
What are the types of devices in that application
  Keyboard
  Mouse
  Joystick
  Speakers (?)
  Low Resolution Printers (?)

## Slide 24: Low Data Rate Computer Peripherals
Describe how the network is initiated.
  Power-up of computer system

## Slide 25: Low Data Rate Computer Peripherals
How do devices attach and detach from the network.
  Once assigned, a peripheral is always attached to the same system on power-up
Is human intervention required?
  Initial “introduction” only

## Slide 26: Low Data Rate Computer Peripherals
Describe the traffic flow of the data
  Keystrokes: 800 bps typical maximum, 10 bit payload per packet
  Mouse movement 500 bps, 50 bit payload
  Joystick 1000 bps upstream, 50 bit payload
  Joystick 200 bps downstream, 20 bit payload

## Slide 27: Low Data Rate Computer Peripherals
How often are messages sent?
  Constant during computer usage

## Slide 28: Low Data Rate Computer Peripherals
How much latency in the message transfer is acceptable?
  Human threshold: 100 ms typical, but must be consistent

## Slide 29: Low Data Rate Computer Peripherals
Describe the network topology
  Master (computer chassis) / Slave (peripherals)

## Slide 30: Low Data Rate Computer Peripherals
Does this network have to interface to another network?
  no

## Slide 31: Low Data Rate Computer Peripherals
If two low-rate networks are in range of one another, should they interact?
  no

## Slide 32: Low Data Rate Computer Peripherals
Do the devices support authentication and security?
  Both are important

## Slide 33: Low Data Rate Computer Peripherals
What is the data traffic type?
  Asynchronous for lowest rate
  Synchronous may be needed if speakers can be supported

## Slide 34: Low Data Rate Computer Peripherals
What are the battery life requirements?
  1 Month

## Slide 35: Low Data Rate Computer Peripherals
What is the physical size of the low-rate transceiver?
  Compact Flash size

## Slide 36: Low Data Rate Computer Peripherals
What is the range requirement of the application?
  1 to 2 meters

## Slide 37: Low Data Rate Computer Peripherals
What is the estimate market size (units) of the proposed application?
  Annual production of personal computers

## Slide 38: Low Data Rate Computer Peripherals
Will this application benefit from location awareness?
  no