## Slide 1
IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Collaborative Coexistence Mechanism: TDMA of Bluetooth and 802.11
Date Submitted: January 16, 2001
Source: Steve Shellhammer Company: Symbol Technology, Inc.
Address: One Symbol Plaza, Holtsville NY 11742
Voice: (631) 738-4302, FAX: (631) 738-4618, E-Mail: shell@symbol.com
Re: Submission of a Coexistence Mechanism in response to IEEE 802.15-00/009r4
Abstract: This is a proposal to P802.15.2 for a collaborative coexistence mechanism between Bluetooth and 802.11b
Purpose: This is a submission to IEEE 802.15.2 of a Recommended Practice for a Collaborative Coexistence Mechanism.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: IEEE P802.15 Working Group for Wireless Personal Area NetworksTM
Collaborative Coexistence
Mechanism Submission:
TDMA of 802.11 and Bluetooth

## Slide 3: Review of Multiple Access Techniques
Time Division Multiple Access (TDMA)
  Used in Bluetooth within a piconet (TDD)
  A Stochastic version used in 802.11 within the coverage of an access point
Frequency Division Multiple Access (FDMA)
  Used for frequency planning of multiple 802.11b access points to cover an physical area

## Slide 4: Review of Multiple Access Techniques
Code Division Multiple Access (CDMA)
  Used within Bluetooth to minimize piconet to piconet interference

## Slide 5: Review of Multiple Access Techniques
The goal of these multiple access techniques is to make the signals (nearly) orthogonal.
By making the signals (nearly) orthogonal we minimize mutual interference.

## Slide 6: Problem to Solve
Find a technique to allow Bluetooth and 802.11b to operate in the same portable unit (e.g. laptop or hand-held computer).
Prevent interference within the unit.
If possible, prevent interference from other nearby units.

## Slide 7: Evaluate our Multiple Access Choices
TDMA
  Results in total orthogonality if Bluetooth and 802.11 time intervals do not overlap
  Works at even very high interference power levels
FDMA
  Orthogonality depends on performance of the filters in the radio
  Will not work with very high interference levels

## Slide 8: Evaluate our Multiple Access Choices
CDMA
  Only applies to like systems (e.g. both direct sequence) with high processing gain.
  Requires power control.
  Does not apply to our problem.

## Slide 9: Multiple Access Choice
For a Collocated Coexistence Mechanism the best choice is some type of TDMA to ensure orthogonality, independent of interference power levels and filter performance.

## Slide 10: Proposed TDMA Scheme
We propose allocating time slots for 802.11 and Bluetooth.
Subdivide the 802.11 beacon-to-beacon interval into a two subintervals
  One subinterval for 802.11
  One subinterval for Bluetooth

## Slide 11: TDMA Scheme
IEEE 802.11b Interval
Bluetooth Interval
802.11 Beacon

## Slide 12: Benefits of TDMA Approach
Since each radio has its own subinterval, both radios will operate properly, due to total orthogonality.
This works even if the two radio are very close to one another, for example, in the same hand-held computer or PDA. The two radios can be separated from one another by only a few centimeters.

## Slide 13: Benefits of TDMA Approach
Only the Bluetooth radio in the portable unit needs to be modified. That Bluetooth radio needs to be the master of the Piconet.
Standard Bluetooth-enabled devices work with this approach. Since they are slaves they only speak when spoken to. They naturally stay within Bluetooth interval.

## Slide 14: Benefits of TDMA Approach
This approach solves interference from nearby 802.11 and Bluetooth devices, since all the systems are synchronized.
  During the 802.11 interval, no Bluetooth devices transmit.
  During Bluetooth interval, no 802.11 devices transmit.

## Slide 15: Benefits of TDMA Approach
It is possible to make 802.11 radios, that do not have this feature, limit their transmissions to the 802.11 interval.
This is done by sending out, from the AP, a clear-to-send (CTS) signal at the end of the 802.11 interval.
All 802.11 radios will stay off the air for the duration prescribed in the CTS signal.

## Slide 16: Benefits of TDMA Approach
Works with all versions of 802.11, since the solution is at the Media Access Control (MAC) layer, and does not depend on the specifics of the Physical (PHY) layer.
It is possible to multiplex the antenna in the portable system between 802.11 and Bluetooth.

## Slide 17: Limitation of TDMA Approach
Only supports ACL links.
SCO link is very regular and has a very short period (3.75 ms) it is difficult to fit any 802.11 packets in-between SCO packets.

## Slide 18: Implementation Requirements
The 802.11 mobile units all share a common clock which is derived from the Access Point clock.
The 802.11 clock is used in timing the 802.11 and Bluetooth intervals.
Each 802.11 mobile unit must be modified to perform all 802.11 transactions during the 802.11 interval.

## Slide 19: Implementation Requirements
The 802.11 mobile unit must send a synchronization signal to the Bluetooth radio.
  One implementation is for the 802.11 radio to produce a “media free” signal.
0
1
Media Free
802.11 Interval
Bluetooth Interval
802.11 Interval
Bluetooth Interval

## Slide 20: Implementation Requirements
The Bluetooth Master must ensure all Bluetooth traffic is completed during the Bluetooth interval.
The Bluetooth Master services each of the slaves and stops early enough so the last slave it talks to has time to send its packet, before the Bluetooth interval ends.

## Slide 21: Implementation Requirements
The duration of the 802.11 and Bluetooth intervals can be made programmable.
This allows the System Administrator the ability to allocate capacity between 802.11 and Bluetooth.
Optionally the AP can send out a CTS at the end of the 802.11 interval.

## Slide 22: Implementation Requirements
Since the Bluetooth devices cannot transmit during the 802.11 interval they might as well be asleep.
The Bluetooth Master can service each Bluetooth slave and then put it into Hold mode, until the next Bluetooth interval.

## Slide 23: Implementation Requirements

## Slide 24: Address Questions in 802.15-00/009r4
1. This is a “Collocated Collaborative Coexistence Mechanism.”
2. Performance is described in the Appendix.
3. This does not effect the 802.11 standard. It does require an additional feature to restrict when 802.11 transmits.

## Slide 25
Address Questions in 802.15-00/009r4
3b. This does not impact the Bluetooth specification. It does require an additional feature to restrict when the Bluetooth Master transmits.
4. There is no regulator impact. This is allowed under FCC Part 15.247. We need to verify that it is allowed outside the US, but I believe that it is allowed.

## Slide 26: Address Questions in 802.15-00/009r4
5. The complexity of implementing this coexistence mechanism is quite low.
  The is a very simple interface between the 802.11 and Bluetooth systems.
  The digital hardware would be very minimal if any.
  Some 802.11 MAC and Bluetooth Link Manager software is required.

## Slide 27: Address Questions in 802.15-00/009r4
6. These systems are interoperable with systems that do not include this coexistence mechanism.
  This is true for both 802.11 and Bluetooth.
  The Bluetooth slaves automatically follow the mechanism.
  The CTS signal can be used to get other 802.11 systems to follow the coexistence mechanism.

## Slide 28
Address Questions in 802.15-00/009r4
7. There is no impact to high network layers, for either 802.11 or Bluetooth.
8. This mechanism supports all 802.11 and Bluetooth classes of operation.
9. The only limitation is that it does not support Bluetooth SCO packets.
10.No impact on power management. Fits well with Bluetooth Hold mode.

## Slide 29: Synergy with Mobilian Submission
Both this submission and the Mobilian submission multiplex the two radios within the portable unit (e.g. laptop or PDA).
  This submission is a form of programmable TDMA
  Mobilian’s submission is a form of dynamic TDMA.

## Slide 30: Synergy with Mobilian Submission
There are advantages to each of the two approaches.
It would be straightforward to implement a combination of the two approaches.
Our recommendation (after speaking with Mobilian) is to combine these two submission.

## Slide 31: Conclusions
A TDMA based Collaborative Coexistence Mechanism has been proposed.
Symbol Technologies is currently implementing this approach for a major Package Delivery company.
We propose merging this proposal with the Mobilian proposal.

## Slide 32: Appendix - Performance
This coexistence mechanism applies to the 10 cm separation case, since we assume the two radios are in the same portable unit.
The performance of this coexistence mechanism is independent of the separation of the Bluetooth and 802.11 radios.

## Slide 33: Appendix - Performance
It is believed that both the 802.11 and Bluetooth radios will operate quite poorly at 10 cm, if no coexistence mechanism is implemented.
Therefore, we will only address performance with this coexistence mechanism implemented.

## Slide 34: Appendix - Performance
Let t1 = duration of 802.11 interval.
Let t2 = duration of Bluetooth interval.
Then t1 + t2 = T = 802.11 beacon period, which is typically 100 ms.
Let p = t1 / T
Let q = 1 - p = t2 / T

## Slide 35: Appendix - Performance
802.11 Throughput
  The 802.11 throughput is p times the ideal 802.11 throughput. For example, if p = 0.5 then you have half the throughput of an ideal 802.11 system without Bluetooth interference.
Bluetooth Throughput
  The Bluetooth throughput is q times the ideal Bluetooth throughput, without 802.11 interference.

## Slide 36: Appendix - Performance
802.11 Latency
  Since most 802.11 traffic occurs soon after the beacon, in many cases the latency increase is minor. A detailed simulation would be needed to determine the latency more accurately.

## Slide 37: Appendix - Performance
Bluetooth Latency
  The increase in average latency is (p/2) t1.
  The increase in worst case latency is t1.
  Example
    t1 = 50 ms
    T = 100 ms
    The increase in average latency is 12.5 ms.
    The increase in worst case latency is 50 ms.