## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: MAC CTRB Parameters Issues
Date Submitted: [9 July 2001]
Source: [Mark E. Schrader] Company [Eastman Kodak Co.]
Address [4545 E. River Rd., Rochester, NY 14650-0898]
Voice:[+1.716.781.9561], FAX: [+1.716.781.9733], E-Mail:[mark.e.schrader@kodak.com]
Re: [IEEE 802.15.3 MAC]
Abstract: QoS based Channel Time Request Block parameters are defined mathematically. Some issues and limits of the timing are defined and briefly discussed. QoS is shown to to simple from the PNC perspective when only allocated bandwidth is important..
Purpose: Channel Time Request Block parameters toward building a QoS algorithm.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Problem Overview
Find the smallest set (3) of parameters usable for ISOC (QoS-based) requests in the Channel Time Request Block (CTRB).
Define the parameters mathematically with variables that are usable by the channel time requestor.
Identify issues and solutions.

## Slide 3: Variable Definitions
fd = bits per second of delivered data.
NB = bits of source buffer available to store the data to be communicated.
NMPDU = bits of the data portion of one packet of data.
NOH = Equivalent bits of overhead of one packet of data including: actual MAC header bits, slot guard times, PHY or PLCP overhead, etc., everything-but-data, etc. It simplifies the explanation to express this as an equivalent number of bits.

## Slide 4: Definitions Continued
NE = Channel (PHY) encoding, bits per symbol
fs = Channel symbol rate, symbols per second.
Tbcn = Beacon Period

## Slide 5: QoS Parameter 1: Allocation Period Length, TAP
TAP = NB / fd
This is how often the NB buffer must be sent to get the desired delivered data rate fd.
This is the size of the source buffer divided by the desired data rate.

## Slide 6: Relationships I
We need to send NP packets over the network in order to transmit one buffer:
NP = NB / NMPDU Assume an integer for simplicity.
NT = NMPDU + NOH, the total number of symbols that would have to be sent over the network to cover both the data and the overhead.

## Slide 7: QoS Parameter 2: Time Requested Per Allocation Period, TAGS
TAGS is the total time requested for GTS allocated in order to send one buffer.
TAGS = ( NP ) ( NT / NE fS ).
For the sending NP packets,
of equivalent size, NT = ( NMPDU + NOH )
with a PHY encoding of NE bits per symbol
and a PHY symbol rate of fS.

## Slide 8: Relationships 2
1 / NE fS is a constant as long as the symbol rate is unchanged.
From before: NP = NB / NMPDU
Stating the obvious: NT and NP will also be constants if the transmit packet size and the transmit buffer size both remain constant.

## Slide 9: QoS Parameter 3: maximum allocation delay, TMAD
TMAD defines an allowable time jitter to the allocation of time slots by the piconet coordinator, PNC.
The maximum allocation delay starts at the end of the allocation period, but does not affect the PNC’s reference timing of the maximum allocation delay itself. It allows some variability in position of the slot(s) that is not cumulative.

## Slide 10
TMAD
TAGS
TAP
The TAGS (blue) time is the total amount of slot time that must be allocated by the PNC within the TMAD (green) time after the PNC determined start of the TAP interval (vertical arrows).

## Slide 11: Possible PNC Slot Allocations
TAP
TMAD

## Slide 12: Comments and Issues 1
This is ISOC slot specification.
A request for a fixed offset from the beacon for low power devices will require different QoS parameters and be an ASYNC specification for fixed slots. Should this be allowed?
If a QoS request defined both the a fixed delay from the beacon and a fixed rate, it would set the beacon period. Should this “super QoS” mode be allowed?

## Slide 13: Comments and Issues 2
Any arbitrary ISOC parameters requested must take into account accommodating the beacon. The occurrence of the beacon could delay some or all of a member’s ISOC time slots beyond its requested interval.
In return, the PNC must be able guarantee a limit to the size of the beacon, therefore the CAP size also, except when no ISOC devices are present or ISOC devices are in phase with the beacon.

## Slide 14
TAP
TMAD
Beacon
Alternative 1 Start of TAP
Alternative 2 Start of TAP
Delayed Interval
The Beacon May Upset the timing of ISOC Slots

## Slide 15: TAP Adjustment to Beacon Delay
How should the TAP be adjusted if the beacon forces the slot allocation to be late. Should the next allocation be early according to the current TAP interval (Alternative 1), or should it be late and sync off the most recent slot allocation (blue) (Alternative 2)?
The user could specify if we defined the QoS parameter switch.

## Slide 16: Data Rate (fd) Only Driven QoS
    And if TSLOTi is the total slot time.
    Then:
    fs TSLOTi / TBCN  NAGS / TAP
    TSLOTi  TBCN TAGS / TAP
    TSLOTi  ( TBCN fd ) / ( fS NE UC )
    where UC is channel utilization (simplified)
    = NMPDU / ( NOH + NMPDU )

## Slide 17: Requirements for Data Rate Only QoS
The transmit buffer is large enough to accept GTS slots anywhere in the superframe.
The amount of bandwidth being requested is available based on the unused CFP time present in the superframe.
Parameters: TAP / TAGS = fd, TMAD = 0xFFFF, which will be a special value indicating “use entire CFP”.