## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Nokia PHY submission to Task Group 4]
Date Submitted: [02 July, 2001]
Source: [Jukka Reunamäki] Company [Nokia]
Address [Visiokatu 1, P.O.Box 100, FIN-33721 Tampere, Finland]
Voice:[+358 7180 35331], FAX: [+358 7180 35935], E-Mail:[jukka.reunamaki@nokia.com]
Re: [Original document]
Abstract: [Submission to Task Group 4 for consideration as the Low Rate PHY for 802.15.4]
Purpose: [IEEE 802.15.4 PHY proposal for evaluation]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Nokia PHYsical layer submission to IEEE 802.15 Task Group 4
Presented by
Jukka Reunamäki
Nokia

## Slide 3: Contents
Nokia proposal in brief
Self-evaluation against criteria
Conclusion
Background slides

## Slide 4: The TG4 success circle
Make it
cheaper
Address the
economics
of the scale
The trillion
consumer devices
Where are the
economics of
Scale ?
How to enter into
the consumer market ?
How to
do it ?

## Slide 5: How to spark the success circle rolling?
Design the system so that in can be deployed with minor effort into devices already having Bluetooth, e.g. cell phones
Hence TG4 PHY :
  must be implementable to existing BT devices with minor complexity increment
  must allow low cost, low complexity sub dollar stand alone devices
The solution
  common RF section with Bluetooth must be possible
  but
  some Bluetooth parameters must be relaxed

## Slide 6: The 6's to Bluetooth
The proposal takes BT as the basis but adjusts the following crucial parameters to remarkably differ from BT in terms of power consumption and cost
1. FSK Modulation index increased to above 2.2 => a) relaxed requirements on the receiver and transmitter, enables the simplest and maximally integrated direct conversion receivers b) allows higher RF imperfections
2. Symbol rate dropped to 200 kbps, => a) longer symbol duration ~no inter symbol interference i.e. no need for baseband coding b) allows the reuse of BT channel raster although higher modulation index c) lower sample rate, i.e. lower peak power consumption

## Slide 7: The 6's to Bluetooth
3. Reduced TxP to –1.25 …-30 dBm=> lower power consumption, a possibility for button battery powered devices, no need for FH nor spreading
4. No frequency hopping => a) faster device discovery (inquiry) process b) lower complexity
5. Relaxed Rx IIP3 -30 dB => lowered Rx power consumption
6. Additional frequencies in the edges of the ISM band => minimal interference from BT and IEEE802.11b to the most vital device discovery frequencies of the Nokia's MAC proposal.

## Slide 8: Modulation index
FSK Modulation index increased to above 2.2
Relaxed requirements on the receiver and transmitter
  enables the simplest and maximally integrated direct conversion transceivers
  allows higher RF imperfections
Constant envelope for low power TX architecture
Spectrum efficiency sacrificed for minimum complexity and low power RX implementation

## Slide 9: Symbol rate
Symbol rate dropped to 200 kbps
  Allows the re-use of BT filters although higher modulation index
  Data rate scalability achieved with lower activity, shorter packets and possible repetition coding
  Long symbol duration results in small ISI in indoor channels
  200 kbps aggregate capacity considered adequate from application point of view

## Slide 10: Reduced TxP to –1.25 …-30 dBm
IEEE TG 4 is about low power
  lower power consumption, a possibility for button battery powered devices
  no need for FH nor spreading
Personal area applications do not need long range
  High transmit power leads to higher power consumption => and causes more interference to others
However, more range can be achieved by means of higher TX power (only -1.25 dBm proposed)
  FCC 15.249 addresses average power!
    Low duty cycles => high TX powers possible
  Using 915 MHz band means 8.5 dB gain in free space propagation

## Slide 11: No frequency hopping
Enables faster and low power consuming device discovery and connection set-up
Reduce the oscillator re-tuning overhead
lower complexity

## Slide 12: Relaxed Rx IIP3
The linearity requirement of LNA in Bluetooth is the key disenabler for using Bluetooth with button batteries
Relaxation in interference susceptibility accepted to alleviate RX linearity requirements
-32.0
-31.0
-30.0
-29.0
-28.0
-27.0
-26.0
1.0000
1.5000
2.0000
2.5000
Relative current
IIP3 (dBm)

## Slide 13: Usage of ISM band edges
Additional frequencies in the edges of the ISM band
  minimal interference from BT and IEEE802.11b to the most vital device discovery frequencies of the Nokia's MAC proposal.
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth channels
Channels of the
proposed system
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe

## Slide 14: Spread spectrum vs. narrowband
Narrowband
  Possibility for common PHY with Bluetooth
  Lower sampling rates and smaller power consumption
  More non-overlapping channels in the system band
  Less complex baseband
  Operation under FCC 15.249 (US) and ERC rec 70-03 SRD (Europe)
  Less interference prone in frequency domain

## Slide 15: Spread spectrum vs. narrowband
Spread Spectrum
  Enables +20dBm transmission
    seldom needed in low power WPAN
    narrowband also allows higher range by means of coding and/or increased Tx power with low duty cycle
  Synchronization time
    the gain not significant with respect of increased complexity and power consumption

## Slide 16: Self-evaluation against IEEE 802.15.4 criteria document (revision 5)

## Slide 17: Unit manufacturing cost ($)
Estimate: 2 $
Area of analog circuitry: 6 mm2
Gate count of digital section: 40k
Number of external parts: 5..10 pcs

## Slide 18: Interference and susceptibility
In-band (> 1st ACI) -20 dB
Out of the band -20 dBm

## Slide 19: Intermodulation resistance
Values
  IIP3 = -30 dBm
  C/IBER = 1e-4, sensitivity + 3 dB = 10 dB
PCW interferer = -52 dBm
IMD
C/I

## Slide 20: Jamming resistance
76 frequency channels unaffected
Actually, an interferer of 100 mW at the distance of 3 m blocks the receiver of the proposed system if RX P1dB < -30 dBm.)

## Slide 21: Jamming resistance cont.

## Slide 22: Jamming resistance cont.

## Slide 23: Jamming resistance cont.

## Slide 24: Jamming resistance cont.

## Slide 25: Interoperability
False, but Device sharing both 802.15.1 and the proposed system can have a common RF due to modulation schemes close to each other and similar channel center frequencies.

## Slide 26: Manufactureability and time to market
Regarding RF and BB the system shares and relaxes ideas already implemented in 802.15.1 and various paging systems.
MAC is a simple bit-pipe with carrier sensing already implemented in 802.11.
Time to market is limited by the availability of the final standard.

## Slide 27: Regulatory impact
Default is 2.45 GHz ISM band
  Operation under FCC 15.249 (US) and ERC rec 70-03 SRD (Europe)

## Slide 28: Maturity of solution
None of the approaches used in the proposed system are more complex than in currently available 802.15.1 products.

## Slide 29: Scalability
Range
  More range can be achieved by means of higher TX power
  FCC 15.249 addresses average power!
Cost
  Device classes potentially provide possibility for cost optimization
Data rate
  Scalability implemented through packet sizing and duty cycles
Frequency band of operation
  Narrow transmit bandwidth basically allows usage of a number of different frequency bands, e.g. 433 MHz (Europe), 868 MHz (Europe), 915 (US), 2.4 GHz (global)

## Slide 30: Location awareness
Mainly an upper layer issue, but point-to-any-point topology enables determining of location relative to other devices

## Slide 31: Application dependent power consumption
Sleep 22 W
Idle, device registeration and network infrasture management 60 W (based on 0.34% duty cycle)

## Slide 32: Size and form factor
Total IC area ~ 6 mm2
Package size (W x L x H) 6 x 6 x 1 mm3
External component count (SMD passives) 5...10 pcs
Size of SMD passives 0.5 x 1.0 x 0.5 mm3/pc
Module size (without antenna) 1 cm2 with components on both sides of PWB

## Slide 33: Frequency band
Default is 2.45 GHz ISM band
  83 channels, center frequencies at 2401 + k x 1 MHz, where k = 0...82
Optional bands: 902-928 MHz in US and 433.050 - 434.790 MHz in Europe
  Smaller propagation loss, potentially less interference
Any band wide enough and available for short-range devices can be used

## Slide 34: Number of simultaneously operating full-throughput PANs
Blocking not considered!
Before any filtering C/I = 0 dB, but ACI suppression is 15 dB and hence transmission with BER = 1e-4 is ensured in other than in the co-located channel.
There are 77 unicast channel frequencies

## Slide 35: Signal acquisition method
Preamble should be long enough to assist frequency and symbol synchronization
  Preferably zero DC
Sync word indicates the start of the header
  3 consecutive Barker codes of length 7
Header and payload left to be defined in the MAC layer
Preamble
32 bits
Header + payload + strong CRC's etc.
(defined by MAC layer)
Sync
word
21 bits

## Slide 36: Sensitivity
Power level: -89.5 dBm
PER: 0.8% (10 byte packet)
BER: 1e-4

## Slide 37: Power consumption
TX analog/digital parts (active peak) 10.5 mW / 1.5 mW
  Assuming Pout = -20 dBm
RX analog/digital parts (active peak) 9.5 mW / 2.0 mW
  Assuming NF = 15 dB, IIP3 = -30 dBm
Total idle time power consumption (analog & digital) 22 W
Average consumption (based on 0.34% duty cycle) 60 W

## Slide 38: Self-evaluation conclusions
Nokia IEEE 802.15.4 physical layer proposal comprising
  Primarily operates in the 2.45 GHz ISM band, 1 MHz channel separation
  200 kbps maximum data rate, scalability achieved by means of packet sizing
  Operation range from 1 to 10 meters
Spectrum efficiency, link performance and interference tolerance sacrificed for minimum power, minimum complexity PHY implementation

## Slide 39: Background slides

## Slide 40: General PHY requirements
Minimized RF and BB complexity
Very low cost
Relaxed performance requirements
Strongly minimized power consumption
Unlicensed operation frequency band
FCC and ETSI compliance
Mature, low risk approach

## Slide 41: Power consumption and operation time
Idle time power consumption assumed to be 1/1000 of power consumption in active mode.

## Slide 42: Implications of power consumption requirements
Transceiver should consume about 10-25 times less power than current Bluetooth approaches to be feasible for button batteries
  It is possible with very low duty cycles (<< 1%)
  In active mode the whole transceiver including digital processing should consume only ~4 mW with small button cell and ~12 mW with large button cell
  Idle time dominates power consumption in case of low duty cycles
  Synthesizer is also critical

## Slide 43: Channel structure in 2400-2483.5 MHz
83 channels, center frequencies at 2401 + k x 1 MHz, where k = 0...82
    Compatibility with Bluetooth
    Outermost channels benefitially located
2400
2401
2402
2403
2481
2482
2483
2480
Bluetooth channels
Channels of the
proposed system
IEEE 802.11b channel
in North America and Europe
IEEE 802.11b channel
in Europe

## Slide 44: Device classes for different applications
Smaller TX power => smaller operating space and power consumption
Fixed frequency => potentially simpler implementation
Generally, sensitivity is not the dominant item from power consumption point of view if the requirements are reasonable (i.e. NF  15)

## Slide 45: Bit rate and modulation
Maximum physical layer bit rate 200 kbps
    Data rate scalability achieved with lower activity, shorter packets and possible repetition coding
    Long symbol duration results in small ISI in indoor channels
    200 kbps aggregate capacity considered adequate from application point of view
2GFSK modulation with modulation index h = 2...3 and BT = 0.5
    Constant envelope for low power TX architecture
    Spectrum efficiency sacrificed for minimum complexity and low power RX implementation
    Relaxed requirements for phase noise and I/Q imperfections

## Slide 46: Modulation spectrum
2GFSK modulation with modulation index h = 2.5, BT = 0.5

## Slide 47: Transmit spectrum with different modulation indexes

## Slide 48: Performance in AWGN channel
C/NBER = 1e-3 = 13 dB
C/NBER = 1e-3 = 13.5 dB
2GFSK, modulation index h = 2.5, BT = 0.5,
f-3 dB, highpass = 50 kHz, f-3 dB, lowpass = 300 kHz
C/NBER = 1e-4 = 15.0 dB
C/NBER = 1e-4 = 14.5 dB

## Slide 49: Performance in flat fading Rayleigh channel
X % signifies that raw BER is equal to or better than that indicated by the curves at a corresponding C/N value in X % of flat fading Rayleigh channels.

## Slide 50: Channel coding
By default no channel coding of any kind utilized
    Coding does not help much when the transmitted frame is overlapped by high power interference in both frequency and time
    Increases baseband complexity
    No need to extend range by means of coding
    Real-time services are not in focus
Data reliability ensured by 32-bit CRC checks (providing residual error rate down to 1e-9) and upper layer retransmissions
If needed, repetition coding can be used

## Slide 51: Link budget at 2.45 GHz
Fading margin of 13 dB ensures that C/N = 14.5 dB or better in > 95% of
the channels at range of 25/10/3/1 m.

## Slide 52: Example: link budget of unbalanced link with directive antenna
A link formed between devices with different capabilities e.g. based on power supply constraints

## Slide 53: Susceptibility to interference
2.45 GHz ISM band will be congested
Low power system cannot compete with TX power
Relaxation in interference susceptibility accepted to alleviate RX linearity requirements
    RX linearity requirements similar to Bluetooth (IIP3 = -15...-20 dBm) would not result in low-power RX, since RX linearity directly affects power consumption
    In case of co-channel interference, strong adjacent channel interference, blocking or intermodulation, packets are retransmitted

## Slide 54: Intermodulation resistance – a strong function of IIP3
IMD
C/I
RX
C/I = 7 dB
TX
Bluetooth TX
Bluetooth TX

## Slide 55: Co-channel Bluetooth interference rejection

## Slide 56: Blocking when RX IIP3  -30 dBm
How far away should a simultaneous transmission occur not to block the receiver?
Assumption: P1dB  IIP3 - 10 dB
RX (IIP3 
-30 dBm)
Bluetooth TX
transmitting
at 0 dBm
TX
IEEE 802.11b
WLAN TX
transmitting
at 20 dBm
Another TX of the
proposed system
transmitting
at -10 dBm
0 m
0.3 m
1 m
10 m

## Slide 57: TX implementation example
UP-
CONVERSION
+
POWER
AMPLIFIER
CHANNEL
FILTER
DAC
LOWPASS
FILTER
DAC
90º
0º
LO

## Slide 58: RX implementation example

## Slide 59: Effect of finite I/Q image rejection